## Slide 1: CS 352 Reliability: Stop and Wait
CS 352, Lecture 9.1
http://www.cs.rutgers.edu/~sn624/352
Srinivas Narayana

## Slide 2: Transport
Application
Transport
Network
Host-to-Net
…
FTP
HTTP
SMTP
DNS
TCP
UDP
IP
802.11
X.25
ATM
HTTPS

## Slide 3: Modularity through layering
Link: best-effort local pkt delivery
Network: best-effort global pkt delivery
Transport: provide guarantees to apps
Apps: useful user-level functions
HTTP
FTP
TFTP
NV
TCP
UDP
IP
Ether
ATM
WiFi
…

## Slide 4: How do apps get perf guarantees?
The network core provides no guarantees on packet delivery
Transport software on the endpoint oversees implementing guarantees on top of a best-effort network
Three important kinds of guarantees
  Reliability
  Ordered delivery
  Resource sharing in the network core
Transmission Control Protocol (TCP)

## Slide 5: Reliable data delivery

## Slide 6: Packet loss
Sender
Receiver
How might a sender and receiver ensure that data is delivered reliably (despite some packets being lost)?
TCP uses three mechanisms

## Slide 7: Coping with packet loss: (1) ACK
Key idea: Receiver returns an acknowledgment (ACK) per packet sent
If sender receives an ACK, it knows that the receiver got the packet.
Sender
Receiver
ACK
packet
ACK
packet

## Slide 8: Coping with packet corruption: (1) ACK
ACKs also work to detect packet corruption on the way to the receiver
  One possibility: A receiver could send a negative acknowledgment, or a NAK, if it receives a corrupted packet
  Q: How to detect corrupted packet?
    One method: Checksum!
TCP only uses positive ACKs.
Sender
Receiver
NAK
packet
ACK
packet

## Slide 9: Coping with packet loss: (2) RTO
What if a packet is dropped?
Key idea: Wait for a duration of time (called retransmission timeout or RTO) before re-sending the packet
In TCP, the onus is on the sender to retransmit lost data when ACKs are not received
Note that retransmission works also if ACKs are lost or delayed
Sender
Receiver
ACK
RTO
Retransmission

## Slide 10: How should the RTO be set?
A good RTO must predict the round-trip time (RTT) between the sender and receiver
  RTT: the time to send a single packet and receive a (corresponding) single ACK at the sender
Intuition: If an ACK hasn’t returned, and our (best estimate of) RTT has elapsed, the packet was likely dropped.
RTT can be measured directly at the sender. No receiver involvement needed.
Sender
Receiver
ACK
RTO

## Slide 11: Coping with packet duplication
Sender
Receiver
ACK
RTO
If ACKs delayed beyond the RTO, sender may retransmit the same data
  Receiver wouldn’t know that it just received duplicate data from this retransmitted packet
Add some identification to each packet to help distinguish between adjacent transmissions
  This is known as the sequence number
Duplicate
packet received!
(Receiver doesn’t know…)

## Slide 12: Coping with packet loss: (3) Sequence #s
Sender
Receiver
ACK
RTO
A bad scenario: Suppose an ACK was delayed beyond the RTO; sender ended up retransmitting the packet.
At the receiver: sequence number helps disambiguate a fresh transmission from a retransmission
  Sequence number same as earlier: retransmission
  Fresh sequence number: fresh data
0
0

## Slide 13: Coping with packet loss: (3) Sequence #s
Sender
Receiver
RTO
A good scenario: packet successfully received and ACK returned within RTO
Sequence numbers of successively transmitted packets are different
Receiver knows these are not duplicate, because sequence numbers are different
SEQ 0
SEQ 1
ACK
RTO

## Slide 14: Coping with packet loss: (3) Sequence #s
Sender
Receiver
RTO
A good scenario: packet successfully received and ACK returned within RTO
Sequence numbers of successively transmitted packets are different
Further, the receiver informs the sender which packet was ACK’ed using an ACK sequence number
RTO
Receiver knows these are not duplicate, because sequence numbers are different
ACK
ACK 0
ACK 1
SEQ 0
SEQ 1

## Slide 15: Q: What is the seq# of third packet?
Sender
Receiver
ACK 1
RTO
Goal: Avoid ambiguity on which packet was received/ACK’ed from both the sender and receiver’s perspective
One possibility: keep incrementing the seq #: 2, 3, …
Alternative: since seq # 0 was successfully ACK’ed earlier, it is OK to reuse seq #0 for next transmission.
  Seq #s reused if enough time elapsed
SEQ 0
SEQ 1
ACK 0
???
RTO

## Slide 16: Summary: Stop-and-Wait Reliability
Sender sends a single packet, then waits for an ACK to know the packet was successfully received. Then the sender transmits the next packet.
If ACK is not received until a timeout (RTO), sender retransmits the packet
Disambiguate duplicate vs. fresh packets using sequence numbers that change on “adjacent” packets
Sender
Receiver
RTT
RTO
SEQ 0
ACK 0
SEQ 1
Retransmit

## Slide 18: CS 352 Reliability: TCP Metadata
CS 352, Lecture 9.2
http://www.cs.rutgers.edu/~sn624/352
Srinivas Narayana

## Slide 19: Review: Stop-and-Wait Reliability
Sender sends a single packet, then waits for an ACK to know the packet was successfully received. Then the sender transmits the next packet.
If ACK is not received until a timeout (RTO), sender retransmits the packet
Disambiguate duplicate vs. fresh packets using sequence numbers that change on “adjacent” packets
Sender
Receiver
RTT
RTO
SEQ 0
ACK 0
SEQ 1
Retransmit

## Slide 20: Q1: Where are seq & ACK #s written to?
Naturally, in the packet header!

## Slide 21: TCP header structure
Source port, destination port (connection demultiplexing)
Size of the TCP header (in 32-bit words)
Basic error detection through checksums (similar to UDP)

## Slide 22: TCP header structure
Identifies data in the packet from sender’s perspective
TCP uses byte seq #s
Identifies the data being ACKed from the receiver’s perspective.
TCP uses next seq # that the receiver is expecting.

## Slide 23: A TCP exchange
A small demo