## Slide 1
Lecture 4, Computer Networks (198:552)
Transport

## Slide 2: Network Core: Best effort packet delivery
Routers (typically) make no guarantees about
… whether packets get delivered
… whether packets will reach without being corrupted
… whether packets will reach the other side in order
… the app performance experienced by a user
So how are we still able to get good performance over the Internet?

## Slide 3: Network Edge: Application guarantees
How should endpoints provide guarantees to applications?
Transport software on the endpoint is in charge of implementing guarantees on top of an unreliable network
  Reliability
  Ordered delivery
  Packet delay not exceeding 50 ms?

## Slide 4: Modularity through layering
Link: best-effort local pkt delivery
Network: best-effort global pkt delivery
Transport: provide guarantees to apps
Apps: useful user-level functions
HTTP
FTP
TFTP
NV
TCP
UDP
IP
Ether
ATM
WiFi
…
Protocols “stacked” in endpoint and router software/hardware

## Slide 5: Transmission Control Protocol (TCP)
Multiplexing/demultiplexing
  Determine which conversation a given packet belongs to
  All transports need to do this
Reliability and flow control
  Ensure that data sent is delivered to the receiver application
Ordered delivery
  Ensure bits pushed by sender arrive at receiver app in order
  Q: why would packets ever be received out of order?
Congestion control
  Ensure that data sent doesn’t overwhelm network resources
  Q: which network resource?

## Slide 6: Reliable data delivery

## Slide 7: Packet loss
Sender
Receiver
How might a sender and receiver ensure that data is delivered reliably (despite some packets being lost)?
TCP uses two mechanisms

## Slide 8: Coping with packet loss: (1) ACK
Key idea: Receiver returns an acknowledgment (ACK) per packet sent
If sender receives an ACK, it knows that the receiver got the packet.
What if a packet was lost and ACK never arrives?
Sender
Receiver
ACK
packet
ACK
packet

## Slide 9: Coping with packet loss: (2) RTO
Key idea: Wait for a duration of time (called retransmission timeout or RTO) before re-sending the packet
In TCP, the onus is on the sender to retransmit lost data when ACKs are not received
Retransmission works also if ACKs are lost or delayed
Sender
Receiver
ACK
RTO

## Slide 10: Sending one packet per ACK enough?
Should sender wait for an ACK before sending another packet?
Consider:
  Round-trip-time: 100 milliseconds
  Packet size: 12,000 bits
  Link rate: 12 Mega bits/s
  Suppose no packets are dropped
At what rate is the sender getting data across to the receiver?
Sender
Receiver
RTT
120 Kilo bit/s (1% of link rate)

## Slide 11: Amount of “in-flight” data
We term the amount of unACKed data as data “in flight”
With just one packet in flight, the data rate is limited by the packet delay (RTT) rather than available bandwidth (link rate)
Idea: Keep many packets in flight!
More packets in flight improves throughput

## Slide 12: Keeping many packets in flight
In our example before, if there are, say 4 packets in flight, throughput is 480 Kbits/s!
We just improved the throughput 4 times by keeping 4 packets in flight
Trouble: what if some packets (or ACKs) are dropped?
How should the sender retransmit?
Sender
Receiver
RTT

## Slide 13: Keeping track of packets (and ACKs)
Every packet contains a sequence number
  (In reality, every byte has a sequence number)
ACK echoes the sequence number of the packet that is acknowledged
Sender retransmits only those packets whose sequence numbers haven’t been ACKed
Sender
Receiver
1
2
3
4
1
2
3
4
5

## Slide 14: Ordered Delivery

## Slide 15: Reordering at the receiver side
Let’s suppose receiver gets packets 1, 2, and 4, but not 3 (dropped)
Suppose you’re trying to download a Word document containing a report
What would happen if transport at the receiver directly presents packets 1, 2, and 4 to the Word application?
Sender
Receiver
1
2
3
4
1
2
4
5

## Slide 16: Reordering at the receiver side
Reordering can also happen due to packets taking different paths through a network
Receiver needs a general strategy to ensure that data is presented to the application in order of transmission
Sender
Receiver
1
2
3
4
1
2
4
5
3

## Slide 17: Buffering at the receiver side
1
2
1
2
4
1
2
4
3
Application can read up to here
Network writes here
Memory on the receiver machine

## Slide 18: Buffering at the receiver side
The TCP receiver uses a memory buffer to hold packets until they can be read by the application in order
This process is known as TCP reassembly

## Slide 19: Implications of TCP reassembly
Packets cannot be delivered to an application if there is an in-order packet missing from the receiver’s buffer
  TCP application throughput will suffer if there is too much packet reordering in the network
There is only so much the receiver can buffer before dropping subsequent packets (even if successfully arrived at receiver)
  A TCP sender can only send as much as the free receiver buffer space available before packets are dropped at the receiver
  This number is called the receiver window size
  TCP is said to implement flow control

## Slide 20: Congestion control

## Slide 21: How should multiple endpoints share net?
It is difficult to know where the bottleneck link is
It is difficult to know how many other endpoints are using that link
Endpoints may join and leave at any time
Network paths may change over time, leading to different bottleneck links (with different link rates) over time

## Slide 22
The approach that the Internet takes is to use a distributed algorithm to converge to an efficient and fair outcome.

## Slide 23
The approach that the Internet takes is to use a distributed algorithm to converge to an efficient and fair outcome.
No one can centrally view or control all the endpoints and bottlenecks in the Internet.
Every endpoint must try to reach a globally good outcome by itself: i.e., in a distributed fashion.

## Slide 24
The approach that the Internet takes is to use a distributed algorithm to converge to an efficient and fair outcome.
If there is spare capacity in the bottleneck link, the endpoint should use it.

## Slide 25
The approach that the Internet takes is to use a distributed algorithm to converge to an efficient and fair outcome.
If there are N endpoints sharing a bottleneck link, they should be able to get equitable shares of the link’s capacity.

## Slide 26
The approach that the Internet takes is to use a distributed algorithm to converge to an efficient and fair outcome.
So, how to achieve this?

## Slide 27: Feedback from network offers clues…
Signals
  Packets being dropped (ex, RTO fires)
  Packets being delayed
  Rate of incoming ACKs
Knobs
  What can you change to “probe” the sending rate?
  Suppose receiver buffer is unbounded:
    The amount of in-flight data is called the congestion window
  Increase congestion window: e.g., by x or by a factor of x
  Decrease congestion window: e.g., by x or by a factor of x
“Implicit” feedback signals
(more on explicit signals later)

## Slide 28
Time for an activity

## Slide 29: ACK clocking: steady state behavior

## Slide 30: But how to get to steady state?
Slow start?
Additive increase, multiplicative decrease (AIMD)
Congestion
Window
halved
Loss
time

## Slide 31: Why AIMD?
(bDx1+aI, bDx2+aI)
User 1: x1
User 2: x2
fairness
line
efficiency
line
(x1,x2)
(bDx1,bDx2)
Converges to fairness
Converges to efficiency
Increments to rate smaller as fairness increases

## Slide 32: Packet Scheduling

## Slide 33: Are endpoint algorithms alone enough?
What if an endpoint is malicious or buggy?
Want the network core to do something more about resource allocation than best effort

## Slide 34: Network model
Bottleneck queue
(max size B)
Queuing delay
Flows
Packet-switched core network
Link rate

## Slide 35: First-in first-out (FIFO) queue + tail-drop
1
1
2
a
b
a
2
b
Buffer size
Dropped packets

## Slide 36: First-in first-out (FIFO) queue + tail-drop
1
2
a
b
3
4
5
6
1
a
2
3
5
6
4
b
Buffer size
Dropped packets
Head of line blocking (HOL)
Can you guess what happens in the next round-trip time interval?

## Slide 37: ACK-clocking makes it worse: lucky case
7
8
b
c
9
10
11
12
7
b
8
9
11
12
10
Buffer size
Dropped packets
13
13

## Slide 38: ACK-clocking makes it worse: unlucky case
7
8
b
c
9
10
11
12
7
13
8
9
11
12
10
b
Buffer size
Dropped packets
13

## Slide 39: Network monopolized by “bad” endpoints
An ACK signals the source of a free router buffer slot
  Further, ACK clocking means that the source transmits again
Contending packet arrivals may not be random enough
  Blue flow can’t capture buffer space for a few round-trips
Sources which sent successfully earlier get to send again
A FIFO tail-drop queue incentivizes sources to misbehave!

## Slide 40: Packet scheduling on routers
We will discuss packet scheduling algorithms implemented on routers in detail later in this course.
Goal: Achieve a predetermined resource allocation regardless of endpoint behavior
How to make such allocation “efficient”?
  Implement on routers at high speeds
  Achieve equitable sharing of network bandwidth & queues
  Use available bandwidth effectively