## Slide 1: The Network Layer: Protocols DHCP, ICMP, NAT, IPv6
CS 352, Lecture 14, Spring 2020
http://www.cs.rutgers.edu/~sn624/352
Srinivas Narayana

## Slide 2: Course announcements
Quiz 5 due Tuesday
  Will be released later today
Recording of Wednesday’s lecture available
  See Piazza for details
  We are working on converting video into a format that’s more accessible than WebEx’s ARF… stay tuned

## Slide 3: Where we are: The network layer
Application
Transport
Network
Host-to-Net
…
FTP
HTTP
SMTP
DNS
TCP
UDP
IP
802.11
X.25
ATM
HTTPS
The network layer exists on every endpoint and router.

## Slide 4: Review of concepts
Router components
Input port: line termination, forwarding function
  Forwarding: based on IP destination.
  Longest-prefix matching
Switching fabric: memory, bus, crossbar
Output port: buffer management and scheduling
high-speed
switching
fabric
route
processor
router input ports
router output ports

## Slide 5: Poll #1
If an ISP X owns two prefixes 128.0.0.0/16 and 128.1.0.0/16, which IP prefix can the rest of the Internet use in its forwarding rules to route data towards X?
  (a) 128.0.0.0/8
  (b) 128.0.0.0/24
  (c) 128.0.0.0/15
  (d) None of the above

## Slide 6: Poll #2
Suppose a router has two forwarding rules. Which port should pkt with destination IP 192.168.0.56 go out of?
    192.168.0.0/16 -> port 1
    192.168.0.0/24 -> port 2
  (a) port 1
  (b) port 2
  (c) neither port
  (d) both ports

## Slide 7: The Internet Protocol (IP)

## Slide 8: IP datagram format
ver
length
32 bits
data
(variable length,
typically a TCP
or UDP segment)
16-bit identifier
header
checksum
time to
live
32 bit source IP address
IP protocol version
number
header length
(bytes)
max number
remaining hops
(decremented at
each router)
for
fragmentation/
reassembly
total datagram
length (bytes)
upper layer protocol
to deliver payload to
head.
len
type of
service
“type” of data
flgs
fragment
offset
upper
layer
32 bit destination IP address
Options (if any)
E.g. timestamp,
record route
taken, specify
list of routers
to visit.
how much overhead with TCP?
20 bytes of TCP
20 bytes of IP
= 40 bytes + app layer overhead

## Slide 9: IP Fragmentation & Reassembly
network links have MTU (max.transfer size) - largest possible link-level frame.
  different link types, different MTUs
large IP datagram divided (“fragmented”) within net
  one datagram becomes several datagrams
  reassembled only at the destination, at the IP layer
  IP header bits used to identify, order related fragments
fragmentation:
in: one large datagram
out: 3 smaller datagrams
reassembly

## Slide 10: IP Fragmentation and Reassembly
ID
=x
offset
=0
fragflag
=0
length
=4000
ID
=x
offset
=0
fragflag
=1
length
=1500
ID
=x
offset
=185
fragflag
=1
length
=1500
ID
=x
offset
=370
fragflag
=0
length
=1040
One large datagram becomes
several smaller datagrams
Example
4000 byte datagram
MTU = 1500 bytes
(includes IP headers)
1480 bytes in data field
offset =
1480/8

## Slide 11: Poll #3
Which header does the IP source and destination live in?
  (a) TCP header
  (b) IP header
  (c) Application-layer header
  (d) None of the above

## Slide 12: Dynamic Host Configuration
How does an endpoint get its IP address?

## Slide 13: IP addresses: how to get one?
Q: How does a host get IP address?
Hard-coded by system admin in a file
  UNIX: /etc/network/interfaces
  Windows: controlpanel -> network -> configuration -> tcp/ip -> properties
DHCP: Dynamic Host Configuration Protocol: dynamically get address from as server
  “plug-and-play”

## Slide 14: Similar bootstrapping problems
How does a host get its IP address?
How does a host know its local DNS server?
How does a host know its subnet mask?
How does a host know which router is its “gateway” to other networks?

## Slide 15: DHCP: Dynamic Host Configuration Protocol
goal: allow host to dynamically obtain its IP address from network server when it joins network
  can renew its lease on address in use
  allows reuse of addresses (only hold address while connected/“on”)
  support for mobile users who want to join network
DHCP overview:
  host broadcasts “DHCP discover” msg [optional]
  DHCP server responds with “DHCP offer” msg [optional]
  host requests IP address: “DHCP request” msg
  DHCP server sends address: “DHCP ack” msg

## Slide 16: DHCP client-server scenario
223.1.1.0/24
223.1.2.0/24
223.1.3.0/24
223.1.1.1
223.1.1.3
223.1.1.4
223.1.2.9
223.1.3.2
223.1.3.1
223.1.1.2
223.1.3.27
223.1.2.2
223.1.2.1
DHCP
server
arriving DHCP
client needs
address in this
network

## Slide 17: DHCP client-server scenario
DHCP server: 223.1.2.5
arriving
client
DHCP discover
src : 0.0.0.0, 68
dest.: 255.255.255.255,67
yiaddr: 0.0.0.0
transaction ID: 654
DHCP offer
src: 223.1.2.5, 67
dest: 255.255.255.255, 68
yiaddrr: 223.1.2.4
transaction ID: 654
lifetime: 3600 secs
DHCP request
src: 0.0.0.0, 68
dest:: 255.255.255.255, 67
yiaddrr: 223.1.2.4
transaction ID: 655
lifetime: 3600 secs
DHCP ACK
src: 223.1.2.5, 67
dest: 255.255.255.255, 68
yiaddrr: 223.1.2.4
transaction ID: 655
lifetime: 3600 secs
Broadcast: is there a DHCP server out there?
Broadcast: I’m a DHCP server! Here’s an IP address you can use
Broadcast: OK. I’ll take that IP address!
Broadcast: OK. You’ve got that IP address!

## Slide 18: DHCP Protocol
Server 1
Server 2
Client
DHCPDISCOVER
DHCPDISCOVER
DHCPOFFER
DHCPOFFER
DHCPREQUEST
DHCPREQUEST
DHCPACK
Collects replies
Selects server 2

## Slide 19: DHCP: more than IP addresses
DHCP can return more than just allocated IP address on subnet:
  address of first-hop router for client to reach other subnets
    Also called the gateway router
  name and IP address of the local DNS server
  subnet mask of the IP network the host is on
    Useful to know whether other endpoint is inside or outside the current IP network

## Slide 20: DHCP Relay Agents
DHCP relay agents allow DHCP servers to handle requests from other subnets
DHCP
Relay
Agent
Client
IP
Gateway
Router
IP
Gateway
Router
DHCP
Server

## Slide 21: DHCP: An example
connecting laptop needs its IP address, addr of first-hop router, addr of DNS server: use DHCP
router with DHCP
server built into
router
DHCP request encapsulated in UDP, encapsulated in IP, encapsulated in 802.1 Ethernet
Ethernet frame broadcast (dest: FFFFFFFFFFFF) on LAN, received at router running DHCP server
Ethernet demuxed to IP demuxed, UDP demuxed to DHCP
168.1.1.1
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
DHCP
DHCP
DHCP
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
DHCP
DHCP
DHCP

## Slide 22: DHCP: An example
router with DHCP
server built into
router
168.1.1.1
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
DHCP
DHCP
DHCP
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
DHCP
DHCP
DHCP
DHCP server formulates DHCP ACK containing client’s IP address, subnet mask, IP address of first-hop router for client, name & IP address of DNS server
encapsulation of DHCP server, frame forwarded to client, demuxing up to DHCP at client
client now knows its IP address, name and IP address of DNS server, IP address of its first-hop router

## Slide 23: Poll #4
What functions does the DHCP protocol serve?
  (a) discovering a usable IP address when a host joins
  (b) discovering the local DNS server address
  (c) discovering the gateway router of the local IP network
  (d) all of the above

## Slide 24: Poll #5
When a host joins a new network, how does it know the IP address of the DHCP server?
  (1) this is a static configuration on all endpoints
  (2) it broadcasts a message to discover DHCP servers
  (3) neither of the above

## Slide 25: Summary
IP addresses don’t have to be manually configured into hosts
DHCP allows “ignorant” hosts to receive IP addresses (and more) at start-up time
DHCP solves important bootstrapping problems in attaching new hosts to a network

## Slide 26: Internet Control Message Protocol (ICMP)

## Slide 27: ICMP
Protocol for error detection and reporting
    tightly coupled with IP, unreliable
ICMP messages delivered in IP packets
ICMP functions:
  Announce reachability and network errors
  Announce “time exceeded” errors for IP packets
  Announce network congestion
ICMP assists network troubleshooting in general

## Slide 28: ICMP message
IP header
Source, Destination Address, TTL, ...
ICMP MSG
Message type, Code, Checksum,
Data

## Slide 29: ICMP: Internet Control Message Protocol
Type Code description
0 0 echo reply (ping)
3 0 dest. network unreachable
3 1 dest host unreachable
3 2 dest protocol unreachable
3 3 dest port unreachable
3 6 dest network unknown
3 7 dest host unknown
4 0 source quench (congestion
control - not used)
8 0 echo request (ping)
9 0 route advertisement
10 0 router discovery
11 0 TTL expired
12 0 bad IP header
Time for an activity!

## Slide 30: Specific uses of ICMP
Echo request reply
  Can be used to check if a host is alive
Destination unreachable
  Invalid address and/or port
TTL expired
  Routing loops, or too far away

## Slide 31: Ping
Uses ICMP echo request/reply
Source sends ICMP echo request message to the destination address
Destination replies with an ICMP echo reply message containing the data in the original echo request message
Source can calculate round trip time (RTT) of packets
If no echo reply comes back, then the destination is unreachable

## Slide 32: Ping (cont’d)
R1
R2
R3
A
B
Time
Echo request
Echo reply

## Slide 33: Ping example

## Slide 34: Traceroute
Traceroute records the route that packets take
A clever use of the IP TTL (time to live) field
In general, when a router receives a packet, it decrements the TTL on that packet
If TTL=0, router sends an ICMP time exceeded message back to sender
traceroute progressively increases TTL of the packets it sends out
  Every time an ICMP time exceeded message is received, record the sender’s (router’s) address
  Repeat until the destination host is reached or an error message occurs
If packet reaches the destination, the dest host usually sends an ICMP port unreachable

## Slide 35: Traceroute (cont’d)
R1
R2
R3
A
B
TTL=1, Dest = B,
port = invalid
TTL=2, Dest = B
TTL=3, Dest = B
TTL=4, Dest = B
Te (R1)
Te (R2)
Te (R3)
Pu (B)
Time
Te = Time exceeded
Pu = Port unreachable

## Slide 36: Traceroute example

## Slide 37: Poll #6
What’s the IP header field that traceroute changes for each packet that it sends out to a given destination?
  (1) IP source address
  (2) IP source port
  (3) IP TTL
  (4) IP length

## Slide 38: Network Address Translation (NAT)
How do you survive in a society where names are scarce?

## Slide 39: NAT: Network Address Translation
10.0.0.1
10.0.0.2
10.0.0.3
10.0.0.4
138.76.29.7
local network
(e.g., home network)
10.0.0/24
rest of
Internet
All datagrams leaving local
network have same source IP address: 138.76.29.7, with
different source IP port numbers

## Slide 40: NAT: Network Address Translation
10.0.0.1
10.0.0.2
10.0.0.3
S: 10.0.0.1, 3345
D: 128.119.40.186, 80
1
10.0.0.4
138.76.29.7
1: host 10.0.0.1
sends datagram to
128.119.40.186, 80
NAT translation table
WAN side addr LAN side addr
138.76.29.7, 5001 10.0.0.1, 3345
…… ……
S: 128.119.40.186, 80
D: 10.0.0.1, 3345
4
S: 138.76.29.7, 5001
D: 128.119.40.186, 80
2
2: NAT router
changes datagram
source addr from
10.0.0.1, 3345 to
138.76.29.7, 5001,
updates table
S: 128.119.40.186, 80
D: 138.76.29.7, 5001
3
3: Reply arrives
dest. address:
138.76.29.7, 5001
4: NAT router
changes datagram
dest addr from
138.76.29.7, 5001 to 10.0.0.1, 3345

## Slide 41: NAT: Network Address Translation
Features: local network uses just one IP address as far as outside world is concerned:
  range of addresses not needed from ISP: just one IP address for all devices
  can change addresses of devices in local network without notifying outside world
  can change ISP without changing addresses of devices in local network
  Devices inside local network not explicitly addressable
  Devices inside local network invisible to the outside world (a security plus) unless the device inside connects first.
Your home WiFi router uses NATs.
If you’re home, you’re behind a NAT right now.

## Slide 42: The impact of NATs

## Slide 43: NAT: Network Address Translation
16-bit port-number field:
  60,000 simultaneous connections with a single LAN-side address!
NAT is controversial:
  Routers should only work upto the network layer, not transport ports!
  violates “end-to-end argument”
    NAT must be taken into account by app designers
    e.g., P2P applications like skype
  Purists: address shortage should instead be solved by IPv6

## Slide 44: Think about…
How do the hosts inside the home network get their IP addresses?
How does your home router get its externally visible IP address?

## Slide 45: Poll #7
The translation table at the NAT router contains
  (1) Local IP address
  (2) Local IP port
  (3) Remote IP address
  (4) Remote IP port
  (5) All of the above

## Slide 46: Poll #8
Network Address Translation
  (1) reduces the demand for fresh IPv4 addresses
  (2) keeps internal IP addresses hidden from the outside world
  (3) requires support from the NAT gateway router
  (4) all of the above

## Slide 47: Internet Protocol v6 (IPv6)

## Slide 48: Recent Developments: IPv6
IPv4 has limited address space (32 bits) and is running out of addresses. 32 bits are not enough!
More devices: phones, watches, your refrigerator(!), …
Real-time traffic and mobile users are also becoming more common
IP version 6

## Slide 49: IPv6: Main changes from IPv4
Large address space:
  128-bit addresses (16 bytes)
  Allows up to 340,282,366,920,938,463,463,374,607,431,768,211,456 unique addresses (3.4 x 10 38 )
Fixed length headers (40 bytes)
  Improves the speed of packet processing in routers
IPv6 “options” processing happens through a separate mechanism

## Slide 50: IPv6 datagram format
priority: identify priority among datagrams in flow
flow Label: identify datagrams in same “flow”
(concept of“flow” left undefined)
next header: identify upper layer protocol for data
data
destination address
(128 bits)
source address
(128 bits)
payload len
next hdr
hop limit
flow label
pri
ver
32 bits

## Slide 51: Other changes from IPv4
checksum: removed entirely to reduce processing time at each hop
options: allowed, but outside of header, indicated by “Next Header” field
ICMPv6: new version of ICMP
  additional message types, e.g. “Packet Too Big”
  multicast group management functions

## Slide 52: IPv4 vs IPv6: Can you tell the differences?

## Slide 53: IPv6 Flows
Support for “flows”
  Flows help support real-time service in the Internet
  A “flow” is a number in the IPv6 header that can be used by routers to see which packets belong to the same stream
  Guarantees can then be assigned to certain flows
  Example:
    Packets from flow 10 should receive rapid delivery
    Packets from flow 12 should receive reliable delivery

## Slide 54: IPv6 Addresses
Classless addressing/routing (similar to CIDR)
Notation: xx:xx:xx:xx:xx:xx:xx:xx
  x = 4-bit hex number
  contiguous 0s are compressed: 47CD::A456:0124
  IPv6 compatible IPv4 address: ::128.64.18.87
    First 96 bits are 0
  Global unicast addresses start with 001….
  2000::/3 prefix

## Slide 55: IPv6: Adoption
Google: 8% of clients access services via IPv6
NIST: 1/3 of all US government domains are IPv6 capable
Long (long!) time for deployment, use
  20 years and counting!
Think of application-level changes in last 20 years: WWW, Facebook, streaming media, Skype, …
Why?