## Slide 1: Administrivia
Review 1 due tomorrow
  Email your reviews to me
Office hours on Thursdays 10—12
MUD: Send me your top 1—3 questions on this lecture

## Slide 2
Lecture 5, Computer Networks (198:552)
Packet Scheduling

## Slide 3: Resource allocation in the core
Edge: Run transports to provide app guarantees
Core: Transmit packets with best-effort guarantees
The Internet

## Slide 4: Resource allocation in the core
Edge: Run transports to provide app guarantees
Core: Transmit packets with best-effort guarantees
But what about malicious or buggy endpoints?
The Internet

## Slide 5: Network model
Bottleneck queue
(max size B)
Queuing delay
Flows
Packet-switched core network
Link rate

## Slide 6: First-in first-out (FIFO) queue + tail-drop
1
1
2
a
b
a
2
b
Buffer size
Dropped packets

## Slide 7: First-in first-out (FIFO) queue + tail-drop
1
2
a
b
3
4
5
6
1
a
2
3
5
6
4
b
Buffer size
Dropped packets
Head of line blocking (HOL)

## Slide 8: What happens in the next round-trip time interval?

## Slide 9: ACK-clocking makes it worse: lucky case
7
8
b
c
9
10
11
12
7
b
8
9
11
12
10
Buffer size
Dropped packets
13
13

## Slide 10: ACK-clocking makes it worse: unlucky case
7
8
b
c
9
10
11
12
7
13
8
9
11
12
10
b
Buffer size
Dropped packets
13

## Slide 11: Network monopolized by “bad” endpoints
An ACK signals the source of a free router buffer slot
  Further, ACK clocking means that the source transmits again
Contending packet arrivals may not be random enough
  Blue flow can’t capture buffer space for a few round-trips
Sources which sent successfully earlier get to send again
A FIFO tail-drop queue incentivizes sources to misbehave!

## Slide 12: Goal: Better resource sharing in the core
What’s a fair resource allocation?
How to achieve a predetermined resource allocation?
  … regardless of source behavior?
How to make the allocation “efficient”?
  Use the available bandwidth effectively
  Build routers that work at high link rates
  Maybe even be a little unfair to apps to be more efficient overall

## Slide 13: Fair Resource Allocation
Allocate how? among who?

## Slide 14: Fair and efficient use of a resource
Suppose n users share a single resource
  Like the bandwidth on a single link
  E.g., 3 users sharing a 30 Gbit/s link
What is a fair allocation of bandwidth?
  Suppose user demand is “elastic” (i.e., unlimited)
  Allocate each a 1/n share (e.g., 10 Gbit/s each)
But, “equality” is not enough
  Which allocation is best: [5, 5, 5] or [18, 6, 6]?
  [5, 5, 5] is more “fair”, but [18, 6, 6] more efficient
  What about [5, 5, 5] vs. [22, 4, 4]?

## Slide 15: Fair use of a single resource
What if some users have inelastic demand?
  E.g., 3 users where 1 user only wants 6 Gbit/s
  And the total link capacity is 30 Gbit/s
Should we still do an “equal” allocation?
  E.g., [6, 6, 6]
  But that leaves 12 Gbps unused
Should we allocate in proportion to demand?
  E.g., 1 user wants 6 Gbps, and 2 each want 20 Gbit/s
  Allocate [4, 13, 13]?
Or, give the least demanding user all she wants?
  E.g., allocate [6, 12, 12]?

## Slide 16: Max-min fairness
Protect the less fortunate
  Any attempt to increase the allocation of one user
  … necessarily decreases the allocation of another user with equal or lower allocation
Fully utilize a “bottlenecked” resource
  If demand exceeds capacity, the link is fully used

## Slide 17: Max-min fairness
Progressive filling algorithm
  Grow all rates until some users stop having demand
  Continue increasing all remaining rates until link is fully utilized
If all users have elastic demands, single resource shared evenly
Link rate L
Link rate L/N
Link rate L/N
Link rate L/N
N elastic users
…

## Slide 18: Resource Allocation Over Paths
Maximum throughput: [30, 30, 0]
  Total throughput of 60, but user C starves
Max-min fairness: [15, 15, 15]
  Equal allocation, but throughput of just 45
Proportional fairness: [20, 20, 10]
  Balance trade-off between throughput and equality
  Throughput of 50, and penalize C for using 2 busy links
Three users A, B, and C
Two 30 Gbit/s links
A
B
C

## Slide 19: Scheduling and Buffer Management
7
b
8
9
11
12
10
c
Buffer size
Scheduling:
Allocating link bandwidth & queueing delays
(1) Which packet to send next?
(2) When to send the next packet?
Buffer management/Active Queue Management (AQM)
Allocating buffer capacity
Which packets to mark or drop?
When to mark or drop?

## Slide 20: Allocate fairly among who?
Traffic sources?
  Web servers, video servers, etc. need more than their fair share
Traffic destinations?
  Vulnerable to malicious sources denying service to receivers
Source-destination pairs?
  Can open up connections to many destinations
Application flows? (i.e., src + dst + transport ports)
  Malicious app can open up many such flows
Administrative entities? (e.g., Rutgers NetID, ISP, …)
  How is a router to identify packets belonging to an entity?
Abstract entity:
a flow

## Slide 21: Scheduling Algorithms
Which packet to send next?
When to send the next packet?

## Slide 22: A taxonomy
Granularity of allocation
  Per-packet vs. per-flow vs bit-by-bit
Pre-emptive vs. non-pre-emptive
  Do you interrupt the current packet/flow if another shows up?
Size-aware vs. unaware
  Do you take into account flow or packet sizes in scheduling?
Class-based vs. shared
  Are some flows strictly higher priority than others?
Work-conserving vs. non-conserving
  Do you always use spare link capacity when there is demand?
How complex is the implementation?
7
b
8
9
11
12
10

## Slide 23: Common scheduling algorithms (1/2)
FIFO over packets (example in previous slides)
Round-robin over packets of different flows
  You would have seen these in the FQ & DRR papers
Shortest Remaining Processing Time (SRPT)
  Flow-size-aware allocation which strictly prioritizes short flows
  Flow-size-unaware variant may “predict” demand using a known flow size distribution

## Slide 24: Common scheduling algorithms (2/2)
Processor sharing
  Assume each flow gets a fair share of the link every unit of time
  Ideal: each flow starts receiving service immediately upon arrival
Rate limiting
  Non-work-conserving: flow can’t send even if more demand than limit
Class-based prioritization
  Pre-determined flow classes with strict priorities over each other
  Starve low priority flows if higher priority flows are always sending
There are many variants and combinations of these!

## Slide 25: Exercise: When does a flow finish?
Consider a workload mix of “long” and “short” flows arriving at a Q
  Ex: A flow may have as few as 2 packets or as many as 105
Suppose a scheduling algorithm provides each flow:
  An average per-packet delay d (e.g., 50 ms)
  An average link bandwidth share t (e.g., 10 Mbit/s)
Which among d & t determines when a short flow finishes? Why?
  How about a long flow?
If you don’t know the workload mix, is there an optimal sch. alg.?
  If so, which one? If not, why not?

## Slide 26: Analysis and Simulation of a Fair Queueing Algorithm
ACM SIGCOMM ’89
Alan Demers, Srinivasan Keshav, and Scott Shenker

## Slide 27: An ideal to emulate: Processor sharing
Fair-share bandwidth in the most fine-grained fashion possible
  If there are N active flows, each flow gets 1/Nth of the link rate
  “Bit by bit round robin” (BR)
Implementing BR directly on routers is unrealistic. Why?
  One reason: consider the processing of the bit downstream
  E.g., where to route the bit?
…

## Slide 28: Emulate bit-by-bit round robin (BR)?
How about round robin over packets?
Unfair! A flow can use larger packets and gain larger bandwidth
Instead, determine when a packet would finish with BR
    Depends only on packet arrival time & # of active flows
    Let’s call this the “virtual finish time”
FQ: Transmit packets in the order of the virtual finish times
  Buffer management: drop pkt of the flow with the largest backlog

## Slide 29: How close is FQ to BR?
Total # bytes transmitted by a flow in BR and FQ aren’t different by more than the maximum packet size
  Independent of the number of active flows!
Why?
A “slack” parameter, delta, used to reduce the virtual finish time for inactive flows
  Doesn’t affect long-term throughput

## Slide 30: Discussion of FQ
Is the slack parameter the best method to handle “delay allocation”?
  What are the pros and cons of this method?
  Can you think of other methods?
If there are N active flows, how much per-packet work does FQ need to do to determine the next packet to schedule?
Why does the performance of a scheduling algorithm depend on the endpoint algorithm?
What happens in a network of FQs?
  Is there a variant that considers path-level resource usage?

## Slide 31: Efficient Fair Queueing using Deficit Round Robin
ACM SIGCOMM ’95
M. Shreedhar and George Varghese

## Slide 32: Problem: Complexity of implementing FQ
If there are N active flows, FQ needs to do O(log N) work to fetch the next packet to transmit
Reason: must maintain a sorted list of virtual finish times of at least the first packet of each active flow
Can we avoid maintaining a sorted list somehow?

## Slide 33: Idea: Keep track of pkt size unfairness
Basic idea: round robin over packets of different flows
Maintain an active list of flows; hash flows to a queue
Maintain a “quantum” for each queue that is refilled every round
  By the maximum packet size
Transmit as many packets as allowed by the queue’s quantum
If a packet is larger than the quantum, the flow keeps the quantum

## Slide 34: Discussion of DRR
Assume N active flows
Why is the quantum added every round the maximum pkt size?
What are the throughput guarantees provided by DRR?
  Short-term guarantees? Asymptotic?
  Elastic demands? Inelastic demands?
What are the delay guarantees provided by DRR?
  Worst case: may wait until N maximum size packets transmitted!
  Combine with class-based (strict) prioritization + contracts
How would you maintain an active flow list in hardware?

## Slide 35: Administrivia
Review 1 due tomorrow
  Email your reviews to me
Office hours on Thursdays 10—12
MUD: Send me your top 1—3 questions on this lecture