## Slide 1
Lecture 2, Computer Networks (198:552)
Fall 2019
Internet Architecture

## Slide 2: What happens when you browse?
The Internet
(1) Request gmail.com for your mail
(2) Google churns on your request
(3) Receive & display the response!

## Slide 3: But how does your laptop know where the google.com server is, and how to reach it?

## Slide 4: But how does your laptop know where the google.com server is, and how to reach it?
Addressing
Both your laptop and google.com have many addresses.

## Slide 5: But how does your laptop know where the google.com server is, and how to reach it?
Routing
There may be many kinds of networks between you and google, each using its own way to stitch together the path

## Slide 6: Addressing

## Slide 7
The Internet
Rutgers campus network
Hardware address (MAC address)
Ex: 00-15-C5-49-04-A9
Network address (IP address)
Ex: 192.168.1.4
Transport address (port)
Ex: 64058
How do I identify my network interface (device)?
Whose network am I attached to?
With which app is this conversation associated?

## Slide 8
Hardware address (MAC address)
Ex: 00-15-C5-49-04-A7
Network address (IP address)
Ex: 10.1.1.104
Transport address (port)
Ex: 4096
Application address (URL)
Ex: mail.google.com
The Internet
Google’s network

## Slide 9
Software and hardware for networking are arranged in layers.
Layering provides modularity:
Each layer has a distinct function
& interacts with other layers through well-defined interfaces.

## Slide 10: Modularity through layering
Link: best-effort local pkt delivery
Network: best-effort global pkt delivery
Transport: provide guarantees to apps
Apps: useful user-level functions
HTTP
FTP
TFTP
NV
TCP
UDP
IP
Ether
ATM
WiFi
…
Protocols “stacked” in endpoint and router software/hardware
IP is the “thin waist” of the Internet, enabling
interoperability across apps & network media

## Slide 11
Link layer
Network
Transport
Applications
The Internet
Link layer
Network
Transport
Applications
The Internet
Packet takes on info at each layer
Packet starts as an
app “payload”

## Slide 12
Link layer
Network
Transport
Applications
Link layer
Network
Transport
Applications
Link layer
Network
Link layer
Network

## Slide 13
Link layer
Network
Transport
Applications
Link layer
Network
Transport
Applications
Link layer
Network
Link layer
Network
Routers do not typically have transport or app functionality
(more on this later.)

## Slide 14
Time for an activity

## Slide 15: Where do all the addresses come from?
You, as the user, only know the application address of your destination (google.com)
Do we need all these addresses, or can we get rid of some?
  Should addresses correspond to the endpoint, or point of attachment, or to the application?
How does your laptop find all the other addresses?

## Slide 16: Addresses and what they correspond to
Transport address (TCP/UDP port): app-level conversation
Network-level address (IP address): point of attachment
Link-level address (MAC address): device

## Slide 17: Directories
Directories map a name to an address
Simplistic designs
  Central directory
  Ask everyone (e.g., flooding in ARP)
  Tell everyone (e.g., pushing /etc/hosts)
  Fix a value a priori (e.g., dst port 80 is typically HTTP)
Scalable distributed designs
  Hierarchical namespace (e.g., Domain Name System)
  Flat name space (e.g., Distributed Hash Table)

## Slide 18: Domain Name System
requesting host
cis.poly.edu
gaia.cs.umass.edu
root DNS server
local DNS server
dns.poly.edu
1
2
3
4
5
6
authoritative DNS server
dns.cs.umass.edu
7
8
TLD DNS server
Host at cis.poly.edu wants IP address for gaia.cs.umass.edu
Recursive query: #1
Iterative queries: #2, 4, 6

## Slide 19: Routing

## Slide 20: Path computation: Routing
“I know where you are, but how do I get there?”
End-to-end paths (e.g., source routing)
  Each node picks the best end-to-end path
Spanning tree (e.g., Ethernet)
  One tree that connects every pair of nodes
Shortest paths (e.g., OSPF, IS-IS, RIP)
  Shortest-path tree rooted at each node
Locally optimal paths (e.g., BGP)
  Each node selects the best among its neighbors
More on this in the next lecture…

## Slide 21: The Internet’s approach to routing
aggregate routers into regions known as “autonomous systems” (AS) (a.k.a. “domains”)
inter-AS routing
routing among AS’es
gateways perform inter-domain routing (as well as intra-domain routing)
intra-AS routing
routing among hosts, routers in same AS (“network”)
all routers in AS must run same intra-domain protocol
routers in different AS can run different intra-domain routing protocol
gateway router: at “edge” of its own AS, has link(s) to router(s) in other AS’es

## Slide 22: Interconnected ASes
3b
1d
3a
1c
2a
AS3
AS1
AS2
1a
2c
2b
1b
Intra-AS
Routing
algorithm
Inter-AS
Routing
algorithm
Forwarding
table
3c
Paths configured by both intra- and inter-AS routing algorithm
  intra-AS routing determine entries for destinations within AS
  inter-AS & intra-AS determine entries for external destinations

## Slide 23: What happens when you browse?
The Internet
(1) Request gmail.com for your mail
(2) Google churns on your request
(3) Receive & display the response!
But how did the Google server and your laptop attach to the network in the first place? How did they get assigned their addresses?

## Slide 24: The roles of the endpoint

## Slide 25: The roles of endpoint network software
Bootstrapping the host into the network
  How does the endpoint get an address?
  How does the endpoint make itself known to others?
Providing an interface to networked applications
  How do higher-level applications access the network?
  What abstractions does the host provide to apps?
Distributed resource sharing
  What roles does the host play in network resource allocation decisions?
… apart from other things.

## Slide 26: (1) Bootstrapping host into network
The lowest level address is hard-wired
  The network adapter (NIC) comes with MAC address
Higher-level addresses can be statically or dynamically configured
IP address
  Statically configured, or dynamically with DHCP
TCP port
  Pick a transient value, ex. HTTP src port
  … or a value agreed upon a priori, ex. HTTP dst port such as 80
Link layer
Network
Transport
Applications
adapter

## Slide 27: Dynamic Host Configuration Protocol
arriving endpoint
DHCP server
DHCP discover
(broadcast)
DHCP offer
DHCP request
DHCP ACK
(broadcast)
Host learns IP address,
Subnet mask, Gateway address, DNS server(s), and a lease time.

## Slide 28: (2) Socket: the interface to applications
Best-effort packet delivery is a clumsy abstraction
  Applications typically want higher-level abstractions
  Messages, uncorrupted data, reliable in-order delivery
Applications communicate using “sockets”
  Stream socket: reliable stream of bytes (like a file)
  Message socket: unreliable message delivery
socket
socket
User process
User process
Operating
System
Operating
System

## Slide 29: Two Basic Transport Features
Demultiplexing: port numbers
Error detection: checksums
Web server
(port 80)
Client host
Server host 128.2.194.242
Echo server
(port 7)
Service request for
128.2.194.242:80
(i.e., the Web server)
OS
Client
IP
payload
detect corruption

## Slide 30: Two Main Transport Layers
User Datagram Protocol (UDP)
  Just provides demultiplexing and error detection
  Header fields: port numbers, checksum, and length
  Low overhead, good for query/response and multimedia
Transmission Control Protocol (TCP)
  Adds support for a “stream of bytes” abstraction
  Retransmitting lost or corrupted data
  Putting out-of-order data back in order
  Preventing overflow of the receiver buffer
  Adapting the sending rate to alleviate congestion
  Higher overhead, good for most stateful applications

## Slide 31: Socket: the interface to applications
A socket is associated with five pieces of information:
  Source and destination IP address
  Source and destination port
  Kind of transport protocol (TCP/UDP)
Together referred to as the connection five-tuple
socket
socket
User process
User process
Operating
System
Operating
System

## Slide 32: Discussion
Is a socket between two IP addresses the right abstraction?
  Mobile hosts?
  Replicated services?
Is end-to-end error detection and correction the right model?
  High loss environments?
  Expense of retransmitting over the entire path?

## Slide 33: (3) Distributed sharing of the network
Best-effort network easily becomes overloaded
  No mechanism to “block” excess calls
  Instead excess packets are simply dropped
Examples
  Shared Ethernet medium: frame collisions
  Ethernet switches and IP routers: full packet buffers
Quickly leads to congestion collapse
Load
Useful work
“congestion
collapse”
Increase in load that results in a decrease in useful work done.

## Slide 34: Endpoints adjust to congestion
End hosts adapt their sending rates: congestion control
  In response to network conditions
Learning that the network is congested
  Shared Ethernet: carrier sense multiple access
    Seeing your own frame collide with others
  IP network: observing your end-to-end performance
    Packet delay or loss over the end-to-end path
Adapting to congestion
  Slowing down the sending rate for the greater good
  Slow down too little: don’t effectively relieve congestion
  Slow down too much: lose application performance

## Slide 35: Ethernet back-off mechanism
Carrier sense: wait for link to be idle
  If idle, start sending; if not, wait until idle
Collision detection: listen while transmitting
  If collision: abort transmission, and send jam signal
Exponential back-off: wait before retransmitting
  Wait random time, exponentially larger on each retry

## Slide 36: TCP congestion control (much more later)
Additive increase, multiplicative decrease
  On packet loss, divide congestion window in half
  On success for last window, increase window linearly
time
Window
halved
Loss
Other mechanisms: slow start, fast retransmit vs. timeout loss, etc.

## Slide 37: Discussion
What role should the network play in resource allocation?
  Explicit feedback to the endpoints?
  Enforcing an explicit rate allocation?
What is a good definition of fairness?
What about hosts who cheat to hog resources?
  How to detect cheating? How to prevent/punish?