## Slide 1: The Transport Layer: De/Multiplexing, Reliability
CS 352, Lecture 6, Spring 2020
http://www.cs.rutgers.edu/~sn624/352
Srinivas Narayana

## Slide 2: Course announcements
Quiz 2 will go online later today
  Submit on Sakai by Tuesday 10 pm
  30-minute time limit
Project 1 will be released later today
  Check the Sakai resources section for a tarfile with instructions

## Slide 3: Review of concepts
Application-layer protocols: DNS, HTTP, SMTP
HTTP caching: why?
Content distribution networks (CDNs):
  Origin server, CDN DNS server, CDN cache servers, client
  Use indirection
Simple Mail Transfer Protocol (SMTP): req/resp protocol
  User agents, sending mail server, receiving mail server
  SMTP commands, mail headers, response codes
  Mail access protocols: POP, IMAP, HTTP
    Support pull rather than push

## Slide 4: POP vs IMAP
POP3
Stateless server
UA-heavy processing
UA retrieves email from server, then typically deleted from server
Latest changes are at the UA
Simple protocol (list, retr, del within a POP session)
IMAP4
Stateful server
UA and server processing
Server sees folders, etc. which are visible to UAs
Changes visible at the server
Complex protocol

## Slide 5: What about web-based email?
Connect to mail servers via web browser
  Ex: gmail, outlook, etc.
Browsers speak HTTP
Email servers speak SMTP
Need a bridge to retrieve email using HTTP

## Slide 6: Web based email
HTTP server
HTTP
server
SMTP
Client
SMTP server
Internet
HTTP
HTTP

## Slide 7: More themes from app-layer protocols
Separation of concerns. Examples:
  Content rendering for users (browser, UA) separate from protocol operations (mail server)
  Reliable mail sending and receiving: mail UA doesn’t need to be “always on” to send or receive email reliably
In-band vs. out-of-band control:
  In-band: headers determine the actions of all the parties of the protocol
  There are protocols with out-of-band control, e.g., FTP
Keep it simple until you really need complexity
  ASCII-based design; stateless servers. Then introduce:
  Cookies for HTTP state
  IMAP for email organization
  Security extensions
  Different methods to set up and use underlying connections, etc.

## Slide 8: The Transport Layer

## Slide 9: Transport
Application
Transport
Network
Host-to-Net
…
FTP
HTTP
SMTP
DNS
TCP
UDP
IP
802.11
X.25
ATM
HTTPS

## Slide 10: Transport services and protocols
Provide logical communication between app processes running on different hosts
Transport protocols run @ hosts
  send side: breaks app messages into segments, passes to network layer
  recv side: reassembles segments into messages, passes to app layer
More than one transport protocol available to apps
  Internet: TCP and UDP
application
transport
network
data link
physical
application
transport
network
data link
physical

## Slide 11: Transport vs. network layer
Network layer: logical communication between endpoints
Transport layer: logical communication between processes
  relies on and enhances network layer services
Household analogy:
12 kids sending letters to 12 kids
processes = kids
app messages = letters in envelopes
endpoints = houses
transport protocol = Alice and Bob who de/mux to in-house siblings
network-layer protocol = postal service

## Slide 12: What transport guarantees do you want?
Reliability
  Don’t drop messages
  Don’t corrupt messages
Performance
  Get messages to other side as soon as possible
  As cheaply as possible
Ordering
  Don’t reorder messages

## Slide 13: Internet transport-layer protocols
Reliable, in-order delivery: Transmission Control Protocol (TCP)
  congestion control, flow control, connection setup
Unreliable, unordered delivery: User Datagram Protocol (UDP)
  A small extension to underlying network layer protocol, IP
Services not available:
  delay guarantees
  bandwidth guarantees
application
transport
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
application
transport
network
data link
physical
logical end-end transport

## Slide 14: Layering: in terms of packets
Data
Port #
Src, Dst
IP addr
Host-to-Net
Addresses (S, D)
send(data)
port
IP
port
receive(data)
Other apps
Other apps
Application
Operating System

## Slide 15: User Datagram Protocol

## Slide 16: UDP: User Datagram Protocol [RFC 768]
Best effort service. UDP segments may be:
  Lost
  Delivered out of order to app
UDP is connectionless
  Each UDP segment handled independently of others (i.e. no “memory” across packets)
DNS uses UDP
  UDP suitable for one-off req/resp
  Also for loss-tolerant delay-sensitive apps, e.g., video calling
Why are UDP’s guarantees even okay?
Simple & Low overhead
No delays due to connection establishment
  UDP can send data immediately
No memory for connection state at sender & receiver
Small segment header
UDP can blast away data as fast as desired
  UDP has no congestion control

## Slide 17: How demultiplexing works
Host receives IP datagrams
  Datagram contains a transport-level segment
  each segment has source IP address, destination IP address
  each segment has source, destination port number
Host uses IP addresses & port numbers to direct segment to appropriate app-level socket
source port #
dest port #
32 bits
application
data
(message)
UDP segment format
length
checksum
Length of
segment
(header + data)

## Slide 18
Time for an activity

## Slide 19: Connectionless demultiplexing
Create sockets with endpoint-local port numbers to receive data
// Example: Python UDP socket
sock = socket(AF_INET, SOCK_DGRAM);
// can bind sock to specific local port
When creating data to send into a UDP socket, you must specify the remote IP address and port.
sock.sendto(msg, (“128.1.2.3”, 4500));
When endpoint receives UDP segment:
  Lookup a table with the key (destination IP, destination port) to check if a corresponding socket exists
  Direct UDP segment to socket
Datagrams with different source IP addresses and/or source port numbers are directed to the same socket
  Subtle difference from TCP demultiplexing.

## Slide 20: UDP client + server (Python API)
UDPreceiver():
try:
rsd=socket.socket(socket.AF_INET, socket.SOCK_DGRAM)
except socket.error as err:
exit()
# Define the port on which you want to receive from the server
Rport = 50007
myip = socket.gethostbyname(socket.gethostname())
# connect to the server on local machine
server_binding=(myip, Rport)
rsd.bind(server_binding)
data, addr = rsd.recvfrom(1024)
# no need to “accept” a connection from other side before receiving data!
print(data.decode("utf-8"))
# Close the receiver socket
rsd.close()
exit()
UDPsender():
try:
ssd=socket.socket(socket.AF_INET, socket.SOCK_DGRAM)
except socket.error as err:
exit()
# Define the port on which you want to send to the receiver
RPort = 50007
hisip=socket.gethostbyname(“ilab.cs.rutgers.edu”)
receiver_binding=(hisip, RPort)
MESSAGE="hello world"
msg=MESSAGE.encode('utf-8’)
ssd.sendto(msg, receiver_binding)
# no “connection” to other side needed before sending data!
# Close the sender socket
ssd.close()
exit()

## Slide 21: Error Detection
Necessary, but insufficient, for reliability

## Slide 22: Data may get corrupted along the way…
Bits flipped from 01 or 10
Packet bits lost
How to detect errors?
Idea: compute a function over the data
  Store the result along with the data
Function must be easy to compute
Function & stored data efficient to verify
Ideas for functions?
source port #
dest port #
32 bits
application
data
(message)
UDP segment format
length
checksum

## Slide 23: From the UDP specification (RFC 768)
Checksum is the 16-bit one's complement of the one's complement sum of a pseudo header of information from the IP header, the UDP header, and the data, padded with zero octets at the end (if necessary) to make a multiple of two octets.
The pseudo header conceptually prefixed to the UDP header contains the source address, the destination address, the protocol, and the UDP length.

## Slide 24: UDP Checksum
Sender:
treat segment contents as sequence of 16-bit integers
checksum: addition (1’s complement sum) of segment contents
sender puts checksum value into UDP checksum field
Receiver:
compute checksum of received segment
check if computed checksum equals checksum field value:
NO - error detected
YES - no error detected.

## Slide 25: UDP checksum example
Note: when adding numbers, a carryout from the most significant bit needs to be added to the result
Example: add two 16-bit integers
1 1 1 1 0 0 1 1 0 0 1 1 0 0 1 1 0
1 1 1 0 1 0 1 0 1 0 1 0 1 0 1 0 1
1 1 0 1 1 1 0 1 1 1 0 1 1 1 0 1 1
1 1 0 1 1 1 0 1 1 1 0 1 1 1 1 0 0
1 0 1 0 0 0 1 0 0 0 1 0 0 0 0 1 1
wraparound
sum
checksum

## Slide 26: Internet Checksum Example
Complement of the sum is stored in the checksum field
At the receiver, all the byte fields are added along with the checksum
Sum + checksum must be all 1s
  All 1s, No error else discard packet
UDP checksum is optional in IPv4
UPD checksum is mandatory in IPv6

## Slide 27: User Datagram Protocol
A thin shim around best-effort network delivery
  Lightweight to send one-off request/response messages
  Lightweight transport for loss-tolerant delay-sensitive applications
Provides basic multiplexing/demultiplexing for applications
No reliability, performance, or ordering guarantees
Can do basic error detection (bit flips) using checksums
  Error detection is a necessary condition for reliability
  But need to do much more for reliability. Subject of the next lecture.