## Slide 1: CS 352 Network Address Translation
CS 352, Lecture 17.1
http://www.cs.rutgers.edu/~sn624/352
Srinivas Narayana

## Slide 2: Network
Application
Transport
Network
Host-to-Net
…
FTP
HTTP
SMTP
DNS
TCP
UDP
IP
802.11
X.25
ATM
HTTPS
The main function of the network layer is to
move packets from one endpoint to another.

## Slide 3: Background: The Internet’s growing pains
Networks had incompatible addressing
  IPv4 versus other network-layer protocols (X.25)
  Routable address ranges different across networks
Entire networks were changing their Internet Service Providers
  ISPs didn’t have to route directly to internal endpoints, just to the gateway
IPv4 address exhaustion
  Insufficient large IP blocks even for large networks
  Rutgers (AS46) has > 130,000 publicly routable IP addresses
  IIT Madras (a well-known public university in India, AS141340) has 512
  (Source: ipinfo.io)

## Slide 4: Network Address Translation
When a router modifies fields in an IP packet to:
Enable communication across networks with different (network-layer) addressing formats and address ranges
Allow a network to change its connectivity to the Internet en masse by modifying the source IP to a (publicly-visible) gateway IP address
Masquerade as an entire network of endpoints using (say) one publicly visible IP address
  Effect: use fewer IP addresses for more endpoints!

## Slide 5: Typical NAT setup
10.0.0.1
10.0.0.2
10.0.0.3
10.0.0.4
138.76.29.7
local network
10.0.0/24
rest of
the Internet
The gateway’s IP, 138.76.29.7 is publicly visible
The local endpoint IP addresses in 10.0.0/24 are private
All datagrams leaving local network have the same source IP as the gateway
Gateway router

## Slide 6: Typical NAT setup
10.0.0.1
10.0.0.2
10.0.0.3
10.0.0.4
local network
10.0.0/24
rest of
the Internet
That is, for the rest of the Internet, the gateway masquerades as a single endpoint representing (hiding) all the private endpoints.
The entire network just needs one (or a few) public IP addresses.
Gateway router
138.76.29.7

## Slide 7: Typical NAT setup
10.0.0.1
10.0.0.2
10.0.0.3
10.0.0.4
local network
10.0.0/24
rest of
the Internet
The NAT gateway router accomplishes this by using a different transport port for each distinct (transport-level) conversation between the local network and the Internet.
Gateway router
138.76.29.7

## Slide 8: Typical NAT setup
10.0.0.1
10.0.0.2
10.0.0.3
S: 10.0.0.1, 3345
D: 128.119.40.186, 80
1
1: host 10.0.0.1
sends datagram to
an external host,
128.119.40.186, at port 80
S: 128.119.40.186, 80
D: 10.0.0.1, 3345
4
S: 138.76.29.7, 5001
D: 128.119.40.186, 80
2
2: NAT router
changes datagram
src addr, port from
10.0.0.1, 3345 to
138.76.29.7, 5001,
Updates table
S: 128.119.40.186, 80
D: 138.76.29.7, 5001
3
3: Reply arrives to
dst addr, port
138.76.29.7, 5001
4: NAT gateway
changes datagram
dest addr, port from
138.76.29.7, 5001 to
10.0.0.1, 3345
Translation table
Internet-side Local side
138.76.29.7, 5001 10.0.0.1, 3345
…… ……
4: Map back

## Slide 9: Features of IP-masquerading NAT
Use one or a few public IPs: You don’t need a lot of addresses from your ISP
Change addresses of devices inside the local network freely, without notifying the rest of the Internet
Change the public IP address freely independent of network-local endpoints
Devices inside the local network are not publicly visible, routable, or accessible
Most IP masquerading NATs block incoming connections originating from the Internet
  Only way to communicate is if the internal host initiates the conversation

## Slide 10: If you’re home, you’re likely behind NAT
Most access routers (e.g., your home WiFi router) implement network address translation
You can check this by comparing your local address (visible from ifconfig) and your externally-visible IP address (e.g., type “what’s my IP address?” on your browser search bar)

## Slide 11: If you’re home, you’re likely behind NAT

## Slide 12: Limitations of IP-masquerading NATs
Connection limit due to 16-bit port-number field
  ~64K total simultaneous connections with a single public IP address
NAT can be controversial
  “Routers should only manipulate headers up to the network layer, not modify headers at the transport layer!”
Application developers must take NAT into account
  e.g., peer-to-peer applications like Skype
Purists: address shortage should instead be solved by IPv6
  (subject of the next module)

## Slide 14: CS 352 Internet Protocol: Version 6
CS 352, Lecture 17.2
http://www.cs.rutgers.edu/~sn624/352
Srinivas Narayana

## Slide 15: IPv4 address space exhaustion
The Internet has run out of IPv4 address blocks to allocate
Yet, demand for more (public) IP addresses is increasing
  More organizations moving online, new services, more replication
  More devices: your phone, your watch, your smart refrigerator
Fundamental issue: 32-bit addresses are not numerous enough
IP version 6 (IPv6)

## Slide 16: IPv6: Main changes from IPv4
Large address space: 128-bit addresses (16 bytes)
  Allows up to 3.4 x 1038 unique addresses
Fixed length headers (40 bytes)
  Improves the speed of packet processing in routers
  IPv6 options processing happens through a separate mechanism: using the field corresponding to the upper-layer protocol
New control message protocol: ICMPv6
No datagram fragmentation
  The ICMPv6 packet too big control message informs the source

## Slide 17: IPv6: Main changes from IPv4
New quality of service bits: flow label and traffic class
  Flow label: denotes packets belonging to the same conversation
  How the field is populated (ie: what exactly belongs to a “flow”) isn’t specified
  Routers may choose to provide performance guarantees to flows of specific traffic classes (more on this later)
No IP checksum: remove redundant error detection mechanisms
  Checksums exist already on common transport (TCP/UDP) and link layer (Ethernet) headers

## Slide 18: IPv6 datagram format
Version: 6
Class and flow label: for traffic differentiation at routers
Next header: same as the upper-layer protocol in IPv4. Also used to include IPv6 options
Hop limit: same as TTL in IPv4
payload len
next hdr
hop limit
flow label
class
ver
32 bits
source address
(128 bits)
destination address
(128 bits)

## Slide 19: IPv6 datagram format
Version: 6
Class and flow label: for traffic differentiation at routers
Next header: same as the upper-layer protocol in IPv4. Also used to include IPv6 options
Hop limit: same as TTL in IPv4
data
payload len
next hdr
hop limit
flow label
class
ver
32 bits
source address
(128 bits)
destination address
(128 bits)

## Slide 20: Can you spot the differences?
data
payload len
next hdr
hop limit
flow label
class
ver
32 bits
source address
(128 bits)
destination address
(128 bits)
ver
length
data
(variable length,
typically a TCP
or UDP segment)
16-bit identifier
header
checksum
time to
live
32-bit source IP address
hdr
len
type of
service
flags
fragment
offset
upper
protocol
32-bit destination IP address
Options (if any)
32 bits

## Slide 21: IPv6 addresses
IPv6 uses IPv4-CIDR-like (classless) addressing
Notation: xx:xx:xx:xx:xx:xx:xx:xx
  x = 4-bit hex number
  Contiguous 0s are compressed: 47CD::A456:0124
An IPv4-compatible IPv6 address has a prefix of 96 0-bits
  Example: ::128.64.18.87
Globally routable unicast addresses must start with bits 001
CIDR prefixes written the usual way:
  Example: 2000::/48 can contain 280 endpoints

## Slide 22: IPv6 adoption
~0% of Internet hosts used IPv6 for a long time (about 30 years)
In 2012, Google and a bunch of large orgs decided to support IPv6 irrevocably.
Source: https://www.google.com/intl/en/ipv6/statistics.html#tab=ipv6-adoption
When IP became a mainstream network-layer protocol, IPv4 was baked into router hardware.
Now, about 1/3rd of Internet hosts (contacting Google) support IPv6.
IPv6 adoption has been
trending up.

## Slide 24: CS 352 Address Resolution Protocol
CS 352, Lecture 17.3
http://www.cs.rutgers.edu/~sn624/352
Srinivas Narayana

## Slide 25: Background: Let’s peek into the link layer
Each network adapter has a hardware address or a MAC address
  E.g., the Wi-Fi adapter on your laptop has one
Assigned by the manufacturer, not expected to vary over time
  Think about it as an identifier for the device
To communicate over a single link, a sender needs the destination hardware address
Directory mechanisms like DNS and bootstrapping mechanisms like DHCP provide IP addresses
Given an IP address, how does an endpoint find the hardware address?

## Slide 26: Address Resolution Protocol (ARP)
ARP solves the following problem. Given an IP, find the machine’s hardware address
  IP  MAC resolution
All endpoints that are looked up are expected to be within the same network
Hence, address resolution can use broadcast:
  We don’t need to develop directory mechanisms like DNS
  Send (ARP) queries to everyone, asking for a MAC given an IP

## Slide 27: ARP packet format
Hardware type: link-layer protocol
  Example: Ethernet (1)
Hardware address length:
  Example: Ethernet = 6 bytes
Protocol Type: network-layer protocol
  Example: IPv4 (0x0800)
Protocol address length
  Example: IPv4 = 4 bytes
Operation:
  ARP request: 1, reply: 2
Sender’s addresses
Address to be resolved (or response)

## Slide 28: ARP operation
Ethernet Address:
05:23:f4:3d:e1:04
IP Address:
128.195.1.20
Ethernet Address:
98:22:ee:f1:90:1a
IP Address:
128.195.1.38
Ethernet Address:
12:04:2c:6e:11:9c
IP Address:
128.195.1.122
Wants to transmit
to 128.195.1.38
ARP request
Who has 128.195.1.38?
Tell 128.195.1.20
Different target IP address: ignore ARP
ARP request broadcast
Hardware type: Ethernet
Protocol type: IPv4
Hardware addr length: 6
Protocol addr length: 4
Operation: 2 (reply)
Sender hardware addr: 05:23:f4:3d:e1:04
Sender protocol addr:
128.195.1.20
Target HW addr:
98:22:ee:f1:90:1a
Target protocol addr:
128.195.1.38
Matching target IP: send reply
A
B
C

## Slide 29: Communicating outside the local net?
Suppose endpoint A wants to communicate with endpoint B that is in a different network
ARP broadcast outside the local network is too expensive
  How does one limit the scope of the broadcast? Internet-wide?
Besides, the hardware address format used by B’s network might be different from that of A’s network!
ARPs are not meaningful across network boundaries
Communicating to a network-external endpoint just means sending the packet to the gateway router
  Host can know that a destination is external using IP addr and netmask
  Host can talk to the gateway using DHCP (to get IP) and ARP (to get MAC)

## Slide 30: Summary of ARP
A useful mechanism to allow hosts inside a network to communicate:
ARP protocol helps resolve IP addresses into MAC addresses using a broadcast mechanism
Communication outside the local network requires ARP-ing for and sending packets to the gateway