## Slide 1: CS 352 Bandwidth-Delay Product
CS 352, Lecture 13.1
http://www.cs.rutgers.edu/~sn624/352
Srinivas Narayana

## Slide 2: Transport
Application
Transport
Network
Host-to-Net
…
FTP
HTTP
SMTP
DNS
TCP
UDP
IP
802.11
X.25
ATM
HTTPS

## Slide 3: How do apps get perf guarantees?
The network core provides no guarantees on packet delivery
Transport software on the endpoint oversees implementing guarantees on top of a best-effort network
Three important kinds of guarantees
  Reliability
  Ordered delivery
  Resource sharing in the network core
Transmission Control Protocol (TCP)

## Slide 4: Review: Congestion control so far
Algorithm by which multiple endpoints efficiently and fairly share bottleneck link
So far, we’ve looked at just efficiency.
Steady state: ACK clocking (keep the pipe full, but don’t congest it)
Getting to steady state:
  Slow start: exponential increase
  TCP New Reno: Additive increase
  TCP BBR: gain cycling & filters
TCP congestion control algorithm
Bottleneck link
Knobs:
Sending rate
Congestion window
Signals:
ACKs
Loss (RTOs), etc.

## Slide 5: Goal of steady state operation
Sender
Receiver
Send packet burst (as allowed by window)
Receive data packet
Send ACK
Receive ACK
Data
ACKs
(1) Keep transmissions ACK-clocked: Send new data on ACK
(2) Keep transmissions over the bottleneck link back to back

## Slide 6: Steady state cwnd for a single flow
Suppose the bottleneck link has rate C
Suppose the propagation round-trip delay (propRTT) between sender and receiver is T
Ignore transmission delays for this example;
Assume steady state: highest sending rate with no bottleneck congestion
Q: how much data is in flight over a single RTT?
C * T data i.e., amount of data unACKed at any point in time
ACKs take time T to arrive (without any queueing). In the meantime, sender is transmitting at rate C

## Slide 7: The Bandwidth-Delay Product
C * T = bandwidth-delay product:
  The amount of data in flight for a sender transmitting at the ideal rate during the ideal round-trip delay of a packet
Note: this is just the amount of data “on the pipe”
Data
C * T

## Slide 8: The Bandwidth-Delay Product
Q: What happens if cwnd > C * T?
  i.e., where are the rest of the in-flight packets?
A: Waiting at the bottleneck router queues
Data
C * T

## Slide 9: Router buffers and the max cwnd
Router buffer memory is finite: queues can only be so long
  If the router buffer size is B, there is at most B data waiting in the queue
If cwnd increases beyond C * T + B, data is dropped!
Data
C * T
B

## Slide 10: Summary
Bandwidth-Delay Product (BDP) governs the window size of a single flow at steady state
The bottleneck router buffer size governs how much the cwnd can exceed the BDP before packet drops occur

## Slide 12: CS 352 Detecting & Reacting to Losses
CS 352, Lecture 13.2
http://www.cs.rutgers.edu/~sn624/352
Srinivas Narayana

## Slide 13: Detecting packet loss
So far, all the algorithms we’ve studied have a coarse loss detection mechanism: RTO timer expiration
  Let the RTO expire, drop cwnd all the way to 1 MSS
Analogy: you’re driving a car
  You’re waiting until the next car in front is super close to you (RTO) and then hitting the brakes really hard (set cwnd := 1)
  Q: Can you see obstacles from afar and slow down proportionately?
That is, can the sender see packet loss coming in advance?
  And reduce cwnd more gently?

## Slide 14: Can we detect loss earlier than RTO?
Key idea: use the information in the ACKs. How?
Suppose successive (cumulative) ACKs contain the same ACK#
  Also called duplicate ACKs
  Occur when network is reordering packets, or one (but not most) packets in the window were lost
Reduce cwnd when you see many duplicate ACKs
  Consider many dup ACKs a strong indication that packet was lost
  Default threshold: 3 dup ACKs, i.e., triple duplicate ACK
  Make cwnd reduction gentler than setting cwnd = 1; recover faster

## Slide 15: Fast Retransmit & Fast Recovery

## Slide 16: Distinction: In-flight versus window
So far, window and in-flight referred to the same data
Fast retransmit & fast recovery differentiate the two notions
0
1
2
3
4
5
6
7
1
0
Last cumulative
ACK’ed seq #
Last transmitted
seq #
cwnd = 6
0
1
2
3
4
5
6
7
1
0
inflight = 3
Triple duplicate ACKs
(assume subsequent 3 pieces of data were successfully received)
Sender’s view:
cwnd is the interval between the last cumulatively ACK’ed seq# and the last transmitted seq#
inflight is the data currently believed to be in flight.

## Slide 17: TCP fast retransmit (RFC 2581)
The fact that ACKs are coming means that data is getting delivered to the receiver, albeit with some loss.
Note: Before the dup ACKs arrive, we assume inflight = cwnd
TCP sender does two actions with fast retransmit

## Slide 18: TCP fast retransmit (RFC 2581)
(1) Reduce the cwnd and in-flight gently
  Don’t drop cwnd all the way down to 1 MSS
Reduce the amount of in-flight data multiplicatively
  Set inflight  inflight / 2
  That is, set cwnd = (inflight / 2) + 3MSS
  This step is called multiplicative decrease
  Algorithm also sets ssthresh to inflight / 2

## Slide 19: TCP fast retransmit (RFC 2581)
Example: Suppose cwnd and inflight (before triple dup ACK) were both 8 MSS.
After triple dup ACK, reduce inflight to 4 MSS
Assume 3 of those 8 MSS no longer in flight; set cwnd = 7 MSS
Last cumulative
ACK’ed seq #
cwnd = inflight = 8
5
0
1
2
3
4
5
6
7
1
0
5
2
3
4
6
7
1
0
Assumed not in flight (dup ACK)
inflight = 4
cwnd = 7

## Slide 20: TCP fast retransmit (RFC 2581)
(2) The seq# from dup ACKs is immediately retransmitted
That is, don’t wait for an RTO if there is sufficiently strong evidence that a packet was lost

## Slide 21: TCP fast recovery (RFC 2581)
Sender keeps the reduced inflight until a new ACK arrives
  New ACK: an ACK for the seq# that was just retransmitted
  May also include the (three or more) pieces of data that were subsequently delivered to generate the duplicate ACKs
Conserve packets in flight: transmit some data over lossy periods (rather than no data, which would happen if cwnd := 1)

## Slide 22: TCP fast recovery (RFC 2581)
Keep incrementing cwnd by 1 MSS for each dup ACK
Last cumulative
ACK’ed seq #
cwnd = 6
inflight = 3
0
1
2
3
4
5
6
7
1
0
5
2
3
4
5
6
7
1
0
Assumed not in flight (dup ACK)

## Slide 23: TCP fast recovery (RFC 2581)
Keep incrementing cwnd by 1 MSS for each dup ACK
Last cumulative
ACK’ed seq #
cwnd = 7
inflight = 3
0
1
2
3
4
5
6
7
1
0
5
2
3
4
6
7
1
0
Assumed not in flight (dup ACK)

## Slide 24: TCP fast recovery (RFC 2581)
Keep incrementing cwnd by 1 MSS for each dup ACK
Last cumulative
ACK’ed seq #
cwnd = 8
inflight = 3
0
1
2
3
4
5
6
7
1
0
5
2
3
4
6
7
1
0
Assumed not in flight (dup ACK)

## Slide 25: TCP fast recovery (RFC 2581)
Eventually a new ACK arrives, acknowledging the retransmitted data and all data in between
Deflate cwnd to half of cwnd before fast retransmit.
  cwnd and inflight are aligned and equal once again
Perform additive increase from this point!
cwnd = 3
inflight = 3
0
1
2
3
4
5
6
7
1
0
5
2
3
4
6
7
1
0
New ACK acknowledged this data
Last cumulative
ACK’ed seq #

## Slide 26: Additive Increase/Multiplicative Decrease
1K
Time
Triple duplicate ACK
Slow start
In-flight data
Say MSS = 1 KByte
Default ssthresh = 64KB = 64 MSS
Switch to additive increase at cwnd = ssthresh = 64K
Perceived loss occurs at cwnd = 80K
(2) Set inflight = ssthresh = 40K
Additive increase
Additive increase
Fast retransmit: (1) retransmit dup-ACKed segment
Fast recovery keeps inflight stable until new ACK
New ACK
RTO
RTO: window drops all the way to 1 MSS
Multiplicative decrease

## Slide 27
TCP New Reno performs additive increase and multiplicative decrease of its congestion window.
In short, we often refer to this as AIMD.
Multiplicative decrease is a part of all TCP algorithms, including BBR.
[It is necessary for fairness across TCP flows.]

## Slide 28: Summary of TCP loss detection
Fast Retransmit
Triple dup ACK: sufficiently strong signal that network has dropped data, before RTO
Immediately retransmit data
Multiplicatively decrease in-flight data to half of its value
Fast Recovery
Maintain this reduced amount of in-flight data as long as dup ACKs arrive
  Data is successfully getting delivered
When new ACK arrives, do additive increase from there on
Don’t wait for an RTO and then set the cwnd to 1 MSS
  Tantamount to waiting to get super close to the car in front and then jamming the brakes really hard
Instead, react proportionately by sensing pkt loss in advance

## Slide 30: CS 352 Computing the Retransmit Timeout
CS 352, Lecture 13.3
http://www.cs.rutgers.edu/~sn624/352
Srinivas Narayana

## Slide 31: TCP timeout (RTO)
Useful for reliable delivery and congestion control
How to pick the RTO value?
  Too long: slow reaction to loss
  Too short: premature retransmissions which are wasteful
Want: RTO must predict the upper bound of RTTs resulting from a successful packet + ACK
Intuition: somehow use the observed RTT (sampleRTT)
  Can we just directly set the latest RTT as the RTO?
No. RTT can vary significantly!
  Intermittent congestion, path changes, signal quality changes on wireless channel, etc.

## Slide 32: Estimate an “average” RTT
Exponential weighted moving average (typical alpha = 1/8)
RTT (milliseconds)
RTT: gaia.cs.umass.edu to fantasia.eurecom.fr
sampleRTT
EstimatedRTT
EstimatedRTT = (1 - )*EstimatedRTT + *SampleRTT

## Slide 33: Accounting for RTT variance
RTT samples can have a large variance
Use a safety margin in the RTO estimate to account for variance

## Slide 34: TCP timeout computation
DevRTT = (1-)*DevRTT +
*|SampleRTT-EstimatedRTT|
(typically,  = 0.25)
RTO = EstimatedRTT + 4*DevRTT
average RTT
safety margin
Conceptually, there is an RTO timer for each seq #.

## Slide 35: Too many timers?
Timers are expensive – we don’t want one per sequence #
  Interrupts, OS data structures, and book-keeping
The TCP stack maintains just one “real” timer per connection
When a packet is transmitted, its transmission time is recorded
The only real timer in the system is the RTO for the first unACK’ed segment
  Expiration interval: RTO
If ACK before RTO fires: set timer for next unACK’ed segment, based on recorded transmission time of that segment
If RTO fires: retransmit the segment, restart RTO timer

## Slide 36: Retransmission ambiguity

## Slide 37: Real RTT of a retransmitted segment?
Receiver
Sender
RTO
RTT?
RTT?
ACK arrives
Retransmission ambiguity
Aside: problem would go away if packets had a flag to indicate retransmission, or a field to uniquely identify each transmission and its ACK
(TCP has neither)

## Slide 38: How to estimate RTT/RTO despite retxmit?
One solution: Never update RTT measurements based on ACKs from retransmitted packets
Problem: Sudden change in RTT, coupled with many retransmissions, can cause system to update RTT very late
  Ex: Primary path failure leads to a high-RTT secondary path
If RTT estimates are not updated, the RTO estimate isn’t, and that leads to a host of other problems.
  Ex: Unnecessary retransmissions since RTOs needlessly expire

## Slide 39: Karn’s algorithm
Use back-off as part of the sampleRTT computation
Whenever packet loss (RTO), RTO is increased by a factor
  Conservatively assume that RTT may have increased since the last unambiguous RTTsamples were obtained
Use this increased RTO as RTO estimate for the next segment
  Don’t use the estimatedRTT from stale sampleRTT
Only after an ACK is received for a successful transmission is the RTO timer set to a value obtained from EstimatedRTT

## Slide 40: Summary
RTO computation is an important part of TCP’s behavior under loss
TCP uses both an average RTT as well as the variance to obtain a safe prediction of an upper bound of a successful RTT
Resolve retransmission ambiguity under path changes by avoiding sampleRTT measurements and multiplicatively increasing the RTO each time

## Slide 42: CS 352 TCP Connection Management
CS 352, Lecture 13.4
http://www.cs.rutgers.edu/~sn624/352
Srinivas Narayana

## Slide 43: TCP connections need lots of bookkeeping
Socket buffer memory
Entries in connection lookup tables
Data structures and parameters (e.g., sequence numbers) in the operating system kernel
These resources can get expensive on machines running many connections, e.g., web servers

## Slide 44: Handshake
Before starting data transmission, TCP client and server perform a handshake and agree on parameters
TCP is bidirectional: independent set of sequence numbers for each direction
Sequence numbers start from a random initial value
Specific TCP flags indicate connection initiation and acceptance
Client
Server
Client app
Server app
connect()
accept()
Client  server seq #
Server  client seq #
SYN
SYN / ACK

## Slide 45: TCP flags in the header

## Slide 46: 2-way handshake not enough
Suppose the server receives the first SYN packet and decides to allocate all the resources needed for the connection.
What happens if a malicious client sends a ton of SYN packets?
Asymmetric work: client doesn’t need to allocate any resources of its own
  Just have to send a well-crafted packet
However, server’s resources exhausted!
SYN flood attack: a form of denial of service
Client
Server
Client app
Server app
connect()
accept()
SYN
SYN
SYN
SYN
SYN

## Slide 47: Consequences
The server should not allocate resources upon receiving the first client message (SYN)
The server cannot carry any application data in SYN/ACK
  Server hasn’t yet allocated all necessary resources
Client cannot send any data in the SYN packet
Recall: HTTP requires an RTT for the handshake before sending HTTP request
Client
Server
Client app
Server app
connect()
accept()
SYN
SYN
SYN
SYN
SYN

## Slide 48: Mitigating the denial of service problem
Key idea: Make the client do more work before allocating server resources
The client should send at least one more packet, responding to the data in the server’s SYN/ACK, before the server decides to call the connection established
  That is, before all required server resources like buffers are allocated
Result: 3-way handshake
Per-connection finite state machine tracks this process

## Slide 49: TCP 3-way handshake
Client
Server
CLOSED
SYN-SENT
connect()
LISTEN
SYN-RCVD
CLOSED
bind()
listen()
ESTAB
Send SYN
Upon receiving SYN
ESTAB
Upon receiving ACK
Upon receiving SYN/ACK
SYN
ACK
SYN/ACK
Return from
connect()
accept()
Return from
accept()
Server
resources
only allocated
at this point
Send SYN/ACK
Send ACK
This packet can contain application data!

## Slide 50: TCP: Closing a connection
Client, server each close their side of connection
  send TCP segment with FIN bit = 1
In general, TCP is full-duplex: both sides can send
However, FIN is unidirectional: stop one side of the communication
Respond to received FIN with ACK
  On receiving FIN, ACK can be combined with own FIN
Simultaneous FIN exchanges can be handled

## Slide 51: Summary of TCP connection management
TCP connections have associated resources: managing them requires book-keeping the establishment of a connection carefully
Simple 2-way handshakes suffer from denial of service vulnerability
  Moral: don’t allocate resources on the first client message
3-way handshake mitigates this issue by making client work harder
  Client must send ACK to server’s SYN/ACK before server can handle data
  The cost: increased time before sending application data from client