## Slide 1: The Link Layer: Wireless LANs
CS 352, Lecture 21, Spring 2020
http://www.cs.rutgers.edu/~sn624/352
Srinivas Narayana

## Slide 2: Course announcements
Quiz grades:
  Drop 2 lowest scores
Final exam
  All multiple choice
  One or more correct: scored as #right - #wrong options

## Slide 3: Review of concepts
Link layer
Application
Transport
Network
Link layer
…
FTP
HTTP
SMTP
DNS
TCP
UDP
IP
802.11
802.3
ATM
HTTPS
Ethernet

## Slide 4: Review of concepts
Link layer: medium access control
Want: efficiency, fairness, simplicity, distribution
Channel partitioning: TDMA, FDMA
Random access
  Slotted ALOHA
  Pure ALOHA
  Carrier sensing
  Collision Detection
  Ethernet CSMA/CD: Exponential back-off
Turn-taking
Randomly contending is too inefficient (pure ALOHA is 18% asymptotically efficient)
Listen before speaking, and as you speak
One of the most fundamental and reused ideas in all of computer systems

## Slide 5: Wireless and Mobile Networks
Background:
# wireless (mobile) phone subscribers now far exceeds # wired phone subscribers
# wireless Internet-connected devices far exceeds # wireline Internet-connected devices
  laptops, Internet-enabled phones promise anytime untethered Internet access
  Your refrigerator, microwave, and car are connected
two important (but different) challenges
  wireless: communication over wireless link
  mobility: handling the mobile user who changes point of attachment to network

## Slide 6: Elements of a wireless network
network
infrastructure

## Slide 7: Elements of a wireless network
wireless hosts
laptop, smartphone
run applications
may be stationary (non-mobile) or mobile
  wireless does not always mean mobility
network
infrastructure

## Slide 8: Elements of a wireless network
base station
typically connected to wired network
relay - responsible for sending packets between wired network and wireless host(s) in its “area”
  e.g., cell towers, 802.11 access points
network
infrastructure

## Slide 9: Elements of a wireless network
wireless link
typically used to connect mobile(s) to base station
also used as backbone link
multiple access protocol coordinates link access
various data rates, transmission distance
network
infrastructure

## Slide 10: Wireless network taxonomy
single hop
multiple hops
infrastructure
(e.g., APs)
no
infrastructure
host connects to
base station (WiFi,
WiMAX, cellular)
which connects to
larger Internet
no base station, no
connection to larger
Internet (Bluetooth,
ad hoc nets)
host may have to
relay through several
wireless nodes to
connect to larger
Internet: mesh net
no base station, no
connection to larger
Internet. May have to
relay to reach
a given wireless node
MANET, VANET

## Slide 11: Wireless network characteristics

## Slide 12: Wireless Link Characteristics (1)
important differences from wired link ….
  decreased signal strength: radio signal attenuates as it propagates through matter (path loss)
  interference from other sources: standardized wireless network frequencies (e.g., 2.4 GHz) shared by other devices (e.g., phone); devices interfere
  multipath propagation: radio signal reflects off objects ground, arriving at destination at slightly different times
…. make communication across (even a point to point) wireless link much more challenging

## Slide 13: Wireless Link Characteristics (2)
SNR: signal-to-noise ratio
  larger SNR – easier to extract signal from noise (a “good thing”)
SNR versus BER tradeoffs
  given physical layer: increase power -> increase SNR->decrease BER
  given SNR: choose physical layer that meets BER requirement, giving highest thruput
    SNR may change with mobility: dynamically adapt physical layer (modulation technique, rate)
10
20
30
40
QAM256 (8 Mbps)
QAM16 (4 Mbps)
BPSK (1 Mbps)
SNR(dB)
BER
10-1
10-2
10-3
10-5
10-6
10-7
10-4

## Slide 14: Wireless network characteristics
Multiple wireless senders and receivers create additional problems (beyond multiple access):
A
B
C
Hidden terminal problem
B, A hear each other
B, C hear each other
A, C can not hear each other means A, C unaware of their interference at B
A
B
C
A’s signal
strength
space
C’s signal
strength
Signal attenuation:
B, A hear each other
B, C hear each other
A, C can not hear each other interfering at B

## Slide 15: IEEE 802.11 Wireless LAN
802.11b
2.4-5 GHz unlicensed spectrum
up to 11 Mbps
802.11a
  5-6 GHz range
  up to 54 Mbps
802.11g
  2.4-5 GHz range
  up to 54 Mbps
802.11n: multiple antennae
  2.4-5 GHz range
  up to 200 Mbps
all use CSMA/CA for multiple access
all have base-station and ad-hoc network versions

## Slide 16: 802.11: Channels, association
802.11b: 2.4GHz-2.485GHz spectrum divided into 11 channels at different frequencies
  AP admin chooses frequency for AP
  interference possible: channel can be same as that chosen by neighboring AP!
host: must associate with an AP
  scans channels, listening for beacon frames containing AP’s name (SSID) and MAC address
  selects AP to associate with
  may perform authentication
  will typically run DHCP to get IP address in AP’s subnet

## Slide 17: WiFi (802.11) multiple access
CSMA/CA

## Slide 18: Review: MAC protocols: Taxonomy
three broad classes:
channel partitioning
  divide channel into smaller “pieces” (time slots, frequency, code)
  allocate piece to node for exclusive use
random access
  channel not divided, allow collisions
  “recover” from collisions
“taking turns”
  nodes take turns, but nodes with more to send can take more or longer turns

## Slide 19: Review: Ethernet CSMA/CD algorithm
1. NIC receives datagram from network layer, creates frame
2. If NIC senses channel idle, starts frame transmission. If NIC senses channel busy, waits until channel idle, then transmits.
3. If NIC transmits entire frame without detecting another transmission, NIC is done with frame !
4. If NIC detects another transmission while transmitting, aborts and sends jam signal
5. After aborting, NIC enters binary (exponential) backoff:
  after mth collision, NIC chooses K at random from {0,1,2, …, 2m-1}. NIC waits K·512 bit times, returns to Step 2
  longer backoff interval with more collisions

## Slide 20: IEEE 802.11: multiple access
avoid collisions: 2+ nodes transmitting at same time
802.11: CSMA - sense before transmitting
  don’t collide with ongoing transmission by other node
802.11: no collision detection!
  difficult to receive (sense collisions) when transmitting due to weak received signals (fading)
  can’t sense all collisions in any case: hidden terminal, fading
  goal: avoid collisions: CSMA/C(ollision)A(voidance)
space
A
B
C
A
B
C
A’s signal
strength
C’s signal
strength

## Slide 21: IEEE 802.11 MAC Protocol: CSMA/CA
802.11 sender
1 if sense channel idle for DIFS then
  transmit entire frame (no CD)
2 if sense channel busy then
  start random backoff time
  timer counts down while channel idle
  transmit when timer expires
  if no ACK, increase random backoff interval, repeat 2
802.11 receiver
- if frame received OK
return ACK after SIFS (ACK needed due to hidden terminal problem)
sender
receiver
DIFS
data
SIFS
ACK
SIFS < DIFS

## Slide 22: Avoiding collisions (more)
idea: allow sender to “reserve” channel rather than random access of data frames: avoid collisions of long data frames
sender first transmits small request-to-send (RTS) packets to BS using CSMA
  RTSs may still collide with each other (but they’re short)
BS broadcasts clear-to-send CTS in response to RTS
CTS heard by all nodes
  sender transmits data frame
  other stations defer transmissions
avoid data frame collisions completely
using small reservation packets!

## Slide 23: Collision Avoidance: RTS-CTS exchange
AP
A
B
time
RTS(A)
RTS(B)
RTS(A)
CTS(A)
CTS(A)
DATA (A)
ACK(A)
ACK(A)
reservation collision
defer

## Slide 24: Wireless multiple access
Code Division Multiple Access (CDMA)

## Slide 25: Code Division Multiple Access (CDMA)
unique “code” assigned to each user; i.e., code set partitioning
  all users share same frequency, but each user has own “chipping” sequence (i.e., code) to encode data
  allows multiple users to “coexist” and transmit simultaneously with minimal interference (if codes are “orthogonal”)
encoded signal = (original data) X (chipping sequence)
decoding: inner-product of encoded signal and chipping sequence

## Slide 26: CDMA encode/decode
slot 1
slot 0
d1 = -1
1
1
1
1
1
-
1
-
1
-
1
-
Zi,m= di.cm
d0 = 1
1
1
1
1
1
-
1
-
1
-
1
-
1
1
1
1
1
-
1
-
1
-
1
-
1
1
1
1
1
-
1
-
1
-
1
-
slot 0
channel
output
slot 1
channel
output
channel output Zi,m
sender
code
data
bits
slot 1
slot 0
d1 = -1
d0 = 1
1
1
1
1
1
-
1
-
1
-
1
-
1
1
1
1
1
-
1
-
1
-
1
-
1
1
1
1
1
-
1
-
1
-
1
-
1
1
1
1
1
-
1
-
1
-
1
-
slot 0
channel
output
slot 1
channel
output
receiver
code
received
input
Di = S Zi,m.cm
m=1
M
M

## Slide 27: CDMA: two-sender interference
using same code as sender 1, receiver recovers sender 1’s original data from summed channel data!
Sender 1
Sender 2
channel sums together transmissions by sender 1 and 2

## Slide 28: Summary of the wireless link layer
Wireless medium is very different from wired
  Signal attenuation (“fading”) much more important to handle
  Hidden terminal problem
Consequences of differences:
  Link-layer ACKs
  Transmission delays to control contention: SIFS, DIFS
  Link reservation (RTS/CTS)
  Conservative backoff timer (count down only when idle)
Medium access control
  Frequency division multiple access (AP channels in WiFi)
  Random access (CSMA/CA for transmitting to/from WiFi AP)
  Code division multiple access (simultaneous transmission in cellular networks)