## Slide 1
Lecture 20, Computer Networks (198:552)
Backbone Traffic Engineering

## Slide 2: Do IP Networks Manage Themselves?
In some sense, yes:
  TCP senders send less traffic during congestion
  Routing protocols adapt to topology changes
But, does the network run efficiently?
  Congested link when idle paths exist?
  High-delay path when a low-delay path exists?
How should routing adapt to the traffic?
  Avoiding congested links in the network
  Satisfying application requirements (e.g., delay)
… these are the essential questions of traffic engineering

## Slide 3: Routing With “Static” Link Weights
Routers flood information to learn topology
  Determine “next hop” to reach other routers…
  Compute shortest paths based on link weights
Link weights configured by network operator
3
2
2
1
1
3
1
4
5
3

## Slide 4: Setting the Link Weights
How to set the weights
  Inversely proportional to link capacity?
  Proportional to propagation delay?
  Network-wide optimization based on traffic?
3
2
2
1
1
3
1
4
5
3
3

## Slide 5: Measure, Model, and Control
Topology/
Configuration
Offered
traffic
Changes to
the network
Operational network
Network-wide
“what if” model
measure
control

## Slide 6: Key Ingredients
Measurement
  Topology: monitoring of the routing protocols
  Traffic matrix: passive traffic measurement
Network-wide models
  Representations of topology and traffic
  “What-if” models of shortest-path routing
Network optimization
  Efficient algorithms to find good configurations
  Operational experience to identify constraints

## Slide 7: Optimization Problem
Input: graph G(R,L)
  R is the set of routers
  L is the set of unidirectional links
  cl is the capacity of link l
Input: traffic matrix
  Mi,j is traffic load from router i to j
Output: setting of the link weights
  wl is weight on unidirectional link l
  Pi,j,l is fraction of traffic from i to j traversing link l

## Slide 8: Equal-Cost Multipath (ECMP)
0.5
0.5
0.5
0.5
0.25
0.25
0.25
0.25
1.0
1.0
Values of Pi,j,l

## Slide 9: Objective Function
Computing the link utilization
  Link load: ul = Si,j Mi,j Pi,j,l
  Utilization: ul/cl
Objective functions
  min(maxl(ul/cl))
  min(Sl f(ul/cl))
f(x)
x

## Slide 10: Complexity of Optimization Problem
NP-complete optimization problem
  No efficient algorithm to find the link weights
  Even for simple objective functions
What are the implications?
  Have to resort to searching through weight settings
Clearly suboptimal, but effective in practice
  Fast computation of the link weights
  Good performance, compared to “optimal” solution

## Slide 11: Incorporating Operational Realities
Minimize number of changes to the network
  Changing just 1 or 2 link weights is often enough
Tolerate failure of network equipment
  Weights settings usually remain good after failure
  … or can be fixed by changing one or two weights
Limit dependence on measurement accuracy
  Good weights remain good, despite random noise
Limit frequency of changes to the weights
  Joint optimization for day & night traffic matrices

## Slide 12: Central Control over Distributed Routing
Stefano Visicchio et al., ACM SIGCOMM’15

## Slide 13: Context: Scalable & robust backbone TE
Traditional IGPs perform distributed computations
  Scalable
  Robust to link and node failures
  But not flexible in terms of expressed paths
SDNs perform (logically) centralized path computations
  Highly flexible
  But handling large networks is challenging
  Handling topology updates is challenging
Could we combine the best of both worlds?

## Slide 14: An example

## Slide 15: Key idea: Lies to the routers

## Slide 16: Another example

## Slide 17: Workflow

## Slide 18: Fibbing: Expressiveness

## Slide 19: Key primitives required
Initial setting of static routing weights: “Fibbing-compliance”
Local and global scoping of IGP announcements
Forwarding traffic to fake nodes on any desired link

## Slide 20: Augmentation algorithms

## Slide 21: Cross-destination optimization

## Slide 22: A comparison of approaches

## Slide 23: Acknowledgment
Slides heavily adapted from material by Jennifer Rexford and Stefano Visicchio