## Slide 1: CS 352 Detecting & Reacting to Losses
CS 352, Lecture 13.1
http://www.cs.rutgers.edu/~sn624/352
Srinivas Narayana

## Slide 2: Transport
Application
Transport
Network
Host-to-Net
…
FTP
HTTP
SMTP
DNS
TCP
UDP
IP
802.11
X.25
ATM
HTTPS

## Slide 3: How do apps get perf guarantees?
The network core provides no guarantees on packet delivery
Transport software on the endpoint oversees implementing guarantees on top of a best-effort network
Three important kinds of guarantees
  Reliability
  Ordered delivery
  Resource sharing in the network core
Transmission Control Protocol (TCP)

## Slide 4: Review: Congestion control so far
Algorithm by which multiple endpoints efficiently and fairly share bottleneck link
So far, we’ve looked at just efficiency.
Steady state: ACK clocking (keep the pipe full, but don’t congest it)
Getting to steady state:
  Slow start: exponential increase
  TCP New Reno: Additive increase
  TCP BBR: gain cycling & filters
TCP congestion control algorithm
Bottleneck link
Knobs:
Sending rate
Congestion window
Signals:
ACKs
Loss (RTOs), etc.

## Slide 5: Detecting packet loss
So far, all the algorithms we’ve studied have a coarse loss detection mechanism: RTO timer expiration
  Let the RTO expire, drop cwnd all the way to 1 MSS
Analogy: you’re driving a car
  You’re waiting until the next car in front is super close to you (RTO) and then hitting the brakes really hard (set cwnd := 1)
  Q: Can you see obstacles from afar and slow down proportionately?
That is, can the sender see packet loss coming in advance?
  And reduce cwnd more gently?

## Slide 6: Can we detect loss earlier than RTO?
Key idea: use the information in the ACKs. How?
Suppose successive (cumulative) ACKs contain the same ACK#
  Also called duplicate ACKs
  Occur when network is reordering packets, or one (but not most) packets in the window were lost
Reduce cwnd when you see many duplicate ACKs
  Consider many dup ACKs a strong indication that packet was lost
  Default threshold: 3 dup ACKs, i.e., triple duplicate ACK
  Make cwnd reduction gentler than setting cwnd = 1; recover faster

## Slide 7: Fast Retransmit & Fast Recovery

## Slide 8: Distinction: In-flight versus window
So far, window and in-flight referred to the same data
Fast retransmit & fast recovery differentiate the two notions
0
1
2
3
4
5
6
7
1
0
Last cumulative
ACK’ed seq #
Last transmitted
seq #
cwnd = 6
0
1
2
3
4
5
6
7
1
0
inflight = 3
Triple duplicate ACKs
(assume subsequent 3 pieces of data were successfully received)
Sender’s view:
cwnd is the interval between the last cumulatively ACK’ed seq# and the last transmitted seq#
inflight is the data currently believed to be in flight.

## Slide 9: TCP fast retransmit (RFC 2581)
The fact that ACKs are coming means that data is getting delivered to the receiver, albeit with some loss.
Note: Before the dup ACKs arrive, we assume inflight = cwnd
TCP sender does two actions with fast retransmit

## Slide 10: TCP fast retransmit (RFC 2581)
(1) Reduce the cwnd and in-flight gently
  Don’t drop cwnd all the way down to 1 MSS
Reduce the amount of in-flight data multiplicatively
  Set inflight  inflight / 2
  That is, set cwnd = (inflight / 2) + 3MSS
  This step is called multiplicative decrease
  Algorithm also sets ssthresh to inflight / 2

## Slide 11: TCP fast retransmit (RFC 2581)
Example: Suppose cwnd and inflight (before triple dup ACK) were both 8 MSS.
After triple dup ACK, reduce inflight to 4 MSS
Assume 3 of those 8 MSS no longer in flight; set cwnd = 7 MSS
Last cumulative
ACK’ed seq #
cwnd = inflight = 8
5
0
1
2
3
4
5
6
7
1
0
5
2
3
4
6
7
1
0
Assumed not in flight (dup ACK)
inflight = 4
cwnd = 7

## Slide 12: TCP fast retransmit (RFC 2581)
(2) The seq# from dup ACKs is immediately retransmitted
That is, don’t wait for an RTO if there is sufficiently strong evidence that a packet was lost

## Slide 13: TCP fast recovery (RFC 2581)
Sender keeps the reduced inflight until a new ACK arrives
  New ACK: an ACK for the seq# that was just retransmitted
  May also include the (three or more) pieces of data that were successively delivered so as to generate the duplicate ACKs
Conserve packets in flight: transmit some data over lossy periods, rather than no data, e.g., by setting cwnd = 1

## Slide 14: TCP fast recovery (RFC 2581)
Keep incrementing cwnd by 1 MSS for each dup ACK
Last cumulative
ACK’ed seq #
cwnd = 6
inflight = 3
0
1
2
3
4
5
6
7
1
0
5
2
3
4
5
6
7
1
0
Assumed not in flight (dup ACK)

## Slide 15: TCP fast recovery (RFC 2581)
Keep incrementing cwnd by 1 MSS for each dup ACK
Last cumulative
ACK’ed seq #
cwnd = 7
inflight = 3
0
1
2
3
4
5
6
7
1
0
5
2
3
4
6
7
1
0
Assumed not in flight (dup ACK)

## Slide 16: TCP fast recovery (RFC 2581)
Keep incrementing cwnd by 1 MSS for each dup ACK
Last cumulative
ACK’ed seq #
cwnd = 8
inflight = 3
0
1
2
3
4
5
6
7
1
0
5
2
3
4
6
7
1
0
Assumed not in flight (dup ACK)

## Slide 17: TCP fast recovery (RFC 2581)
Eventually a new ACK arrives, acknowledging the retransmitted data and all data in between
Deflate cwnd to half of cwnd before fast retransmit.
  cwnd and inflight are aligned and equal once again
Perform additive increase from this point!
cwnd = 3
inflight = 3
0
1
2
3
4
5
6
7
1
0
5
2
3
4
6
7
1
0
New ACK acknowledged this data
Last cumulative
ACK’ed seq #

## Slide 18: Additive Increase/Multiplicative Decrease
1K
Time
Triple duplicate ACK
Slow start
In-flight data
Say MSS = 1 KByte
Default ssthresh = 64KB = 64 MSS
Switch to additive increase at cwnd = ssthresh = 64K
Perceived loss occurs at cwnd = 80K
(2) Set inflight = ssthresh = 40K
Additive increase
Additive increase
Fast retransmit: (1) retransmit dup-ACKed segment
Fast recovery keeps inflight stable until new ACK
New ACK
Upon triple dup ACK, don’t drop the window all the way to 1MSS; instead do multiplicative decrease
RTO
RTO: window drops all the way to 1 MSS

## Slide 19
TCP New Reno performs additive increase and multiplicative decrease of its congestion window.
In short, we often refer to this as AIMD.
Multiplicative decrease is a part of all TCP algorithms, including BBR.
[It is necessary for fairness across TCP flows.]

## Slide 20: Summary of TCP loss detection
Fast Retransmit
Triple dup ACK: sufficiently strong signal that network has dropped data, before RTO
Immediately retransmit data
Multiplicatively decrease in-flight data to half of its value
Fast Recovery
Maintain this reduced amount of in-flight data as long as dup ACKs arrive
  Data is successfully getting delivered
When new ACK arrives, do additive increase from there on
Don’t wait for an RTO and then set the cwnd to 1 MSS
  Tantamount to waiting to get super close to the car in front and then jamming the brakes really hard
Instead, react proportionately by sensing pkt loss in advance

## Slide 22: CS 352 Computing the Retransmit Timeout
CS 352, Lecture 13.2
http://www.cs.rutgers.edu/~sn624/352
Srinivas Narayana

## Slide 23: TCP timeout (RTO)
Useful for reliable delivery and congestion control
How to pick the RTO value?
  Too long: slow reaction to loss
  Too short: premature unnecessary retransmissions
Intuition: somehow use the observed RTT (sampleRTT)
  Can we just directly set the latest RTT as the RTO?
RTT can vary significantly!
  Intermittent congestion, path changes, signal quality changes on wireless channel, etc.

## Slide 24: Estimated RTT
Exponential weighted moving average (typical alpha = 1/8)
RTT (milliseconds)
RTT: gaia.cs.umass.edu to fantasia.eurecom.fr
sampleRTT
EstimatedRTT
EstimatedRTT = (1- )*EstimatedRTT + *SampleRTT

## Slide 25: Timeout == estimated RTT + safety
Estimated RTT can have a large variance
  Use a larger safety margin if larger variance

## Slide 26: Timeout == estimated RTT + safety
DevRTT = (1-)*DevRTT +
*|SampleRTT-EstimatedRTT|
(typically,  = 0.25)
TimeoutInterval = EstimatedRTT + 4*DevRTT
estimated RTT
“safety margin”

## Slide 27: Managing a single timer
data rcvd from app:
create segment with seq #
seq # is byte-stream number of first data byte in segment
start timer if not already running
  think of timer as for oldest unacked segment
  expiration interval: TimeOutInterval
timeout:
retransmit segment that caused timeout
restart timer
ack rcvd:
if ack acknowledges previously unacked segments
  update what is known to be ACKed
  restart timer if there are still unacked segments

## Slide 28: Problem with sampleRTT calculation
2K
SEQ=0
Receiver
Sender
Sender Timeout
2K
SEQ=0
RTT?
RTT?
ACK = 2048

## Slide 29: Retransmission ambiguity
If you retransmitted, how do you measure sampleRTT for it?
  Measure RTT from original data segment?
  Measure RTT from most recent (retransmitted) segment?
There could be an error in RTT estimate, since we can’t be sure
One solution
  Never update RTT measurements based on acknowledgements from retransmitted packets
Problem: Sudden change in RTT, coupled with many retransmissions, can cause system to update RTT very late
  Ex: Primary path failure leads to a slower secondary path

## Slide 30: Karn’s algorithm
Use back-off as part of sampleRTT computation
Whenever packet loss, RTO is increased by a factor
Use this increased RTO as RTO estimate for the next segment (not from EstimatedRTT)
Only after an acknowledgment received for a successful transmission is the timer set to new RTT obtained from EstimatedRTT

## Slide 32: CS 352 TCP Connection Establishment
CS 352, Lecture 13.3
http://www.cs.rutgers.edu/~sn624/352
Srinivas Narayana

## Slide 33: Connection Management
before exchanging data, sender/receiver “handshake”:
agree to establish connection
agree on connection parameters
connection state: ESTAB
connection variables:
  seq # client-to-server
  server-to-client
  rcvBuffer size
  at server,client
application
network
connection state: ESTAB
connection Variables:
  seq # client-to-server
  server-to-client
  rcvBuffer size
  at server,client
application
network
Socket clientSocket =
newSocket("hostname","port number");
Socket connectionSocket = welcomeSocket.accept();
Connection Management

## Slide 34: Agreeing to establish a connection
Q: will 2-way handshake always work in network?
variable delays
retransmitted messages (e.g. req_conn(x)) due to message loss
message reordering
can’t “see” other side
2-way handshake:
Let’s talk
OK
ESTAB
ESTAB
choose x
req_conn(x)
ESTAB
ESTAB
acc_conn(x)

## Slide 35: 2-way handshake failure scenarios
retransmit
req_conn(x)
ESTAB
req_conn(x)
half open connection!
(no client!)
client terminates
server
forgets x
connection
x completes
retransmit
req_conn(x)
ESTAB
req_conn(x)
data(x+1)
retransmit
data(x+1)
accept
data(x+1)
choose x
req_conn(x)
ESTAB
ESTAB
acc_conn(x)
client terminates
ESTAB
choose x
req_conn(x)
ESTAB
acc_conn(x)
data(x+1)
accept
data(x+1)
connection
x completes
server
forgets x

## Slide 36: TCP 3-way handshake
SYNbit=1, Seq=x
choose init seq num, x
send TCP SYN msg
ESTAB
SYNbit=1, Seq=y
ACKbit=1; ACKnum=x+1
choose init seq num, y
send TCP SYNACK
msg, acking SYN
ACKbit=1, ACKnum=y+1
received SYNACK(x)
indicates server is live;
send ACK for SYNACK;
this segment may contain
client-to-server data
received ACK(y)
indicates client is live
SYNSENT
ESTAB
SYN RCVD
client state
LISTEN
server state
LISTEN

## Slide 37: TCP state machine (partially shown)
closed
L
listen
SYN
rcvd
SYN
sent
ESTAB
socket clientSocket =
socket.connect("hostname","port number");
SYN(seq=x)
socket connectionSocket = serverSocket.accept();
SYN(x)
SYNACK(seq=y,ACKnum=x+1)
create new socket for
communication back to client
SYNACK(seq=y,ACKnum=x+1)
ACK(ACKnum=y+1)
ACK(ACKnum=y+1)
L

## Slide 38: TCP: closing a connection
client, server each close their side of connection
  send TCP segment with FIN bit = 1
In general, TCP is full-duplex: both sides can send
But FIN is unidirectional: stop one side of the communication
respond to received FIN with ACK
  on receiving FIN, ACK can be combined with own FIN
simultaneous FIN exchanges can be handled

## Slide 39: TCP: closing a connection
FIN_WAIT_2
CLOSE_WAIT
FINbit=1, seq=y
ACKbit=1; ACKnum=y+1
ACKbit=1; ACKnum=x+1
wait for server
close
can still
send data
can no longer
send data
LAST_ACK
CLOSED
TIMED_WAIT
timed wait
for 2*max
segment lifetime
CLOSED
FIN_WAIT_1
FINbit=1, seq=x
can no longer
send but can
receive data
clientSocket.close()
client state
server state
ESTAB
ESTAB