## Slide 1: Reliable Data Delivery
Lecture 11 http://www.cs.rutgers.edu/~sn624/352-S22
Srinivas Narayana

## Slide 2: Quick recap of concepts
Tp layer
Interface1
Port1
Port2
Port3
TCP established:
(src IP, src port, dst IP, dst port)
TCP listening:
(dst IP, dst port)
UDP:
(dst IP, dst port)
Endpoint
Interface2
socket
Incoming packet
UDP: Abstraction to send & receive one-off packets. That’s it.
dst port #
…
Src IP address
Dst IP address
…
src port #
length
chksum
Packet at the network layer
UDP segment structure
App

## Slide 3: Error Detection in the Transport Layer

## Slide 4: Why error detection?
Network provides best effort service
UDP is a simple and low overhead transport
  Data may be lost
  Data may be corrupted along the way (e.g., 1 -> 0)
  Data may be reordered
However, simple error detection is possible!
  Was the data I received the same data the remote machine sent?
Error detection is a useful feature for all transport protocols including TCP

## Slide 5: Error Detection in UDP and TCP
Key idea: have sender compute a function over the data
  Store the result in the packet
  Receiver can check the function’s value in received packet
An analogy: you’re sending a package of goodies and want your recipient to know if goodies were leaked along the way
Your idea: weigh the package; stamp the weight on the package
  Have the recipient weigh the package and cross-check the weight with the stamped value

## Slide 6: Requirements on error detection function
Function must be easy to compute
Function must change (whp) if the packet changes
  If the packet was modified through these changes, the function value must change
Function must be easy to verify
UDP and TCP use a class of function called a checksum
  Very common idea: used in multiple parts of networks and computer systems

## Slide 7: UDP & TCP’s Checksum function
Sender:
treat segment contents as sequence of 16-bit integers
checksum: addition (1’s complement sum) of segment contents
sender puts checksum value into UDP/TCP checksum field
Receiver:
compute a checksum of the received segment, including the checksum in packet itself
check if the resulting (computed) checksum is 0
NO – an error is detected
YES – assume no error

## Slide 8: Computing 1’s complement sum
Very similar to regular (unsigned) binary addition.
However, when adding numbers, a carryout from the most significant bit needs to be added to the result
Example: add two 16-bit integers
1 1 1 1 0 0 1 1 0 0 1 1 0 0 1 1 0
1 1 1 0 1 0 1 0 1 0 1 0 1 0 1 0 1
1 1 0 1 1 1 0 1 1 1 0 1 1 1 0 1 1
1 1 0 1 1 1 0 1 1 1 0 1 1 1 1 0 0
1 0 1 0 0 0 1 0 0 0 1 0 0 0 0 1 1
wraparound
sum
checksum

## Slide 9: From the UDP specification (RFC 768)
Checksum is the 16-bit one's complement of the one's complement sum of a pseudo header of information from the IP header, the UDP header, and the data, padded with zero octets at the end (if necessary) to make a multiple of two octets.
The pseudo header conceptually prefixed to the UDP header contains the source address, the destination address, the protocol, and the UDP length.
Warning: Technical language ahead

## Slide 10: Some observations on checksums
Checksums don’t detect all bit errors
  Consider (x, y) vs. (x – 1, y + 1) as adjacent 16-bit values in packet
  Analogy: you can’t assume the package hasn’t been meddled with if its weight matches the one on the stamp. More smarts needed for that. 
  But it’s a lightweight method that works well in many cases
Checksums are part of the packet; they can get corrupted too
  The receiver will just declare an error if it finds an error
  However, checksums don’t enable the receiver to detect where the error lies or correct the error(s)
  Checksum is an error detection mechanism; not a correction mechanism.

## Slide 11: Some observations on checksums
Checksums are insufficient for reliable data delivery
  If a packet is lost, so is its checksum
UDP and TCP use the same checksum function
  TCP also uses the lightweight error detection capability
  However, TCP has more mature mechanisms for reliable data delivery (up next!)

## Slide 12: Playing with checksums
Let’s craft some UDP packets (again)!
sudo tcpdump -i lo udp –XAvvv # observe packets
sudo scapy # tool used to send crafted packets
send(IP(dst="127.0.0.1")/UDP(sport=1024, dport=2048)/"hello world”, iface="lo")
Let’s play with the checksums a bit!

## Slide 13: Summary of UDP
A simple transport: Send or receive a single packet from/to the correct application process. That’s it
  Just a thin shim around network layer’s best-effort delivery
  No connection building, no latency
  Suitable for one-off request/response messages
  Suitable for loss-tolerant but delay-sensitive applications
No reliability, performance, or ordering guarantees
Can do basic error detection (bit flips) using checksums
  Error detection is necessary to deliver data reliably, but it is insufficient

## Slide 14: Reliable data delivery

## Slide 15: Packet loss
Sender
Receiver
How might a sender and receiver ensure that data is delivered reliably (despite some packets being lost)?
TCP uses three mechanisms

## Slide 16: Coping with packet loss: (1) ACK
Key idea: Receiver returns an acknowledgment (ACK) per packet sent
If sender receives an ACK, it knows that the receiver got the packet.
Sender
Receiver
ACK
packet
ACK
packet

## Slide 17: Coping with packet corruption: (1) ACK
ACKs also work to detect packet corruption on the way to the receiver
  One possibility: A receiver could send a negative acknowledgment, or a NAK, if it receives a corrupted packet
  Q: How to detect corrupted packet?
    One method: Checksum!
TCP only uses positive ACKs.
Sender
Receiver
NAK
packet
ACK
packet

## Slide 18: Coping with packet loss: (2) RTO
What if a packet is dropped?
Key idea: Wait for a duration of time (called retransmission timeout or RTO) before re-sending the packet
In TCP, the onus is on the sender to retransmit lost data when ACKs are not received
Note that retransmission works also if ACKs are lost or delayed
Sender
Receiver
ACK
RTO
Retransmission

## Slide 19: How should the RTO be set?
A good RTO must predict the round-trip time (RTT) between the sender and receiver
  RTT: the time to send a single packet and receive a (corresponding) single ACK at the sender
Intuition: If an ACK hasn’t returned, and our (best estimate of) RTT has elapsed, the packet was likely dropped.
RTT can be measured directly at the sender. No receiver involvement needed.
Sender
Receiver
ACK
RTO

## Slide 20: Coping with packet duplication
Sender
Receiver
ACK
RTO
If ACKs delayed beyond the RTO, sender may retransmit the same data
  Receiver wouldn’t know that it just received duplicate data from this retransmitted packet
Add some identification to each packet to help distinguish between adjacent transmissions
  This is known as the sequence number
Duplicate
packet received!
(Receiver doesn’t know…)

## Slide 21: Coping with packet loss: (3) Sequence #s
Sender
Receiver
ACK
RTO
A bad scenario: Suppose an ACK was delayed beyond the RTO; sender ended up retransmitting the packet.
At the receiver: sequence number helps disambiguate a fresh transmission from a retransmission
  Sequence number same as earlier: retransmission
  Fresh sequence number: fresh data
0
0

## Slide 22: Coping with packet loss: (3) Sequence #s
Sender
Receiver
RTO
A good scenario: packet successfully received and ACK returned within RTO
Sequence numbers of successively transmitted packets are different
Receiver knows these are not duplicate, because sequence numbers are different
SEQ 0
SEQ 1
ACK
RTO

## Slide 23: Coping with packet loss: (3) Sequence #s
Sender
Receiver
RTO
A good scenario: packet successfully received and ACK returned within RTO
Sequence numbers of successively transmitted packets are different
Further, the receiver informs the sender which packet was ACK’ed using an ACK sequence number
RTO
Receiver knows these are not duplicate, because sequence numbers are different
ACK
ACK 0
ACK 1
SEQ 0
SEQ 1

## Slide 24: Q: What is the seq# of third packet?
Sender
Receiver
ACK 1
RTO
Goal: Avoid ambiguity on which packet was received/ACK’ed from both the sender and receiver’s perspective
One possibility: keep incrementing the seq #: 2, 3, …
Alternative: since seq # 0 was successfully ACK’ed earlier, it is OK to reuse seq #0 for next transmission.
  Seq #s reused if enough time elapsed
SEQ 0
SEQ 1
ACK 0
???
RTO

## Slide 25: Summary: Stop-and-Wait Reliability
Sender sends a single packet, then waits for an ACK to know the packet was successfully received. Then the sender transmits the next packet.
If ACK is not received until a timeout (RTO), sender retransmits the packet
Disambiguate duplicate vs. fresh packets using sequence numbers that change on “adjacent” packets
Sender
Receiver
RTT
RTO
SEQ 0
ACK 0
SEQ 1
Retransmit