## Slide 1: Routing (part 3)
Lecture 25
http://www.cs.rutgers.edu/~sn624/352-F24
Srinivas Narayana

## Slide 2
The network layer enables reachability.
We’ll see protocols that solve subproblems.
How does an endpoint get an address?
DHCP
How does an endpoint talk to another within the same network?
ARP
How does an endpoint talk to another outside its network?
Routing protocols
OSPF, RIP, BGP
Gateways
NAT
Debugging?
ICMP

## Slide 3
Distance vector protocols
Routing protocols
Link state
protocols
Every router is aware of the existence of every other router.
Messages reveal information on the full network (graph) structure.
Message exchange and forwarding tables scale with network size.
These assumptions/settings cannot work on the Internet.

## Slide 4: The Internet is a large federated network
AT&T
Comcast
Verizon
Several autonomously run organizations: No one “boss”
Organizations cooperate, but also compete
e.g., AT&T has little commercial interest in revealing its internal network structure to Verizon.

## Slide 5: The Internet is a large federated network
AT&T
Comcast
Verizon
Several autonomously run organizations: No one “boss”
Organizations cooperate, but also compete
Message exchanges must
not reveal internal network details.
Algorithm must work with “incomplete” information about its neighbors’ internal topology.

## Slide 6: The Internet is a large federated network
AT&T
Comcast
Verizon
Internet today: > 70,000 unique autonomous networks
Internet routers: > 800,000 forwarding table entries
Keep messages & tables as small as possible. Don’t flood
Algorithm must be incremental: don’t recompute the whole table on every message exchanged.

## Slide 7: Inter-domain Routing
Routing approaches so far (LS + DV) are applicable within one autonomous system (AS), e.g., Rutgers
  Called intra-domain routing protocols
The Internet uses Border Gateway Protocol (BGP)
All AS’es speak BGP. It is the glue that holds the Internet together
BGP is a path vector protocol
Distance vector protocols
Routing protocols
Link state
protocols
Path vector protocols
Messages?
Algorithm?

## Slide 8: Q1. BGP Messages
Routing Announcements or Advertisements
  “I am here” or “I can reach here”
  Occur over a TCP connection (BGP session) between routers
Route announcement = destination + attributes
  Destination: IP prefix
Route Attributes:
  AS-level path
  Next hop
  Several others: origin, MED, community, etc.
An AS promises to use advertised path to reach destination
Only route changes are advertised after BGP session established
2b
2d
2c
2a
X
“I am here.”
Dst: 128.1.2.0/24
AS path: X
“I can reach X”
Dst: 128.1.2.0/24
AS path: AS2, X
AS 2
1b
1d
1c
1a
No link metrics, distances!
Exchange paths: path vector
Loop detection is easy
(no “count to infinity”)

## Slide 9: Q1. Next Hop
Next hop conceptually denotes the first router interface that begins the AS-level path
  The meaning of this attribute is context-dependent
In an announcement arriving from a different AS (eBGP), next hop is the router in the next AS which sent the announcement
  Example: Next Hop of the eBGP announcement reaching 1c is 2a
1b
1d
1c
1a
2b
2d
2c
2a
AS 1
AS 2
eBGP announcement:
AS2, X
X

## Slide 10: Q1. Next Hop
Suppose router 1c imports the path (more on this soon)
Router 1c will propagate the announcement inside the AS using iBGP
The next hop of this (iBGP) announcement is set to 1c
  In particular, the next hop is an AS1 internal address
1b
1d
1c
1a
2b
2d
2c
2a
AS 1
AS 2
eBGP announcement:
AS2, X
X

## Slide 11: Q2. The algorithm
A BGP router does not consider every routing advertisement it receives by default to make routing decisions!
  An import policy determines whether a route is even considered a candidate
Once imported, the router performs route selection
A BGP router does not propagate its chosen path to a destination to all other AS’es by default!
  An export policy determines whether a (chosen) path can be advertised to other AS’es and routers
Policy considerations make BGP very different from intra-domain (LS / DV) protocols
Programmed by network operator

## Slide 12: Policies in BGP

## Slide 13: Policy arises from business relationships
Customer-provider relationships:
  E.g., Rutgers is a customer of AT&T
Peer-peer relationships:
  E.g., Verizon is a peer of AT&T
Business relationships depend on where connectivity occurs
  “Where”, also called a “point of presence” (PoP)
  e.g., customers at one PoP but peers at another
  Internet-eXchange Points (IXPs) are large PoPs where ISPs come together to connect with each other (often for free)

## Slide 14: BGP Export Policy
A,B,C are provider networks
X,W,Y are customers (of provider networks)
X is dual-homed: attached to two networks
policy to enforce: X does not want to route from B to C via X
  So, X will not announce to B a route to C
A
B
C
W
X
Y
legend:
customer
network:
provider
network
Suppose an ISP only wants to route traffic to/from its customer networks (does not want to carry transit traffic between other ISPs)

## Slide 15: BGP Export Policy
A announces path Aw to B and to C
B will not announce BAw to C:
  B gets no “revenue” for routing CBAw, since none of C, A, w are B’s customers
C will route CAw (not using B) to get to w
A
B
C
W
X
Y
legend:
customer
network:
provider
network
Suppose an ISP only wants to route traffic to/from its customer networks (does not want to carry transit traffic between other ISPs)

## Slide 16: BGP Import Policy
Suppose C announces path Cy to x
Further, y announces a direct path (“y”) to x
Then x may choose not to import the path Cy to y since it has a peer path (“y”) towards y
A
B
C
W
X
Y
legend:
customer
network:
provider
network
Suppose an ISP wants to minimize costs by avoiding routing through its providers when possible.

## Slide 17: Q2. BGP Route Selection
When a router imports more than one route to a destination IP prefix, it selects route based on:
  local preference value attribute (import policy decision -- set by network admin)
  shortest AS-PATH
  closest NEXT-HOP router
  Several additional criteria: You can read up on the full, complex, list of criteria, e.g., at https://www.cisco.com/c/en/us/support/docs/ip/border-gateway-protocol-bgp/13753-25.html

## Slide 18: Example of route selection
Suppose AS A and B are connected to each other both in North America (NA) and in Europe (EU)
A source in NA wants to reach a destination in EU
There are two paths available
  Assume same local preference
  Same AS path length
Closest next hop-router: choose path via B1 rather than B2
A1
B1
A2
B2
Src-NA
Dst-EU
AS B
AS A
NA
EU

## Slide 19: Example of route selection
Choosing closest next-hop results in early exit routing
  Try to exit the local AS as early as possible
  Also called hot potato routing
Reduce resource use within local AS
  potentially at the expense of another AS
A1
B1
A2
B2
Src-NA
Dst-EU
AS B
AS A
NA
EU

## Slide 20: Computing the forwarding table
1b
1d
1c
1a
2b
2d
2c
2a
3b
3d
3c
3a
AS2
AS3
AS1
X
Suppose a router in AS1 wants to forward a packet destined to external prefix X.
How is the forwarding table entry for X at 1d computed?
How is the forwarding table entry for X at 1c computed?

## Slide 21: eBGP and iBGP announcements
Based on AS2 import policy, AS2 router 2c imports and selects path AS3,X, propagates (via iBGP) to all AS2 routers
1b
1d
1c
1a
2b
2d
2c
2a
3b
3d
3c
3a
AS2
AS3
AS1
X
AS3,X
AS2,AS3,X
AS2 router 2c receives path announcement AS3,X (via eBGP) from AS3 router 3a
Based on AS2 export policy, AS2 router 2a announces (via eBGP) path AS2, AS3, X to AS1 router 1c

## Slide 22: eBGP and iBGP announcements
AS1 gateway router 1c learns path AS2,AS3,X from 2a (next hop 2a)
1b
1d
1c
1a
2b
2d
2c
2a
3b
3d
3c
3a
AS2
AS3
AS1
X
AS3,X
AS2,AS3,X
A given router may learn about multiple paths to destination:
AS3,X
AS1 gateway router 1c learns path AS3,X from 3a (next hop 3a)
Through BGP route selection process, AS1 gateway router 1c chooses path AS3,X, and announces path within AS1 via iBGP (next hop 1c)

## Slide 23: Setting forwarding table entries
1b
1d
1c
1a
2b
2d
2c
2a
3b
3d
3c
3a
AS2
AS3
AS1
X
AS3,X
AS2,AS3,X
AS3,X
recall: 1a, 1b, 1d learn about dest X via iBGP from next-hop 1c: “path to X goes through 1c”
1d: intra-domain routing: to get to 1c, forward over outgoing local interface 1
NH
interface
…
…
1c
…
…
1
dest
Next-Hop
…
…
X
…
…
1c
1
2
3
IP Dst
Out port
X
1
Forwarding table

## Slide 24: Setting forwarding table entries
1b
1d
1c
1a
2b
2d
2c
2a
3b
3d
3c
3a
AS2
AS3
AS1
X
AS3,X
AS2,AS3,X
AS3,X
recall: 1c learns about dest X via eBGP from next-hop 3a: “path to X goes through 3a”
1c: to get to link-local neighbor 3a, forward out interface 2
NH
interface
…
…
3a
…
…
2
dest
Next-Hop
…
…
X
…
…
3a
1
2
3
IP Dst
Out port
X
2
Forwarding table

## Slide 25: Summary: Inter-domain routing
Federation and scale introduce new requirements for routing on the Internet
BGP is the protocol that handles Internet routing
Path vector: exchange paths to a destination with attributes
Policy-based import of routes, route selection, and export

## Slide 26: BGP’s impact: October ’21 FB++ outage
https://engineering.fb.com/2021/10/05/networking-traffic/outage-details/
By Doug Madory - https://www.kentik.com/blog/facebooks-historic-outage-explained/, CC BY 4.0, https://commons.wikimedia.org/w/index.php?curid=110816752
FB network
FB’s DNS servers
Rest of the Internet
BGP route withdrawal:
“I can’t reach FB anymore”
BGP route withdrawal: don’t use me to get to FB
No remote access (no more reachability due to BGP withdrawal of DC and DNS servers)
Restricted physical access (prox can’t verify, can’t access prox server)

## Slide 27: Network Address Translation (NAT)

## Slide 28: Background: The Internet’s growing pains
Networks had incompatible addressing
  IPv4 versus other network-layer protocols (X.25)
Entire networks were changing their Internet Service Providers
  ISPs don’t want to route directly to internal endpoints
IPv4 address exhaustion
  Insufficient large IP blocks even for large networks
  Rutgers (AS46) has > 130,000 publicly routable IP addresses
  IIT Madras (a well-known public university in India, AS141340) has 512
  (Source: ipinfo.io)

## Slide 29: Network Address Translation
When a router modifies fields in an IP packet to:
Enable communication across networks with different (network-layer) addressing formats and address ranges
Allow a network to change its connectivity to the Internet en masse by modifying the source IP to a (publicly-visible) gateway IP address
Masquerade as an entire network of endpoints using (say) one publicly visible IP address
  Effect: use fewer IP addresses for more endpoints!
We’ll see a standard design: “Network address and port translation” (NAPT, RFC 2663)

## Slide 30: Typical NAT setup (NAPT)
10.0.0.1
10.0.0.2
10.0.0.3
10.0.0.4
138.76.29.7
local network
10.0.0/24
rest of
the Internet
The gateway’s IP, 138.76.29.7 is publicly visible
The local endpoint IP addresses in 10.0.0/24 are private
All datagrams leaving local network have the same source IP as the gateway
Gateway router

## Slide 31: Typical NAT setup (NAPT)
10.0.0.1
10.0.0.2
10.0.0.3
10.0.0.4
local network
10.0.0/24
rest of
the Internet
That is, for the rest of the Internet, the gateway masquerades as a single endpoint representing (hiding) all the private endpoints.
The entire network just needs one (or a few) public IP addresses.
Gateway router
138.76.29.7

## Slide 32: Typical NAT setup (NAPT)
10.0.0.1
10.0.0.2
10.0.0.3
10.0.0.4
local network
10.0.0/24
rest of
the Internet
The NAT gateway router accomplishes this by using a different transport port for each distinct (transport-level) conversation between the local network and the Internet.
Gateway router
138.76.29.7

## Slide 33: Typical NAT setup (NAPT)
10.0.0.1
10.0.0.2
10.0.0.3
S: 10.0.0.1, 3345
D: 128.119.40.186, 80
1
1: host 10.0.0.1
sends datagram to
an external host,
128.119.40.186, at port 80
S: 128.119.40.186, 80
D: 10.0.0.1, 3345
4
S: 138.76.29.7, 5001
D: 128.119.40.186, 80
2
2: NAT router
changes datagram
src addr, port from
10.0.0.1, 3345 to
138.76.29.7, 5001,
Updates table
S: 128.119.40.186, 80
D: 138.76.29.7, 5001
3
3: Reply arrives to
dst addr, port
138.76.29.7, 5001
4: NAT gateway
changes datagram
dest addr, port from
138.76.29.7, 5001 to
10.0.0.1, 3345
Translation table
Internet-side Local side
138.76.29.7, 5001 10.0.0.1, 3345
…… ……
4: Map back
138.76.29.7
SNAT
DNAT

## Slide 34: Features of IP-masquerading NAT
Use one or a few public IPs: You don’t need a lot of addresses from your ISP
Change addresses of devices inside the local network freely, without notifying the rest of the Internet
Change the public IP address freely independent of network-local endpoints
Devices inside the local network are not publicly visible, routable, or accessible
Most IP masquerading NATs block incoming connections originating from the Internet
  Only way to communicate is if the internal host initiates the conversation

## Slide 35: If you’re home, you’re likely behind NAT
Most access routers (e.g., your home WiFi router) implement network address translation
You can check this by comparing your local address (visible from ifconfig) and your externally-visible IP address (e.g., type “what’s my IP address?” on your browser search bar)

## Slide 36: If you’re home, you’re likely behind NAT

## Slide 37: On public cloud, you’re behind NAT
VM
Physical Machine
Each VM believes it has its own (vritual) IP subnet.
VM
Each VM believes it has its own (virtual) IP subnet.
Physical Machine
Physical
IP subnet used
NAT
NAT

## Slide 38: Limitations of IP-masquerading NATs
Connection limit due to 16-bit port-number field
  ~64K total simultaneous connections with a single public IP address
NAT can be controversial
  “Routers should only manipulate headers up to the network layer, not modify headers at the transport layer!”
Application developers must take NAT into account
  e.g., peer-to-peer applications
Internet “purists”: instead, solve address shortage with IPv6
  32-bit IP addresses are just not enough
  Esp. with more devices (your watch, your fridge, …) coming online