## Slide 1: Pipelined Reliability
Lecture 14
http://www.cs.rutgers.edu/~sn624/352-F24
Srinivas Narayana

## Slide 2: Review: Stop-and-Wait Reliability
Sender sends a single packet, then waits for an ACK to know the packet was successfully received. Then the sender transmits the next packet.
If ACK is not received until a timeout (RTO), sender retransmits the packet
Disambiguate duplicate vs. fresh packets using sequence numbers that change on “adjacent” packets
Sender
Receiver
RTT
RTO
SEQ 0
ACK
SEQ 1
Retransmit

## Slide 3
Sending one packet per RTT makes the data transfer rate limited by the time between the endpoints, rather than the bandwidth.
Ensure you got the (one) box safely; make W trips
Ensure you get W boxes safely; make just 1 trip!
Keep many packets in flight

## Slide 4: Making reliable data transfer efficient

## Slide 5: Pipelined reliability
Data in flight: data that has been sent, but sender hasn’t yet received ACKs from the receiver
  Note: can refer to packets in flight or bytes in flight
New packets sent at the same time as older ones still in flight
New packets sent at the same time as ACKs are returning
More data moving in same time!
Improves throughput
  Rate of data transfer

## Slide 6: Pipelined reliability
Stop and wait: send 1 packet per RTT
Pipelined: send W packets per RTT
If W packets are in flight, throughput improves W times compared to stop-and-wait
For now, assume we fix W
  Later: how to determine W?
Sender
Receiver
RTT
RTO

## Slide 7
Pipelining makes reliable data transfer efficient.
However, pipelining also makes it more complex.
Which packets were successfully delivered?
Which packets should the sender retransmit?
Which packets are currently in flight?

## Slide 8: Sliding Windows

## Slide 9: Setup
Assume packets are labeled by sequence numbers
  Increasing from 0, …, N-1, then roll back to 0
Assume ACKs indicate the sequence numbers of data that was received
  Note: Didn’t need this for stop-and-wait
Convention: ACK#s carry the next sequence number expected
  Used in TCP
Our discussion uses packet seq #s
  However, TCP uses byte seq #s
Sender
Receiver
SEQ 0
ACK 1
SEQ 1
SEQ N-1
SEQ 0
…
ACK 2

## Slide 10: Sliding window (sender side)
Window: Sequence numbers of in-flight data
Window size: The amount of in-flight data (unACKed)
Sender’s point of view:
Window size = 3
Last seq # known to be received (ACK recv’d at sender)
Last sequence # sent
0
1
2
3
4
5
6
7
1
0
Sequence numbers restart from 0 beyond a point (finite space on header)
Transmissions later in time
0
4
2
6
7
5
1
3

## Slide 11: Sliding window (sender side)
Suppose sequence number 2 is acknowledged by the receiver
  Sender receives the ACK. Sender can transmit sequence # 5
  The window “slides” forward
0
1
2
3
4
5
6
7
1
0
Window size = 3
Last seq # known to be received (ACK recv’d at sender)
Last sequence # sent
Sender’s point of view:
0
4
2
6
7
5
1
3

## Slide 12: Sliding window (sender side)
Suppose sequence number 2 is acknowledged by the receiver
  Sender receives the ACK. Sender can transmit sequence # 5
  The window “slides” forward
0
1
2
3
4
5
6
7
1
0
Window size = 3
Last seq # known to be received (ACK recv’d at sender)
Last sequence # sent
Sender’s point of view:
0
4
2
6
7
5
1
3

## Slide 13: Sliding window (receiver side)
Window of in-flight packets can look different between sender and the receiver
Receiver only accepts sequence #s allowed by the current receiver window
0
1
2
3
4
5
6
7
1
0
Window size = 3
Last seq # received and ACK’ed by receiver
Highest sequence # accepted
Receiver’s point of view:
Receiver will not accept this seq #. Packet dropped

## Slide 14: Summary of sliding windows
Sender and receiver can keep several packets of in-flight data
  Book-keep the sequence numbers using the window
Windows slide forward as packets are ACKed (at receiver) and ACKs are received (at sender)
Common case: Improve throughput by sending and ACKing more packets in the same duration

## Slide 15
Pipelining makes reliable data transfer efficient.
However, pipelining also makes it more complex.
Which packets were successfully delivered?
Which packets should the sender retransmit?
Which packets are currently in flight?

## Slide 16: Which packets to retransmit?

## Slide 17: How to identify dropped packets?
Suppose 4 packets sent, but 1 dropped. How does sender know which one(s) dropped?
Recall: Receiver writes sequence numbers on the ACK indicating successful reception
Key idea: Sender can infer which data was received successfully using the ACK #s
  Hence, sender can know which data to retransmit
Q1: Should receivers ACK subsequent packets upon detecting data loss?
Q2: If so, what sequence number should receiver put on the ACK?
Sender
Receiver
RTT
RTO
Should this ACK exist ???
SEQ 1
SEQ 2
SEQ 3
SEQ 4
ACK 2
ACK 3
ACK ??

## Slide 18: Receiver strategies upon packet loss
Sender
Receiver
1
2
3
4
5
ACK pkts after a drop?
Go-back-N
Selective Repeat
What # on ACK?
Last seq# in order
Cumulative ACK
Seq# ranges received so far
Selective ACK
No
Yes
TCP’s default

## Slide 19: Sliding Window with Go Back N
When the receiver notices missing data:
It simply discards all data with greater sequence numbers
  i.e.: the receiver will send no further ACKs
The sender will eventually time out (RTO) and retransmit all the data in its sending window
Subtle: conceptually, separate timer per byte to infer RTO

## Slide 20: Go back N
Discarded by
receiver
Dropped packet
(or) Packet with
error
RTO
ACK 1
Time
Sender
Receiver
Maximum
window size = 8
Maximum
window size = 8
0
0
1
1
ACK 2
2
E
3
D
4
D
2
3
2
ACK 3
4
5
6
3
4
5
ACK 4
ACK 5
ACK 6
6
ACK 7

## Slide 21: Go back N
Go Back N can recover from erroneous or missing packets.
But it is wasteful.
If there are errors, the sender will spend time and network bandwidth retransmitting data the receiver has already seen.

## Slide 22: Selective repeat with cumulative ACK
Idea: sender should only retransmit dropped/corrupted data.
The receiver stores all the correct frames that arrive following the bad one. (Note that the receiver requires memory to hold data for each sequence number in the receiver window.)
When the receiver notices a skipped sequence number, it keeps acknowledging the first in-order sequence number it wants to receive. This is termed cumulative ACK.
When the sender times out waiting for an acknowledgement, it just retransmits the first unacknowledged data, not all its successors.
Recall that RTO applies independently to each sequence #

## Slide 23: Selective repeat with cumulative ACK
Buffered by
receiver in
its memory
Packet with
error (or)
dropped packet
RTO
ACK 1
Time
Sender
Receiver
Maximum
window size = 8
Maximum
window size = 8
0
0
1
1
ACK 2
2
E
3
4
2
5
2
ACK 5
6
5
ACK 6
6
ACK 7
3
4
ACK 2
ACK 2

## Slide 24: Selective repeat with selective ACK
Buffered by
receiver in
its memory
Frame with
error
RTO
ACK 1
Time
Sender
Receiver
Maximum
window size = 8
Maximum
window size = 8
0
0
1
1
ACK 2
2
E
3
4
2
5
2
ACK 5
6
5
ACK 6
6
ACK 7
3
4
ACK 2
SACK 3
ACK 2
SACK 3--4
Assume that SACKs reported alongside cumulative ACK

## Slide 25: TCP: Cumulative & Selective ACKs
Sender retransmits the seq #s it thinks aren’t received successfully yet
Pros & cons: selective vs. cumulative ACKs
  Precision of info available to sender
  Redundancy of retransmissions
  Packet header space
  Complexity (and bugs) in transport software
On modern Linux, TCP uses selective ACKs by default
Sender
Receiver
1
2
3
4
2
3
4
5
5