## Slide 1: 552: Six Basic Problems in Networking
Srinivas Narayana
Fall 2020

## Slide 2: What is a network?
Carrier of information between two or more entities
Entities may be hosts/endpoints (used interchangeably)
  your laptop, cell phone, etc.
Entities may also be devices in the middle of the network
  For example, your WiFi router
The interconnection between entities is any physical medium capable of carrying information: we call physical media links
  copper wire, lasers (over optic fibre), microwave, cable (coax), satellite link, wireless link (cellular, 802.11, bluetooth)

## Slide 3: A single link multiple access network
Send bits of data in packets or frames
How do we differentiate among many receivers?
Every endpoint as a link level address: also called a MAC address
Packets have a destination address on them
However, can’t have every computer in the world on the same link!
  Physical limits on power / distance over which info travels over a single link

## Slide 4: A single link multiple access network
Even on a single link, you need to worry about a few things:
Converting digital data to physical signals over the medium (encode/decode)
How do we decide who speaks? (medium access control problem)
Detecting and correcting errors
1

## Slide 5: A multi-link network
Connect multiple links via routers
Need to figure out how to move packets from one host to another host, e.g., how to reach google.com from your laptop
Known as the routing problem
Key Q: How should packets be moved from A to reach B?
Router
Router
Router
2

## Slide 6: In general, networks give no guarantees
Packets may be lost, corrupted, reordered, on the way to the destination
  Best effort delivery
Advantage: The network becomes very simple to build
  Don’t have to make it reliable
  Don’t need to implement any performance guarantees
  Don’t need to maintain packet ordering
  Almost any medium can deliver individual packets
    RFC 1149: “IP Datagrams over Avian Carriers”
The early Internet thrived since (transient) disruptions are okay

## Slide 7: Guarantees for applications
How should endpoints provide guarantees to applications?
Transport software on the endpoint oversees implementing guarantees on top of an unreliable network
Two important guarantees
  Reliability
  Ordered delivery of data

## Slide 8: Sending data into a multi-link network
How quickly should endpoints send data into a network?
Known as the congestion control problem
Congestion control algorithms at source endpoints react to remote network congestion. Part of the transport sw/hw stack.
Key question: How to vary the sending rate based on network signals?
3

## Slide 9: Sending data into a multi-link network
How should a router transmit packets when network resources are scarce?
Known as the packet scheduling problem
Key question: which packet to transmit over a constrained network link, and when?
  Related: the buffer management problem
4

## Slide 10: Building a high-speed network
As a network designer/operator, you’d like routers to connect endpoints with high performance
The interconnection problem: how do you interconnect the routers to achieve high end-to-end performance between endpoints?
  Designing the core of the network
  Applicable to large clusters (e.g., run by Google or Instagram) as well as a single high-speed router
5

## Slide 11: Operating a high-speed network
As a network operator, you want to ensure your network is doing what you think it’s doing:
  E.g., pkts going in the routes they ought to
  E.g., access control policies
The verification problem: ensuring that network mechanisms in operations satisfy policies of interest
  Verification is stronger than testing: we want to show the absence of bugs
  Applicable to large networks, and also single programs running on hosts
6

## Slide 12: Other “meta” problems
Flexibility: How to make it easy to program networks?
  Support a wide range of developer and operator policies
  Applicable to routing, transport, packet scheduling
Performance: How to ensure the network is “fast”?
  User tolerance is wearing thin (e.g., web: 300 ms + always up)
  Application + server footprints increasing (10K servers/req/job)
  Nanoseconds may matter; we’ll see examples later