## Slide 1: Host-to-network layer: (a) Physical Layer
The physical layer transmits the raw bit stream between two endpoints of a physical link
Functions:
  Modulation of bits over physical signals
  Performing bit-serial or parallel signal transmission
  Half- or Full-duplex transmission
Concerns
  How many pins does the network connector have?
  How is physical connectivity set up or torn down?

## Slide 2: Host-to-network layer: (b) Data Link Layer
The data link layer provides the network layer with what appears to be an error-free link to the other side of the link
Functions:
  Provides reliable transfer of information between two adjacent nodes
  Creates frames, or packets, from bits and vice versa
  Provides frame-level error control

## Slide 3: Network Layer
Network layer protocols move (“route”) host data towards destination
Best effort: network will try its best, but no guarantees.
Network layer implemented differently on hosts and routers
Functions:
  Responsible for routing decisions
  Routing may be fixed or dynamic

## Slide 4: Transport Layer
Handles host to host data transmission concerns
  Almost fully implemented on hosts
  Hides the details of the network from the application
    Example: If we replace a point-to-point link with a satellite link, it doesn’t affect the behavior of the upper layers
Functions:
  Reliable delivery: Packet retransmission upon loss
  Ordered delivery: Reassemble packets in order at receiver
  Flow control: Ensure that the receiving host isn’t overwhelmed
  Congestion control: Ensure that routers aren’t overwhelmed

## Slide 5: Application Layer
Implements application-specific communication between hosts running applications of the same “type”
  Ex: between your web browser and a web server (HTTP)
Functions:
  Provides session support and presentation support
  Session state, encryption, encoding
Examples:
  FTP, HTTP, SMTP (email), SIP (Session Initiation Protocol)

## Slide 6: Hourglass Design
An artifact of the history of the Internet
  Addressing a need to have diverse kinds of networks cooperate
The Internet Protocol (IP) is the “glue” connecting different physical technologies, transports, and applications
…
FTP
HTTP
SIP
RTSP
TCP
UDP
IP
NET
1
NET
2
NET
n
HTTPS

## Slide 7: Design principles of the Internet
“multiplexed utilization of existing interconnected networks”

## Slide 8: Design principles of the Internet
Accommodate heterogeneity
  Interoperate with different technologies, autonomous organizations
Resilience to failure
  Parts of the network must operate despite others failing
Scale
  Distributed management, networks of different sizes and host types
Intelligence is at the endpoints (“the end-to-end argument”)
  Much easier to engineer a network with fewer guarantees (best effort)
  Hosts and applications share fate anyway

## Slide 10: Backup slides

## Slide 11: Issues at each layer
Application
Transport
Network
Link
Routing
End-to-end
Access
Address
Port#

## Slide 12: functionality at each layer
Application
Transport
Network
Link
Routing
Access
IP Address
Port#
E-2-E

## Slide 13: Internet Design Principles
  Scale
    Protocols should work in networks of all sizes and distances
  Incremental deployment
    New protocols need to be deployed gradually
  Heterogeneity
    Different technologies, autonomous organizations
  End-to-end argument
    Application requirements, to the extent possible should be delegated to the edges; application knows best
    Encryption: Should the network provide as default or let applications or end points implement encryption on a need basis?

## Slide 14: Measuring a Network’s Performance
A Brief Introduction

## Slide 15: Some Definitions
Packet length: size of a packet (units = bits or bytes)
Channel speed or bandwidth: How fast the channel can transmit bits (units = bits/second or Bytes/second or packets/second)
Packet transmission time: amount of time to transmit an entire packet (units = seconds)
Propagation delay: Delay imposed by the properties of the link. Depends on the link’s distance (units = seconds)
Total transfer time =propagation delay + packet transmission time

## Slide 16: Digression: Units
Bits are the units used to describe an amount of data in a network
  1 kilobit (Kbit) = 1 x 103 bits = 1,000 bits
  1 megabit (Mbit) = 1 x 106 bits = 1,000,000 bits
  1 gigabit (Gbit) = 1 x 109 bits = 1,000,000,000 bits
Seconds are the units used to measure time
  1 millisecond (msec) = 1 x 10-3 seconds = 0.001 seconds
  1 microsecond (msec) = 1 x 10-6 seconds = 0.000001 seconds
  1 nanosecond (nsec) = 1 x 10-9 seconds = 0.000000001 seconds
Bits per second are the units used to measure channel capacity/bandwidth and throughput
  bit per second (bps)
  kilobits per second (Kbps)
  megabits per second (Mbps)
Bytes (8 bits a byte) Mega bytes, Giga bytes, Tera bytes, Peta Bytes, Exa bytes

## Slide 17: Example
packet length = 1500 bytes
channel capacity = 10 Mbps
propagation delay factor = 5 msec/km
A
B
500 m
How long does it take a single bit to travel on the link from A to B?
How long does it take A to transmit an entire packet onto the link?

## Slide 18: Propagation Delay
How long does it take a single bit to travel on the link from A to B of length 500 m with a prop. delay factor = 5 msec/km ?
Another way to ask this question:
If it takes a signal 5 msec to travel 1 kilometer, then how long does it take a signal to travel 500 meters?
5 msec
1000 m
=
500 m
t
Solving for t…
t = 2.5 msec

## Slide 19: Packet Transmission Time
1500 x 8 bits
How long does it take A to transmit an entire packet onto the link?
Relevant information: packet length = 1500 bytes
channel speed = 10 Mbps
Another way to ask this question:
If the link can transmit 10 million bits in a second, how many seconds does it take to transmit 1500 bytes (8x1500 bits)?
10 Mbits
1 sec
=
t
Solving for t…
t = 0.0012 sec (or 1.2 msec)

## Slide 20: Message switching vs Packet switching
Link speed is 1000 Bytes/sec. (ignore prop delay)
Packet size is 100 Bytes, file size is 1000 Bytes
Find total time to transfer the entire file under the two switching techniques
  Msg switching
  Packet switching
R1

## Slide 21: Message switching vs Packet switching
Link speed is 1000 Bps. (prop delay for each link=10 msec)
Packet size is 100 bytes, file size is 1000 bytes
Find total time to transfer the entire file under the two switching techniques
  Msg switching
  Packet switching
R1

## Slide 22: Message switching vs Packet switching
Link speed is 1000 Bytes per second . (ignore prop delay, ignore header overhead)
Packet size is 100 Bytes, file size is 1000 Bytes
Find total time to transfer the entire file under the two switching techniques
L1
L2
L3
R1
R2