## Slide 1
Lecture 2, Computer Networks (198:552)
Internet Architecture

## Slide 2: Edge vs. core division of labor
Core: the network consisting of routers
  Best-effort packet delivery
Edge: the endpoints
  Transport mechanisms to satisfy app needs
The Internet

## Slide 3: What happens when you browse?
The Internet

## Slide 4: What happens when you browse?
The Internet
(1) Request gmail.com for your mail
(2) Google churns on your request
(3) Receive & display the response!

## Slide 5: But how does your laptop know how to reach gmail.com?

## Slide 6: Directories!
“You know my name, now find my street address”
In networking, an address can mean many things
Both your laptop and Google’s servers have many addresses

## Slide 7
The Internet
Rutgers campus network
Hardware address (MAC address)
Ex: 00-15-C5-49-04-A9
Network address (IP address)
Ex: 192.168.1.4
Transport address (port)
Ex: 64058
How do I identify my network interface (device)?
Whose network am I associated with?
With which app is this conversation associated?

## Slide 8
Hardware address (MAC address)
Ex: 00-15-C5-49-04-A7
Network address (IP address)
Ex: 10.1.1.104
Transport address (port)
Ex: 4096
Application address (URL)
Ex: mail.google.com
The Internet
Google’s network

## Slide 9: Modularity through layering
Link: best-effort local pkt delivery
Network: best-effort global pkt delivery
Transport: provide guarantees to apps
Apps: useful user-level functions
HTTP
FTP
TFTP
NV
TCP
UDP
IP
Ether
ATM
WiFi
…
Protocols “stacked” in endpoint and router software/hardware
IP is the “thin waist” of the Internet, enabling
interoperability across apps & network media

## Slide 10
Link layer
Network
Transport
Applications
The Internet
Link layer
Network
Transport
Applications
The Internet
Pkt takes on info at each layer
Pkt starts as an
app “payload”

## Slide 11
Link layer
Network
Transport
Applications
Link layer
Network
Transport
Applications
Link layer
Network
Link layer
Network

## Slide 12
Link layer
Network
Transport
Applications
Link layer
Network
Transport
Applications
Link layer
Network
Link layer
Network
The core does not (usually) contain transport or app functionality.

## Slide 13: How does your laptop find gmail.com?
So many network addresses…
Ideas?

## Slide 14
The Internet
Rutgers campus network
Hardware address (MAC address)
Network address (IP address)
Transport address (port)
How do I identify my network interface (device)?
Whose network am I associated with?
With which app is this conversation associated?

## Slide 15: Directories and Routing

## Slide 16: Types of Directories
Directories map a name to an address
Simplistic designs
  Central directory
  Ask everyone (e.g., flooding in ARP)
  Tell everyone (e.g., pushing /etc/hosts)
Scalable distributed designs
  Hierarchical namespace (e.g., DNS)
  Flat name space (e.g., Distributed Hash Table)

## Slide 17: Path computation
“I know where you are, but how do I get there?”
End-to-end paths (e.g., source routing)
  Each node picks the best end-to-end path
Spanning tree (e.g., Ethernet)
  One tree that connects every pair of nodes
Shortest paths (e.g., OSPF, IS-IS, RIP)
  Shortest-path tree rooted at each node
Locally optimal paths (e.g., BGP)
  Each node selects the best among its neighbors

## Slide 18: The role of the endpoint

## Slide 19: The role of the endpoint
Network discovery and bootstrapping
  How does the endpoint join the network?
  How does the endpoint get an address?
Interface to networked applications
  What interface to higher-level applications?
  How does the host realize that abstraction?
Distributed resource sharing
  What roles does the host play in network resource allocation decisions?

## Slide 20: Learning a host’s address
Who am I?
  Hard-wired: MAC address
  Static configuration: IP interface configuration
  Dynamically learned: IP address configured by DHCP
Who are you?
  Hard-wired: IP address in a URL, or in the code
  Dynamically looked up: ARP or DNS
me
you
adapter
adapter
Rutgers
campus net

## Slide 21: Mapping between identifiers
Dynamic Host Configuration Protocol (DHCP)
  Given a MAC address, assign a unique IP address
  … and tell host other stuff about the Local Area Network
  To automate the boot-strapping process
Address Resolution Protocol (ARP)
  Given an IP address, provide the MAC address
  To enable communication within the Local Area Network
Domain Name System (DNS)
  Given a host name, provide the IP address
  Given an IP address, provide the host name

## Slide 22: Dynamic Host Configuration Protocol
arriving client
DHCP server
DHCP discover
(broadcast)
DHCP offer
DHCP request
DHCP ACK
(broadcast)
Host learns IP address,
Subnet mask, Gateway address, DNS server(s), and a lease time.

## Slide 23: Address Resolution Protocol (ARP)
Every host maintains an ARP table
  (IP address, MAC address) pair
Consult the table when sending a packet
  Map destination IP address to destination MAC address
  Encapsulate and transmit the data packet
But, what if the IP address is not in the table?
  Sender broadcasts: “Who has IP address 1.2.3.156?”
  Receiver responds: “MAC address 58-23-D7-FA-20-B0”
  Sender caches the result in its ARP table

## Slide 24: Domain Name System
requesting host
cis.poly.edu
gaia.cs.umass.edu
root DNS server
local DNS server
dns.poly.edu
1
2
3
4
5
6
authoritative DNS server
dns.cs.umass.edu
7
8
TLD DNS server
Host at cis.poly.edu wants IP address for gaia.cs.umass.edu
Recursive query: #1
Iterative queries: #2, 4, 6

## Slide 25: Why so many addresses?
Can we get rid of some of these addresses? De we need all three?
Should addresses correspond to the point of attachment, or to the endpoint itself?
How do you prevent spoofing addresses?

## Slide 26: Interface to Applications

## Slide 27: Socket Abstraction
Best-effort packet delivery is a clumsy abstraction
  Applications typically want higher-level abstractions
  Messages, uncorrupted data, reliable in-order delivery
Applications communicate using “sockets”
  Stream socket: reliable stream of bytes (like a file)
  Message socket: unreliable message delivery
socket
socket
User process
User process
Operating
System
Operating
System

## Slide 28: Two Basic Transport Features
Demultiplexing: port numbers
Error detection: checksums
Web server
(port 80)
Client host
Server host 128.2.194.242
Echo server
(port 7)
Service request for
128.2.194.242:80
(i.e., the Web server)
OS
Client
IP
payload
detect corruption

## Slide 29: Two Main Transport Layers
User Datagram Protocol (UDP)
  Just provides demultiplexing and error detection
  Header fields: port numbers, checksum, and length
  Low overhead, good for query/response and multimedia
Transmission Control Protocol (TCP)
  Adds support for a “stream of bytes” abstraction
  Retransmitting lost or corrupted data
  Putting out-of-order data back in order
  Preventing overflow of the receiver buffer
  Adapting the sending rate to alleviate congestion
  Higher overhead, good for most stateful applications

## Slide 30: Questions
Is a socket between two IP addresses the right abstraction?
  Mobile hosts?
  Replicated services?
What does the network know about the traffic?
  Inferring the application from the port numbers?
Is end-to-end error detection and correction the right model?
  High loss environments?
  Expense of retransmitting over the entire path?

## Slide 31: Distributed Resource Sharing

## Slide 32: Resource allocation challenges
Best-effort network easily becomes overloaded
  No mechanism to “block” excess calls
  Instead excess packets are simply dropped
Examples
  Shared Ethernet medium: frame collisions
  Ethernet switches and IP routers: full packet buffers
Quickly leads to congestion collapse
Load
Goodput
“congestion
collapse”
Increase in load that results in a decrease in useful work done.

## Slide 33: Endpoints adjusting to congestion
End hosts adapt their sending rates
  In response to network conditions
Learning that the network is congested
  Shared Ethernet: carrier sense multiple access
    Seeing your own frame collide with others
  IP network: observing your end-to-end performance
    Packet delay or loss over the end-to-end path
Adapting to congestion
  Slowing down the sending rate, for the greater good
  But, host doesn’t know how bad things might be…

## Slide 34: Ethernet back-off mechanism
Carrier sense: wait for link to be idle
  If idle, start sending; if not, wait until idle
Collision detection: listen while transmitting
  If collision: abort transmission, and send jam signal
Exponential back-off: wait before retransmitting
  Wait random time, exponentially larger on each retry

## Slide 35: TCP congestion control
Additive increase, multiplicative decrease
  On packet loss, divide congestion window in half
  On success for last window, increase window linearly
t
Window
halved
Loss
Other mechanisms: slow start, fast retransmit vs. timeout loss, etc.

## Slide 36: Questions
What role should the network play in resource allocation?
  Explicit feedback to the end hosts?
  Enforcing an explicit rate allocation?
What is a good definition of fairness?
What about hosts who cheat to hog resources?
  How to detect cheating? How to prevent/punish?
What about wireless networks?
  Difficulty of detecting collisions (due to fading)
  Loss caused by interference, not just congestion

## Slide 37: End-to-End Arguments in System Design (ACM Trans. on Computer Systems, November 1984)
J. Saltzer, D. Reed, and D. Clark

## Slide 38: End-to-end argument
Operations should occur only at the end points
… unless needed for performance optimization
2
4
5
3
1
Many things can go wrong: disk errors, software errors, hardware errors, communication errors, …

## Slide 39: Trade-offs
Put functionality at each hop
  All applications pay the price
  End systems still need to check for errors
Place functionality only at the ends
  Slower error detection
  End-to-end retransmission wastes bandwidth
Compromise solution?
  Reliable end-to-end transport protocol (TCP)
  Plus file checksums to detect file-system errors

## Slide 40: Discussion
When should the network support a function anyway?
  E.g., link-layer retransmission in wireless networks?
Who’s interests are served by the e2e argument?
How does a network operator influence the network without violating the e2e argument?
Does the design of IP and TCP make it *hard* to violate the e2e argument?
  E.g., middlebox functionality like NATs, firewalls, proxies
Should the e2e argument apply to routing?

## Slide 41: The Design Philosophy of the DARPA Internet Protocols ACM SIGCOMM, 1988
David Clark

## Slide 42: Life in the 1970s…
Multiple unconnected networks
  ARPAnet, data-over-cable, packet satellite (Aloha), packet radio, …
Heterogeneous designs
  Addressing, max packet size, handling of lost/corrupted data, fault detection, routing, …
ARPAnet
satellite net

## Slide 43: Goals of initial Internet designers
Interconnect and multiplex resources of existing networks
Survive failures:
  Must communicate so long as there is a physical path
  Don’t place any state in the network core!
Support multiple types of communication service
  Best-effort network: don’t impose any guarantees
  Have endpoints build services with the desired guarantees
Others: distributed resource mgmt, easy host attachment, …

## Slide 44: Discussion
Were the initial designers right to prioritize the goals they did?
  Which goals still seem valid today, and which ones not?
  Which goals were crucial to the Internet’s success?
Should network designers have resorted to best-effort?
  Hard to measure: Compare to civil engineers and bridges
  Accountability is hard when things go wrong
Is there a better substrate to offer multiple types of service?
  What might be the associated costs?
  What would you do differently today?

## Slide 45: Until next time…
MUD: Send me your top 1—3 questions on this lecture
Readings for next class: 4D, ALF
  Papers can take a few hours to understand, and that’s OK
Start thinking of project ideas
  Discuss during office hours