## Slide 1: Administrivia
Review 1 paper assignments are out
  See me after lecture if you haven’t yet received your assignment
MUD: Send me your top 1—3 questions on this lecture
Brainstorm project ideas (teams of 1—3)
  Discuss with me during office hours or by appointment
Today: Some more examples of division of labor….

## Slide 2: End-to-end arguments in system design
(ACM Trans. on Computer Systems, November 1984)
J. Saltzer, D. Reed, and D. Clark

## Slide 3: End-to-end argument
Operations should occur only at the end points
… unless needed for performance optimization
2
4
5
3
1
Many things can go wrong: disk errors, software errors, hardware errors, communication errors, …

## Slide 4: Trade-offs
Put functionality at each hop
  All applications pay the price
  End systems still need to check for errors
Place functionality only at the ends
  Slower error detection
  End-to-end retransmission wastes bandwidth
Compromise solution?
  Reliable end-to-end transport protocol (TCP)
    Plus file checksums to detect file-system errors
  “Reasonably reliable” communication network

## Slide 5
Lecture 3, Computer Networks (198:552)
Control-Data Plane Separation

## Slide 6: Edge vs. Core
Core: the network consisting of routers
Edge: the endpoints
The Core
What’s here?

## Slide 7: Core: Split into data and control planes
Data plane: handle packets
  Handle individual packets as they arrive
  Forward, drop, or buffer
  Mark, schedule, measure, …
Control plane: handle events
  Compute paths through the network
  Track changes in network topology
  Reserve resources along a path
Motivated by need for high-speed packet forwarding

## Slide 8: Adding the management plane
Make networks run well
  The right traffic reaches the right destination
  Traffic flows over short, uncongested paths
  Failure recovery happens quickly
  Routers don’t run out of resources
A control loop with the network
  Measure (sense): topology, traffic, performance, …
  Control (actuate): configure control and data planes

## Slide 9: Data and Control Planes in a Router
Switching
fabric
Processor
Line card
Line card
Line card
Line card
Line card
Line card
data plane
control plane

## Slide 10: Forwarding vs. Routing
Forwarding: data plane
  Router directs packets to an output port
  … by looking up a forwarding table
Routing: control plane
  Routers talk amongst themselves
  .. to compute the forwarding table
Destination IP | Subnet mask | Output port
10.0.0.0 | 255.255.255.0 | 4
8.4.5.3 | 255.0.0.0 | 1

## Slide 11: Each router creates its own forwarding table … but the computation itself is distributed.

## Slide 12: Routing protocols enable FT computation
What does the protocol compute?
  Spanning tree, shortest path, local policy, arbitrary end-to-end paths
What algorithm does the protocol run?
  Spanning-tree construction, distance vector, link-state routing, path-vector routing, source routing, end-to-end signaling
How do routers learn end-host locations?
  Learning/flooding, injecting into the routing protocol, dissemination using a different protocol, and directory server

## Slide 13: What does the protocol compute?
(the outcome, not the computation)

## Slide 14: Different ways to represent paths
Trade-offs
  State required to represent the paths
  Efficiency of the resulting paths
  Ability to support multiple paths
  Complexity of computing the paths
  Which nodes are in charge
Applied in different settings
  LAN, intra-domain, inter-domain

## Slide 15: Spanning tree (Ethernet)
One tree that reaches every node
  Single path between each pair of nodes
  No loops, so can support broadcast easily
Disadvantages
  Paths are sometimes long
  Some links are not used at all

## Slide 16: Shortest paths (OSPF/IS-IS)
Shortest path(s) between each pair of nodes
  Separate shortest-path tree rooted at each node
  Minimum hop count or minimum sum of edge weights
Disadvantages
  All nodes need to agree on the link metrics
  Multipath routing is limited to Equal cost multiPath
Set by network administrator

## Slide 17: Local policy at each hop (BGP)
Locally best path
  Local policy: each node picks the path it likes best
  … among the paths chosen by its neighbors
Disadvantages
  More complicated to configure and model
2
3
1
4
d
5
6
1 d
1 2 d
2 1 d
2 d
3 2 d
3 4 d
4 d
5 4 d
6 4 d
6 5 4 d
2
3
1
4
d
5
6
1 d
1 2 d
2 1 d
2 d
4 d
3 2 d
3 4 d
5 4 d
6 4 d
6 5 4 d

## Slide 18: End-to-end path selection (IP src route)
End-to-end path selection
  Each node picks its own end to end paths
  … independent of what other paths other nodes use
Disadvantages
  More state and complexity in the nodes
  Hop-by-hop destination-based forwarding is not enough

## Slide 19: How to compute paths?

## Slide 20: Spanning tree algorithm (Ethernet)
Elect a root
  The switch with the smallest identifier
  And form a tree from there
Algorithm
  Repeatedly talk to neighbors
    “I think node Y is the root”
    “My distance from Y is d”
  Update information based on neighbors
    Smaller id as the root
    Smaller distance d+1
  Don’t use interfaces not in the path
root
One hop
Three hops

## Slide 21: Spanning tree example: switch #4
Switch #4 thinks it is the root
  Sends (4, 0) message to 2 and 7
Switch #4 hears from #2
  Receives (2, 0) message from 2
  … and thinks that #2 is the root
  And realizes it is just one hop away
Switch #4 hears from #7
  Receives (2, 1) from 7
  And realizes this is a longer path
  So, prefers its own one-hop path
  And removes 4-7 link from the tree
1
2
3
4
5
6
7

## Slide 22: Shortest-path problem
Compute: path costs to all nodes
  From a given source u to all other nodes
  Cost of the path through each outgoing link
  Next hop along the least-cost path to s
3
2
2
1
1
4
1
4
5
3
u
s
6

## Slide 23: Link-state: Dijkstra’s algorithm
S = {u}
for all nodes v
if (v is adjacent to u)
D(v) = c(u,v)
else D(v) = ∞
add w with smallest D(w) to S
update D(v) for all adjacent v:
D(v) = min{D(v), D(w) + c(w,v)}
until all nodes are in S
Flood the topology information to all nodes
Each node computes shortest paths to other nodes
Initialization
Loop

## Slide 24: Link-state routing example (OSPF/IS-IS)
3
2
2
1
1
4
1
4
5
3
3
2
2
1
1
4
1
4
5
3
3
2
2
1
1
4
1
4
5
3
3
2
2
1
1
4
1
4
5
3

## Slide 25: Link-state routing example (cont.)
3
2
2
1
1
4
1
4
5
3
3
2
2
1
1
4
1
4
5
3
3
2
2
1
1
4
1
4
5
3
3
2
2
1
1
4
1
4
5
3

## Slide 26: Link-state: Shortest-path tree
Shortest-path tree from u
Forwarding table at u
3
2
2
1
1
4
1
4
5
3
u
v
w
x
y
z
s
t
v
(u,v)
w
(u,w)
x
(u,w)
y
(u,v)
z
(u,v)
link
s
(u,w)
t
(u,w)
Counter-intuitive: Operators may set the link metric to achieve certain shortest-path trees with the protocol

## Slide 27: Path-vector routing (BGP)
Key idea: advertise the entire path
Distance vector: send distance metric per dest d
Path vector: send the entire path for each dest d
3
2
1
d
“d: path (2,1)”
“d: path (1)”
data traffic
data traffic

## Slide 28: Path-vector: Fast loop detection
Node can easily detect a loop
  Look for its own node identifier in the path
  E.g., node 1 sees itself in the path “3, 2, 1”
Node can simply discard paths with loops
3
2
1
“d: path (2,1)”
“d: path (1)”
“d: path (3,2,1)”

## Slide 29: Path-vector: Flexible policies
Each node can apply local policies
  Path selection: Which path to use?
  Path export: Which paths to advertise?
Examples
  Node 2 may prefer the path “2, 3, 1” over “2, 1”
  Node 1 may not let node 3 hear the path “1, 2”
2
3
1
2
3
1

## Slide 30
Why are these algorithms distributed?

## Slide 31: Learning the location of the endpoints

## Slide 32: Finding the endpoints
Computing the forwarding table
  Still must figure out where the endpoints are
How to find the endpoints?
  Learning/flooding (Ethernet)
  Injecting into the routing protocol
  Dissemination using a different protocol
  Central directory service
Ways to curb scaling challenges
  E.g., spanning tree per VLAN for endpoint flooding

## Slide 33: Ex: Disseminate with another protocol
One router learns the route
… and shares the information with other routers
learn a route to d
(e.g., via BGP)
disseminate route to other routers
Internal BGP (iBGP) used in backbone networks

## Slide 34: Conclusion
Routing is a distributed computation
  With challenges in scalability and handling dynamics
Different solutions for different environments
  Ethernet LAN: spanning tree, MAC learning, flooding
  Enterprise: link-state routing, injecting subnet addresses
  Backbone: link-state routing inside, path-vector routing with neighboring domains, and iBGP dissemination
  Data centers: many different solutions, still in flux
    An active research area…

## Slide 35: Clean-slate 4D architecture
ACM Computer Communications Review (CCR) 2005
Greenberg et al.

## Slide 36: Three goals of 4D architecture
Network-level objectives
  Configure the network globally; not each router
  E.g., minimize the maximum link utilization
  E.g., connectivity under all layer-two failures
Network-wide views
  Complete visibility to drive decision-making
  Traffic matrix, network topology, equipment
Direct control
  Direct, complete control over data-plane configuration
  Packet forwarding, filtering, marking, buffering…

## Slide 37: 4D: The four planes
Decision: all management and control logic
Dissemination: communication to/from the routers
Discovery: topology and traffic monitoring
Data: packet handling
routers
Decision
Dissemination
Discovery
Data
Network-level objectives
Direct control
Network-wide views

## Slide 38: Decision plane
All mgmt logic implemented on “decision elements” (servers)
  … which make all decisions for the network
Decision elements use network-wide views to compute data plane state that meets objectives
  … then directly writes this state to routers!
Decision
Dissemination
Discovery
Data
Network-level objectives
Direct control
Network-wide views

## Slide 39: Decision plane
All mgmt logic implemented on “decision elements” (servers)
  … which make all decisions for the network
Decision elements use network-wide views to compute data plane state that meets objectives
  … then directly writes this state to routers!
Decision
Dissemination
Discovery
Data
Network-level objectives
Direct control
Network-wide views

## Slide 40: Dissemination plane
Provides a robust communication channel to each router
May run over same links as user data
  However, logically separate and independently controlled
Decision
Dissemination
Discovery
Data
Network-level objectives
Direct control
Network-wide views

## Slide 41: Discovery Plane
Each router discovers its own resources and its local environment
Each router propagates information (e.g., topology, traffic) to the decision elements via dissemination plane
Decision
Dissemination
Discovery
Data
Network-level objectives
Direct control
Network-wide views

## Slide 42: Data Plane
Spatially distributed routers/switches
Forward, drop, buffer, shape, mark, rewrite, …
Can deploy with new or existing technology
Decision
Dissemination
Discovery
Data
Network-level objectives
Direct control
Network-wide views

## Slide 43: Practical technical challenges
Scalability: Decision elements responsible for many routers
Response time: Delays between decision elements and routers
Reliability: Surviving failures of decision elements, routers, and the dissemination plane
Consistency: Ensuring multiple decision elements behave consistently
Security: Network vulnerable to attacks on decision elements
Interoperability: Legacy routers and neighboring domains
Networking meets Distributed Systems

## Slide 44: Architectural considerations for new protocols
ACM SIGCOMM conference 1990
David Clark and David Tennenhouse

## Slide 45
Switching
fabric
Processor
Line card
Line card
Line card
Line card
Line card
Line card
data
plane
control
plane
Data
manipulation
Transfer
control
Router
Endpoint transport
data plane
control plane

## Slide 46: What limits performance of transport?
Transfer control: do infrequently over connection lifetime
  Flow and congestion control
  Loss and reordering, app multiplexing, …
Data manipulation: on every byte!
  Moving data from network adapter to endpoint memory
  Per-packet error correction
  Presentation conversion
00-FA-4C-2D-…
(on the wire)
struct keyval {
key: #...;
val: #...;
location: …;
}

## Slide 47: Two key ideas
App-level framing (ALF)
  Transport knows little about what data loss means to the app
  Transport should deliver data to app as App Data Units (ADUs)
    Natural boundary for error correction and application processing
Integrated layer processing (ILP)
  Process ADU to completion, including all data manipulation
  Performance improvement:
    Reduction in number of memory accesses
    Remove indirect overheads due to cache misses and TLB flushes

## Slide 48: Discussion
Does ALF support any functionality that TCP/UDP don’t?
Does ALF run contrary to layered design?
  Pros and cons of these two implementations?
Is presentation conversion still the dominant bottleneck?
  Why? Why not? If not, what has changed?
Why should we always run presentation conversion at its full rate?
What systems design principles did you derive from this paper?

## Slide 49: Until next time…
MUD: Send me your top 1—3 questions on this lecture
Readings for next class: Jacobson’s TCP, XCP
Brainstorm project ideas (teams of 1—3)

## Slide 52: Backup slides

## Slide 53: Discussion questions for E2E argument
When should the network support a function anyway?
  E.g., link-layer retransmission in wireless networks?
Whose interests are served by the e2e argument?
How does a network operator influence the network without violating the e2e argument?
Does the design of IP and TCP make it *hard* to violate the e2e argument?
  E.g., middlebox functionality like NATs, firewalls, proxies
Should the e2e argument apply to routing?

## Slide 54: Distance Vector: Bellman-Ford Algo
Define distances at each node x
  dx(y) = cost of least-cost path from x to y
Update distances based on neighbors
  dx(y) = min {c(x,v) + dv(y)} over all neighbors v
3
2
2
1
1
4
1
4
5
3
u
v
w
x
y
z
s
t
du(z) = min{c(u,v) + dv(z),
c(u,w) + dw(z)}
Used in RIP and EIGRP

## Slide 55: Distance Vector: Count to Infinity
Link cost changes:
Good news travels fast
Bad news travels slow - “count to infinity” problem!
X
Z
1
4
50
Y
60
algorithm
continues
on!

## Slide 56: End-to-End Signaling
Establish end-to-end path in advance
  Learn the topology (as in link-state routing)
  End host or router computes and signals a path
Routers supports virtual circuits
  Signaling: install entry for each circuit at each hop
  Forwarding: look up the circuit id in the table
1
2
1: 7
2: 7
link 7
1: 14
2: 8
link 14
link 8
Used in MPLS with RSVP

## Slide 57: Source Routing
Similar to end-to-end signaling
  But the data packet carries the hops in the path
  … rather than the routers storing big tables
End-host control
  Tell the end host the topology
  Let the end host select the end-to-end path
Variations of source routing
  Strict: specify every hop
  Loose: specify intermediate points
Used in IP source routing (but almost always disabled)