## Slide 1
Lecture 8, Computer Networks (198:552)
Measurement

## Slide 2: Why measure networks?
ISP
Application QoS
Throughput
Delay
Loss
Jitter
ISP
ISP
Availability
Congestion/overload
Long-term demands
SLO violations
Application QoS
Problematic ISPs
Problematic CDNs

## Slide 3: Measurements for ISP Network Operators

## Slide 4: Example (1): Excess Traffic
Multi-homed customer
Two large flows of traffic
New egress point for first flow

## Slide 5: Example (2): DoS Attack
Web server at its knees…
Install packet
filter
Web server back to life…

## Slide 6: Example (3): Link Failure
Link failure
New route overloads a link
Routing change alleviates congestion

## Slide 7: Measurements for ISP network operators
Control
Measure
Detect link or path-level problems
Measure incoming traffic demands
“Measure” forwarding updates!
Route and schedule traffic
Filter traffic
Provision additional capacity
Diagnose root cause
Determine how to route traffic

## Slide 8: How do ISPs measure today?
Periodic link statistics
  SNMP counters
  Example: port1: 500 packets transmitted, 13 dropped
Periodic flow statistics
  NetFlow, sFlow, IPFIX
  Example: src: 10.0.0.1, dst:8.8.8.8, inport: 4, count: 45
Active end-to-end probes
  Ping: 64 bytes from 128.6.68.140: icmp_seq=0 ttl=55 time=6.575 ms
  Traceroute: more to come
User complaints!
  Customer phone calls, NANOG posts

## Slide 9: Diagnosis & Traffic engineering
Control plane issues
  New routes
  Link failures
  Network upgrades!
Data plane issues
  DoS attack
  Flash crowds
  Poor demand prediction, in general
“Decision plane” issues
  Poor provisioning
  Lack of peering
Lot of neat algorithms
& measurement systems
Quality of input data matters!
Scope to do a lot more…

## Slide 10: Challenge: Measurement data reduction
A network can’t capture every packet with timestamps
  Too much data!
Filter to restrict to data of interest
  Ex: by source, by app, by (physical) port, …
Sample to thin the data stream for exact computations
  Systematic, random, stratified
  “Consistently” sample same/distinct packet at each hop
Aggregate (ex: by flow) to summarize data over many packets
  One problem: too many flows
  Sketches: aggregation that approximates with limited memory

## Slide 11: Challenge: Joining traffic with forwarding
Web server at its knees…
Install packet
filter
Web server back to life…
Where is DoS traffic entering the network?
How do I know which traffic is DoS traffic?
Are there other links that are affected?
Should you reroute other traffic that is affected?

## Slide 12: End-to-End Measurements

## Slide 13: Why end-to-end measurements?
Endpoints could directly measure what matters to users
ISPs may not be willing to share data
  Proprietary design, net neutrality, …
  Data shared improperly may violate user privacy!
Indirect view: can’t say for sure why something happens
  Hard to corroborate with ground truth
  Possible to use multiple endpoints and span ISP boundaries!

## Slide 14: Metrics and tools
Reachability: ping & its variants
Path: traceroute & its variants
Available bandwidth: speedtest, iperf, pathrate, …
Delays and loss rate: a selection of the above tools

## Slide 15: Traceroute
Launch a probe packet towards DST, with a TTL of 1
Each router hop decrements the TTL of the packet by 1
When TTL hits 0, router returns ICMP TTL Exceeded
SRC host receives this ICMP, displays a traceroute “hop”
Repeat from step 1, with TTL incremented by 1, until…
DST host receives probe returns ICMP Dest Unreach
Notes: ACK https://www.nanog.org/meetings/nanog45/presentations/Sunday/RAS_traceroute_N45.pdf Richard Steenbergen NANOG 45

## Slide 16: Traceroute: Example output (1/2)
[552]$ traceroute google.com
traceroute to google.com (172.217.10.78), 64 hops max, 52 byte packets
1 fios_quantum_gateway (192.168.1.1) 1.628 ms 1.537 ms 1.506 ms
2 lo0-100.nwrknj-vfttp-354.verizon-gni.net (74.102.79.1) 2.093 ms 2.486 ms 1.835 ms
3 b3354.nwrknj-lcr-21.verizon-gni.net (100.41.137.110) 4.962 ms 2.935 ms 3.985 ms
4 * * *
5 0.et-10-1-5.gw7.ewr6.alter.net (140.222.2.233) 3.864 ms
0.et-11-1-0.gw7.ewr6.alter.net (140.222.239.27) 3.503 ms
0.et-10-1-5.gw7.ewr6.alter.net (140.222.2.233) 3.581 ms
6 209.85.149.208 (209.85.149.208) 3.949 ms 4.222 ms 4.669 ms
7 * * *
8 108.170.226.198 (108.170.226.198) 9.154 ms
108.170.237.214 (108.170.237.214) 7.080 ms
72.14.234.64 (72.14.234.64) 10.782 ms
9 lga34s14-in-f14.1e100.net (172.217.10.78) 4.097 ms
108.170.248.66 (108.170.248.66) 5.462 ms
108.170.248.20 (108.170.248.20) 9.410 ms

## Slide 17: Traceroute: Example output (2/2)
[552]$ traceroute rutgers.edu
traceroute to rutgers.edu (128.6.68.140), 64 hops max, 52 byte packets
1 fios_quantum_gateway (192.168.1.1) 1.536 ms 1.083 ms 1.098 ms
2 lo0-100.nwrknj-vfttp-354.verizon-gni.net (74.102.79.1) 2.343 ms 1.932 ms 1.948 ms
3 b3354.nwrknj-lcr-21.verizon-gni.net (100.41.137.110) 3.124 ms
b3354.nwrknj-lcr-22.verizon-gni.net (100.41.137.112) 4.026 ms 2.766 ms
4 * * *
5 * * *
6 0.ae1.gw1.phil.alter.net (140.222.0.221) 6.599 ms
0.ae6.gw1.phil.alter.net (140.222.0.223) 5.401 ms 5.670 ms
7 rutgers-gw.customer.alter.net (63.65.75.238) 5.061 ms 6.937 ms 6.205 ms
8 172.29.8.17 (172.29.8.17) 5.321 ms 5.475 ms 10.577 ms
9 172.29.6.63 (172.29.6.63) 6.500 ms 7.154 ms 7.254 ms
10 172.29.6.45 (172.29.6.45) 6.808 ms 6.799 ms 6.612 ms
11 172.28.193.138 (172.28.193.138) 8.201 ms 7.956 ms 8.180 ms
...
64 * * *

## Slide 18: Some problems with traceroute
Control traffic (ICMP) and data traffic may see different behavior
  Router CPU versus forwarding table
  Probes load-balanced differently
A different packet observes each hop
  Route changes while packet “in transit”
Not all routers may respond to ICMP messages
  Hidden routers
  Anonymous routers
  Improper processing
One-way measurement

## Slide 19: End-to-End Routing Behavior in the Internet
LBNL Technical Report (1996)
Vern Paxson

## Slide 20: Methodology
Traceroute between NPDs distributed worldwide (add pic)
Exponential sampling/PASTA property
  Why?
  What might happen otherwise?
D1: unidirectional traceroutes
D2: “paired” traceroutes
Confidence intervals for probability that an event occurred
Measurements sample half of the Internet by AS weight

## Slide 21: Pathologies in Internet routing
Forwarding loops!
  Persistent and temporary
Circuitous routing
Routing transients
  Recovery times are bimodal
Route fluttering
Partitioned network
Temporary outages, some > 30 seconds
Too many hops
Pathologies correlated with operator change and congestion

## Slide 22: Summary of pathologies

## Slide 23: Routing stability
Why does routing stability matter?
Prevalence: how frequently do you see a route?
  PASTA ensures that samples see “true” stable behavior
Persistence: how long does a given route persist over time?
  Challenging to measure!
  Example: R1, R2, R1, but samples miss the intermediate R2

## Slide 24: Routing prevalence

## Slide 25: Routing persistence

## Slide 26: Routing asymmetry
49% of D2 measurements saw asymmetric paths!
  visiting a different city each way around
  30% with a different AS!
Trend worsening over time

## Slide 27: A summary
No guarantees on where your traffic might end up
  A black-hole!
  Somewhere unintended (US eastLondon goes through Israel)
Routes are dominated by single winner but can be quite flappy
  Implications on what performance apps might expect
  What measurement tools provide
Asymmetry makes a lot of things complex
  Diagnosis: Assumptions about where problems lie
  Flow state in the core: can’t assume you’ll see return traffic

## Slide 28: Limitations of the study
Representativeness:
  Routes within an AS may not have similar characteristics!
  Sample a really small subset of actual Internet paths
Methodology:
  PASTA doesn’t hold when the network is down
  Hard to extrapolate trends in Internet evolution with just 2 points
E2E measurements:
  Fundamentally hard to corroborate with ground truth

## Slide 29: Reverse Traceroute
Usenix NSDI 2010
Ethan Katz-Bassett, Harsha V. Madhyastha, Vijay Kumar Adhikari, Colin Scott, Justine Sherry, Peter van Wesep, Thomas Anderson, and Arvind Krishnamurthy

## Slide 30: Can we find the reverse path?
Routes aren’t always symmetric!
What are reverse routes useful for?

## Slide 31: Main techniques
Distributed set of vantage points issuing forward traceroutes
  Create an “atlas” of nodes and paths to the source
Incrementally stitch reverse path until you hit an atlas node
IP record route: grab first (few) router IP address(es) on return path
  Recursively reverse traceroute from there!
Timestamp option: verify whether a router is on reverse path
Source spoofing: sample reverse path without forward path
  Use prior mapping of vantage points “closest” to the destination
When all else fails, assume symmetric routing

## Slide 32: How accurate is reverse traceroute?
Ground truth: actual traceroutes from D to S
Overlap in hops of reverse and (ground truth) traceroute
  Close to 87% in the median
Why are there differences between the two?
Reverse paths used undiscovered peering links

## Slide 33: (E2E) Measurement research challenges
Ground truth
  Explaining empirical observations
  Aliasing, router identification, AS identification, …
Representativeness
Measuring without bias
  PASTA
Coordinating distributed vantage points
Probing overheads
Detailed knowhow of the Internet and its quirks!
  Ex: IP timestamp marked only when router sees itself on top
How will the conclusions evolve over time?