## Slide 1: Router Design
Lecture 21
http://www.cs.rutgers.edu/~sn624/352-F24
Srinivas Narayana

## Slide 2: Review of concepts
Net layer
Network layer’s main function: moving data from one endpoint to another
Analogy: postal system
endpoint
endpoint
Network
layer
Forwarding
Routing
Data plane
Control plane
Addressing (IPv4)
Locate, not identify
10000000 11000011 00000001 01010000
128
195
1
80
.
.
.
IP prefixes
==
zip code
Classless (CIDR)
128.195.0.0/20

## Slide 3: Advantages of prefix-based IP organization
Aggregate information across endpoints for forwarding & routing
  Don’t reason about individual addresses; do prefixes instead
  Reduce the sizes of information exchanged and router data structures
Prefixes (not individual IPs) are allocated to organizations by Internet registries
  Each organization is delegated the work of assigning individual IPs
Facilitates movement of entire groups of hosts between organizations
(CIDR) IP address is decoupled from an explicit prefix length
  Different routers can interpret an address with different prefix lengths
  E.g., further away: more aggregated (shorter prefix); closer to destination: more granular (longer prefix)

## Slide 4: Next we’ll talk about routers
Access routers
Internet core router
Data center top-of-rack switch

## Slide 5: What’s inside a router?

## Slide 6: Router architecture overview
high-speed
switching
fabric
route
processor
router input ports
router output ports
Control plane
Data plane
Review: Forwarding function: move packets from one input port to another.
Review: assuming distributed routing, routing function: decide which ports packets need to exit

## Slide 7: Different and evolving designs
There are different kinds of routers, with their own designs
  Access routers (e.g., home WiFi), chassis/core routers, top-of-rack switches
Router designs have also evolved significantly over time
For simplicity and concreteness, we will learn about one high-speed router design from the early 2000s.
Called the MGR (multi-gigabit router). It could support an aggregate rate of 50 Gbit/s (1 G = 109)
  Today’s single-chip routers can support aggregate rates of ~10 Tbit/s (1 T = 1012)

## Slide 8: Input port functions
Line termination: receives physical (analog) signals and turns them into digital signals (physical layer)
Rate of link connecting to a single port termed line speed or line rate (modern routers: 100+ Gbit/s)
Link layer: performs medium access control functions (e.g., Ethernet)
Line
Term
Link
Layer
/ MAC
(receive)
…
…
Switching fabric
Input port
Input port
Input port
Output port
Output port
Output port

## Slide 9: Input port functions
Route lookup: high-speed lookup of which output port the packet is destined to
Goal: must complete this processing at the line rate
Queueing: packets may wait in per-output-port queues if packets are arriving too fast for the switching fabric to send them to the output port
Line
Term
Link
Layer
/ MAC
(receive)
Route
lookup
switching
fabric
…
…
Switching fabric
Input port
Input port
Input port
Output port
Output port
Output port
Per-output
Queues

## Slide 10: Route lookups
Packet forwarding in the Internet is based on the destination IP address on the packet.
Example: if dst IP on packet is 65.45.145.34, it matches the prefix 65.0.0.0/8 (netmask 255.0.0.0) in table
(IP & netmask == prefix)
The packet is forwarded out port 3.
Example 2: what about dst IP 128.9.5.6?
Line
Term
Link
Layer
Route
lookup
Per-output
Queues
Outgoing Port
Dst-network
Port
Forwarding Table
Route Lookup Data Structure
65.0.0.0/8
128.9.0.0/16
149.12.0.0/19
3
1
7
Parse
Transport
Network
Link layer
Extract destination IP address

## Slide 11: Route lookups
Number of entries in the forwarding table matters.
Fitting into router memory
Designing hardware and software for fast lookups
Line
Term
Link
Layer
Route
lookup
Per-output
Queues
Outgoing Port
Dst-network
Port
Forwarding Table
Route Lookup Data Structure
65.0.0.0/8
128.9.0.0/16
149.12.0.0/19
3
1
7
Parse
Transport
Network
Link layer
Extract destination IP address

## Slide 12: Route lookups
Recall: IP addresses can be aggregated based on shared prefixes.
The number of table entries in a router is proportional to the number of prefixes, NOT the number of endpoints.
Today: ~ 1 million prefixes.
Line
Term
Link
Layer
Route
lookup
Per-output
Queues
Outgoing Port
Dst-network
Port
Forwarding Table
Route Lookup Data Structure
65.0.0.0/8
128.9.0.0/16
149.12.0.0/19
3
1
7
Parse
Transport
Network
Link layer
Extract destination IP address

## Slide 13: Route lookups
Destination-IP-based forwarding has consequences.
Forwarding behavior is independent of the source: legitimate source vs. malicious attack traffic
Forwarding behavior is independent of the application: web traffic vs. file download vs. video
IP-based packet processing is “baked into” router hardware: evolving the IP protocol faces tall deployment hurdles
Line
Term
Link
Layer
Route
lookup
Per-output
Queues
Outgoing Port
Dst-network
Port
Forwarding Table
Route Lookup Data Structure
65.0.0.0/8
128.9.0.0/16
149.12.0.0/19
3
1
7
Parse
Transport
Network
Link layer
Extract destination IP address

## Slide 14: Output port functions
Components in reverse order of those in the input port
This is where most routers have the bulk of their packet buffers
  Recall discussions regarding router buffers from transport
MGR uses per-port output buffers, but modern routers have shared memory buffers
  More efficient use of memory under varying demands
Line
Termination
Link
Layer
/ MAC
(transmit)
Queues
…
…
Switching fabric
Input port
Input port
Input port
Output port
Output port
Output port
Switching
fabric
To output link

## Slide 15: Output port functions
Two important policy decisions
Scheduling: which among the waiting packets gets to be transmitted out the link?
  Ex: First-In-First-Out (FIFO)
Buffer management: which among the packets arriving from the fabric get space in the packet buffer?
  Ex: Tail drop: later packets dropped first
Line
Termination
Link
Layer
/ MAC
(transmit)
Queues
…
…
Switching fabric
Input port
Input port
Input port
Output port
Output port
Output port
Switching
fabric
To output link

## Slide 16: Fabrics: Types
…
…
Switching fabric
Input port
Input port
Input port
Output port
Output port
Output port
Input port writes packets into shared memory.
Output port reads the packet when output link ready to transmit.
Single shared channel to move data from input to output port.
Easy to build buses; technology is quite mature.
Each input port has a physical data path to every output port.
Switch at the cross-over points turns on to connect pairs of ports.
Fabric goal: Ferry as many packets as possible from input to output ports as quickly as possible.

## Slide 17: Fabrics: Types
…
…
Switching fabric
Input port
Input port
Input port
Output port
Output port
Output port
Modern high-speed routers use highly optimized shared-memory-based interconnects.
Crossbars can get expensive as the number of ports grows (N2 connections for N ports)
MGR uses a crossbar and schedules (in,out) port pairs.

## Slide 18: Nonblocking fabrics
High-speed switching fabrics designed to be nonblocking:
  If an output port is “available”, an input port can always transmit to it without being blocked by the switching fabric itself
  Nontrivial to achieve
Crossbars are nonblocking by design
Shared memory can be designed to be nonblocking if memory accesses can be made fast enough
…
…
Switching fabric
Input port
Input port
Input port
Output port
Output port
Output port

## Slide 19: Nonblocking fabrics
With a nonblocking fabric, queues aren’t formed due to the switching fabric.
  With a nonblocking fabric, there are no queues due to inefficiencies at the input port or the switching fabric
Queues only form due to contention for the output port
  Fundamental, unavoidable, given the route
…
…
Switching fabric
Input port
Input port
Input port
Output port
Output port
Output port

## Slide 20: Nonblocking fabrics
With a nonblocking fabric, queues aren’t formed due to the switching fabric.
  With a nonblocking fabric, there are no queues due to inefficiencies at the input port or the switching fabric
Queues only form due to contention for the output port
  Fundamental, unavoidable, given the route
Typically, these queues form on the output side
  But can also “backpressure” to the input side if there is high contention for the output port
  i.e.: can’t move pkts to output Qs since buffers full, so buffer @ input
…
…
Switching fabric
Input port
Input port
Input port
Output port
Output port
Output port

## Slide 21: Control (plane) processor
A general-purpose processor that “programs” the data plane:
  Forwarding table
  Scheduling and buffer management policy
Implements the routing algorithm by processing routing protocol messages
  Mechanism by which routers collectively solve the Internet routing problem
  More on this soon.
…
…
Switching fabric
Input port
Input port
Input port
Output port
Output port
Output port
Control Processor

## Slide 22
Routing
Algorithm
data
plane
control
plane
1
2
0111
values in arriving
packet header, i.e, destination IP address
3
Data plane
per-packet processing
(~ tens of nanoseconds)
Control plane
Traditional distributed routing: per route-change processing
(~ a few tens of seconds)
Router design: the bigger picture

## Slide 23: Longest Prefix Matching

## Slide 24: Review: Route lookup
Table lookup matches a packet against an IP prefix
  Ex: 65.12.45.2 matches 65.0.0.0/8
Prefixes are allocated to organizations by Internet registries
But organizations can reallocate a subset of their IP address allocation to other orgs
Outgoing Port
Dst-network
Port
Forwarding Table
Route Lookup Data Structure
65.0.0.0/8
128.9.0.0/16
149.12.0.0/19
3
1
7
Parse
Transport
Network
Link layer
Extract destination IP address

## Slide 25: Example of IP block reallocation
200.23.16.0/23
200.23.18.0/23
200.23.30.0/23
ISP A
Organization 1
Organization 8
Internet
Organization 2
200.23.20.0/23
Organization 3
.
.
.
.
.
.
ISP A owns the IP block 200.23.16.0/20.
Suppose ISP A reallocates a part of its IP block to orgs 1… 8
Dst IP Prefix | Output port
65.0.0.0/8 | 3
128.9.0.0/16 | 1
… | …
200.23.16.0/20 | 7 (towards A)
There is an announcement mechanism (BGP) by which ISP A can inform the rest of the Internet about the prefixes it owns.
It is enough to announce a coarse-grained prefix 200.23.16.0/20 rather than 8 separate sub-prefixes.
[BGP] Send me pkts destined to
200.23.16.0/20
Route Aggregation
Save forwarding table memory
Fewer routing protocol msgs
ISP = Internet Service Provider

## Slide 26: Example of IP block reallocation
200.23.16.0/23
200.23.18.0/23
200.23.30.0/23
ISP A
Organization 1
Organization 8
Internet
Organization 2
200.23.20.0/23
Organization 3
.
.
.
.
.
.
ISP A owns the IP block 200.23.16.0/20.
Suppose ISP A reallocates a part of its IP block to orgs 1… 8
Dst IP Prefix | Output port
65.0.0.0/8 | 3
128.9.0.0/16 | 1
… | …
200.23.16.0/20 | 7 (towards A)
Now suppose one of these organizations adds another ISP for its Internet service and prefers using the new ISP.
Note: it’s possible for the organization to retain its assigned IP block.
[BGP] Send me pkts destined to
200.23.16.0/20

## Slide 27: Example of IP block reallocation
200.23.16.0/23
200.23.18.0/23
200.23.30.0/23
ISP A
Organization 1
Organization 8
Internet
Organization 2
200.23.20.0/23
Organization 3
.
.
.
.
.
.
ISP A owns the IP block 200.23.16.0/20.
Suppose ISP A reallocates a part of its IP block to orgs 1… 8
Dst IP Prefix | Output port
65.0.0.0/8 | 3
128.9.0.0/16 | 1
… | …
200.23.16.0/20 | 7 (towards A)
200.23.18.0/23
Organization 2
ISP B
[BGP] Announce 200.23.18.0/23
(besides other IP prefixes)
[BGP] Send me pkts destined to
200.23.16.0/20

## Slide 28: Example of IP block reallocation
200.23.16.0/23
200.23.18.0/23
200.23.30.0/23
ISP A
Organization 1
Organization 8
Internet
Organization 2
200.23.20.0/23
Organization 3
.
.
.
.
.
.
ISP A owns the IP block 200.23.16.0/20.
Suppose ISP A reallocates a part of its IP block to orgs 1… 8
Dst IP Prefix | Output port
65.0.0.0/8 | 3
128.9.0.0/16 | 1
200.23.18.0/23 | 4 (towards B)
200.23.16.0/20 | 7 (towards A)
200.23.18.0/23
Organization 2
ISP B
[BGP] Announce 200.23.18.0/23
(besides other IP prefixes)
[BGP] Send me pkts destined to
200.23.16.0/20

## Slide 29: A closer look at the forwarding table
200.23.18.0/23 is inside 200.23.16.0/20
A packet with destination IP address 200.23.18.xx is in both prefixes
  i.e., both entries match
Q: How should the router choose to forward the packet?
  Ideally: The org prefers B, so should choose B
Dst IP Prefix | Output port
65.0.0.0/8 | 3
128.9.0.0/16 | 1
200.23.18.0/23 | 4 (towards B)
200.23.16.0/20 | 7 (towards A)
200.23.16.0/20
The Internet uses a policy to prioritize: Longest Prefix Matching

## Slide 30: Longest Prefix Matching (LPM)
Use the longest matching prefix, i.e., the most specific route, among all prefixes that match the packet.
Policy borne out of the Internet’s IP allocation model: prefixes and sub-prefixes are handed out
Internet routers use longest prefix matching.
  How would you implement this in software?
  Interesting algorithmic and design challenges in developing software and hardware
Dst IP Prefix | Output port
65.0.0.0/8 | 3
128.9.0.0/16 | 1
200.23.18.0/23 | 4 (towards B)
200.23.16.0/20 | 7 (towards A)
200.23.16.0/20

## Slide 31
Internet routers perform longest-prefix matching on destination IP addresses of packets.

## Slide 32: Why is LPM useful?
Help organizations move in one block to a different ISP while retaining their IP prefix assignment.
  IPs unchanged: e.g., don’t have to update DNS for services in the org
Also enable an organization (e.g. Rutgers) to connect to two or more Internet Service Providers (ISPs) and express routing preferences
  Announce longer prefixes to make the rest of the Internet prefer a certain path

## Slide 33: Why is LPM useful?
An ISP (e.g., Verizon) has allocated a sub-prefix (or “subnet”) of a larger prefix that the ISP owns to an organization (e.g., Rutgers)
Further, the ISP announces the aggregated prefix to the Internet to save on number of forwarding table memory and number of announcements
The organization (e.g., Rutgers) is reachable over multiple paths (e.g., through another ISP like AT&T)
The organization has a preference to use one path over another, and expresses this by announcing the longer (more specific) prefix
Routers in the Internet must route based on the longer prefix
Rutgers
Verizon
AT&T
Agg. route
Specific route
(longer prefix)