## Slide 1
Lecture 8, Computer Networks (198:552)
Fall 2019
Data Centers
Part II
Notes: Slide material heavily adapted courtesy of Albert Greenberg, Changhoon Kim, Mohammad Alizadeh.

## Slide 2: What are data centers?
Large facilities with 10s of thousands of networked servers
  Compute, storage, and networking working in concert
  “Warehouse-Scale Computers”

## Slide 3: Cloud Computing: The View from Apps
On-demand
  Use resources when you need it; pay-as-you-go
Elastic
  Scale up & down based on demand
Multi-tenancy
  Multiple independent users share infrastructure
  Security and resource isolation
  SLAs on performance & reliability
Dynamic Management
  Resiliency: isolate failure of servers and storage
  Workload movement: move work to other locations

## Slide 4: What’s different about DCNs?
Single administrative domain
  Change all endpoints and switches if you want
  No need to be compatible with outside world
Unique network properties
  Tiny round trip times (microseconds)
  Massive multipath topologies
  Shallow-buffered switches
Latency and tail-latency critical
  Network is a backplane for large-scale parallel computation
Together, serious implications for the transport, network, link layer designs you can (and should) use

## Slide 5
Challenges in DCNs

## Slide 6: Data center costs
Amortized Cost* | Component | Sub-Components
~45% | Servers | CPU, memory, disk
~25% | Power infrastructure | UPS, cooling, power distribution
~15% | Power draw | Electrical utility costs
~15% | Network | Switches, links, transit
  *3 yr amortization for servers, 15 yr for infrastructure; 5% cost of money
The Cost of a Cloud: Research Problems in Data Center Networks. Sigcomm CCR 2009. Greenberg, Hamilton, Maltz, Patel.
Notes: Source: http://web.cse.ohio-state.edu/icdcs2009/Keynote_files/greenberg-keynote.pdf

## Slide 7: Server costs
30% server utilization considered “good” in data centers
Application demands uneven across the resources
  Each server has CPU, memory, disk: most applications exhaust one resource, stranding the others
Long provisioning timescales
  New servers purchased quarterly at best
Uncertainty in demand
  Demand for a new service can spike quickly
Risk management
  Not having spare servers to meet demand brings failure just when success is at hand
Session state and storage constraints
  If the world were stateless servers, life would be good
Notes: Source: Albert Greenberg keynote, ICDCS 2009

## Slide 8: Goal: Agility -- any service, any server
Turn the servers into a single large fungible pool
Dynamically expand and contract service footprint as needed
Place workloads where server resources are available
Easier to maintain availability
  If one rack goes down, machines from another still available
Want to view DCN as a pool of compute connected by one big high-speed fabric

## Slide 9: Steps to achieving Agility
Workload (compute) management
  Means for rapidly installing a service’s code on a server
  Virtual machines, disk images, containers
Storage management
  Means for a server to access persistent data
  Distributed filesystems (e.g., HDFS, blob stores)
Network and Routing management
  Means for communicating with other servers, regardless of where they are in the data center
??

## Slide 10: Agility means that the DCN needs…
Massive bisection bandwidth
  Topologies
  Routing (Multiple paths  Load balancing)
Ultra-Low latency (<10 microseconds)
  The right transport? Switch scheduling/buffer management?
  Schedule packets or control transmission rates?
  Centralized or distributed control?
Effective Resource Management (across servers & switches)
  Multi-tenant performance isolation
  App-aware network scheduling (e.g., for big data)
Support for next-generation hardware & apps
  ML, RDMA, rack-scale computing, memory disaggregation

## Slide 11: Conventional DC network
Source: “Data Center: Load balancing Data Center Services”, Cisco 2004
CR
CR
AR
AR
AR
AR
. . .
S
S
DC-Layer 3
Internet
S
S
A
A
A
…
S
S
A
A
A
…
. . .
DC-Layer 2
Key
CR = Core Router (L3)
AR = Access Router (L3)
S = Ethernet Switch (L2)
A = Rack of app. servers
~ 1,000 servers/pod == IP subnet

## Slide 12: Layer 2 vs. Layer 3
Ethernet switching (layer 2)
  Fixed IP addresses and auto-configuration (plug & play)
  Seamless mobility, migration, and failover
  Broadcast limits scale (ARP)
  Spanning Tree Protocol: no multipath routing
IP routing (layer 3)
  Scalability through hierarchical addressing
  Multipath routing through equal-cost multipath
  More complex configuration
  Can’t migrate w/o changing IP address

## Slide 13: Conventional DC Network Problems
CR
CR
AR
AR
AR
AR
S
S
S
S
A
A
A
…
S
S
A
A
A
…
. . .
S
S
S
S
A
A
A
…
S
S
A
A
A
…
~ 5:1
~ 40:1
~ 200:1
Dependence on high-cost proprietary routers
Extremely limited server-to-server capacity

## Slide 14
CR
CR
AR
AR
AR
AR
S
S
S
S
S
S
S
S
S
S
S
S
IP subnet (VLAN) #1
~ 200:1
Resource fragmentation, significantly lowering cloud utilization (and cost-efficiency)
IP subnet (VLAN) #2
A
A
A
…
A
A
A
…
A
A
…
A
A
…
A
A
A
Conventional DC Network Problems
Notes: Green host from the green IP subnet / VLAN#2 cannot respond to the request from the machine in the IP subnet / VLAN#1! This means that special rules must be installed on the switches to route VLAN 2 data within the sub-tree under the second pair of AR’s in this network.

## Slide 15
CR
CR
AR
AR
AR
AR
S
S
S
S
S
S
S
S
S
S
S
S
IP subnet (VLAN) #1
~ 200:1
Complicated manual L2/L3 re-configuration
IP subnet (VLAN) #2
A
A
A
…
A
A
A
…
A
A
…
A
A
…
A
A
A
Conventional DC Network Problems
Resource fragmentation, significantly lowering cloud utilization (and cost-efficiency)

## Slide 16: Google’s DCN Challenges & Approaches
Source: Jupiter rising: a decade of Clos topologies and centralized control in Google’s data center network. SIGCOMM’15

## Slide 17
Building a high-speed
switching fabric

## Slide 18: A single (n X m)-port switching fabric
Different designs of switching fabric possible
Assume n ingress ports and m egress ports, half duplex links

## Slide 19: A single (n X m)-port switching fabric
We are OK with any design such that:
Any port can connect to any other directly if all other ports free
Nonblocking: if input port x and output port y are both free, they should be able to connect
  Regardless of other ports being connected.
  If not satisfied, switch is blocking.
Electrical/mechanical/electronic crossover

## Slide 20: High port density + nonblocking == hard!
Low-cost nonblocking crossbars are feasible for small # ports
However, it is costly to be nonblocking with a large number of ports
If each crossover is as fast as each input port,
  Number of crossover points == n * m
  Cost grows quadratically on the number of input ports
Else, crossover must transition faster than the port
  … so that you can keep the number of crossovers small
Q: How is this relevant to the data center network fabric?