## Slide 1
Lecture 21, Computer Networks (198:552)
Fall 2019
Congestion Control for
Data Centers
Material adapted from slides by Mohammad Alizadeh

## Slide 2: Review: TCP congestion control
Keep some in-flight (un-ACK’ed) packets: congestion window
Adjust window based on several algorithms:
  Startup: slow start
  Steady state: AIMD
  Loss: fast retransmission, fast recovery
Main question for this lecture:
  (How) should this design change for data centers?

## Slide 3: DC Transport Requirements
High throughput, low latency, burst tolerance

## Slide 4
INTERNET
Servers
Fabric
100Kbps–100Mbps links
~100ms latency
10–40Gbps links
~10–100μs latency
Transport inside the DC

## Slide 5
INTERNET
Servers
Fabric
web
app
data-base
map-reduce
HPC
monitoring
cache
Interconnect for distributed compute workloads
Transport inside the DC
Notes: Specifically, while some of the traffic in data center networks is sent across the Internet, the majority of data center traffic is between the servers within the data center and never leaves the data center.

## Slide 6: Data center workloads
Mice and Elephants
Short messages
(e.g., query, coordination)
Large flows
(e.g., data update, backup)
Low Latency
High Throughput

## Slide 7: Incast
TCP timeout
Worker 1
Worker 2
Worker 3
Worker 4
Aggregator
RTOmin = 300 ms
Synchronized fan-in congestion
Vasudevan et al. (SIGCOMM’09)

## Slide 8: Trace of a real incast event
Maybe, reduce RTO to mitigate this

## Slide 9: Jittering to mitigate incast
Requests are jittered over 10ms window.
Jittering switched off around 8:30 am.
MLA Query Completion Time (ms)
Jittering trades of median for high percentiles
Notes: 1. Incast really happens – see this actual screenshot from production tool
2. People care, they’ve solved it at application by jittering.
3. They care about the 99.9th percentile, 1-1000 customers

## Slide 10: HOL Blocking and Buffer Pressure
Queue buildup increases latency for everyone
(Reducing RTO doesn’t help latency)

## Slide 11: Another possibility: Delay-based CC
Keep just a few packets in queues by observing delays
Adjust window such that only a few packets are in queue
RTT estimates need to be very accurate and precise
  Can be challenging in low-RTT data centers

## Slide 12: Data Center TCP (DCTCP)
Design of the congestion control algorithm

## Slide 13: Review: TCP algorithm
Sender 1
Sender 2
Receiver
ECN = Explicit Congestion Notification
Time
Window Size (Rate)
Additive Increase:
W  W+1 per round-trip time
Multiplicative Decrease:
W  W/2 per drop or ECN mark
ECN Mark (1 bit)
Notes: DCTCP is based on the existing Explicit Congestion Notification framework in TCP.
----- Meeting Notes (3/7/12 12:24) -----
Remember to mention "SAWTOOTH"

## Slide 14: DCTCP: Main idea
Extract multi-bit feedback from single-bit stream of ECN marks
  Reduce window size based on fraction of marked packets

## Slide 15: DCTCP: Main idea
ECN Marks | TCP | DCTCP
1 0 1 1 1 1 0 1 1 1 | Cut window by 50% | Cut window by 40%
0 0 0 0 0 0 0 0 0 1 | Cut window by 50% | Cut window by 5%
Window Size (Bytes)
Window Size (Bytes)
Time (sec)
Time (sec)
TCP
DCTCP
Notes: Start with: “How can we extract multi-bit information from single-bit stream of ECN marks?”
- Standard deviation: TCP (33.6KB), DCTCP (11.5KB)

## Slide 16: DCTCP algorithm
Switch side:
  Mark packets when Queue Length > K.
  Sender side:
  Maintain running average of fraction of packets marked (α).
  Adaptive window decreases:
    Note: decrease factor between 1 and 2.
B
K
Mark
Don’t
Mark
Notes: very simple marking mechanism
not all the tunings other aqms have
on the source side, the source is tryign to estimate the fraction of packets getting marked
using the obs that there is a stream of ecn marks coming back – more info in the stream than in any single bit
trying to maintain smooth rate variations to operate well even when using shallow buffers, and only a few flows (no stat mux)
F over the last RTT. In TCP there is always a way to get the next RTT from the window size. Comes from the self-clocking of TCP.
Only changing the decrease. Simplest version – makes a lot of sense. So generic could apply it to any algorithm – CTCP, CUBIC – how to cut its window leaving increase part to what it already does. Have to be careful here.

## Slide 17: Efficient and “lossless” ACK generation

## Slide 18: DCTCP vs TCP
(KBytes)
Experiment: 2 flows (Win 7 stack), Broadcom 1Gbps Switch
ECN Marking Thresh = 30KB
Buffer is mostly empty
DCTCP mitigates Incast by creating a
large buffer headroom

## Slide 19: Why it works
Low Latency
  Small buffer occupancies → low queuing delay
2. High Throughput
  ECN averaging → smooth rate adjustments, low variance
3. High Burst Tolerance
  Large buffer headroom → bursts fit
  Aggressive marking → sources react before packets are dropped

## Slide 20: Setting parameters: A bit of analysis
Packets sent in this
RTT are marked
How much buffering does DCTCP need for 100% throughput?
Need to quantify queue size oscillations (stability).
Time
(W*+1)(1-α/2)
W*
Window Size
W*+1
B
K

## Slide 21: Setting parameters: A bit of analysis
K > (1/7) C x RTT
for TCP:
K > C x RTT
B
K
How small can queues be without loss of throughput?
Need to quantify queue size oscillations (Stability).

## Slide 22: Bing benchmark (baseline)
Background Flows
Query Flows
Notes: To transition to scaled traffic: people always want to get more out of their network.

## Slide 23: Convergence time
DCTCP takes at most ~40% more RTTs than TCP
  “Analysis of DCTCP”, SIGMETRICS 2011
Intuition: DCTCP makes smaller adjustments than TCP, but makes them much more frequently
TCP
DCTCP
Notes: In the first part of the talk, we established that what we need from DCTCP is to maintain small queues, without loss of throughput
Now in the case of TCP, the question of how much buffering is needed for high throughput has been studied and is known in the literature as the buffer sizing problem.
… and I’ll show you how to get low var…

## Slide 24: CC evaluation: several aspects!
Throughput, delays, flow completion times
Fairness, convergence times
Specific impairments:
  incast (many to one, all to all)
  collateral damage from incast
  buffer pressure
Impact on background traffic
Multi-hop versus single-hop bottlenecks

## Slide 25: CC Deployment Concerns
Life ain’t easy in the fast lane

## Slide 26: Practical deployment concerns in DCs
Coexistence with legacy protocols like TCP Cubic
  Application code can’t be upgraded in one shot
Minimum window size matters during heavy incast events
  e.g., 2 packets versus 1 packet!
Setting pkt flags appropriately at senders, receivers, and routers
  Non “ECN-capable” flagged packets will be dropped when Q > K
  … including the SYN packets of any connection
Receive-buffer tuning
  Receive buffer must be at least BDP, but what is the BDP?