## Slide 1: CS 352 Link Layer: Introduction
CS 352, Lecture 22.1
http://www.cs.rutgers.edu/~sn624/352
Srinivas Narayana

## Slide 2: Link layer
Application
Transport
Network
Link
…
FTP
HTTP
SMTP
DNS
TCP
UDP
IP
802.11
802.3
ATM
HTTPS
The main function of the link layer is link-local delivery:
getting packets from one side of the link to the other.
Ethernet

## Slide 3: Link layer: introduction
Terminology:
Endpoints and routers: nodes
communication channels that connect adjacent nodes along communication path: links
  wired links, wireless links, local area networks (LANs)
layer-2 packet: frame, encapsulates (IP) datagram
Link layer has the responsibility of
transferring datagram from one node
to physically adjacent node over a link.
Slides in this presentation were heavily adapted from those of Kurose and Ross, who own the copyright on the material.

## Slide 4: Link layer: context
Datagram transferred by different link layer protocols over different links
  e.g., Ethernet on first link, frame relay on intermediate links, 802.11 on last link
Each link layer protocol may provide different services
  e.g., some links may provide additional reliability mechanisms
Analogy:
trip from Piscataway, NJ to Palo Alto, CA
  limo: Piscataway to JFK
  plane: JFK to San Francisco
  train: San Francisco to Palo Alto
tourist = datagram
transport segment (road/flight/rail) = communication link
transportation mode (car/plane/train) = link layer protocol

## Slide 5: Where is the link layer implemented?
in every endpoint & router
link layer implemented in network interface card (NIC)
  Ethernet, WiFi card or chip
  Router input and output ports
At endpoint, attaches into its system buses (e.g., PCIe)
combination of hardware, software, firmware
controller
physical
cpu
memory
host bus
(e.g., PCI)
network interface
application
transport
network
link
link
physical

## Slide 6: Interfaces communicating
controller
physical
memory
CPU
controller
physical
cpu
memory
application
transport
network
link
link
physical
application
transport
network
link
link
physical
sending side:
encapsulates datagram in frame
adds error checking bits, reliable data transfer, flow control, etc.
receiving side:
looks for errors, reliable data transfer, flow control, etc.
extracts datagram, passes to upper layer at receiving side
linkh
linkh
datagram
datagram
datagram
Usually, check if MAC dstaddr same as NIC’s

## Slide 7: Link layer (MAC) addresses

## Slide 8: Link layer addresses
Review: we’ve looked at 32-bit IPv4 addresses
  network-layer address for interface
  used for layer 3 (network layer) forwarding
  e.g.: 128.119.40.136
MAC or physical or link-layer address
  Used “locally” to get frame from one interface to another physically-connected interface (same subnet, in IP-addressing sense)
  This course: Ethernet family of link layer protocols
  48-bit Ethernet MAC address burned in NIC ROM
    Sometimes, the address can be set in software
hexadecimal (base 16) notation
(each “numeral” represents 4 bits)
  e.g.: 1A-2F-BB-76-09-AD

## Slide 9: MAC addresses
each interface on LAN
has unique 48-bit MAC address
has a locally unique 32-bit IP address (as we’ve seen)
1A-2F-BB-76-09-AD
58-23-D7-FA-20-B0
0C-C4-11-6F-E3-98
71-65-F7-2B-08-53
Ethernet LAN
(wired or wireless)
137.196.7/24
137.196.7.78
137.196.7.14
137.196.7.88
137.196.7.23

## Slide 10: MAC addresses
MAC address allocation administered by IEEE
manufacturer buys portion of MAC address space (to assure uniqueness)
Analogy:
  MAC address: like Social Security Number
  IP address: like postal address
MAC is a flat address: portability
  e.g., can move interface from one Ethernet LAN to another
  Recall: IP address is not portable: depends on IP network to which node is attached

## Slide 11: Link layer services

## Slide 12: Link layer: services
Line termination (serialize/deserialize)
  Physical signaling (into the wire) & extracting digital signal (out of the wire)
  Encapsulate datagram into frame (framing). Add header, trailer
Error detection:
  errors caused by signal attenuation, noise.
  receiver detects errors, signals retransmission, or drops frame
Error correction:
  receiver identifies and corrects bit error(s) without retransmission
Medium access control
  channel medium access in a shared medium:
  “Who should talk?”

## Slide 13: Link layer: services
Line termination (serialize/deserialize)
  Physical signaling (into the wire) & extracting digital signal (out of the wire)
  Encapsulate datagram into frame (framing). Add header, trailer
Error detection:
  errors caused by signal attenuation, noise.
  receiver detects errors, signals retransmission, or drops frame
Error correction:
  receiver identifies and corrects bit error(s) without retransmission
Medium access control
  channel medium access in a shared medium:
  “Who should talk?”
This lecture
Next 2 lectures

## Slide 14: Link layer: services: there’s more!
Reliable delivery between adjacent nodes
  Seldom used on low bit-error links
  Not strictly needed for functionality
  An optimization that significantly improves performance over pure end-to-end reliable delivery over high-error-rate links (e.g., wireless)
Flow control:
  pacing between adjacent sending and receiving nodes
  Used in lossless link layer technologies (e.g., Infiniband, lossless Ethernet)
Not covered in this course

## Slide 15: Link layer: services
Line termination (serialize/deserialize)
  Physical signaling (into the wire) & extracting digital signal (out of the wire)
  Encapsulate datagram into frame (framing). Add header, trailer
Error detection:
  errors caused by signal attenuation, noise.
  receiver detects errors, signals retransmission, or drops frame
Error correction:
  receiver identifies and corrects bit error(s) without retransmission
Medium access control
  channel medium access in a shared medium:
  “Who should talk?”
Next module:
Encoding, error detection, and error correction

## Slide 17: CS 352 Encoding, Error Detection, and Correction
CS 352, Lecture 22.2
http://www.cs.rutgers.edu/~sn624/352
Srinivas Narayana

## Slide 18: Recall: Link layer services
Line termination (serialize/deserialize)
  Physical signaling (into the wire) & extracting digital signal (out of the wire)
  Encapsulate datagram into frame (framing). Add header, trailer
Error detection:
  errors caused by signal attenuation, noise.
  receiver detects errors, signals retransmission, or drops frame
Error correction:
  receiver identifies and corrects bit error(s) without retransmission
Medium access control
  channel medium access in a shared medium:
  “Who should talk?”

## Slide 19: Link layer: services
Line termination (serialize/deserialize)
  Physical signaling (into the wire) & extracting digital signal (out of the wire)
  Encapsulate datagram into frame (framing). Add header, trailer
Error detection:
  errors caused by signal attenuation, noise.
  receiver detects errors, signals retransmission, or drops frame
Error correction:
  receiver identifies and corrects bit error(s) without retransmission
Medium access control
  channel medium access in a shared medium:
  “Who should talk?”
This module:
Encoding, error detection, and error correction

## Slide 20: Handling digital and physical Information

## Slide 21: Encoding and Decoding
Signals propagate over a physical medium
  modulate electromagnetic waves
  e.g., vary voltage
Encode binary data onto signals
  e.g., 0 as low signal and 1 as high signal
  known as Non-Return to zero (NRZ)
Bits
NRZ
0
0
1
0
1
1
1
1
0
1
0
0
0
0
1
0

## Slide 22: Clock sync and recovery
Receiver needs to know when a symbol begins and ends
One approach: send a clock signal together with data signal
  Lowers data rate by 2x!
Another approach: look for transitions in the data signal to re-synchronize the clock
Long strings of 0s and 1s make synchronization challenging
It’s like trying to dance in sync without a beat
Sender
0
1
1
1
1
1
0
Bits
NRZ
Receiver
0
1
1
...
...
0
Bits
NRZ
How many 1s?

## Slide 23: Self-clocking encoding
Bits
NRZ
Clock
Manchester
NRZI
0
0
1
0
1
1
1
1
0
1
0
0
0
0
1
0
Manchester encoding
0 encoded by a positive transition, 1 by a negative transition
Construct using XOR(bit,clock)
Used in early Ethernet standards (up to 10 Mbit/s)

## Slide 24: Error Detection & Correction

## Slide 25: Error detection
EDC: error detection and correction bits (e.g., redundancy)
D: data protected by error checking, may include header fields
Error detection not 100% reliable!
  protocol may miss some errors, but rarely
  larger EDC field yields better detection and correction
datagram
D
EDC
d data bits
bit-error prone link
D’
EDC’
all
bits in D’
OK
?
N
detected
error
otherwise
datagram

## Slide 26: Parity checking
single bit parity:
detect single bit errors
0111000110101011
1
parity
bit
d data bits
two-dimensional bit parity:
detect and correct single bit errors
d1,1
d2,1
di,1
. . .
d1,j+1
d2,j+1
di,j+1
. . .
. . .
d1,j
d2,j
di,j
. . .
di+1,1
di+1,j+1
di+1,j
. . .
. . .
. . .
. . .
row parity
column
parity
0 1 1 1 0 1
1 0 1 0 1 1
1 1 1 1 0 0
1 0 1 0 1 0
no errors:
0 1 1 1 0 1
1 0 1 0 1 1
1 0 1 1 0 0
1 0 1 0 1 0
parity
error
parity
error
detected
and
correctable
single-bit
error:
Even parity: set parity bit so there is an even number of 1’s

## Slide 27: Review: Transport (UDP/TCP) checksum
sender:
treat contents of transport segment as sequence of 16-bit integers
checksum: addition (roughly) of segment content
checksum value put into UDP checksum field
receiver:
compute checksum of received segment
check if computed checksum equals checksum field value:
  Yes: assume no error
  No: declare error
Goal: detect errors (i.e., flipped bits) in transmitted segment

## Slide 28: Cyclic Redundancy Check (CRC)
more powerful error-detection coding than checksums
D: data bits (given, think of these as a binary number)
G: bit pattern (generator), of r+1 bits (given)
Goal: choose r CRC bits, R, such that <D,R> exactly divisible by G
Do all arithmetic mod 2: all additions, subtractions replaced by XOR
  receiver knows G, divides <D,R> by G. If non-zero remainder: error detected!
  can detect all burst errors (continuous bit errors) less than r+1 bits
  widely used in practice (Ethernet, 802.11 WiFi)
r CRC bits
d data bits
D
R
<D,R> = D 2r XOR R
*
bit pattern
formula for bit pattern

## Slide 29: Cyclic Redundancy Check (CRC): example
We want:
  D.2r XOR R = nG
D.2r
G
R = remainder [ ]
or equivalently:
if we divide (mod 2) D.2r by G, want remainder R to satisfy:
Perform long division to compute the remainder. E.g., D = 101110, G = 1001
1 0 0 1
1 0 1 0
1 0 1
0 0 0
1 0 0 1
1 0 0 1
1 0 0 1
0 0 0
1 1 0
1 1 0 0
1 0 1 0
0 1 1
0 1 1
D
R
1 0 0 1
G
0 0 0
1 0 1 1 1 0
2r
*
1
0
1
Mod 2 arithmetic: XOR, not subtraction.
How CRC is computed in software: https://www.kernel.org/doc/html/latest/staging/crc32.html

## Slide 30: Summary
Self-clocking encoding useful to synchronize sender & receiver
Error detection and correction mechanisms:
  Parity bits: single or a few bits of error
  CRCs: bursty errors up to a certain size
Error detection and correction codes widely used across many computer systems

## Slide 32: CS 352 Connecting Multiple Endpoints into a Single Network
CS 352, Lecture 22.3
http://www.cs.rutgers.edu/~sn624/352
Srinivas Narayana

## Slide 33: A small organizational network today
to external
networks
router
Single IP network
mail server
web server
Switches
Located in switching closets, connect directly to endpoints.

## Slide 34: Switching
A switch is a link-layer device
  Examine incoming frame’s destination MAC address
  Selectively forward frame to one-or-more outgoing links when frame is to be forwarded
  Can store link layer frames in switch buffers
Transparent: hosts unaware of presence of switches
Plug-and-play, self-learning
  Switches do not need to be configured

## Slide 35: Switch: multiple simultaneous transmissions
switch with six interfaces (1,2,3,4,5,6)
A
A’
B
B’
C
C’
1
2
3
4
5
6
hosts have dedicated, direct connection to switch
switches buffer packets
Same link layer protocol used on each incoming link
  full duplex links
  No medium access control needed (more next lecture)
switching: A-to-A’ and B-to-B’ can transmit simultaneously

## Slide 36: Switch: multiple simultaneous transmissions
switch with six interfaces (1,2,3,4,5,6)
A
A’
B
B’
C
C’
1
2
3
4
5
6
hosts have dedicated, direct connection to switch
switches buffer packets
Same link layer protocol used on each incoming link
  full duplex links
  No medium access control needed (more next lecture)
switching: A-to-A’ and B-to-B’ can transmit simultaneously
However, A  A’ and C  A’ can’t happen simultaneously

## Slide 37: Switched LAN
If switches don’t need to be configured, how can switches route to the correct endpoints?
Process known as MAC learning or layer-2 bridging
  a configuration-free, learning-based routing protocol

## Slide 38: Switch forwarding table
A
A’
B
B’
C
C’
1
2
3
4
5
6
Ex: how does switch know A’ reachable via interface 4, B’ reachable via interface 5?
Each switch has a MAC table.
Each entry:
  (MAC address of host, interface to reach host, timestamp)
  looks like a forwarding table!
How are entries created and maintained in the MAC table?

## Slide 39: MAC learning
A
A’
B
B’
C
C’
1
2
3
4
5
6
switch learns which hosts can be reached through which interfaces
A A’
Source: A
Dest: A’
MAC addr interface TTL
Switch table
(initially empty)
A
1
60
  when frame received, switch “learns” location of sender: incoming LAN segment
  records sender/location pair in switch table

## Slide 40: MAC learning: frame forwarding
when a frame received at switch:
  1. record incoming link, source MAC address
  2. index switch table using destination MAC address
  3. if entry found for destination then {
  if destination on link from which frame arrived then drop frame
  else forward frame on interface indicated by entry
  }
  else flood /* forward on all ports except arriving interface */
MAC port TTL
A
1
60
Flooding is only acceptable because all endpoints are in the same org/IP network.

## Slide 41: Forwarding: Example
A
A’
B
B’
C
C’
1
2
3
4
5
6
A A’
Source: A
Dest: A’
MAC addr interface TTL
switch table
(initially empty)
A
1
60
A A’
A A’
A A’
A A’
A A’
A’ A
A’
4
60
frame destination A’. Interface unknown (not in table)
flood
destination A location known:
Selectively send on one link
Subsequent A A’ packets not flooded

## Slide 42: Interconnecting switches
MAC learning switches can be connected together
  The algorithm works the same way!
Complication: what if there are loops in the switch topology?
  Flooding may result in the same packet arriving from multiple ports
Ethernet: spanning tree protocol
  Switches discover the switch-level graph
  Process akin to link state advertisements flooding
  Then, switches use a loop-free subset of links
    A spanning tree of the network graph

## Slide 43: Switches vs. routers
Both can store, buffer, and forward.
routers: network-layer devices (examine network-layer headers)
switches: link-layer devices (examine link-layer headers)
Both have forwarding tables.
routers: compute forwarding tables using routing algorithms, link configurations, and announced IP addresses
switches: learn forwarding table using flooding and learning MAC addresses

## Slide 44: Summary
Enterprises often use switches for their ease of configuration and plug-and-play nature
  Switched Ethernet: popular in dorms and office buildings
Switches can discover endpoints
Flooding facilitates reachability across endpoints. Only possible as all endpoints part of the same IP network
MAC learning records where endpoints send from, enabling the discovery of endpoint-port associations without prior knowledge