## Slide 1: Multimedia: Real-time Conversations
CS 352, Lecture 24, Spring 2020
http://www.cs.rutgers.edu/~sn624/352
Srinivas Narayana

## Slide 2: Course announcements
Project 3 due today
No more quizzes!
Final exam over a 5-day window (05/07—05/12)
  If you need any special arrangements, you must contact me ASAP
  Exam on Sakai; 2-hour block
  Open book. Same conditions and honor code as second mid-term
  No googling or collaboration allowed

## Slide 3: Review of concepts
DASH: media presentation description; dynamic, adaptive
Voice over IP (VoIP):
  Real-time guarantees: need delay < 400ms
  Delay loss in addition to (congestive) loss
  Adaptive playout: adjust playout delay for each talk spurt
  Loss recovery using forward error correction & interleaving
Case study: Skype: peers as relay nodes
  Connectivity across NATs requires a special infrastructure
  A common theme to provide media connectivity: SIP
  This lecture: RTP and SIP

## Slide 4: Protocols for real-time communication: RTP and SIP

## Slide 5: Real-Time Protocol (RTP)
RTP specifies packet structure for packets carrying audio, video data
RFC 3550
RTP packet provides
  payload type identification
  packet sequence numbering
  time stamping
RTP runs in end systems
RTP packets encapsulated in UDP segments
interoperability: if two VoIP applications run RTP, they may be able to work together

## Slide 6: RTP runs on top of UDP
RTP libraries provide transport-layer interface
that extends UDP:
  port numbers, IP addresses
  payload type identification
  packet sequence numbering
  time-stamping

## Slide 7: RTP example
example: sending 64 kbps PCM-encoded voice over RTP
application collects encoded data in chunks, e.g., every 20 msec = 160 bytes in a chunk
audio chunk + RTP header form RTP packet, which is encapsulated in UDP segment
RTP header indicates type of audio encoding in each packet
  sender can change encoding during conference
RTP header also contains sequence numbers, timestamps

## Slide 8: RTP header
payload type (7 bits): indicates type of encoding currently being used. If sender changes encoding during call, sender
informs receiver via payload type field
  Payload type 0: PCM mu-law, 64 kbps
  Payload type 3: GSM, 13 kbps
  Payload type 7: LPC, 2.4 kbps
  Payload type 26: Motion JPEG
  Payload type 31: H.261
  Payload type 33: MPEG2 video
sequence # (16 bits): increment by one for each RTP packet sent
  detect packet loss, restore packet sequence
payload type
sequence number type
time stamp
Synchronization
Source ID
Miscellaneous fields

## Slide 9: RTP header
timestamp field (32 bits long): sampling instant of first byte in this RTP data packet
  for audio, timestamp clock increments by one for each sampling period (e.g., each 125 usecs for 8 KHz sampling clock)
  if application generates chunks of 160 encoded samples, timestamp increases by 160 for each RTP packet when source is active. Timestamp clock continues to increase at constant rate when source is inactive.
SSRC field (32 bits long): identifies source of RTP stream. Each stream in RTP session has distinct SSRC
payload type
sequence number type
time stamp
Synchronization
Source ID
Miscellaneous fields

## Slide 10: SIP: Session Initiation Protocol [RFC 3261]
long-term vision:
all telephone calls, video conference calls take place over Internet
people identified by names or e-mail addresses, rather than by phone numbers
can reach callee (if callee so desires), no matter where callee roams, no matter what IP device callee is currently using

## Slide 11: SIP services
SIP provides mechanisms for call setup:
  for caller to let callee know she wants to establish a call
  caller, callee can agree on media type, encoding
  Possible to end call with specific reasons
determine current IP address of callee:
  maps mnemonic identifier to current IP address
call management:
  add new media streams during call
  change encoding during call
  invite others
  transfer, hold calls

## Slide 12: Example: setting up call to known IP address
Alice’s SIP invite message indicates her port number, IP address, encoding she prefers to receive (PCM mu-law)
Bob’s 200 OK message indicates his port number, IP address, preferred encoding (GSM)
SIP messages can be sent over TCP or UDP
default SIP port number is 5060

## Slide 13: Setting up a call (more)
codec negotiation:
  suppose Bob doesn’t have PCM mlaw encoder
  Bob will instead reply with 606 Not Acceptable Reply, listing his encoders. Alice can then send new INVITE message, advertising different encoder
rejecting a call
  Bob can reject with replies “busy,” “gone,” “payment required,” “forbidden”
media can be sent over RTP or some other protocol

## Slide 14: Example of SIP message
INVITE sip:bob@domain.com SIP/2.0
Via: SIP/2.0/UDP 167.180.112.24
From: sip:alice@hereway.com
To: sip:bob@domain.com
Call-ID: a2e3a@pigeon.hereway.com
Content-Type: application/sdp
Content-Length: 885
c=IN IP4 167.180.112.24
m=audio 38060 RTP/AVP 0
Notes:
HTTP message syntax
sdp = session description protocol
Call-ID is unique for every call
Here we don’t know Bob’s IP address
  intermediate SIP servers needed
Alice sends, receives SIP messages using SIP default port 5060
Alice specifies in header that SIP client sends, receives SIP messages over UDP

## Slide 15: Name translation, user location
caller wants to call callee, but only has callee’s name or e-mail address.
need to get IP address of callee’s current host:
  user moves around
  DHCP protocol
  user has different IP devices (PC, smartphone, car device)
result can be based on:
  time of day (work, home)
  caller (don’t want boss to call you at home)
  status of callee (calls sent to voicemail when callee is already talking to someone)
An infrastructure of SIP servers to support mobility and callee resolution

## Slide 16: SIP registrar
REGISTER sip:domain.com SIP/2.0
Via: SIP/2.0/UDP 193.64.210.89
From: sip:bob@domain.com
To: sip:bob@domain.com
Expires: 3600
one function of SIP server: registrar
when Bob starts SIP client, client sends SIP REGISTER message to Bob’s registrar server
register message: to support mobility at Bob’s end

## Slide 17: SIP proxy
another function of SIP server: proxy
Alice sends invite message to her proxy server
  contains address sip:bob@domain.com
  proxy responsible for routing SIP messages to callee, possibly through multiple proxies
Bob sends response back through the same set of SIP servers
Alice’s proxy returns Bob’s SIP response message to Alice
  contains Bob’s IP address
SIP proxy analogous to local DNS server plus indirect routing relay
Alice and Bob’s media traffic sent directly between each other

## Slide 18: SIP example: jim@umass.edu calls keith@poly.edu
1
1. Jim sends INVITE message to UMass SIP proxy.
2. UMass proxy forwards request
to Poly registrar server
2
3. Poly server returns redirect response, indicating that it should try keith@eurecom.fr
3
5. eurecom registrar forwards INVITE to 197.87.54.21, which is running keith’s SIP client
5
4
4. Umass proxy forwards request
to Eurecom registrar server
8
6
7
6-8. SIP response returned to Jim
9
9. Data flows between clients
UMass SIP proxy
Poly SIP
registrar
Eurecom SIP
registrar
197.87.54.21
128.119.40.186

## Slide 19: Internetworking PSTN and SIP?
A gateway is required to convert SIP messages to circuit switched signaling in the public switched telephone network (PSTN) and vice-versa
SIP proxy server will contact PSTN gateway
A PSTN gateway initiates call to the PSTN callee
Two-way audio conversation occurs through the PSTN gateway

## Slide 20: Summary of real-time multimedia
Important to bound playout delays, adapt to loss
Fixed and adaptive playout delays at the granularity of “talk spurts”
Forward error correction mechanisms to avoid retransmissions and conceal packet loss
Relay-based call routing: used by Skype and SIP services
  Useful to overcome NATs
  Locate users through generic names, amidst mobility
  Need extra infrastructure to make all this real

## Slide 21: Outro

## Slide 22: The big picture
Computer networks are a stack of layers
  Built that way for modularity
  Each layer does one set of functions very well
  Each layer depends on the layers beneath it
  But modularity can sometimes result in inefficiency
Many general and useful principles
  Borrowed from real life (ex: listen before you speak)
  Borrowed from systems in general (ex: use indirection for flexibility)
  Applicability goes the other way as well (ex: how to meter freeway ramps)

## Slide 23: CS 352 for the impatient
A set of slides summarizing the most important things to take away from this course
“Too long; didn’t read” versions of 352 at
https://www.cs.rutgers.edu/~sn624/352-S20/lectures/tldr.pptx
https://www.cs.rutgers.edu/~sn624/352-S20/lectures/tldr.pdf

## Slide 24: You’ve gone through 24 lectures of 352…
now what?

## Slide 25: A few possibilities
The course is over. Go about life as usual
Apply your new-found skills to solve a problem you care about
Develop a deeper understanding of these technologies
Consider improving the state of the art

## Slide 26: (1) Go about life as usual
This material will still be useful for a good “CS life”
  Deeper understanding of the abstractions you use (ex: sockets. How big should socket buffers be?)
  Why we need certain technologies (ex: video bit-rate adaptation)
  A more nuanced understanding of real issues (ex: how are ISPs impacting net neutrality using QoS mechanisms?)
  Enhanced abilities to troubleshoot your own tech problems (ex: why is website X not loading? Is it my Internet connection or the other end?)

## Slide 27: (2) Solve a problem you care about
Most concepts we discussed are supported by real, open-source, freely-available software
  Many technology and protocol specifications are freely available (RFCs)
  Linux kernel source code
  Open source software routers
  Open source browsers (Mozilla), mail clients (mutt), video clients
  Most protocols are “open source”
  Free or cheap infrastructure: EC2 servers, domain names, certificates

## Slide 28: (2) Solve a problem you care about
Improve video chat performance?
Improve the usability of secure email?
Improve web transfer performance?
Make it easier to diagnose home wifi issues?
<your idea here?>

## Slide 29: (3) Deepen your understanding
Fall 2020: CS 552 “Computer Networks”
  A deeper take on the fundamentals of Internet design
  https://www.cs.rutgers.edu/~sn624/552-F19/index.html
Some questions we’ll talk about:
  How does Google serve your web traffic so quickly?
  How do large networks verify that their networks are functioning well?
  How are high-speed routers built?
  What transpires inside large data centers run by Amazon & Facebook?
  How should you optimize your web-app to load faster on browsers?
  … and more

## Slide 30: (3) Deepen your understanding
552 requires
  Paper readings
  Deep understanding
  Engaging in lively class discussions
You will be assessed mainly through a software project
  On a topic of your choice that you are excited about
  The only requirement is that it must be connected to class material
Every assessment is “take home”; there will be no exams.

## Slide 31: (4) Push the state of the art
Many of you will embark on CS-related careers
  Can use your 352 know-how to do cutting-edge work in your org
Some of you may consider graduate school
  Networking is a great area to work in
  Some of the most cited papers in CS, at least 2 Turing awards
  552 is a good place to lay a foundation for this path
If you’re interested in working on small research projects, contact me.

## Slide 32: Now it’s time for…
Any questions, general or specific, about the course
Any topics you’d like me to go over again
Any feedback you’d like to voice about this course