## Slide 1: CS 352 Congestion Control (Part 2)
Lecture 17
http://www.cs.rutgers.edu/~sn624/352-F22
Srinivas Narayana

## Slide 2
application
process
TCP socket
receiver buffers
TCP
code
receiver
from sender
recv()
sender
Multiple locations for bottlenecks
What’s the bottleneck? How to adapt how much data to keep in flight?
Flow Control
Congestion Control
Distributed algorithm converging to an efficient and fair outcome
Sense and React
TCP congestion control algorithm
H
C
Signals
Knobs
Bottleneck link
Loss, ACKs, etc.
Congestion window, sending rate
Steady state?
How to get to steady state?

## Slide 3: Congestion window
The sender maintains an estimate of the amount of in-flight data needed to keep the pipe full without congesting it.
This estimate is called the congestion window (cwnd)
Recall: There is a relationship between the sending rate (throughput) and the sender’s window: sender transmits a window’s worth of data over an RTT duration
  Rate = window / RTT

## Slide 4: Interaction b/w flow & congestion control
Use window = min(congestion window, receiver advertised window)
Overwhelm neither the receiver nor network links & routers
0
1
2
3
4
5
6
7
1
0
Last cumulative
ACK’ed seq #
Last transmitted
seq #
Sender’s view:
Window <= Congestion window (congestion control)
Window <= Advertised window (flow control)

## Slide 5: Review: Goal of steady state operation
Sender
Receiver
Send packet burst (as allowed by window)
Receive data packet
Send ACK
Receive ACK
Data
ACKs
(1) Keep transmissions ACK-clocked: Send new data on ACK
(2) Keep transmissions over the bottleneck link back to back

## Slide 6: Review: Getting to steady: TCP New Reno
1K
Time
Packet drops/
RTO
Slow start
Slow start
Congestion Window
Say MSS = 1 KByte
54 MSS
Set ssthresh to
27 MSS
Loss occurs at cwnd = 40K
Loss occurs at cwnd = 54K
Set ssthresh to
20 MSS
Additive increase
Slow
start
Additive increase
(exponential growth)
Congestion avoidance
Adjusting closer to steady state: different methods…

## Slide 7: TCP BBR: finding the bottleneck link rate
Sender
Receiver
1. Send data at a specific rate
Data gets across the bottleneck at the bottleneck link rate.
2. Receive data packet
3. Send ACK
4. Measure rate of incoming ACKs
Data
ACKs
Use ACK receive rate to determine sending rate

## Slide 8: TCP BBR: finding the bottleneck link rate
Assuming that the link rate of the bottleneck
  == the rate of data getting across the bottleneck link
  == the rate of data getting to the receiver
  == the rate at which ACKs are generated by the receiver
  == the rate at which ACKs reach the sender
Measuring ACK rate provides an estimate of bottleneck link rate
BBR: Send at the maximum ACK rate measured in the recent past
  Update max with new bottleneck rate estimates, i.e., larger ACK rate
  Forget estimates last measured a long time ago
  Incorporated into a rate filter

## Slide 9: TCP BBR: Adjustments by gain cycling
BBR periodically increases its sending rate by a gain factor to see if the link rate has increased (e.g., due to a path change)
…
Time
Sending rate
Steady state operation: constant sending rate
Gain cycle
Detect higher ACK rate:
Update sending rate
Last max ACK rate was measured a while ago. Forget it & use a more recent max ACK rate
…
No change
in ACK rate
Bottleneck link rate increase
Bottleneck link rate decrease
Filter

## Slide 10: Bandwidth-Delay Product

## Slide 11: Steady state cwnd for a single flow
Suppose the bottleneck link has rate C
Suppose the propagation round-trip delay (propRTT) between sender and receiver is T
Ignore transmission delays for this example;
Assume steady state: highest sending rate with no bottleneck congestion
Q: how much data is in flight over a single RTT?
C * T data i.e., amount of data unACKed at any point in time
ACKs take time T to arrive (without any queueing). In the meantime, sender is transmitting at rate C

## Slide 12: The Bandwidth-Delay Product
C * T = bandwidth-delay product:
  The amount of data in flight for a sender transmitting at the ideal rate during the ideal round-trip delay of a packet
Note: this is just the amount of data “on the pipe”
Data
C * T

## Slide 13: The Bandwidth-Delay Product
Q: What happens if cwnd > C * T?
  i.e., where are the rest of the in-flight packets?
A: Waiting at the bottleneck router queues
Data
C * T

## Slide 14: Router buffers and the max cwnd
Router buffer memory is finite: queues can only be so long
  If the router buffer size is B, there is at most B data waiting in the queue
If cwnd increases beyond C * T + B, data is dropped!
Data
C * T
B

## Slide 15: Summary
Bandwidth-Delay Product (BDP) governs the window size of a single flow at steady state
The bottleneck router buffer size governs how much the cwnd can exceed the BDP before packet drops occur
BDP is the ideal desired window size to use the full bottleneck link, without any queueing.
  Accommodating flow control, also the min socket buffer size to use the bottleneck link fully

## Slide 16: Detecting and Reacting to Packet Loss

## Slide 17: Detecting packet loss
So far, all the algorithms we’ve studied have a coarse loss detection mechanism: RTO timer expiration
  Let the RTO expire, drop cwnd all the way to 1 MSS
Analogy: you’re driving a car
  You’re waiting until the next car in front is super close to you (RTO) and then hitting the brakes really hard (set cwnd := 1)
  Q: Can you see obstacles from afar and slow down proportionately?
That is, can the sender see packet loss coming in advance?
  And reduce cwnd more gently?

## Slide 18: Can we detect loss earlier than RTO?
Key idea: use the information in the ACKs. How?
Suppose successive (cumulative) ACKs contain the same ACK#
  Also called duplicate ACKs
  Occur when network is reordering packets, or one (but not most) packets in the window were lost
Reduce cwnd when you see many duplicate ACKs
  Consider many dup ACKs a strong indication that packet was lost
  Default threshold: 3 dup ACKs, i.e., triple duplicate ACK
  Make cwnd reduction gentler than setting cwnd = 1; recover faster

## Slide 19: Fast Retransmit & Fast Recovery

## Slide 20: Distinction: In-flight versus window
So far, window and in-flight referred to the same data
Fast retransmit & fast recovery differentiate the two notions
0
1
2
3
4
5
6
7
1
0
Last cumulative
ACK’ed seq #
Last transmitted
seq #
cwnd = 6
0
1
2
3
4
5
6
7
1
0
inflight = 3
Triple duplicate ACKs
(assume subsequent 3 pieces of data were successfully received)
Sender’s view:
cwnd is the interval between the last cumulatively ACK’ed seq# and the last transmitted seq#
inflight is the data currently believed to be in flight.

## Slide 21: TCP fast retransmit (RFC 2581)
The fact that ACKs are coming means that data is getting delivered to the receiver, albeit with some loss.
Note: Before the dup ACKs arrive, we assume inflight = cwnd
TCP sender does two actions with fast retransmit

## Slide 22: TCP fast retransmit (RFC 2581)
(1) Reduce the cwnd and in-flight gently
  Don’t drop cwnd all the way down to 1 MSS
Reduce the amount of in-flight data multiplicatively
  Set inflight  inflight / 2
  That is, set cwnd = (inflight / 2) + 3MSS
  This step is called multiplicative decrease
  Algorithm also sets ssthresh to inflight / 2

## Slide 23: TCP fast retransmit (RFC 2581)
Example: Suppose cwnd and inflight (before triple dup ACK) were both 8 MSS.
After triple dup ACK, reduce inflight to 4 MSS
Assume 3 of those 8 MSS no longer in flight; set cwnd = 7 MSS
Last cumulative
ACK’ed seq #
cwnd = inflight = 8
5
0
1
2
3
4
5
6
7
1
0
5
2
3
4
6
7
1
0
Assumed not in flight (dup ACK)
inflight = 4
cwnd = 7

## Slide 24: TCP fast retransmit (RFC 2581)
(2) The seq# from dup ACKs is immediately retransmitted
That is, don’t wait for an RTO if there is sufficiently strong evidence that a packet was lost

## Slide 25: TCP fast recovery (RFC 2581)
Sender keeps the reduced inflight until a new ACK arrives
  New ACK: an ACK for the seq# that was just retransmitted
  May also include the (three or more) pieces of data that were subsequently delivered to generate the duplicate ACKs
Conserve packets in flight: transmit some data over lossy periods (rather than no data, which would happen if cwnd := 1)

## Slide 26: TCP fast recovery (RFC 2581)
Keep incrementing cwnd by 1 MSS for each dup ACK
Last cumulative
ACK’ed seq #
cwnd = 6
inflight = 3
0
1
2
3
4
5
6
7
1
0
5
2
3
4
5
6
7
1
0
Assumed not in flight (dup ACK)

## Slide 27: TCP fast recovery (RFC 2581)
Keep incrementing cwnd by 1 MSS for each dup ACK
Last cumulative
ACK’ed seq #
cwnd = 7
inflight = 3
0
1
2
3
4
5
6
7
1
0
5
2
3
4
6
7
1
0
Assumed not in flight (dup ACK)

## Slide 28: TCP fast recovery (RFC 2581)
Keep incrementing cwnd by 1 MSS for each dup ACK
Last cumulative
ACK’ed seq #
cwnd = 8
inflight = 3
0
1
2
3
4
5
6
7
1
0
5
2
3
4
6
7
1
0
Assumed not in flight (dup ACK)

## Slide 29: TCP fast recovery (RFC 2581)
Eventually a new ACK arrives, acknowledging the retransmitted data and all data in between
Deflate cwnd to half of cwnd before fast retransmit.
  cwnd and inflight are aligned and equal once again
Perform additive increase from this point!
cwnd = 3
inflight = 3
0
1
2
3
4
5
6
7
1
0
5
2
3
4
6
7
1
0
New ACK acknowledged this data
Last cumulative
ACK’ed seq #

## Slide 30: Additive Increase/Multiplicative Decrease
1K
Time
Triple duplicate ACK
Slow start
In-flight data
Say MSS = 1 KByte
Default ssthresh = 64KB = 64 MSS
Switch to additive increase at cwnd = ssthresh = 64K
Perceived loss occurs at cwnd = 80K
(2) Set inflight = ssthresh = 40K
Additive increase
Additive increase
Fast retransmit: (1) retransmit dup-ACKed segment
Fast recovery keeps inflight stable until new ACK
New ACK
RTO
RTO: window drops all the way to 1 MSS
Multiplicative decrease

## Slide 31
TCP New Reno performs additive increase and multiplicative decrease of congestion window.
In short, we often refer to this as AIMD.
Multiplicative decrease is a part of all TCP algorithms, including BBR.
[It is necessary for fairness across TCP flows.]

## Slide 32: Summary: TCP loss detection & reaction
Fast Retransmit
Triple dup ACK: sufficiently strong signal that network has dropped data, before RTO
Immediately retransmit data
Multiplicatively decrease in-flight data to half of its value
Fast Recovery
Maintain this reduced amount of in-flight data as long as dup ACKs arrive
  Data is successfully getting delivered
When new ACK arrives, do additive increase from there on
Don’t wait for an RTO and then set the cwnd to 1 MSS
  Tantamount to waiting to get super close to the car in front and then jamming the brakes really hard
Instead, react proportionately by sensing pkt loss in advance