## Slide 1
Lecture 13, Computer Networks (198:552)
Programmable Switches

## Slide 2: SDN router data plane
Switching
fabric
Processor
Net intf
Net intf
Net intf
Net intf
data plane
(part of)
control
plane
Part of the control plane
Data plane implements per-packet decisions
  On behalf of control & management planes
Forward packets at high speed
Manage contention for switch/link resources

## Slide 3: Life of a packet: RMT architecture
Many modern switches share similar architecture
  FlexPipe, Xpliant, Tofino, …
Pipelined packet processing with a 1 GHz clock

## Slide 4: What data plane policies might we need?
Parsing
  Ex: Turn raw bits 0x0a000104fe into IP header 10.0.1.4 and proto 254
Stateless lookups
  Ex: Send all packets with protocol 254 through port 5
Stateful processing
  Ex: If # packets sent from any IP in 10.0/16 exceeds 500, drop
Traffic management
  Ex: Packets from 10.0/16 have high priority unless rate > 10 Kb/s
Buffer management
  Ex: restrict all traffic outside of 10.0/16 to 80% of the switch buffer

## Slide 5: Programmability
Allow network designers/operators to specify all of the above
Needs hardware design and language design
Software pkt processing could incorporate all of these features
  However: limited throughput, low port density, high power
Key Q: Can we achieve programmability with high performance?

## Slide 6: Programmability: Topics today
1: Packet parsing
2: Flexible stateless processing
3: Flexible stateful processing
4, if we have time: complex policies without perf penalties

## Slide 7: (1) Packet parsing: Need to generalize
In the beginning, OpenFlow was simple: Match-Action
  Single rule table on a fixed set of fields (12 fields in OF 1.0)
Needed new encapsulation formats, different versions of protocols, additional measurement-related headers
Number of headers ballooned to 41 in OF 1.4 specification!
  With multiple stages of heterogenous tables

## Slide 8: (1) Parsing abstractions
Goal: can we make transforming bits to headers more flexible?
A parser state machine where each state may emit headers
IP
Ethernet
UDP
TCP
Custom protocol
Payload

## Slide 9: (1) Parsing implementation in hardware
Use TCAM to store state machine transitions & hdr bit locations
Extract fields into packet header vector in a separate action RAM

## Slide 10: (2) How are the parsed headers used?
Headers carried through the rest of the pipeline
  To be used in general-purpose match-action tables
Headers

## Slide 11: (2) Abstractions for stateless processing
Goal: specify a set of tables & control flow between them
Actions: more general than OpenFlow 1.0 forward/drop/count
  Copy, add, remove headers
  Arithmetic, logical, and bit-vector operations!
Set metadata on packet header for control flow between tables

## Slide 12: (2) Table dependency graph (TDG)

## Slide 13: (2) Match-action table implementation
Mental model:
Match and Action units supplied with the Packet Header Vector
Each pipeline stage accesses its own local memory
PHV

## Slide 14: (2) Match-action table implementation
TCAM
ternary match
PHV
PHV
SRAM
Exact match
Action memory
Statistics!
Hardware realization: separately configurable memory blocks

## Slide 15: (2) Match-action table implementation
TCAM
ternary match
PHV
PHV
SRAM
Exact match
Action memory
Statistics!
Hardware realization: separately configurable memory blocks
Match RAM blocks also contain
pointers to action memory and instructions

## Slide 16: (1,2) Parse & pipeline specification with
High-level goals
  Allow reconfiguring packet processing in the field
  Protocol independent
  Target independent
Declarative: specify parse graph and TDG
  Headers, parsing, metadata
  Tables, actions, control flow
P4 separates table configuration from table population

## Slide 17: (1,2) Parse & pipeline specification with
Header and state machine spec
header_type ethernet_t {
fields {
dstMac : 48;
srcMac : 48;
ethType : 16;
}
}
header ethernet_t ethernet;
parser start {
extract(ethernet);
return ingress;
}

## Slide 18: (1,2) Parse & pipeline specification with
table forward {
reads {
ethernet.dstMac: exact;
}
actions {
fwd;
_drop;
}
size: 200;
}
action _drop() {
drop();
}
action fwd(dport) {
modify_field(standard_metadata.
egress_spec, dport);
}
Control Flow
control ingress {
apply(forward);
}
Rule Table
Actions

## Slide 19: (3) Flexible stateful processing
What if the action depends on previously seen (other) packets?
  Example: send every 100th packet to a measurement server
  Other examples: Flowlet switching, DNS TTL change tracking, XCP, …
Actions in a single match-action table aren’t expressive enough
Example: if (pkt.field1 + pkt.field2 == 10) { counter++; }

## Slide 20: (3) An example: “Flowlet” load balancing
Consider the time of arrival of the current packet and the last packet of the same flow
If current packet arrives 1 ms later than the last packet did, consider rerouting the packet to balance load
Else, keep the packet on the same route as the last packet
Q: why might you want to do this?

## Slide 21: (3) Abstraction: Packet transaction
A piece of code along with state that runs to completion on each packet before processing the next [Domino’16]
Why is this challenging to implement on switch hardware?
  Hint: Switch is clocked at 1 GHz!

## Slide 22: (3) Abstraction: Packet transaction
A piece of code along with state that runs to completion on each packet before processing the next [Domino’16]
Why is this challenging to implement on switch hardware?
  Hint: Switch is clocked at 1 GHz!
(1) Switch must process a new packet every 1 ns
  Transaction code may not run completely in one pipeline stage

## Slide 23: (3) Abstraction: Packet transaction
A piece of code along with state that runs to completion on each packet before processing the next [Domino’16]
Why is this challenging to implement on switch hardware?
  Hint: Switch is clocked at 1 GHz!
(1) Switch must process a new packet every 1 ns
  Transaction code may not run completely in one pipeline stage
(2) Read and write to state must happen in the same pipeline stage
  Need atomic operation in hardware

## Slide 24: (3) Insight #1: Stateful atoms
The atoms constitute the switch’s action instruction set: run under 1 ns

## Slide 25: (3) Insight #2: Pipeline the stateless actions
if (pkt.field1 + pkt.field2 == 10) { counter ++; }
Have a compiler do this analysis for us 
Stateless operations (whose results depend only on the current packet) can execute over multiple stages
Only the stateful operation must run atomically in one pipeline stage

## Slide 26: (4) Implementing complex policies
What if you have a very large P4 (or Domino) program?
Ex: too many logical tables in TDG
Ex: logical table keys are too wide
  Sharing memory across stages leads to paucity in physical tables
Ex: too many (stateless) actions per logical table
  Sharing compute across stages leads to paucity in physical tables
Solution in RMT architecture: Re-circulation

## Slide 27: (4) Re-circulation “extends” the pipeline
Recirculate to ingress
But throughput drops by 2x!

## Slide 28: (4) Decouple pkt compute & mem access!
Allow packet processing to run to completion on separate physical processors [dRMT’17]
Aggregate per-stage memory clusters into a shared memory pool
  Crossbar enables all processors to access each memory
Schedule instructions on each core to avoid contention

## Slide 29: (4) RMT: compute and memory access
Stage 1
Stage 2
Stage N
Parser
Match
Action
Match
Action
Match
Action
Deparser
Out
Queues
Memory Cluster 1
Memory Cluster 2
Memory Cluster N
In
keys
results
Pkt Header
Notes: As background, I’ll briefly review how programmable switches are architected in hardware. For concreteness, I’ll focus on the RMT architecture because it is representative of many commercial products today.
In the RMT architecture, a parser turns bytes from the wire into a bag of packet headers. In each pipeline stage, a programmable match unit extracts the relevant part of the packet header as a key to look up in the match-action table. It then sends this to the memory cluster, which performs the lookup and returns a result. This result is used by a programmable action unit to transform the packet headers appropriately.
This process then repeats itself.

## Slide 30: (4) dRMT: Memory disaggregation
Stage 1
Stage 2
Stage N
Parser
Match
Action
Match
Action
Match
Action
Deparser
Out
Queues
Memory Cluster 1
Memory Cluster 2
Memory Cluster N
In
Notes: First, we disagg. memory. We replace the stage-local memory in the pipeline with a shared array of memory clusters accessible from any stage through a crossbar. Now, the stages in aggregate have access to all the memory in the system, because the memory doesn’t belong to any one stage in particular.

## Slide 31: (4) dRMT: Compute disaggregation
Proc. 1
Proc. 2
Proc. N
Match
Action
Match
Action
Match
Action
Out
Queues
Memory Cluster 1
Memory Cluster 2
Memory Cluster N
Distributor
Parser
In
Deparser
Pkt 1
Pkt 2
Pkt N
Notes: Next, we disaggregate compute. We replace each of the pipeline stages that is rigidly forced to always execute matches followed by actions with a match-action processor that can execute matches and actions in any order that respects program dependencies. Now, once packets have been parsed, they are distributed by a distributor to one of the processors in round-robin order. So the first packet goes to processor 1, the second to processor 2, and so on.
Once a processor receives a packet, it is responsible for carrying out all operations on that packet. Unlike the pipeline, packets don’t move around between processors. Let’s look at pkt 2 on proc 2. Over the duration of this packet, the proc might access tables in different memory clusters.