## Slide 1: CS 352 Routing Algorithms: Intro
CS 352, Lecture 18.1
http://www.cs.rutgers.edu/~sn624/352
Srinivas Narayana

## Slide 2: Network
Application
Transport
Network
Host-to-Net
…
FTP
HTTP
SMTP
DNS
TCP
UDP
IP
802.11
X.25
ATM
HTTPS
The main function of the network layer is to
move packets from one endpoint to another.

## Slide 3: Designing the Internet’s “Google Maps”

## Slide 4: Network-layer functions
forwarding: move packets from router’s input to appropriate router output
data plane
control plane
Two approaches to structuring network control plane:
per-router control (traditional)
logically centralized control (software defined networking)
Recall: two network-layer functions:
routing: determine route taken by packets from source to destination

## Slide 5
Per-router control plane
Routing
Algorithm
Individual routing algorithm components in each and every router interact with each other in control plane to compute forwarding tables
data
plane
control
plane

## Slide 6: Routing protocols
Routing protocol goal: determine “good” paths (equivalently, routes), from sending hosts to receiving host, through network of routers
path: sequence of routers packets will traverse in going from given initial source host to given final destination host
“good”: least “cost”, “fastest”, “least congested”
routing: a “top-10” networking challenge!

## Slide 7: Graph abstraction
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5
Graph: G = (N,E)
N = set of routers = { u, v, w, x, y, z }
E = set of links ={ (u,v), (u,x), (v,x), (v,w), (x,w), (x,y), (w,y), (w,z), (y,z) }
Remark: Graph abstraction is useful in other network contexts
Example: P2P, where N is set of peers and E is set of TCP connections

## Slide 8: Graph abstraction: costs
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5
c(x,x’) = cost of link (x,x’)
- e.g., c(w,z) = 5
cost could always be 1, or
inversely related to bandwidth,
or inversely related to
congestion
Cost of path (x1, x2, x3,…, xp) = c(x1,x2) + c(x2,x3) + … + c(xp-1,xp)
Question: What’s the least-cost path between u and z ?
Routing algorithm: find “good” paths from source to
destination router.

## Slide 9: Routing algorithm classification
Q: global or decentralized information?
global:
all routers have complete topology, link cost info
“link state” algorithms
decentralized:
router knows physically-connected neighbors, link costs to neighbors
iterative process of computation, exchange of info with neighbors
“distance vector” algorithms
Q: static or dynamic?
static:
routes change slowly over time
dynamic:
routes change more quickly
  periodic update
  in response to link cost changes

## Slide 10: Routing Protocols
Routing protocols
Link state protocols
Distance vector protocols

## Slide 12: CS 352 Link State Protocols
CS 352, Lecture 18.2
http://www.cs.rutgers.edu/~sn624/352
Srinivas Narayana

## Slide 13: A Link-State Routing Algorithm
Dijkstra’s algorithm
net topology, link costs known to all nodes
  accomplished via link state broadcast
  all nodes have same info
computes least cost paths from one node (‘source”) to all other nodes
  gives forwarding table for that node
iterative: after k iterations, know least cost path to k dest.’s
Notation:
c(x,y): link cost from node x to y; = ∞ if not direct neighbors
D(v): current value of cost of path from source to dest. v
p(v): predecessor node along path from source to v
N': set of nodes whose least cost path definitively known

## Slide 14: Dijsktra’s Algorithm
1 Initialization:
2 N' = {u}
3 for all nodes v
4 if v adjacent to u
5 then D(v) = c(u,v)
6 else D(v) = ∞
7
8 Loop
9 find w not in N' such that D(w) is a minimum
10 add w to N'
11 update D(v) for all v adjacent to w and not in N' :
12 D(v) = min( D(v), D(w) + c(w,v) )
13 /* new cost to v is either old cost to v or known
14 shortest path cost to w plus cost from w to v */
15 until all nodes in N'

## Slide 15: Dijkstra’s algorithm: example
Step
0
1
2
3
4
5
N'
u
ux
uxy
uxyv
uxyvw
uxyvwz
D(v),p(v)
2,u
2,u
2,u
D(w),p(w)
5,u
4,x
3,y
3,y
D(x),p(x)
1,u
D(y),p(y)
∞
2,x
D(z),p(z)
∞
∞
4,y
4,y
4,y
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5

## Slide 16: Constructing forwarding table
u
y
x
w
v
z
resulting shortest-path tree from u:
v
x
y
w
z
(u,v)
(u,x)
(u,x)
(u,x)
(u,x)
destination
link
resulting forwarding table in u:

## Slide 18: CS 352 Distance Vector Protocols
CS 352, Lecture 18.3
http://www.cs.rutgers.edu/~sn624/352
Srinivas Narayana

## Slide 19: Distance vector protocol
Dx(y) = estimate of least cost from x to y
Distance vector: Dx = [Dx(y): y є N ]
Node x knows cost of edge to each neighbor v: c(x,v)
Node x maintains Dx
Node x also maintains its neighbors’ distance vectors
  For each neighbor v, x maintains Dv = [Dv(y): y є N ]
Notes: At each node we need
- an array (known as DV) that lists the current least costs to reach all known destinations
- also need to maintain the next-hop along the least cost path
- the DV’s from all neighbors

## Slide 20: Distance vector protocol
Bellman-Ford equation (dynamic programming)
let
dx(y) := cost of least-cost path from x to y
then
dx(y) = min {c(x,v) + dv(y) }
v
cost to neighbor v
min taken over all neighbors v of x
cost from neighbor v to destination y

## Slide 21: Distance vector protocol
Basic idea:
Each node periodically sends its own distance vector estimate to neighbors
When node a node x receives new DV estimate from neighbor, it updates its own DV using Bellman-Ford equation:
Dx(y) ← minv{c(x,v) + Dv(y)} for each node y ∊ N
Under some conditions, the estimate Dx(y) converge the actual least cost dx(y)
Notes: The algorithm …

## Slide 22: Distance vector: example
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5
Start with dv(z) = 5, dx(z) = 3, dw(z) = 3
du(z) = min { c(u,v) + dv(z),
c(u,x) + dx(z),
c(u,w) + dw(z) }
= min {2 + 5,
1 + 3,
5 + 3} = 4
Node that achieves minimum is next
hop in shortest path ➜ forwarding table
Notes: Just to reaffirm the idea behind Bellman-Ford Equations

## Slide 23
x y z
x
y
z
0 2 7
∞
∞
∞
∞
∞
∞
from
cost to
from
from
x y z
x
y
z
0 2 3
from
cost to
x y z
x
y
z
0 2 3
from
cost to
x y z
x
y
z
∞
∞
∞
∞
∞
cost to
x y z
x
y
z
0 2 7
from
cost to
x y z
x
y
z
0 2 3
from
cost to
x y z
x
y
z
0 2 3
from
cost to
x y z
x
y
z
0 2 7
from
cost to
x y z
x
y
z
∞
∞
∞
7
1
0
cost to
∞
2 0 1
∞ ∞ ∞
2 0 1
7 1 0
2 0 1
7 1 0
2 0 1
3 1 0
2 0 1
3 1 0
2 0 1
3 1 0
2 0 1
3 1 0
time
x
z
1
2
7
y
node x table
node y table
node z table
Dx(y) = min{c(x,y) + Dy(y), c(x,z) + Dz(y)} = min{2+0 , 7+1} = 2
Dx(z) = min{c(x,y) + Dy(z), c(x,z) + Dz(z)}
= min{2+1 , 7+0} = 3
Notes: This example assumes that nodes are computing routes in a lock-step fashion.

## Slide 24: Poll #2
Suppose v is the node that minimizes c(x,v) + dv(y) for a fixed destination y.
The forwarding table entry for y at x chooses the link:
  (a) (x, y)
  (b) (x, v)
  (c) (x, x)
  (d) (y, v)

## Slide 25: Distance vector: link cost changes
link cost changes:
node detects local link cost change
updates routing info, recalculates distance vector
if DV changes, notify neighbors
“good
news
travels
fast”
x
z
1
4
2
y
1
t0 : y detects link-cost change, updates its DV, informs its neighbors.
t1 : z receives update from y, updates its table, computes new least cost to x , sends its neighbors its DV.
t2 : y receives z’s update, updates its distance table. y’s least costs do not change, so y does not send a message to z.

## Slide 26: Problem: Count-to-Infinity
With distance vector routing, good news travels fast, but bad news travels slowly
When a router goes down, it takes can take a long time before all other routers become aware of it

## Slide 27: Count-to-Infinity
A
B
C
D
E
1
2
3
4
3
2
3
4
3
4
3
4
5
4
5
4
5
6
5
6
7
6
7
6
Initially
After 1 exchange
After 2 exchanges
After 3 exchanges
After 4 exchanges
After 5 exchanges
etc… to infinity

## Slide 28: Count-to-infinity
“Bad news travels slowly”
More precisely, reacting appropriately to bad news requires information that only other routers have.
Poisoned reverse:
If Z routes through Y to get to X :
  Z tells Y its (Z’s) distance to X is infinite (so Y won’t route to X via Z)
Do you think this would completely solve count to infinity problem?

## Slide 29: Comparison of LS and DV algorithms
message complexity
LS: with n nodes, E links, O(nE) msgs sent
DV: exchange between neighbors only
  convergence time depends on how many iterations of Bellman-Ford occur, updating the DV
speed of convergence
LS: O(n2) algorithm requires O(nE) msgs
DV: convergence time varies
  may be routing loops (count-to-infinity problem)
robustness: what happens if router malfunctions?
LS:
  node can advertise incorrect link cost
  each node computes only its own table
DV:
  DV node can advertise incorrect path cost
  each node’s table used by others
    error propagate thru network

## Slide 30: Routing protocols are widely deployed
Real protocols using a link-state algorithm
  OSPF “Open Shortest Path First”
  IS-IS: “Intermediate System to Intermediate System”
Real protocols using a distance-vector algorithm
  RIP: “Routing Information Protocol”
    RFC written by our own Chuck Hedrick from LCSR @ Rutgers CS
  IGRP: “Interior Gateway Routing Protocol”
This live lecture is being transmitted over networks deploying one or more of these protocols to compute forwarding tables

## Slide 32: CS 352 Scaling Routing for the Internet
CS 352, Lecture 18.4
http://www.cs.rutgers.edu/~sn624/352
Srinivas Narayana

## Slide 33: Making routing scalable
scale: with billions of destinations:
can’t store all destinations in routing tables!
routing table exchange would swamp links!
administrative autonomy
Internet = network of networks
each network admin may want to control routing in its own network
our routing study thus far - idealized
all routers identical
network “flat”
… not true in practice

## Slide 34: Internet’s approach to scalable routing
aggregate routers into regions known as “autonomous systems” (AS) (a.k.a. “domains”)
inter-AS routing
routing among AS’es
gateways perform inter-domain routing as well as intra-domain routing
All networks run the same inter-domain routing protocol
intra-AS routing
routing among hosts, routers in same AS (“network”)
all routers in the same AS must run same intra-domain protocol
routers in different AS can run different intra-domain routing protocols
gateway router: at “edge” of its own AS, has link(s) to router(s) in other AS’es

## Slide 35: Making routing scalable
Key principle: Hierarchy
… by separation into ASes
… within ASes, using intra-domain areas.
Hierarchy enables autonomy of separate regions.
Compare: federal -> state -> district -> …

## Slide 36
Routing protocols
Link state protocols
e.g., OSPF, IS-IS
Distance vector protocols
e.g., RIP, IGRP
Intra-AS protocols
same protocol within an AS
different algorithms across ASes
(semi-)global view of the network
Also called interior gateway protocols (IGP)
Path vector protocols
e.g., BGP
Inter-AS protocols
common across Ases
each AS knows little about the others