## Slide 1: Administrivia
Review 1
  Specific instructions to structure review in lecture 1 slides 26/27
Office hours moving to Thursday 10—12
MUD: Send me your top 1—3 questions on this lecture
Think about use cases and directions for your project!

## Slide 2
Lecture 4, Computer Networks (198:552)
Congestion Control

## Slide 3: Edge vs. core division of labor
Core: best-effort packet delivery
Edge: end-to-end guarantees to applications
  Transport should figure out how to use the core effectively
The Internet

## Slide 4: The role of the endpoint
Network discovery and bootstrapping
  How does the endpoint join the network?
  How does the endpoint get an address?
Interface to networked applications
  What interface to higher-level applications?
  How does the host realize that abstraction?
Distributed resource sharing
  What roles does the host play in network resource allocation decisions?

## Slide 5: Network model
Bottleneck queue
(max size B)
Queuing delay
Flows
Packet-switched core network
Link rate
(capacity)

## Slide 6: TCP: Reliable & ordered transport
Transmit buffer
Receive buffer
Data
ACKs
Reliable delivery using ACKs
Data ordered using sequence numbers
Receiver assembles data in order
before sending to the application

## Slide 7: But what about performance?
Throughput: the width of the pipe (MBytes/sec)
Delay: the length of the pipe (milliseconds)
Packet drop: leaks from the pipe (percentage of packets)

## Slide 8: What happens at a queue?
Knee – point after which
  Throughput increases very slowly
  Delay increases fast
Cliff – point after which
  Throughput starts to decrease very fast to zero
  Delay approaches infinity
For an M/M/1 queue
  Delay = 1/(1 – utilization)
Load
Load
Throughput
Delay
knee
cliff
congestion
collapse
packet
loss
Persistent queue buildup

## Slide 9: Flow ctrl vs. Cong ctrl vs. Cong avoidance
Flow control:
  Receiver tells sender how much it can accept in its buffer
Congestion avoidance:
  Trying to stay to the left of the knee
Congestion control:
  Trying to stay to the left of the cliff
Final window == min (receiver window, congestion window)

## Slide 10: How should an endpoint transmit data … and not overwhelm queues?

## Slide 11: Control loop
Congestion window: transmitted yet unACKed data
How should an endpoint adapt its congestion window
  … based on congestion signals provided by the network?
Data
ACKs

## Slide 12: Congestion signals
Explicit network signals
  Send packet back to source (e.g., ICMP source quench)
  Set bit in header (e.g., ECN)
  Send direct feedback (e.g., sending rate)
  Unless on every router, still need end-to-end signal
Implicit network signals
  Loss (e.g. TCP New Reno, SACK)
  Delay (e.g. TCP Vegas)
  Easily deployable
  Robustness?
    Wireless?

## Slide 13: Exercise
Buffer size B at the bottleneck queue
Link capacity C
Propagation delay T
What’s the congestion window for a flow at the knee? Cliff?
Is there a network buffer size that’s always sufficient?
Is there a receiver buffer size that’s always sufficient?

## Slide 14: Congestion Avoidance and Control
ACM SIGCOMM ‘88
Van Jacobson and Michael Karels

## Slide 15: One possible set of goals
Equilibrium: stay close to the “cliff”
At equilibrium:
  Don’t send a new packet
  ... until current one leaves the network
Return to equilibrium if you go “over” the cliff
  Try to approach the cliff if below it
Share bandwidth ‘fairly’ across flows
Load
Throughput
knee
cliff
congestion
collapse
packet
loss
Persistent queue buildup

## Slide 16: TCP New Reno: Mechanisms
Packet conservation
Reacting to loss: multiplicative decrease
Probing for more throughput: additive increase
Getting started: slow start
A better retransmission timeout
Fast retransmit
Fast recovery

## Slide 17: TCP congestion control
Additive increase, multiplicative decrease (AIMD)
  On packet loss, divide congestion window in half
  On success for last window, increase window linearly
t
Window
halved
Loss
Mechanisms not shown: slow start, fast retransmit, recovery, timeout loss, etc.

## Slide 18: Discussion of Jacobson’s paper
Is loss always congestive?
  Wireless networks
  Errors and corruption?
Is loss the best congestion signal?
  How about delays?
  Explicit congestion notifications from the network?
Is packet conservation always a good thing?
  Differences in flow propagation delays?
  Detect incipient congestion?
Why AIMD?

## Slide 19: Why AIMD?
Some thoughts from Chiu and Jain’s ‘89 paper,
[CJ89]: “An Analysis of the Increase and Decrease Algorithms for Congestion Avoidance in Computer Networks”

## Slide 20: Efficient allocation
Too slow?
  Underutilize the network
Too fast?
  High delays, lose packets
Every endpoint is doing it
  May all under/over shoot
  Large oscillations
Optimal:
  xi=Xgoal, e.g., link capacity
Efficiency = 1 - distance from efficiency line
User 1: x1
User 2: x2
Efficiency
line
2 user example
overload
underload

## Slide 21: Fair allocation
Max-min fairness
  Flows which share the same bottleneck get the same amount of bandwidth
Assumes no knowledge of priorities
Fairness = 1 - distance from fairness line
User 1: x1
User 2: x2
2 user example
2 getting
too much
1 getting
too much
fairness
line

## Slide 22: Linear window adaptation rules
xi(t): window or rate of the ith user at time t
aI, aD, bI, bD: constant increase/decrease coefficients
All users receive same network feedback
  Binary feedback: sense congestion or available capacity
All users increase or decrease simultaneously

## Slide 23: Multiplicative increase, additive decrease
User 1: x1
User 2: x2
fairness
line
efficiency
line
(x1,x2)
(x1+aD,x2+aD)
(bI(x1+aD), bI(x2+aD))
Does not converge to fairness
  Not stable at all
Does not converge to efficiency
  Stable iff

## Slide 24: Additive increase, additive decrease
User 1: x1
User 2: x2
fairness
line
efficiency
line
(x1,x2)
(x1+aD,x2+aD)
(x1+aD+aI), x2+aD+aI))
Does not converge to fairness
  Stable
Does not converge to efficiency
  Stable iff

## Slide 25: Multiplicative increase, mult. decrease
User 1: x1
User 2: x2
fairness
line
efficiency
line
(x1,x2)
(bdx1,bdx2)
(bIbDx1, bIbDx2)
Does not converge to fairness
  Stable
Converges to efficiency iff

## Slide 26: Additive increase, multiplicative decrease
(bDx1+aI, bDx2+aI)
User 1: x1
User 2: x2
fairness
line
efficiency
line
(x1,x2)
(bDx1,bDx2)
Converges to fairness
Converges to efficiency
Increments smaller as fairness increases
  Effect on metrics?

## Slide 27: Significance of AIMD/CJ89
Characteristics
  Converges to efficiency, fairness
  Easily deployable: feedback is binary
  Fully distributed
  No need to know the full state of the system (e.g., # users, link rates)
[CJ89] result that enabled the Internet to grow beyond the ‘80s
  A scalable Internet required a fully distributed congestion control
  Formed the basis of TCP as we know it

## Slide 28: Modeling
Critical to understanding complex systems
  [CJ89] model relevant even today (since ‘89!)
  106 increase of bandwidth, 1000x increase in number of users
Criteria for good models
  Realistic
  Simple
    Easy to work with
    Easy for others to understand
  Realistic, complex model  useless
  Unrealistic, simple model  may teach something!

## Slide 29: Congestion Control for High Bandwidth-Delay Product Networks
ACM SIGCOMM ‘02
Dina Katabi, Mark Handley, and Charlie Rohrs

## Slide 30: Key ideas
An explicit control system running in the network
  Give direct, multi-bit feedback on transmission windows/rates to endpoints
Separate efficiency control from fairness
Use window X.
X
ACK
I will use window X.

## Slide 31: XCP efficiency control loop
Sender (roughly): cwnd = cwnd +
Why do you need both terms of this equation?
Spare bandwidth
Persistent queue

## Slide 32: XCP fairness rules
If > 0, increase in throughput of all flows must be the same
If < 0, decrease in throughput must be proportional to a flow’s current throughput
Bandwidth shuffling: if too close to convergence, perturb by adding a small window to over-utilize the link

## Slide 33: Discussion of XCP
What window increase/decrease rules are used by XCP?
  Is it fair?
Why couldn’t you separate efficiency & fairness in TCP New Reno?
  Is generating multi-bit feedback harder than binary?
  What about the end-to-end argument?
Deployment concerns?
  Ensuring control loop runs at every bottleneck router?
  Selfish or rogue endpoints?
Should you necessarily push queue size to zero?
  Is it always possible to keep the pipe full?
  How to accommodate noise in measurements or window sizes?

## Slide 34: Some questions to think about…
What should networks provide as feedback for endpoints?
Should the network operate at the cliff, the knee, or elsewhere?
What is a good definition of fairness? Take into account:
  Demands? Usage of multiple resources? App goals?
What about hosts who cheat to hog resources?
  How to detect cheating? How to prevent/punish?
What about wireless networks?
  Loss caused by interference, not just congestion
  Difficulty of detecting collisions (due to fading)

## Slide 36: Backup slides

## Slide 37: Proposition 1 from [Chiu and Jain ’89]
In order to satisfy the requirements of distributed convergence to efficiency and fairness without truncation,
the linear decrease policy should be multiplicative, and
the linear increase policy should always have an additive component, and
optionally it may have a multiplicative component with the coefficient no less than one.

## Slide 38: Fast Retransmit
Don’t wait for window to drain
Resend a segment after 3 duplicate ACKs
  remember a duplicate ACK means that an out-of sequence segment was received
Notes:
  duplicate ACKs due to packet reordering
    why reordering?
  iwindow may be too small to get duplicate ACKs
ACK 2
segment 1
cwnd = 1
cwnd = 2
segment 2
segment 3
ACK 4
cwnd = 4
segment 4
segment 5
segment 6
segment 7
ACK 3
3 duplicate
ACKs
ACK 4
ACK 4
ACK 4

## Slide 39: Fast Recovery
After a fast-retransmit set cwnd to ssthresh/2
  i.e., don’t reset cwnd to 1
But when RTO expires still do cwnd = 1
Fast Retransmit and Fast Recovery  implemented by TCP Reno; most widely used version of TCP today

## Slide 40: Ethernet back-off mechanism
Carrier sense: wait for link to be idle
  If idle, start sending; if not, wait until idle
Collision detection: listen while transmitting
  If collision: abort transmission, and send jam signal
Exponential back-off: wait before retransmitting
  Wait random time, exponentially larger on each retry