## Slide 1: TLB
Questions answered in this lecture:
  Review paging...
  How can page translations be made faster?
  What is the basic idea of a TLB (Translation Lookaside Buffer)?
  What types of workloads perform well with TLBs?
  How do TLBs interact with context-switches? (if time permits)
RUTGERS UNIVERSITY Computer Sciences Department
CS 416/518 Operating Systems Design
Sudarsun Kannan
Disclaimer: Materials derived, reused, and modified from OSTEP book and lectures of Prof. Andrea and Remzi Arpaci-Dusseau and Prof. Yojip Won

## Slide 2: Announcements
Reading: Today cover Chapters 20-22
Project 2: User-level thread library and scheduling
    Start early and finish by March 20th.
Midterm - 03/08 – In class, 5:40pm – 7:00pm
Quiz 2 solution tomorrow
Sample midterm exam solution posted

## Slide 3: Approach 1: Combine Paging and Segmentation
Divide address space into segments (code, heap, stack)
  Segments can be variable length
Divide each segment into fixed-sized pages
Logical address divided into three portions
page offset (12 bits)
page number (8 bits)
seg # (4 bits)
Implementation
  Each segment has a page table
  Each segment track base (physical address) and bounds of page table for that segment

## Slide 4: Quiz: Paging and Segmentation
seg | base | bounds | R W
0 | 0x002000 | 0xff (255) | 1 0
1 | 0x000000 | 0x00 | 0 0
2 | 0x001000 | 0x0f (15) | 1 1
...
0x01f
0x011
0x003
0x02a
0x013
...
0x00c
0x007
0x004
0x00b
0x006
...
0x001000
0x002000
0x002070 read:
0x202016 read:
0x104c84 read:
0x010424 write:
0x210014 write:
0x203568 read:
page offset (12 bits)
page number (8 bits)
seg # (4 bits)
0x004070
0x003016
error
error
error
0x02a568

## Slide 5: Advantages of Paging and Segmentation
Advantages of Segments
  Supports sparse address spaces
    Decreases size of page tables
    If segment not used, not needed for page table
Advantages of Pages
  No external fragmentation
  Segments can grow without any reshuffling
  Can run process when some pages are swapped to disk (next lecture)
Advantages of Both
  Increases flexibility of sharing
    Share either single page or entire segment
    How?

## Slide 6: Disadvantages of Paging and Segmentation
Potentially large page tables (for each segment)
  Must allocate each page table contiguously
  More problematic with more address bits
  Page table size?
    Assume 2 bits for segment, 18 bits for page number, 12 bits for offset
    Each page table is:
      = Number of entries * size of each entry
      = Number of pages * 4 bytes
      = 2^18 * 4 bytes = 2^20 bytes = 1 MB!!!

## Slide 7: Approach 2: Inverted Page Table
Inverted Page Tables
  Only need entries for virtual pages w/ valid physical mappings
Naïve approach: Search through data structure <ppn, vpn+asid> to find match
  Too much time to search entire table
Better: Find possible matches entries by hashing vpn+asid
  Smaller number of entries to search for exact match
Managing inverted page table requires software-controlled TLB
For hardware-controlled TLB, need well-defined, simple approach

## Slide 8: Other Approaches
Inverted Pagetables
Segmented Pagetables
Multi-level Pagetables
  Page the page tables
  Page the pages of page tables…

## Slide 9: 3) Multilevel Page Tables
Goal: Allow each page tables to be allocated non-contiguously
Idea: Page the page tables
  Creates multiple levels of page tables; outer level “page directory”
  Only allocate page tables for pages in use
  Used in x86 architectures (hardware can walk known structure)
outer page (8 bits)
inner page (10 bits)
page offset (12 bits)
30-bit address:
base of page directory

## Slide 10: Quiz: Multilevel
PPN 0x3 - - - - - - - - - - - - - 0x92
valid 1 0 0 0 0 0 0 0 0 0 0 0 0 0 1
page directory
PPN 0x10 0x23 - - 0x80 0x59 - - - - - - - - -
valid 1 1 0 0 1 1 0 0 0 0 0 0 0 0 0
page of PT (@PPN:0x3)
PPN - - - - - - - - - - - - - 0x55 0x45
valid 0 0 0 0 0 0 0 0 0 0 0 0 0 1 1
page of PT (@PPN:0x92)
translate 0x01ABC
outer page (4 bits)
inner page (4 bits)
page offset (12 bits)
20-bit address:
translate 0xFEED0
translate 0x00000
0x23ABC
0x10000
0x55ED0
VPN 0 1 2 - - - - - - - - - - - 15

## Slide 11: Quiz: Address format for multilevel Paging
How should logical address be structured?
  How many bits for each paging level?
Goal?
  Each page table fits within a page
  PTE size * number PTE = page size
    Assume PTE size = 4 bytes
    Page size = 2^12 bytes = 4KB
    2^2 bytes * number PTE = 2^12 bytes
     number PTE = 2^10
   # bits for selecting inner page = 10
Remaining bits for outer page:
  30 – 10 – 12 = 8 bits
outer page
inner page
page offset (12 bits)
30-bit address:

## Slide 12: Problem with 2 levels?
Problem: page directories (outer level) may not fit in a page
Solution:
  Split page directories into pieces
  Use another page dir to refer to the page dir pieces.
PT idx
OFFSET
PD idx 1
VPN
PD idx 0
How large is virtual address space with 4 KB pages, 4 byte PTEs, each page table fits in page given 1, 2, 3 levels?
4KB / 4 bytes  1K entries per level
1 level: 1K * 4K = 2^22 = 4 MB
2 levels: 1K * 1K * 4K = 2^32 ≈ 4 GB
3 levels: 1K * 1K * 1K * 4K = 2^42 ≈ 4 TB
outer page?
inner page
(10 bits)
page offset (12 bits)
64-bit address:

## Slide 13: Review: Paging PROS and CONS
Advantages
  No external fragmentation
    don’t need to find contiguous RAM
  All free pages are equivalent
    Easy to manage, allocate, and free pages
Disadvantages
  Page tables are too big
    Must have one entry for every page of address space
  Accessing page tables is too slow [today’s focus]
    Doubles number of memory references per instruction

## Slide 14: Translation Steps
H/W: for each mem reference: 1. extract VPN (virt page num) from VA (virt addr) 2. calculate addr of PTE (page table entry) 3. read PTE from memory 4. extract PFN (page frame num) 5. build PA (phys addr) 6. read contents of PA from memory into register
(cheap)
(cheap)
(cheap)
(cheap)
(expensive)
(expensive)
Which expensive step will we avoid in today’s lecture?
Which steps are expensive?
3) Don’t always have to read PTE from memory!

## Slide 15: Example: Array Iterator
int sum = 0;
for (i=0; i<N; i++){ sum += a[i];
}
Assume ‘a’ starts at 0x3000
Ignore instruction fetches
load 0x3000
load 0x3004
load 0x3008
load 0x300C …
What virtual addresses?
load 0x100C load 0x7000 load 0x100C load 0x7004 load 0x100C load 0x7008 load 0x100C load 0x700C
What physical addresses?
Observation: Repeatedly access same PTE because program repeatedly accesses same virtual page
Aside: What can you infer?
  ptbr: 0x1000; PTE 4 bytes each
  VPN 3 -> PPN 7

## Slide 16: Strategy: Cache Page Translations
TLB: Translation Lookaside Buffer
(yes, a poor name!)
CPU
RAM
memory interconnect
PT
Translation Cache
Some popular entries

## Slide 17
Tag (virtual page number)
Physical page number (page table entry)
TLB Entry
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
A
Direct mapped (num sets = 16)
Lookup
Calculate set (tag % num_sets)
Search for tag within resulting set
Where is VPN (tag) 18 located?
4
TLB Organization
Incorrect: 2

## Slide 18
Tag (virtual page number)
Physical page number (page table entry)
TLB Entry
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
A
Direct mapped
TLB Organization
Two-way set associative
Set
Index
0
1
2
3
A
B
C
D
Four-way set associative
A
B
C
D
E
L
M
N
O
P
More in Computer Architecture Class

## Slide 19: TLB Associativity Trade-offs
Higher associativity
  + Better utilization, fewer collisions
  Slower
  More hardware
Lower associativity
  + Fast
  + Simple, less hardware
  Greater chance of collisions
TLBs usually fully associative

## Slide 20: Array Iterator (w/ TLB)
int sum = 0;
for (i = 0; i < 2048; i++){ sum += a[i];
}
Assume following virtual address stream:
load 0x1000 load 0x1004 load 0x1008 load 0x100C …
What will TLB behavior look like?

## Slide 21: TLB Accesses: Sequential Example
Physical
Virtual
P1
P2
P2
P1
PT
P1
16 KB
20 KB
24 KB
8 KB
12 KB
4 KB
0 KB
PT
P1 pagetable
1
5
4
…
P2
28 KB
load 0x1000
load 0x1004
load 0x1008
load 0x100c
…
load 0x2000
load 0x2004
load 0x0004
load 0x5000
(TLB hit)
load 0x5004
(TLB hit)
load 0x5008
(TLB hit)
load 0x500C …
load 0x0008
load 0x4000
(TLB hit)
load 0x4004
0
1
2
3
CPU’s TLB
PTBR
Valid | VPN | PPN
1
1
1
2
5
4

## Slide 22: Performance Of TLB?
int sum = 0; for (i=0; i<2048; i++) { sum += a[i]; }
Calculate miss rate of TLB for data:
# TLB misses / # TLB lookups
# TLB lookups?
= number of accesses to a = 2048
# TLB misses?
= number of unique pages accessed
= 2048 / (elements of ‘a’ per 4K page)
= 2K / (4K / sizeof(int)) = 2K / 1K
= 2
Miss rate?
2/2048 = 0.1%
Hit rate? (1 – miss rate)
99.9%
Would hit rate get better or worse with smaller pages?
Worse

## Slide 23: TLB Performance
How can system improve TLB performance (hit rate) given fixed number of TLB entries?
Increase page size
  Fewer unique page translations needed to access same amount of memory
TLB Reach:
  Number of TLB entries * Page Size

## Slide 24: TLB Performance with Workloads
Sequential array accesses almost always hit in TLB
  Very fast!
What access pattern will be slow?
  Highly random, with no repeat accesses

## Slide 25: Workload Access Patterns
int sum = 0;
for (i=0; i<2048; i++) { sum += a[i];
}
int sum = 0; srand(1234); for (i=0; i<1000; i++) { sum += a[rand() % N]; } srand(1234); for (i=0; i<1000; i++) { sum += a[rand() % N]; }
Workload A
Workload B

## Slide 26: Workload Access Patterns
int sum = 0;
for (i=0; i<2048; i++) { sum += a[i];
}
Workload A
time
address
Sequential Accesses
…
Spatial Locality

## Slide 27: Workload Access Patterns
time
address
Repeated Random Accesses
…
Temporal Locality
int sum = 0; srand(1234); for (i=0; i<1000; i++) { sum += a[rand() % N]; } srand(1234); for (i=0; i<1000; i++) { sum += a[rand() % N]; }
Workload B

## Slide 28: Workload Locality
Spatial Locality: future access will be to nearby addresses
Temporal Locality: future access will be repeats to the same data
What TLB characteristics are best for each type?
Spatial:
  Access same page repeatedly; need same vpn->ppn translation
  Same TLB entry re-used
Temporal:
  Access same address near in future
  Same TLB entry re-used in near future
  How near in future? How many TLB entries are there?

## Slide 29: Summary: Better PAGE TABLES
Problem: Simple linear page tables require too much contiguous memory
Many options for efficiently organizing page tables
If OS traps on TLB miss, OS can use any data structure
  Inverted page tables (hashing)
If Hardware handles TLB miss, page tables must follow specific format
  Multi-level page tables used in x86 architecture
  Each page table fits within a page
Next Topic: What if desired address spaces do not fit in physical memory?
.
Disclaimer: Materials reused, modified from OSTEP book and lectures of Prof. Andrea and Remzi Arpaci-Dusseau and Prof. Yojip Won