## Slide 1: Network Layer: Control/data plane, addressing, routers
CS 352, Lecture 10
http://www.cs.rutgers.edu/~sn624/352-S19
Srinivas Narayana
(heavily adapted from slides by Prof. Badri Nath and the textbook authors)

## Slide 2: Next: Network layer
Application
Transport
Network
Host-to-Net
…
FTP
HTTP
SMTP
DNS
TCP
UDP
IP
802.11
X.25
ATM
HTTPS

## Slide 3: Network layer
transport segment from sending to receiving host
on sending side encapsulates segments into datagrams
on receiving side, delivers segments to transport layer
network layer protocols in every host, router
router examines header fields in all IP datagrams passing through it
application
transport
network
data link
physical
application
transport
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical

## Slide 4: Two key network-layer functions
network-layer functions:
forwarding: move packets from router’s input to appropriate router output
routing: determine route taken by packets from source to destination
  routing algorithms
analogy: taking a trip
forwarding: process of getting through single interchange
routing: process of planning trip from source to destination

## Slide 5: Network layer: data plane, control plane
Data plane
local, per-router function
determines how datagram arriving on router input port is forwarded to router output port
forwarding function
Control plane
network-wide logic
determines how datagram is routed among routers along end-end path from source host to destination host
two control-plane approaches:
  traditional routing algorithms: implemented in routers
  software-defined networking (SDN): implemented in (remote) servers
1
2
3
0111
values in arriving
packet header

## Slide 6: IP Addressing

## Slide 7: IPv4 Addresses
32 bits long
Identifier for host, router interface
Notation:
  Each byte is written in decimal in MSB order, separated by dots
  Example: 128.195.1.80 stands for the 32-bit IP address
10000000 11000011 00000001 01010000

## Slide 8: Types of IPv4 Addresses
Unicast Address
  Destination is a single host
Multicast address
  Destination is a group of hosts
Broadcast address
  255.255.255.255
  Destination is all hosts

## Slide 9: IPv4 Address Classes (old)
0
Net
32 bits
Type of Serv.
Host
10
Net
Host
110
Net
Host
1110
Multicast address
1111
Reserved
A
B
C
D
E
Class

## Slide 10: IP Address Classes
Class A:
  For very large organizations
  16 million hosts allowed
Class B:
  For large organizations
  65 thousand hosts allowed
Class C
  For small organizations
  255 hosts allowed
Class D
  Multicast addresses
  No network/host hierarchy

## Slide 11: Problems with Class-based Routing
Too many small networks requiring multiple class C addresses
Running out of class B addresses, not enough nets in class A
Addressing strategy must allow for greater diversity of network sizes

## Slide 12: IP addressing: CIDR
CIDR: Classless InterDomain Routing
  subnet portion of address of arbitrary length
  address format: a.b.c.d/x, where x is # bits in subnet portion of address
11001000 00010111 00010000 00000000
subnet
part
host
part
200.23.16.0/23

## Slide 13: CIDR
An ISP can obtain a block of addresses and partition this further to its customers
  Say an ISP has 200.8.0.0/16 address (65K addresses).
  He has another customer who needs only 64 addresses starting from 200.8.4.128
  Then that block can be specified as 200.8.4.128/26
Notes: Instead of announcing all routes individually ...

## Slide 14: Subnetting
Host id
Subnet id
Network id
Example: Class B address with 8-bit subnetting
165.230
.24
.8
16 bits
8 bits
8 bits
Example
Address:

## Slide 15: Subnet Masks
Subnet masks allow hosts to determine if another IP address is on the same subnet or the same network
Host id
Subnet id
Network id
16 bits
8 bits
8 bits
1111111111111111
11111111
00000000
Mask:
255.255
.255
.0

## Slide 16: Subnet Masks (cont’d)
Are IP addresses A and B on the same subnet?
1. Compute logical AND (A & M).
2. Compute logical AND (B & M).
3. If (A & M) == (B & M) then A and B are
on the same subnet.
Assume IP addresses A and B share subnet mask M.
Example: A and B are class B addresses
A = 165.230.82.52
B = 165.230.24.93
M = 255.255.255.0
Same (classful) network?
Same subnet?

## Slide 17: Example of IP Addressing in a network
223.1.1.1
223.1.1.2
223.1.1.3
223.1.1.4
223.1.2.9
223.1.2.2
223.1.2.1
223.1.3.2
223.1.3.1
223.1.3.27

## Slide 18: What’s inside a router?

## Slide 19: What do routers look like?
Access routers
Core router
Data center top-of-rack switch

## Slide 20
Routing
Algorithm
Traditionally:
Individual routing algorithm components in each and every router interact in the control plane
data
plane
control
plane
1
2
0111
values in arriving
packet header
3
Data plane
per-packet processing
(~ tens of nanoseconds)
Control plane
per route-change processing
(~ a few seconds)
Basic components: Control & Data Planes

## Slide 21: Router architecture overview
high-speed
switching
fabric
routing
processor
router input ports
router output ports
Control plane
Data plane

## Slide 22: Input port functions
line
termination
link
layer
protocol
(receive)
lookup,
forwarding
queueing
switch
fabric
Switching:
using header field values, lookup output port using forwarding table in input port memory (“match plus action”)
goal: complete input port processing at ‘line speed’
queuing: if datagrams arrive faster than forwarding rate into switch fabric
physical layer:
bit-level reception
data link layer:
e.g., Ethernet
(We’ll see this later in the course)

## Slide 23: Destination-based Forwarding in the Internet
header
payload
Packet
Router
Destination Address
Outgoing Port
Dest-network
Port
Forwarding Table
Routing Lookup Data Structure
65.0.0.0/8
128.9.0.0/16
149.12.0.0/19
3
1
7

## Slide 24: Three types of switching fabrics

## Slide 25: Output Ports
Buffering required when datagrams arrive from fabric faster than the transmission rate
  Important implication: if buffers filled up, packets are dropped!
Scheduling discipline chooses among queued datagrams for transmission
  Important implication: Who gets priority is chosen by the scheduler
line
termination
link
layer
protocol
(send)
switch
fabric
datagram
buffer
queueing

## Slide 26: Prefixes and IP lookup

## Slide 27: Example Forwarding Table
0
224
232-1
128.9.0.0/16
65.0.0.0
142.12.0.0/19
65.0.0.0/8
65.255.255.255
Destination IP Prefix | Outgoing Port
65.0.0.0/8 | 3
128.9.0.0/16 | 1
65.0.0.128/25 | 4
142.12.0.0/19 | 7
IP prefix: 0-32 bits
Longest prefix match
Prefix length
128.9.16.14

## Slide 28: Prefixes can Overlap
128.9.16.0/24
128.9.176.0/24
Routing lookup: Find the longest matching prefix (the most specific route) among all prefixes that match the destination address.
0
232-1
128.9.0.0/16
142.12.0.0/19
65.0.0.0/8
128.9.16.14
Longest matching prefix

## Slide 29: Reducing Routing Table Size
service
provider
200.71.0.0
200.71.1.0
200.71.2.0
…..
200.71.255.0
200.71.0.0
200.71.1.0
200.71.2.0
…..
200.71.255.0
Routing
table
Without CIDR:
service
provider
200.71.0.0
200.71.1.0
200.71.2.0
…..
200.71.255.0
Routing
table
With CIDR:
200.71.0.0/16

## Slide 30: Hierarchical addressing: Route aggregation
“Send me anything
with addresses
beginning
200.23.16.0/20”
200.23.16.0/23
200.23.18.0/23
200.23.30.0/23
Fly-By-Night-ISP
Organization 0
Organization 7
Internet
Organization 1
ISPs-R-Us
“Send me anything
with addresses
beginning
199.31.0.0/16”
200.23.20.0/23
Organization 2
.
.
.
.
.
.
Efficient advertisement of routing information!

## Slide 31: LPM: Announcing more specific routes
ISPs-R-Us has a more specific route to Organization 1
Longest prefix match will be used to route IP packets
“Send me anything
with addresses
beginning
200.23.16.0/20”
200.23.16.0/23
200.23.18.0/23
200.23.30.0/23
Fly-By-Night-ISP
Organization 0
Organization 7
Internet
Organization 1
ISPs-R-Us
“Send me anything
with addresses
beginning 199.31.0.0/16
or 200.23.18.0/23”
200.23.20.0/23
Organization 2
.
.
.
.
.
.

## Slide 32: The Internet Protocol (IP)

## Slide 33: IP datagram format
ver
length
32 bits
data
(variable length,
typically a TCP
or UDP segment)
16-bit identifier
header
checksum
time to
live
32 bit source IP address
IP protocol version
number
header length
(bytes)
max number
remaining hops
(decremented at
each router)
for
fragmentation/
reassembly
total datagram
length (bytes)
upper layer protocol
to deliver payload to
head.
len
type of
service
“type” of data
flgs
fragment
offset
upper
layer
32 bit destination IP address
Options (if any)
E.g. timestamp,
record route
taken, specify
list of routers
to visit.
how much overhead with TCP?
20 bytes of TCP
20 bytes of IP
= 40 bytes + app layer overhead

## Slide 34: IP Fragmentation & Reassembly
network links have MTU (max.transfer size) - largest possible link-level frame.
  different link types, different MTUs
large IP datagram divided (“fragmented”) within net
  one datagram becomes several datagrams
  “reassembled” only at final destination
  IP header bits used to identify, order related fragments
fragmentation:
in: one large datagram
out: 3 smaller datagrams
reassembly

## Slide 35: IP Fragmentation and Reassembly
ID
=x
offset
=0
fragflag
=0
length
=4000
ID
=x
offset
=0
fragflag
=1
length
=1500
ID
=x
offset
=185
fragflag
=1
length
=1500
ID
=x
offset
=370
fragflag
=0
length
=1040
One large datagram becomes
several smaller datagrams
Example
4000 byte datagram
MTU = 1500 bytes
1480 bytes in data field
offset =
1480/8

## Slide 38: IP Address Hierarchy
Class A, B, C addresses support two levels of hierarchy
However, the host portion can be further split into “subnets” by the address class owner
  more than 2 levels of hierarchy

## Slide 39: Basic Components
Control Plane
Data plane
per-packet processing
Switching
Forwarding
Table
Routing
Table
Routing
Protocols

## Slide 40: Router Architecture Overview

## Slide 41: Input Port Functions
Decentralized switching:
queuing: if datagrams arrive faster than forwarding rate into switch fabric
Physical layer:
bit-level reception
Data link layer:
e.g., Ethernet
see chapter 5

## Slide 42: Three types of switching fabrics

## Slide 43: Longest prefix match
With CIDR, route entries are prefixes <prefix, CIDR mask>
Can be aggregated
We need to find the longest matching prefix that matches the destination address
Need to search all prefixes of all length (in order) and among prefixes of the same length
128.8.0/16
128.8.2/24
192.2.0/16
128.8.0.24
128.8.2.128
192.2.2.128

## Slide 45: The Internet Protocol (IP)
Provides delivery of packets from one host to any other host in the Internet
Internet packets are called “datagrams” and may be up to 64 kilobytes in length
  although they are typically much smaller