## Slide 1
Paging

## Slide 2: Review
Virtual addresses
Physical addresses
Base + Bounds
External Fragmentation
Paging
VPN to PFN Translation

## Slide 3: Virtual => Physical PAGE Mapping
How should OS translate VPN to PPN?
For segmentation, OS used a formula (e.g., phys addr = virt_offset + base_reg)
For paging, OS needs more general mapping mechanism
What data structure is good?
0
1
0
1
0
1
VPN
offset
1
1
0
1
0
1
1
0
PPN
offset
Address Mapper
Big array: page table
Number of bits in virtual address format does not need to equal
number of bits in physical address format

## Slide 4: The Mapping
Virt Mem
Phys Mem
P2
P3
P1

## Slide 5: Let’s fill in the Page Table
Virt Mem
Phys Mem
0
1
2
3
0
1
2
3
0
1
2
3
P2
P3
0
1
2
3
4
5
6
7
8
9
10
11
P1
Page Tables:
P1
3
1
7
10
P2
0
4
2
6
P3
8
5
9
11
Virt Mem
Phys Mem
0
4
8

## Slide 6: Where are page tables stored?
How big is a typical page table? - assume 32-bit address space - assume 4 KB pages - assume 4 byte entries
  Page table size = Num entries * size of each entry
  Num entries = num virtual pages = 2^(bits for vpn)
  Bits for vpn = 32– number of bits for page offset
    = 32 – lg(4KB) = 32 – 12 = 20
  Num entries = 2^20 = 1 MB
  Page table size = Num entries * 4 bytes = 4 MB per process
Ideally, put it in fast hardware (MMU)…

## Slide 7: Where are page tables stored?
Implication: Store each page table in memory
  Hardware finds page table base with register (e.g., CR3 on x86)
What happens on a context-switch?
  Change contents of page table base register to newly scheduled process
  Save old page table base register in PCB of descheduled process

## Slide 8: Other PT info
What other info is in pagetable entries besides translation?
  valid bit
  protection bits
  present bit (needed later)
  reference bit (needed later)
  dirty bit (needed later)
Page table entries are just bits stored in memory
  Agreement between hardware and OS about interpretation

## Slide 9: Memory Accesses with Pages
0x0010: movl 0x1100, %edi
0x0013: addl $0x3, %edi
0x0019: movl %edi, 0x1100
Assume PT is at phys addr 0x5000
Assume PTE’s are 4 bytes
Assume 4KB pages
How many bits for offset?
Simplified view of page table
2
0
80
99
Use of a page table doubles memory references
Physical Memory Accesses with Paging?
1) Fetch instruction at logical addr 0x0010; vpn?
  Access page table to get ppn for vpn 0
  Mem ref 1: 0x5000
  Learn vpn 0 is at ppn 2
  Fetch instruction at 0x2010 (Mem ref 2)
Exec, load from logical addr 0x1100; vpn?
  Access page table to get ppn for vpn 1
  Mem ref 3: 0x5004
  Learn vpn 1 is at ppn 0
  Movl from 0x0100 into reg (Mem ref 4)
12
Earlier: How many mem refs with segmentation?
5 (3 instrs, 2 movl)

## Slide 10: Advantages of Paging
No external fragmentation
  Any page can be placed in any frame in physical memory
Fast to allocate and free
  Alloc: No searching for suitable free space
  Free: Doesn’t have to coallesce with adjacent free space
  Just use bitmap to show free/allocated page frames
Simple to swap-out portions of memory to disk (later lecture)
  Page size matches disk block size
  Can run process when some pages are on disk
  Add “present” bit to PTE

## Slide 11: Disadvantages of Paging
Internal fragmentation: Page size may not match size needed by process
  Wasted memory grows with larger pages
Additional memory references  time-inefficient!
  Page table must be stored in memory
  MMU stores only base address of page table
Storage for page tables substantial  space-inefficient!
  Simple page table: Requires PTE for all pages in address space
    Naively, page table entry needed even if page not allocated
  Problematic with dynamic stack and heap within address space
  Page tables must be allocated contiguously in memory
    Due to linear access of page table entries
Stack
Code
Heap

## Slide 12: Reducing Page Table sizes

## Slide 13: How big are page tables?
PTE’s are 2 bytes, and 32 possible virtual page numbers
PTE’s are 2 bytes, virtual addrs are 24 bits, pages are 16 bytes
PTE’s are 4 bytes, virtual addrs are 32 bits, and pages are 4 KB
PTE’s are 4 bytes, virtual addrs are 64 bits, and pages are 4 KB
How big is each page table?
32 * 2 bytes = 64 bytes
2 bytes * 2^(24 – lg 16) = 2^21 bytes (2 MB)
4 bytes * 2^(32 – lg 4K) = 2^22 bytes (2 MB)
4 bytes * 2^(64 – lg 4K) = 2^54 bytes

## Slide 14: Why ARE Page Tables so Large?
code
heap
stack
Virt Mem
Phys Mem
Waste!

## Slide 15: Many invalid page table entries
PFN valid prot
10 1 r-x
- 0 -
23 1 rw-
- 0 -
- 0 -
- 0 -
- 0 -
- 0 -
- 0 -
- 0 -
- 0 -
28 1 rw-
4 1 rw-
…many more invalid…
how to avoid storing these?
Format of linear page tables:

## Slide 16: Avoid the simple linear page table
Use more efficient (but complex) data structures, instead of the simple big array
Any data structure is possible in principle*
*assuming software managed TLB

## Slide 17: Some approaches
Inverted Pagetables
Segmented Pagetables
Multi-level Pagetables
  Page the page tables
  Page the pagetables of page tables…

## Slide 18: Approach 1: Inverted Page Table
Inverted Page Tables
  Only need entries for virtual pages w/ valid physical mappings
Naïve approach: Search through data structure <ppn, vpn+ASID> to find match
  Too much time to search entire table
Better: Find possible matches entries by hashing vpn+ASID
  Smaller number of entries to search for exact match

## Slide 19: Valid PTEs are Contiguous
Note “hole” in addr space: valids vs. invalids are clustered
How did OS avoid allocating holes in phys memory?
Use ideas from segmentation!
PFN valid prot
10 1 r-x
- 0 -
23 1 rw-
- 0 -
- 0 -
- 0 -
- 0 -
- 0 -
- 0 -
- 0 -
- 0 -
28 1 rw-
4 1 rw-
…many more invalid…
how to avoid storing these?

## Slide 20: Approach 2: Segmented Page Tables
Divide address space into segments (code, heap, stack)
  Segments can be variable length
Divide each segment into fixed-sized pages
Logical address divided into three portions
page offset (12 bits)
page number (8 bits)
seg # (4 bits)
Ideas
Each segment has a page table
Each segment tracks the base (physical address) and bounds of the page table for that segment

## Slide 21: Combining Paging and Segmentation
seg | base | bounds | R W
0 | 0x002000 | 0xff (255) | 1 0
1 | 0x000000 | 0x00 | 0 0
2 | 0x001000 | 0x0f (15) | 1 1
...
0x01f
0x011
0x003
0x02a
0x013
...
0x00c
0x007
0x004
0x00b
0x006
...
0x001000
0x002000
0x002070 read:
0x202016 read:
0x104c84 read:
0x010424 write:
0x210014 write:
0x203568 read:
page offset (12 bits)
page number (8 bits)
seg # (4 bits)
0x004070
0x003016
error
error
error
0x02a568
Page table

## Slide 22
Advantages of Segments
  Supports sparse address spaces
    Decreases size of page tables
    If segment not used, not needed for page table
Advantages of Pages
  No external fragmentation
  Segments can grow without any reshuffling
  Can run process when some pages are swapped to disk (next lecture)
Advantages of Both
  Increases flexibility of sharing
    Share either single page or entire segment. How?

## Slide 23: Disadvantages of Paging with Segmentation
Potentially large page tables (for each segment)
  Must allocate each page table contiguously
  More problematic with more address bits
  Page table size?
    Assume 2 bits for segment, 18 bits for page number, 12 bits for offset
    Each page table is:
      = Number of entries * size of each entry
      = Number of pages * 4 bytes
      = 2^18 * 4 bytes = 2^20 bytes = 1 MB!!!

## Slide 24: Other Approaches
Inverted Pagetables
Segmented Pagetables
Multi-level Pagetables
  Page the page tables
  Page the pages of page tables…

## Slide 25: 3) Multilevel Page Tables
Goal: Allow page tables to be allocated non-contiguously
Idea: Page the page tables
  Creates multiple levels of page tables; outer level page directory
  Only allocate page tables for pages in use
  Used in x86 architectures (hardware can walk known structure)
outer page (8 bits)
inner page (10 bits)
page offset (12 bits)
30-bit address:
base of page directory

## Slide 26: Multilevel example
PPN 0x3 - - - - - - - - - - - - -
0x92
valid 1 0 0 0 0 0 0 0 0 0 0 0 0 0 1
page directory
PPN 0x10 0x23 - - 0x80 0x59 - - - - - - - - -
valid 1 1 0 0 1 1 0 0 0 0 0 0 0 0 0
page of PT (@PPN:0x3)
PPN - - - - - - - - - - - - - 0x55 0x45
valid 0 0 0 0 0 0 0 0 0 0 0 0 0 1 1
page of PT (@PPN:0x92)
translate 0x01ABC
outer page (4 bits)
inner page (4 bits)
page offset (12 bits)
20-bit address:
translate 0xFEED0
translate 0x00000
0x23ABC
0x10000
0x55ED0
VPN 0 1 2 - - - - - - - - - - - 15

## Slide 27: Address format for Multilevel Paging
How should logical address be structured?
  How many bits for each paging level?
Goal?
  Each page table fits within a page
  PTE size * number PTE = page size
    Assume PTE size = 4 bytes
    Page size = 2^12 bytes = 4KB
    number PTE per page = (2^12 bytes per page) / (4 bytes per PTE)
     number PTE = 2^10
   # bits for selecting inner page = 10
Remaining bits for outer page:
  30 – 10 – 12 = 8 bits
outer page
inner page
page offset (12 bits)
30-bit address: