## Slide 1: CS 352 Circuit & Packet Switching
Lecture 2.1
http://www.cs.rutgers.edu/~sn624/352
Srinivas Narayana

## Slide 2: Review of definitions
Endpoint or Host: Machine running user application
Packet: a unit of data transmission (ex: 1500 bytes)
Link: a physical communication channel between two or more machines
Router: A machine that processes packets moving them from one link to another towards a destination
Network: Collection of interconnected machines
Address: a unique name given to a machine (more later)

## Slide 3: How do machines talk?

## Slide 4: How do machines communicate?
With 1s and 0s
  Computers only deal with 1s and 0s
  So do networks
How do we transmit 1s and 0s in a network?

## Slide 5: Physical transmission on a single link
Physical signaling (light, AC voltages, etc.) are often analog
Convert bits to signals through modulation of the physical characteristics of signals: encoding
Convert signals back to digital by decoding physical signals

## Slide 6: Multi-link networks
Need a way to move data across links
We use the term switching to denote physically moving data from one link to another
Router
Router

## Slide 7: Switching schemes
Host applications transfer data containing many messages.
(1) Circuit Switching
(2) Message Switching
(3) Packet Switching

## Slide 8: Circuit switching
Provides service by setting up the full path of connected links from the origin to the destination
Example: Telephone network

## Slide 9: Circuit switching
1. Setup: Control message sets up a path from origin to destination
2. Return signal informs source that data transmission may proceed
3. Data transmission begins
4. Entire path remains allocated to the transmission (whether used or not)
5. When transmission is complete, source releases the circuit

## Slide 10: Circuit switching
Time
A
B
C
D
Data
Call accept signal
Call request signal
Data
Transmission
Time
Propagation Delay
Total transfer time
Resource reservation
delay

## Slide 11: Message switching
Each message is addressed to a destination
Header: metadata that denotes how to process a message
  Typically includes a destination address
The message “hops” from node to node through a network while allocating only one link at a time
  Compare to circuit switching: all links reserved at the same time, regardless of use.
Analogy: Postal service

## Slide 12: Message switching
When the entire message is received at a router, the next step and link in its journey are selected
If this selected link is busy, the message waits in a queue until the link becomes free
Store and forward switching
  Router waits for all message bits to arrive on incoming link before sending the first bit on outgoing link
  Alternative: cut–through switching sends bits as they arrive

## Slide 13: Message Switching
Time
A
B
C
D
Msg
Msg
Msg
Queueing
Delay
Total transfer time
Header

## Slide 14: Packet switching
Messages are split into smaller pieces called packets
  Packets have a maximum length
  Packets are numbered and addressed
  Packets are sent through the network one at a time
Pipelining: different parts of a message concurrently transmitted over different links
  Provides higher utilization of link resources

## Slide 15: Packet switching
Time
A
B
C
D
Pkt 1
Pkt 2
Pkt 3
Pkt 1
Pkt 2
Pkt 3
Pkt 1
Pkt 2
Pkt 3
Total transfer time
Header
Queueing
Delay
Store and forward
delay

## Slide 16: The Internet uses store-and-forward packet switching.

## Slide 17: Comparisons across switching tech
Circuit switching incurs an initial delay to set up the path
  Packet (and message) switching can start transmitting data right away
Packet switching doesn’t reserve resources for the conversation
  Circuit switching does. Needs admission control
  Packet switching makes resource reservation decisions per packet
Fewer or no guarantees  easier to build
  Telephone networks are more reliable and harder to build

## Slide 18: Comparisons across switching tech
(1) Total Delay to transfer a message
Short Bursty Messages:
Packet < Circuit
Long Continuous Messages:
Circuit < Packet
(2) Header overhead (what % of bits on the wire is metadata?)
Packet > Message
(assuming typical msgs larger than typical pkts)

## Slide 20: CS 352 Measuring Networks
Lecture 2.2
http://www.cs.rutgers.edu/~sn624/352
Srinivas Narayana

## Slide 21: Some definitions
Packet size: length of a packet (bits or bytes), incl. header and data
Bandwidth: For a single link, amount of data it can transmit per unit time (bits/second or Bytes/second or packets/second)
Propagation delay: Time needed to move one bit across (second)
  Imposed by the communication medium; depends on the link “length”
Transmission delay: Time from first bit@sender to last bit@sender
  Determined by link bandwidth and packet size
Queueing delay: Time that a packet waits for transmission
  Determined by contention for the link
Total packet delay: time from first bit@sender to last bit@receiver
  propagation delay + queueing delay + transmission delay for a single packet

## Slide 22
Propagation delay = time for first box to travel the length of the belt
Bandwidth = the number of boxes put on the belt per minute (“rate”)
Suppose we have N boxes in one shipment
Shipment transmission time = N / rate
  The next box is put on the belt (1/rate) minutes after the last
Total transfer time = transmission time + propagation delay
An analogy: Conveyor belt

## Slide 23: Visualizing the delays
Increasing time
Transmission delay at the first link
Propagation delay of first link
Queueing at the router
Propagation delay of second link
Transmission delay at the second link

## Slide 24: Bandwidth and delay
A small demo…

## Slide 26: CS 352 Protocols and Layering
Lecture 2.3
http://www.cs.rutgers.edu/~sn624/352
Srinivas Narayana

## Slide 27: Protocols: The “rules” of networking
Protocols consist of two things
Message format
  structure of messages exchanged with an endpoint
Actions
  operations upon receiving, or not receiving, messages
Example of a Zoom conversation:
  Message format: English words and sentences
  Actions: when a word is heard, say “yes”; when nothing is heard for more than 3 seconds, say “can you hear me?”

## Slide 28: The protocols of the Internet
Standardized by the Internet Engineering Task Force (IETF)
  through RFCs (“Request For Comments”)
Layering
…
FTP
HTTP
SIP
RTSP
TCP
UDP
IP
802.11
X.25
ATM
HTTPS

## Slide 29
The Internet
Rutgers campus network
Hardware address (MAC address)
Ex: 00-15-C5-49-04-A9
Network address (IP address)
Ex: 192.168.1.4
Transport address (port)
Ex: 64058
How do I identify my network interface (device)?
Whose network am I attached to?
With which app is this conversation associated?

## Slide 30
Hardware address (MAC address)
Ex: 00-15-C5-49-04-A7
Network address (IP address)
Ex: 10.1.1.104
Transport address (port)
Ex: 4096
Application address (URL)
Ex: mail.google.com
The Internet
Google’s network

## Slide 31
Software and hardware for networking are arranged in layers.
Layering provides modularity
Each layer has a distinct function
& interacts with other layers through well-defined interfaces.

## Slide 32: Modularity through layering
Link: best-effort local pkt delivery
Network: best-effort global pkt delivery
Transport: provide guarantees to apps
Apps: useful user-level functions
HTTP
FTP
TFTP
NV
TCP
UDP
IP
Ether
ATM
WiFi
…
Protocols “stacked” in endpoint and router software/hardware

## Slide 33
Link layer
Network
Transport
Applications
The Internet
Link layer
Network
Transport
Applications
The Internet
Packet takes on headers at each layer
Packet starts as an
app “payload”

## Slide 34
Link layer
Network
Transport
Applications
Link layer
Network
Transport
Applications
Link layer
Network
Link layer
Network

## Slide 35
Link layer
Network
Transport
Applications
Link layer
Network
Transport
Applications
Link layer
Network
Link layer
Network
Routers do not typically have transport or app functionality
(more on this later.)

## Slide 36: Layering
Network communication is very complex
Layering simplifies understanding, testing, maintaining
Easy to improve or replace protocol at one layer without affecting others

## Slide 37: This course has layers
Application
Transport
Network
Host-to-Net
…
FTP
HTTP
SIP
RTSP
TCP
UDP
IP
802.11
X.25
ATM
HTTPS