## Slide 1: The Transport Layer: Congestion Control
CS 352, Lecture 10, Spring 2020
http://www.cs.rutgers.edu/~sn624/352
Srinivas Narayana

## Slide 2: Course announcements
Project 2 will go online very soon
  Due April 3rd at 10 PM
Mid-term grading almost finished
Project 1 should be returned sometime next week

## Slide 3: Review of concepts
Permissible window size varies over time.
  Receiver application’s reading speed (recv)
  Communicated by the receiver to the sender through a header field
How should the receiver socket buffer be sized?
  What if it’s too large?
  What if it’s too small?
  Want to accommodate bursty transmissions from the sender
Bandwidth-delay product

## Slide 4: Feedback and Actions
The signals and knobs of congestion control

## Slide 5: Feedback from network offers clues…
Signals
  Packets being dropped (ex, RTO fires)
  Packets being delayed
  Rate of incoming ACKs
Knobs
  What can you change to “probe” the sending rate?
  Suppose receiver buffer is unbounded:
  Let’s call the amount of in-flight data per RTT the congestion window
  Increase congestion window: e.g., by x or by a factor of x
  Decrease congestion window: e.g., by x or by a factor of x
“Implicit” feedback signals
(more on explicit signals later)

## Slide 6: Steady state: Self clocking/ACK clocking

## Slide 7: TCP congestion window
Congestion window (cwnd): an estimate of in-flight data needed to keep the pipe full and achieve self-clocking
Sending window = min(congestion window, receiver advertised window). Why min?
  Overwhelm neither the receiver nor network routers
Use sliding window concept
  Window size is adjusted by congestion control

## Slide 8: Finding the right window

## Slide 9
Time for an activity
Notes: Make people guess a random number that you have in mind. See what strategies they come up with.

## Slide 10: TCP slow start
When connection begins, increase rate exponentially until first loss event:
Initially cwnd = 1 MSS
  MSS is “maximum segment size”
Double cwnd every RTT
  Increment cwnd for every ACK received
Initial rate is slow but ramps up exponentially fast
On loss, restart from cwnd := 1 MSS
Is this good enough?
Host A
one segment
RTT
Host B
time
two segments
four segments

## Slide 11: Problems with slow start
Congestion window increases too rapidly
  Example: suppose the right window size cwnd is 17
  cwnd would go from 16 to 32 and then dropping down to 1
  Result: massive packet drops
Congestion window decreases too rapidly
  Suppose the right cwnd is 31, and there is a loss when cwnd is 32
  Slow start will resume all the way back from cwnd 1
  Result: unnecessarily low throughput
Perform finer adjustments of cwnd based on signals
  Want a smooth ride, not a jerky one

## Slide 12: TCP additive increase
TCP does slow start until it is “close” to the correct cwnd
And grows cwnd much slower after that
(1) How does TCP know what is the correct cwnd?
  Remember the recent past
  The last good cwnd without packet drop is a good indicator
  TCP calls this the slow start threshold (ssthresh)
What is the best way to approach the correct value?
  TCP uses additive increase after cwnd hits ssthresh

## Slide 13: TCP additive increase
Start with ssthresh = 64K bytes
Do slow start until ssthresh
Once the threshold is passed, do additive increase
  For each ACK received, cwnd = cwnd + (MSS * MSS) / cwnd
  i.e., one MSS increase for each cwnd worth data ACK’ed
Upon a TCP timeout,
  cwnd = 1 MSS
  Set ssthresh = max(2 * MSS, 0.5 * cwnd)
  i.e., the next linear increase will start at half the current cwnd

## Slide 14: TCP additive increase

## Slide 15: Problems with additive increase
Current loss detection method: RTO for a given sequence number
cwnd drops rapidly to 1 MSS when there is a timeout
  When you drive, you don’t keep accelerating until you suddenly stop the car right next to a crossing pedestrian
Could we detect losses earlier (i.e., before RTO) and react proportionately?
  If you see the pedestrian from afar, you want to slow down gently from a distance

## Slide 16: Detecting and reacting to loss

## Slide 17: Can we detect loss earlier than RTO?
Key idea: use the information in the ACKs. How?
Suppose successive cumulative ACKs contain the same ACK#
  Also called duplicate ACKs
  Possible because network is reordering packets
  Strong indication that the requested sequence number was lost
Reduce cwnd when you see many duplicate ACKs
  Default threshold: 3 dup ACKs, i.e., triple duplicate ACK
  TCP sender does two things upon seeing triple dup ACKs

## Slide 18: TCP fast retransmit (RFC 2581)
(1) Gently reduce the cwnd, not drop all the way down to 1
Set cwnd := cwnd / 2
  Multiplicative decrease
(2) The seq# from dup ACKs is immediately retransmitted
  i.e., don’t wait for RTO if you there is strong evidence packet was lost
Sender keeps reduced cwnd until a new ACK arrives
  i.e., an ACK for a seq# transmitted before fast retransmit entered

## Slide 19
TCP performs additive increase and multiplicative decrease of its congestion window.
This is often termed AIMD.

## Slide 20: Why AIMD?
(bDx1+aI, bDx2+aI)
User 1: x1
User 2: x2
fairness
line
efficiency
line
(x1,x2)
(bDx1,bDx2)
Converges to fairness
Converges to efficiency
Increments to rate smaller as fairness increases