## Slide 1
CPU Virtualization

## Slide 2: Virtualization: The CPU
Questions answered in this lecture:
  What is a process? (Chapter 4-5)
  Why is limited direct execution a good approach for virtualizing the CPU? (Chapter 6)
  What execution state must be saved for a process? (Chapter 6)
  What 3 modes could a process in? (Chapter 6)
RUTGERS UNIVERSITY Computer Sciences Department
CS 416 + 518 Operating Systems Design
Sudarsun Kannan

## Slide 3: What is a Process?
Process: An execution stream in the context of a process state
What is an execution stream?
  Stream of executing instructions
  Running piece of code
  “thread of control”
What is process state?
  Everything that the running code can affect or be affected by
  Registers
    General purpose, floating point, status, program counter, stack pointer
  Address space
    Heap, stack, and code
  Open files

## Slide 4: Processes vs. Programs
A process is different than a program
  Program: Static code and static data
  Process: Dynamic instance of code and data
Can have multiple process instances of same program
  Example: many users can run “ls” at the same time

## Slide 5: Process Creation
code
static data
Program
CPU
Memory

## Slide 6: Process Creation
code
static data
Program
CPU
Memory
code
static data
heap
stack
Process

## Slide 7: Recall: Process Memory Segments
The OS allocates memory for each process - ie. a running program – for data and code
This memory consists of different segments
Stack - for local variables – incl. command line arguments and environment variables
Heap - for dynamic memory
Data segment for – global uninitialised variables (.bss) – global initialised variables (.data)
Code segment typically read-only

## Slide 8: Processes vs. Threads
A process is different than a thread
Thread: “Lightweight process” (LWP)
  An execution stream that shares an address space
  Multiple threads within a single process
Example:
  Two processes examining same memory address 0xffe84264 see different values (I.e., different contents)
  Two threads examining memory address 0xffe84264 see same value (I.e., same contents)

## Slide 9: Virtualizing the CPU
Goal: Give each process the impression that it alone is actively using the CPU
Resources can be shared in time and space
Assume single uniprocessor
  Time-sharing (today’s multi-processors: more nuanced)
But while sharing, processes
should not perform restricted operations
should not run forever or make the entire system slow
One possibility: let the OS inspect each process instruction before running
The problem? Performance

## Slide 10: How to Provide Good CPU Performance?
Direct execution
  Allow user process to run directly on hardware
  OS creates process and transfers control to starting point (i.e., main())
Problems with direct execution?
  Process could do something restricted
    Could read/write other process data (disk or memory)
  Process could run forever (slow, buggy, or malicious)
    OS needs to be able to switch between processes
  Process could do something slow (like I/O)
    OS wants to use resources efficiently and switch CPU to other process
Solution: Limited direct execution:
OS and the hardware maintain some control

## Slide 11: Problem 1: Restricted Ops
How can we ensure user process can’t unilaterally perform restricted operations?
Solution: privilege levels/separation provided by hardware (status bit on a register)
  OS runs in kernel mode (not restricted)
    Instructions for interacting with devices enabled
    Could have many privilege levels (advanced topic)
  User processes run in user mode (restricted mode)
    Interacting with devices directly will trap (software interrupt)
    Pre-set routines that run when privileged/restricted instructions run
How can a process legitimately access a device?
  System calls (function call implemented by OS)
  Change privilege level through system call (trap)

## Slide 12: Legitimate use: System Call
syscall(SYS_call, arg1, arg2, …);

## Slide 13: System Call
RAM
Process P
sys_read
P wants to call read()

## Slide 14: System Call
RAM
Process P
P can only see its own memory because of user mode
(other areas, including kernel, are hidden)

## Slide 15: System Call
RAM
Process P
P wants to call read() but no way to call it directly
http://www.cheat-sheets.org/saved-copy/Linux_Syscall_quickref.pdf
List of Linux System Calls

## Slide 16: System Call
RAM
Process P
movl $6, %eax; int $64
read():
Assembly convention: movl %eax, …
• CPU uses contents of EAX register as source operand

## Slide 17: System Call
RAM
Process P
movl $6, %eax; int $64
trap-table index
syscall-table index

## Slide 18: System Call
RAM
Process P
movl $6, %eax; int $64
Kernel mode: we can do anything!
trap-table index
syscall-table index

## Slide 19: System Call
RAM
Process P
movl $6, %eax; int $64
syscall
sys_read
trap-table index
syscall-table index
Follow entries to correct system call code

## Slide 20: System Call
RAM
Process P
movl $6, %eax; int $64
syscall
sys_read
buf
trap-table index
syscall-table index
Kernel can access user memory to fill in user buffer
return-from-trap at end to return to Process P

## Slide 21: System Call
Num | Function
6 | sys_read
7 | sys_write
$63 | illegal access
$64 | system call
$65 | Device Interrupt
System Call
App
movl $6, %eax; int $64
H/W-level Trap Table
Syscall() {
sysnum = %eax
sys_handle= get_fn_table(sysnum)
sys_handle ();
}
OS
Syscall table

## Slide 22: What to limit?
User processes are not allowed to directly perform:
  Arbitrary memory access
  Disk I/O
  Special x86 instructions like lidt
What if a process tries to do something privileged/restricted on its own?
Typical response: trap (hardware); OS kills process

## Slide 23: Problem 2: How to take the CPU away?
OS requirements for multiprogramming (or multitasking)
  Mechanism: To switch between processes
  Policy: To decide which process to run at what time
Separation of policy and mechanism
  Recurring theme in OS design
  Policy: Decision-maker to optimize some workload performance metric
    Which process to run when?
    Process Scheduler: next lecture
  Mechanism: Low-level code that implements the decision
    "How”?
    Process Dispatcher: Today’s lecture

## Slide 24: Dispatch Mechanism
OS runs dispatch loop
while (1) {
run process A for some time-slice
stop process A and save its context
load context of another process B
}
Question 1: How does dispatcher regain control after the time slice?
Question 2: What execution context must be saved and restored?
Context-switch

## Slide 25: Q1: How does Dispatcher regain control?
Option 1: Cooperative Multi-tasking
  Trust process to relinquish CPU to OS through traps
    Examples: System call, page fault (access page not in main memory), or error (illegal instruction or divide by zero)
    Provide special yield() system call

## Slide 26: Cooperative Approach
P1
yield() call

## Slide 27: Cooperative Approach
OS
yield() call

## Slide 28: Cooperative Approach
OS
yield() return

## Slide 29: Cooperative Approach
P2
yield() return

## Slide 30: Cooperative Approach
P2
yield() call

## Slide 31: Q1: How Does Dispatcher regain control?
Problem with cooperative approach?
Disadvantages: Processes can misbehave
  By avoiding all traps and performing no I/O, can take over entire machine
  Only solution: Reboot!
Not performed in modern operating systems

## Slide 32: Q1: How does Dispatcher regain control?
Option 2: Regain control without cooperation
  Guarantee OS can obtain control periodically. How?
  Enter OS by enabling periodic alarm clock
    Hardware generates timer interrupt (CPU or separate chip)
    Example: Every 10ms
  User must not be able to mask timer interrupt (privileged operation)
  Dispatcher counts interrupts between context switches
    Example: Waiting 20 timer ticks gives 200 ms time slice
    Common time slices range from 10 ms to 200 ms
    Research systems today: ~5 microseconds
Use hardware mechanisms (timer, traps) to regain control

## Slide 33: Q2: What Context must be Saved?
CS416
Eat & Sleep
“Now where was I…”
Context save and restore

## Slide 34: Q2: What Context must be Saved?
Dispatcher must save the context of the process when it’s not running
  Save it in process control block (PCB) (or process descriptor)
  PCB is a structure maintained for each process in the OS
What information is stored in PCB?
  PID
  Process state (I.e., running, ready, or blocked)
  Execution state (all registers, PC, stack pointer) -- Context
  Scheduling priority
  Accounting information (parent and child processes)
  Credentials (which resources can be accessed, owner)
  Pointers to other allocated resources (e.g., open files)
Requires special hardware support. Why?
  Hardware saves process PC and PSR on interrupts

## Slide 35: Q3: What’s inside a PCB?
// the information xv6 tracks about each process
// including its register context and state
struct proc {
char *mem; // Start of process memory
uint sz; // Size of process memory
char *kstack; // Bottom of kernel stack
// for this process
enum proc_state state; // Process state
int pid; // Process ID
struct proc *parent; // Parent process
int killed; // If non-zero, have been killed
struct file *ofile[NOFILE]; // Open files
struct inode *cwd; // Current directory
struct context context; // Switch here to run process
struct trapframe *tf; // Trap frame for the
// current interrupt
};
Conceptually: Separate kernel thread of execution per process

## Slide 36
Process A …
Operating System
Hardware
Program

## Slide 37
timer interrupt save regs(A) to k-stack(A) move to kernel mode jump to trap handler
Process A …
Operating System
Hardware
Program

## Slide 38
Handle the trap Call switch() routine save regs(A) to proc-struct(A) restore regs(B) from proc-struct(B) switch to k-stack(B) return-from-trap (into B)
timer interrupt save regs(A) to k-stack(A) move to kernel mode jump to trap handler
Process A …
Operating System
Hardware
Program
Must have been saved the last time OS switched B out

## Slide 39
Handle the trap Call switch() routine save regs(A) to proc-struct(A) restore regs(B) from proc-struct(B) switch to k-stack(B) return-from-trap (into B)
timer interrupt save regs(A) to k-stack(A) move to kernel mode jump to trap handler
restore regs(B) from k-stack(B) move to user mode jump to B’s IP
Process A …
Operating System
Hardware
Program

## Slide 40
Handle the trap Call switch() routine save regs(A) to proc-struct(A) restore regs(B) from proc-struct(B) switch to k-stack(B) return-from-trap (into B)
timer interrupt save regs(A) to k-stack(A) move to kernel mode jump to trap handler
restore regs(B) from k-stack(B) move to user mode jump to B’s IP
Process A …
Process B …
Operating System
Hardware
Program

## Slide 41: Q3: How is Context Saved?
Example:
Process A has moved from user to kernel mode, OS decides it
must switch from A to B
Save context (PC, registers, kernel stack pointer) of A on kernel stack
Switch SP to kernel stack of B
Restore context from B’s kernel stack
Who has saved registers on B’s kernel stack?
– OS/hardware did, when it switched out B in the past
Now, CPU is running B in kernel mode, return-from-trap to switch to
user mode of B

## Slide 42: Q3: How Context is Saved
Code
Data
User-level Stack
Heap
Proc A
Code
Data
User-level Stack
Proc B
Process Control Block
Kernel stack
Context
OS
Userspace
Process Control Block
Kernel stack
Context
Heap
CPU
Proc A
CPU
Proc B
Switch()
Reg(A)
Reg(B)

## Slide 43: Q4: What Context must be Saved?
// the registers will save and restore
// to stop and subsequently restart a process
struct context {
int eip; // Index pointer register
int esp; // Stack pointer register
int ebx; // Called the base register
int ecx; // Called the counter register
int edx; // Called the data register
int esi; // Source index register
int edi; // Destination index register
int ebp; // Stack base pointer register
};
// the different states a process can be in
enum proc_state { UNUSED, EMBRYO, SLEEPING,
RUNNABLE, RUNNING, ZOMBIE };

## Slide 44: Problem 3: Slow Ops such as I/O?
When running process performs op that does not use CPU, OS switches to process that needs CPU (policy issues)
OS must track state of each process:
  Running:
    On the CPU (only one on a uniprocessor)
  Ready:
    Waiting for the CPU
  Blocked
    Asleep: Waiting for I/O or synchronization to complete
Running
Blocked
Ready
Transitions?

## Slide 45
OS must track every process in system
  Each process identified by unique Process ID (PID)
OS maintains queues of all processes
  Ready queue: Contains all ready processes
  Event queue: One logical queue per event
    e.g., disk I/O and locks
    Contains all processes waiting for that event to complete
Next Lecture: Policy for determining which ready process to run
Problem 3: Slow Ops such as I/O?

## Slide 46: Summary
Virtualization: Context switching gives each process impression it has its own CPU
Direct execution makes processes fast
Limited execution at key points ensures OS retains control
Hardware is crucial for limited direct execution
  Privilege separation: user vs kernel mode
  Timer interrupts
  Automatic register saves and restores

## Slide 47: Process Creation
Two ways to create a process
  Build a new empty process from scratch
  Copy an existing process and change it appropriately
Option 1: New process from scratch
  Steps
    Load specified code and data into memory; Create empty call stack
    Create and initialize PCB (make it look like context-switch)
    Put process on ready list
  Advantages: No wasted work (compared to option 2)
  Disadvantages: Difficult to express all possible options for setup, complex
    Process permissions, where to write I/O, environment variables
    Example: WindowsNT has call with 10 arguments

## Slide 48: Process Creation
Option 2: Clone an existing process and change it
  Example: Unix fork() and exec()
    Fork(): Clones the calling process
    Exec(char *file): Overlays file image on calling process
  Fork()
    Stop current process and save its state
    Make copy of code, data, stack, and PCB
    Add new PCB to ready list
    Any changes needed to child process? Yes!
  Exec(char *file)
    Replace current data and code segments with those in specified file
  Advantages: Flexible, clean, simple
  Disadvantages: Wasteful to perform copy and then overwrite of memory

## Slide 49: Unix Process Creation
Fork/exec crucial to how the user’s shell is implemented!
While (1) {
Char *cmd = getcmd();
Int retval = fork();
If (retval == 0) {
// This is the child process
// Setup the child’s process environment here
// E.g., where is standard I/O, how to handle signals?
exec(cmd);
// exec does not return if it succeeds
printf(“ERROR: Could not execute %s\n”, cmd);
exit(1);
} else {
// This is the parent process; Wait for child to finish
int pid = retval;
wait(pid);
}
}

## Slide 50: Stack Detour

## Slide 51: Stack Detour

## Slide 52: Stack Detour

## Slide 53: Stack Detour

## Slide 54: Stack Detour

## Slide 55: Stack Detour

## Slide 56: Stack Detour

## Slide 57: Stack Detour

## Slide 58: Stack Detour

## Slide 59: Stack Detour

## Slide 60: Stack Detour

## Slide 61: Stack Detour

## Slide 62: Q4: What Context must be Saved?
// the registers will save and restore
// to stop and subsequently restart a process
struct context {
int eip; // Index pointer register
int esp; // Stack pointer register
int ebx; // Called the base register
int ecx; // Called the counter register
int edx; // Called the data register
int esi; // Source index register
int edi; // Destination index register
int ebp; // Stack base pointer register
};
// the different states a process can be in
enum proc_state { UNUSED, EMBRYO, SLEEPING,
RUNNABLE, RUNNING, ZOMBIE };

## Slide 63: Q4: What Context must be Saved?

## Slide 64: Q4: What Context must be Saved?

## Slide 65: Virtualization: The CPU
RUTGERS UNIVERSITY Computer Sciences Department
CS 416 Operating Systems Design
Sudarsun Kannan
Disclaimer: Materials derived, reused, and modified from OSTEP book and lectures of Prof. Andrea and Remzi Arpaci-Dusseau and Prof. Yojip Won