## Slide 1
Lecture 19, Computer Networks (198:552)
Fall 2019
Wide-Area Congestion Control
Notes: Slide material heavily adapted courtesy of Albert Greenberg, Changhoon Kim, Mohammad Alizadeh.

## Slide 2: Review: TCP congestion control
Keep some in-flight (un-ACK’ed) packets: congestion window
Adjust window based on several algorithms:
  Startup: slow start
  Steady state: AIMD
  Loss: fast retransmission, fast recovery
Window versus rate-based protocols

## Slide 3: Queue Dynamics with TCP
Steady-state behavior

## Slide 4: Network model
Bottleneck queue
(max size B)
Queuing delay
Single flow
Packet-switched core network
Link rate C
Propagation delay RTprop

## Slide 5: Sender behavior at steady state
Congestion avoidance: Additive increase, multiplicative decrease (AIMD)
Steady state isn’t static: lose pkts, grow cwnd, lose pkts, …
Congestion
Window
halved
Loss
time

## Slide 6: Sender behavior at steady state
How does the queue size at the bottleneck look, over time?
  Case 1: B = C * RTprop
  Case 2: B > C * RTprop
  Case 3: B < C * RT_prop
Congestion
Window
halved
Loss
time

## Slide 7: Network model
Bottleneck queue
(max size B)
Queuing delay
A few flows (say 3—4)
Packet-switched core network
Link rate C
Propagation delay RTprop
Q: how does queue size look now?

## Slide 8: Network model
Bottleneck queue
(max size B)
Queuing delay
Many flows (say hundreds)
Packet-switched core network
Link rate C
Propagation delay RTprop
Q: how does queue size look now?

## Slide 9: How big should router buffers be?
Classic buffer-sizing rule: B = C * RTprop
  BDP buffer
  Single TCP flow halving its window still gets a throughput of 100% link rate
Q: should buffers be BDP-sized?
Significant implications:
  Massive pkt buffers (e.g., 40 Gbit/s with 200ms RTprop): high cost
  Massive pkt delays: bufferbloat

## Slide 10: TCP BBR

## Slide 11: Key ideas
Bottleneck queue
(max size B)
Queuing delay
Single flow
Link rate C
Propagation delay RTprop
1. Estimate the bottleneck link rate C
2. Estimate the propagation delay RTprop
3. Send at rate C with at most k * C * RTprop packets in flight
Pros and Cons?

## Slide 12: (1) Estimating the bottleneck link rate
Data can’t be delivered to a receiver faster than the bottleneck link rate
Measure the data delivery rate
  And use the maximum value over the recent past
  Important: measurements time out after a certain period
  Occasionally send higher (PROBE_BW cycling) to see if changed
Q: how would you measure delivery rate at the receiver?
Q: how would you measure delivery rate at the sender?

## Slide 13: Measuring delivery rate at the sender
Packets
ACKs
Data that is unACKed at the time of transmitting packet
Normal case: All that data (and only that data) is ACKed by this point
unACKed data at pkt transmit time
Round trip time between pkt-ACK

## Slide 14: Quirk: Often, ACKs are “aggregated”
Packets
ACKs
More data appears to be in flight than there actually is
Idea: use minimum of sent rate and received rate
Q: how would you measure the rate at which data was sent?
(Note: packets of received data and sent data must be the same)

## Slide 15: (2) Estimating RTprop
Use the minimum of the RTT values experienced so far
If you’re sending at high rate, it is difficult to see the true RTprop of the path
  Q: why?
Occasionally send just a few packets in an RTT to measure RTprop (PROBE_RTT cycling)
Also allows achieving fairness among BBR flows

## Slide 16: Issues specific to wide-area

## Slide 17: The Internet: Many things to consider…
Bufferbloat
Token-bucket policers
Cellular base station scheduling
Sometimes compete with few streams, sometimes many
Delayed and aggregated ACKs (WiFi)
Coexisting with legacy protocols (e.g., Cubic)