## Slide 1: Demultiplexing & Error Detection
Lecture 10 http://www.cs.rutgers.edu/~sn624/352-S22
Srinivas Narayana

## Slide 2: Quick recap of concepts
App layer

## Slide 3: Demultiplexing Packets

## Slide 4: Demultiplexing
Machine 1
Machine
Machine 1
Machine 1
IP addr 1
IP addr 2
Port 1
Port 2
…
…
…
…
…
Port 65535
socket()
Ports
Denotes an attachment point with the network.
Link layer
Network
Transport
Applications
Each IP address comes with a full copy of its own ports.

## Slide 5: Demultiplexing
Machine 1
Machine
Machine 1
Machine 1
IP addr 1
IP addr 2
Port 1
Port 2
…
…
…
…
…
Port 65535
socket()
Ports
Network
Transport
Denotes an attachment point with the network.
Each IP address comes with a full copy of its own ports.

## Slide 6: Demultiplexing
Machine 1
Machine
Machine 1
Machine 1
IP addr 1
IP addr 2
Port 1
Port 2
…
…
…
…
…
Port 65535
socket()
Ports
Src IP, Dst IP,
Tp Protocol
Src port, Dst port
Denotes an attachment point with the network.
Each IP address comes with a full copy of its own ports.

## Slide 7: Demultiplexing
Machine 1
Machine
Machine 1
Machine 1
IP addr 1
IP addr 2
Port 1
Port 2
…
…
…
…
…
Port 65535
socket()
Ports
Src IP, Dst IP,
Tp Protocol
Src port, Dst port
Connection lookup: The operating system does a lookup using these data to determine the right socket and app.
Denotes an attachment point with the network.
Each IP address comes with a full copy of its own ports.

## Slide 8: Demultiplexing
Machine 1
Machine
Machine 1
Machine 1
IP addr 1
IP addr 2
Port 1
Port 2
…
…
…
…
…
Port 65535
socket()
Ports
Connection lookup: The operating system does a lookup using these data to determine the right socket and app.
TCP sockets:
(src IP, dst IP, src port, dst port)

Socket ID
Denotes an attachment point with the network.
Each IP address comes with a full copy of its own ports.

## Slide 9: Demultiplexing
Machine 1
Machine
Machine 1
Machine 1
IP addr 1
IP addr 2
Port 1
Port 2
…
…
…
Port 44262
…
Port 65535
socket()
Ports
Connection lookup: The operating system does a lookup using these data to determine the right socket and app.
TCP sockets:
(src IP, dst IP, src port, dst port)

Socket ID
Denotes an attachment point with the network.
Each IP address comes with a full copy of its own ports.

## Slide 10: Demultiplexing
Machine 1
Machine
Machine 1
Machine 1
IP addr 1
IP addr 2
Port 1
Port 2
…
…
…
…
…
Port 65535
socket()
Ports
Connection lookup: The operating system does a lookup using these data to determine the right socket and app.
TCP sockets:
(src IP, dst IP, src port, dst port)

Socket ID
UDP sockets:
(dst IP, dst port)

Socket ID
Denotes an attachment point with the network.
Each IP address comes with a full copy of its own ports.
Connectionless: the socket is shared across all sources!

## Slide 11: Demultiplexing
Machine 1
Machine
Machine 1
Machine 1
IP addr 1
IP addr 2
Port 1
Port 2
…
…
…
…
…
Port 65535
socket()
Ports
Connection lookup: The operating system does a lookup using these data to determine the right socket and app.
TCP sockets** Some caveats!
(src IP, dst IP, src port, dst port)

Socket ID
UDP sockets:
(dst IP, dst port)

Socket ID
Denotes an attachment point with the network.
Each IP address comes with a full copy of its own ports.
Connectionless: the socket is shared across all sources!

## Slide 12: TCP sockets of different types
Listening (bound but unconnected)
# On server side
ss = socket(AF_INET, SOCK_STREAM)
ss.bind(serv_ip, serv_port)
ss.listen() # no accept() yet
Connected (Established)
# On server side
csockid, addr = ss.accept()
# On client side
cs.connect(serv_ip, serv_port)
(src IP, dst IP, src port, dst port)

Socket (csockid NOT ss)

## Slide 13: TCP sockets of different types
Listening (bound but unconnected)
# On server side
ss = socket(AF_INET, SOCK_STREAM)
ss.bind(serv_ip, serv_port)
ss.listen() # no accept() yet
Connected (Established)
# On server side
csockid, addr = ss.accept()
# On client side
cs.connect(serv_ip, serv_port)
(src IP, dst IP, src port, dst port)

Socket (csockid NOT ss)
(dst IP, dst port)

Socket (ss)
accept() creates a new socket with the
4-tuple (established) mapping
Enables new connections to be demultiplexed correctly
Enables existing connections to be demultiplexed correctly

## Slide 14: TCP demultiplexing
When a TCP packet comes in, the operating system:
Looks up table of existing connections using 4-tuple
  If success, send to corresponding (established) socket
If fail (no table entry), look up table of listening connections using just (dst IP, dst port)
  If success, send to corresponding (listening) socket
If fail again (no table entry), send error to client
  Connection refused

## Slide 15: UDP demultiplexing
When a UDP packet comes in, the operating system:
Looks up table of listening UDP sockets using (dst IP, dst port)
  If success, send packet to corresponding socket
  There are no established UDP sockets; they’re all “unconnected”
If fail (no table entry), send error to client
  Port unreachable

## Slide 16: Listing sockets and connections
List all sockets with ss
Create and observe UDP sockets with iperf
Observe a TCP listening socket with iperf (or your own server!)

## Slide 17: User Datagram Protocol

## Slide 18: UDP: User Datagram Protocol [RFC 768]
Best effort service. UDP segments may be:
  Lost
  Delivered out of order to app
UDP is connectionless
  Each UDP segment handled independently of others (i.e. no “memory” across packets)
Suitable for one-off req/resp
  E.g., DNS uses UDP
Also for loss-tolerant delay-sensitive apps, e.g., video calling
Why are UDP’s guarantees even okay?
Simple & low overhead compared to TCP:
No delays due to connection establishment
  UDP can send data immediately
No memory for connection state at sender & receiver
Small segment header
UDP can blast away data as fast as desired
  UDP has no “congestion control”

## Slide 19: UDP segment structure
Length of
segment
(UDP header + data)
application
data
(message)
source port #
dest port #
length
checksum
16 bits
16 bits
Link layer
Network
Transport
Applications
Error detection
info
(more to come)

## Slide 20: UDP segment structure
application
data
(message)
source port #
dest port #
length
checksum
Link layer
Network
Transport
Applications
…
Source IP address
Destination IP address
…

## Slide 21: Review: UDP demultiplexing
application
data
(message)
source port #
dest port #
length
checksum
…
Source IP address
Destination IP address
…
Machine 1
Machine 1
Machine 1
IP 1
IP 2
Port 1
Port 2
…
…
…
Port 44262
…
Port 65535
socket()
Ports

## Slide 22: Seeing UDP packets in action
How to craft and send (UDP) packets?
  It’s simpler than you think!
sudo tcpdump -i lo udp –XAvvv # observe packets
sudo scapy # tool used to send crafted packets
Example: send(IP(dst="127.0.0.1")/UDP(sport=1024, dport=2048)/"hello world”, iface="lo")
See other fields of UDP using UDP().fields_desc
Scapy can send and receive crafted packets!
  However, it requires sudo (superuser privileges)

## Slide 23: Error Detection

## Slide 24: Why error detection?
Network provides best effort service
UDP is a simple and low overhead transport
  Data may be lost
  Data may be corrupted along the way (e.g., 1 -> 0)
  Data may be reordered
However, simple error detection is possible!
  Was the data I received the same data the remote machine sent?
Error detection is a useful feature for all transport protocols including TCP

## Slide 25: Error Detection in UDP and TCP
Key idea: have sender compute a function over the data
  Store the result in the packet
  Receiver can check the function’s value in received packet
An analogy: you’re sending a package of goodies and want your recipient to know if goodies were leaked along the way
Your idea: weigh the package; stamp the weight on the package
  Have the recipient weigh the package and cross-check the weight with the stamped value

## Slide 26: Requirements on error detection function
Function must be easy to compute
Function must capture the likely changes to the packet
  If the packet was corrupted through these likely changes, the function value must change
Function must be easy to verify
UDP and TCP use a class of function called a checksum
  Very common idea: used in multiple parts of networks and computer systems

## Slide 27: UDP & TCP’s Checksum function
Sender:
treat segment contents as sequence of 16-bit integers
checksum: addition (1’s complement sum) of segment contents
sender puts checksum value into UDP checksum field
Receiver:
compute a checksum of the received segment, including the checksum in packet itself
check if the resulting (computed) checksum is 0
NO – an error is detected
YES – assume no error

## Slide 28: Computing 1’s complement sum
Very similar to regular (unsigned) binary addition.
However, when adding numbers, a carryout from the most significant bit needs to be added to the result
Example: add two 16-bit integers
1 1 1 1 0 0 1 1 0 0 1 1 0 0 1 1 0
1 1 1 0 1 0 1 0 1 0 1 0 1 0 1 0 1
1 1 0 1 1 1 0 1 1 1 0 1 1 1 0 1 1
1 1 0 1 1 1 0 1 1 1 0 1 1 1 1 0 0
1 0 1 0 0 0 1 0 0 0 1 0 0 0 0 1 1
wraparound
sum
checksum

## Slide 29: From the UDP specification (RFC 768)
Checksum is the 16-bit one's complement of the one's complement sum of a pseudo header of information from the IP header, the UDP header, and the data, padded with zero octets at the end (if necessary) to make a multiple of two octets.
The pseudo header conceptually prefixed to the UDP header contains the source address, the destination address, the protocol, and the UDP length.

## Slide 30: Some observations on checksums
Checksums don’t detect all bit errors
  Consider (x, y) vs. (x – 1, y + 1) as adjacent 16-bit values in packet
  Analogy: you can’t assume the package hasn’t been meddled with if its weight matches the one on the stamp. More smarts needed for that. 
  But it’s a lightweight method that works well in many cases
Checksums are part of the packet; they can get corrupted too
  The receiver will just declare an error if it finds an error
  However, checksums don’t enable the receiver to detect where the error lies or correct the error(s)
  Checksum is an error detection mechanism; not a correction mechanism.

## Slide 31: Some observations on checksums
Checksums are insufficient for reliable data delivery
  If a packet is lost, so is its checksum
UDP and TCP use the same checksum function
  TCP also uses the lightweight error detection capability
  However, TCP has more mature mechanisms for reliable data delivery (more to come on this)

## Slide 32: Playing with checksums

## Slide 33: Summary of UDP
UDP is a thin shim around network layer’s best-effort delivery
  One-off request/response messages
  Lightweight transport for loss-tolerant delay-sensitive applications
Provides basic multiplexing/demultiplexing for application
No reliability, performance, or ordering guarantees
Can do basic error detection (bit flips) using checksums
  Error detection is necessary to deliver data reliably, but it is insufficient