## Slide 1: CS 352 Internet Protocol (IP)
CS 352, Lecture 16.1
http://www.cs.rutgers.edu/~sn624/352
Srinivas Narayana

## Slide 2: Network
Application
Transport
Network
Host-to-Net
…
FTP
HTTP
SMTP
DNS
TCP
UDP
IP
802.11
X.25
ATM
HTTPS
The main function of the network layer is to
move packets from one endpoint to another.

## Slide 3: IPv4 Datagram Format

## Slide 4
ver
length
32 bits
data
(variable length,
typically a TCP
or UDP segment)
16-bit identifier
header
checksum
time to
live
32-bit source IP address
IP protocol version
number
header length
(bytes)
max number
remaining hops
(decremented at
each router)
for
fragmentation/
reassembly
total datagram
length (bytes)
upper layer protocol to deliver payload to, e.g., TCP, UDP
hdr
len
type of
service
Bits for
traffic differentiation
e.g., audio, web, bulk
(more on this later)
flags
fragment
offset
upper
protocol
32-bit destination IP address
Options (if any)
E.g. timestamp,
record the route
taken, specify
list of routers
to visit (“source routing”)
How much header overhead?
Suppose 20 bytes of TCP
20 bytes of IP
= 40 bytes + app layer overhead

## Slide 5: IP fragmentation and reassembly
Links and transmission media have MTUs (maximum transmission unit):
  Largest possible link-level frame
On a network path, a packet might traverse links with different MTUs
This may result in a large IP datagram to be divided (fragmented) by a router
  Fragments reassembled only at the destination endpoint, at the IP layer
  IP header bits used to identify and reassemble related fragments
Fragmentation
one large datagram goes in
3 smaller datagrams come out
Reassembly
Link with smaller MTU
Network with large MTU
= IP header
= IP payload

## Slide 6: IP fragmentation and reassembly
Suppose a large 4000-byte datagram reaches a router. The next link has MTU 1500 bytes.
  Note: MTU includes IP headers, so does the length field of the IP header. IP payload = 3980 bytes.
Result: 3 datagrams of length 1500, 1500, 1040 bytes resp.
  IP payload = 1480, 1480, 1020 bytes resp. (adds to 3980)
Offset field = index of payload byte / 8
ID
=x
offset
=0
fragflag
=0
length
=4000
ID
=x
offset
=0
fragflag
=1
length
=1500
ID
=x
offset
=185
fragflag
=1
length
=1500
ID
=x
offset
=370
fragflag
=0
length
=1040
1480/8
2960/8

## Slide 7: IP fragmentation and reassembly
At the destination endpoints, the fragments are reassembled using the IP identifier field
  Fragments of the same original datagram share the same IP ID
The fragmentation flag is set to 0 for the terminal fragment, and 1, if other fragments follow
The offset field allows the IP stack to reassemble the fragments in order into a single IP datagram
ID
=x
offset
=0
fragflag
=0
length
=4000
ID
=x
offset
=0
fragflag
=1
length
=1500
ID
=x
offset
=185
fragflag
=1
length
=1500
ID
=x
offset
=370
fragflag
=0
length
=1040
1480/8
2960/8

## Slide 8: The rest of this lecture and the next
We’ll talk about some support protocols and mechanisms for the network layer
  Protocols: DHCP, ICMP, ARP
  Mechanisms: NAT
  We’ll also talk about IP version 6 (IPv6)
Some of these protocols use an IP header underneath their own header (ICMP) or replace the IP header with their own (ARP)
  But these shouldn’t be construed as transport/network protocols
  They are fundamental to supporting IP/network layer functionality
  More appropriately discussed as support protocols for the network layer

## Slide 10: CS 352 Dynamic Host Configuration
CS 352, Lecture 16.2
http://www.cs.rutgers.edu/~sn624/352
Srinivas Narayana

## Slide 11: How does an endpoint get its IP addr?
One possibility: hard-code the IP address on the endpoint
  e.g., a system admin writing addresses in a file
  UNIX: /etc/network/interfaces
  Windows: control panel  network  configuration  TCP/IP  properties
Another possibility: dynamically receive an address “from the network”
  DHCP: Dynamic Host Configuration Protocol
  Provide plug-and-play functionality for endpoints (e.g., phones, laptops)

## Slide 12: Many similar bootstrapping problems
How does a host get its IP address?
How does a host know its local DNS server?
How does a host know its netmask?
  i.e., so that it can know which other hosts are in the same network
How does a host know how to reach other networks?
  i.e., which router is at the “border” of the current network?
  This router is also called the gateway router: crucial for an endpoint to communicate with another endpoint external to the network

## Slide 13: How DHCP works
A new endpoint that just joins a network knows nothing about the network
  It doesn’t even have a network address for its point of attachment
It makes no sense to have it contact a “known” server to receive this information.
The only known mechanism that might work is broadcast:
  Ask everyone!

## Slide 14: How DHCP works
DHCP allows a host to dynamically obtain its IP address from a server on a network when it joins the network
DHCP can allow a host to be mobile across different networks, obtaining IP addresses as needed
DHCP uses leases on addresses
  Host must renew lease periodically
  Allows network to reuse an IP with an expired lease, reclaiming addresses from inactive hosts
223.1.1.0/24
223.1.2.0/24
223.1.3.0/24
223.1.1.1
223.1.1.3
223.1.1.4
223.1.2.9
223.1.3.2
223.1.3.1
223.1.1.2
223.1.3.27
223.1.2.2
223.1.2.1
DHCP
server
DHCP
Client program on the endpoint broadcasts message requesting an IP address.

## Slide 15: DHCP client-server scenario
DHCP server:
223.1.2.5
Arriving
client
DHCP discover
src : 0.0.0.0, 68
dest.: 255.255.255.255,67
yiaddr: 0.0.0.0
transaction ID: 654
DHCP offer
src: 223.1.2.5, 67
dest: 255.255.255.255, 68
yiaddrr: 223.1.2.4
transaction ID: 654
lifetime: 3600 secs
DHCP request
src: 0.0.0.0, 68
dest:: 255.255.255.255, 67
yiaddrr: 223.1.2.4
transaction ID: 655
lifetime: 3600 secs
DHCP ACK
src: 223.1.2.5, 67
dest: 255.255.255.255, 68
yiaddrr: 223.1.2.4
transaction ID: 655
lifetime: 3600 secs
Broadcast: is there a DHCP server out there?
Broadcast: I’m a DHCP server! Here’s an IP address you can use
Broadcast: OK. I’ll take that IP address!
Broadcast: OK. You’ve got that IP address!
DHCP runs on UDP ports 67 (server) and 68 (client)
Client’s initial IP address is set to 0.0.0.0
Yiaddr stands for “your IP address” – an address value the server sends to the client for consideration
Note that the IP allocation has an associated lifetime (lease period)
223.1.2.4

## Slide 16: Multiple DHCP servers can coexist
Server 1
Server 2
Client
DHCPDISCOVER
DHCPDISCOVER
DHCPOFFER
DHCPOFFER
DHCPREQUEST
DHCPREQUEST
DHCPACK
Collects replies
Selects server 2

## Slide 17: DHCP returns more than an IP address
Name and IP address of the local DNS server
Netmask of the IP network the host is on
  Useful to know whether another endpoint is inside or outside the current IP network
Address of the gateway router to enable the endpoint to reach other IP networks

## Slide 18: Your home router runs DHCP
Likely, your home devices (laptops, tablets, phones) are all using DHCP-assigned IP addresses
The DHCP server is running on the control processor of your home’s access router (e.g., WiFi router)
You can access the DHCP client program on Linux using the command dhclient and on Linux using sudo ipconfig <interface> DHCP

## Slide 19: Summary of DHCP
Want endpoints to have plug and play functionality
  Avoid tedious manual configuration of IP addresses and other information
DHCP: a general bootstrapping mechanism for critical information required for network layer functionality
Hosts can be simple: receive information from DHCP servers by broadcasting over the network

## Slide 21: CS 352 Internet Control Message Protocol
CS 352, Lecture 16.3
http://www.cs.rutgers.edu/~sn624/352
Srinivas Narayana

## Slide 22: Internet Control Message Protocol
A protocol for troubleshooting and diagnostics
Works over IP: unreliable delivery of packets
Some functions of ICMP:
  Determine reachability and network errors
  Specify that packets have been in the network for too long

## Slide 23: ICMP message
IP header
ICMP header
Message type, Code, Checksum,
ICMP data
https://en.wikipedia.org/wiki/Internet_Control_Message_Protocol#Control_messages

## Slide 24: Specific uses of ICMP
Echo request reply
  Check remotely if an endpoint is alive and connected
An unreachable destination
  Invalid address and/or port
Knowing if packet’s IP time-to-live expired
  Example, due to routing loops
Look at two tools built using ICMP: ping and traceroute

## Slide 25: Ping
Uses ICMP echo request (type=8, code=0) and reply (type=0, code=0)
Source sends ICMP echo request message to dst address
Destination replies with an ICMP echo reply message containing the data in the original echo request message
Source can calculate round trip time (RTT) of packets
If no echo reply comes back, then the destination is unreachable
Don’t need to have a server program running on the other side
  In general, the remote endpoint can be completely outside your control

## Slide 26: Ping
Time
Echo
request
Echo reply
A
B
R1
R2
R3
Ping time
A small demo…

## Slide 27: Traceroute
A tool that can record the router-level path taken by packets
A clever use of the IP time-to-live (TTL) field
In general, when a router receives an IP packet, it decrements the TTL field on the packet
  A failsafe mechanism to ensure packets don’t keep taking up network resources for too long
If a router receives a packet with TTL=0, it sends an ICMP time exceeded message (type=11, code=0) to the source endpoint

## Slide 28: Traceroute
Traceroute sends multiple packets to a destination endpoint
But it progressively increases the TTL on those packets: 1, 2, ...
Every time a time exceeded message is received, record the router’s IP address
Process repeated until the destination endpoint is reached
If the packet reaches the destination endpoint (i.e.: TTL is high enough), then the endpoint sends a port unreachable message

## Slide 29: Traceroute
Time
TTL=1, dest = B, dstport = invalid
A
B
R1
R2
R3
A small demo…
Time exceeded
Source: R1
TTL = 2
TE(R2)
Port un- reachable
Source: B
Similarly, capture IP addresses of routers at distance 3, 4, …
Have full router-level path until destination

## Slide 30: Summary of ICMP
A protocol for network diagnostics and troubleshooting
Two useful tools: ping and traceroute
Ping: test connectivity to a machine totally outside your control
  Use ICMP echo request and reply
Traceroute: determine router-level path to a remote endpoint
  A smart use of the TTL field in the IP header