## Slide 1: Reliable Data Delivery
Lecture 13
http://www.cs.rutgers.edu/~sn624/352-F24
Srinivas Narayana

## Slide 2: Review
UDP: best-effort delivery + demultiplexing + error detection
Checksum function: 1s complement of the 1s complement sum
Sender: compute checksum & write.
  Receiver: compute checksum, compare to 0
1 1 1 1 0 0 1 1 0 0 1 1 0 0 1 1 0
1 1 1 0 1 0 1 0 1 0 1 0 1 0 1 0 1
1 1 0 1 1 1 0 1 1 1 0 1 1 1 0 1 1
1 1 0 1 1 1 0 1 1 1 0 1 1 1 1 0 0
1 0 1 0 0 0 1 0 0 0 1 0 0 0 0 1 1
wraparound
sum
checksum

## Slide 3: Checksum, why you being weird?
Need a function that is fast to compute, catches likely errors, and easy to verify. Some design considerations:
Basic bit-wise: AND, OR: many inputs map to the same output
XOR: can catch single bit-flips, but not an even number of 1s/0s flipping
  Some sort of addition is preferable to this (carries will show errors)
Addition is commutative, associative, has an identity element (0), is efficient to calculate
  Checksum can appear anywhere in the packet
  Compute checksum by placing a 0 in place originally
  Use operations at the natural bit-width of the machine (16 bits was common)
(Regular) two’s complement addition: errors in higher order bit positions can be missed (the final carry-out bit isn’t part of the checksum)
  One’s complement: adding the final carry-out to the result helps 
Why complement? Why not compare the checksum rather than to 0?
  CPUs have ways of detecting if the last result was 0
Not on the exam
https://datatracker.ietf.org/doc/html/rfc1071

## Slide 4: Some observations on checksums
Checksums don’t detect all bit errors
  Consider (x, y) vs. (x – 1, y + 1) as adjacent 16-bit values in packet
  Analogy: you can’t assume the package hasn’t been meddled with if its weight matches the one on the stamp. More smarts needed for that. 
  But it’s a lightweight method that works well in many cases
Checksums are part of the packet; they can get corrupted too
  The receiver will just declare an error if it finds an error

## Slide 5: Some observations on checksums
Checksums are insufficient for reliable data delivery
  If a packet is lost, so is its checksum
UDP and TCP use the same checksum function
  TCP also uses the lightweight error detection capability
  However, TCP has more mature mechanisms for reliable data delivery (up next!)
Checksum is a mechanism to detect errors, not correct them
  Even when they detect errors, checksums don’t tell you where they lie

## Slide 6: Playing with checksums
Let’s craft some UDP packets (again)!
sudo tcpdump -i lo udp –XAvvv # observe packets
sudo scapy # tool used to send crafted packets
send(IP(dst="127.0.0.1")/UDP(sport=1024, dport=2048)/"hello world”, iface="lo")
Now can you craft two UDP packets with an identical checksum?

## Slide 7: Summary of UDP
A simple transport: Send or receive a single packet from/to the correct application process. That’s it
  Just a thin shim around network layer’s best-effort delivery
  No connection building, no latency
  Suitable for one-off request/response messages
  Sometimes suitable for loss-tolerant but delay-sensitive applications
No reliability, performance, or ordering guarantees
Can do basic error detection (bit flips) using checksums
  Error detection is necessary to deliver data reliably, but it is insufficient

## Slide 8: Reliable data delivery

## Slide 9: Packet loss
Sender
Receiver
How might a sender and receiver ensure that data is delivered reliably (despite some packets being lost)?
TCP uses three mechanisms

## Slide 10: Coping with packet loss: (1) ACK
Key idea: Receiver returns an acknowledgment (ACK) per packet sent
If sender receives an ACK, it knows that the receiver got the packet.
Sender
Receiver
ACK
packet
ACK
packet

## Slide 11: Coping with packet corruption: (1) ACK
ACKs also work to detect packet corruption on the way to the receiver
  One possibility: A receiver could send a negative acknowledgment, or a NAK, if it receives a corrupted packet
  Q: How to detect corrupted packet?
    One method: Checksum!
TCP only uses positive ACKs.
Sender
Receiver
NAK
packet
ACK
packet

## Slide 12: Coping with packet loss: (2) RTO
What if a packet is dropped?
Key idea: Wait for a duration of time (called retransmission timeout or RTO) before re-sending the packet
In TCP, the onus is on the sender to retransmit lost data when ACKs are not received
Note that retransmission works also if ACKs are lost or delayed
Sender
Receiver
ACK
RTO
Retransmission

## Slide 13: How should the RTO be set?
A good RTO must predict the round-trip time (RTT) between the sender and receiver
  RTT: the time to send a single packet and receive a (corresponding) single ACK at the sender
Intuition: If an ACK hasn’t returned, and our (best estimate of) RTT has elapsed, the packet was likely dropped.
RTT can be measured directly at the sender. No receiver or router help needed.
Sender
Receiver
ACK
RTO

## Slide 14: Coping with packet duplication
Sender
Receiver
ACK
RTO
If ACKs delayed beyond the RTO, sender may retransmit the same data
  Receiver wouldn’t know that it just received duplicate data from this retransmitted packet
Add some identification to each packet to help distinguish between adjacent transmissions
  This is known as the sequence number
Duplicate
packet received!
(Receiver doesn’t know…)

## Slide 15: Coping with packet loss: (3) Sequence #s
Sender
Receiver
ACK
RTO
A bad scenario: Suppose an ACK was delayed beyond the RTO; sender ended up retransmitting the packet.
At the receiver: sequence number helps disambiguate a fresh transmission from a retransmission
  Sequence number same as earlier: retransmission
  Fresh sequence number: fresh data
0
0

## Slide 16: Coping with packet loss: (3) Sequence #s
Sender
Receiver
RTO
A good scenario: packet successfully received and ACK returned within RTO
Sequence numbers of successively transmitted packets are different
Receiver knows these are not duplicate, because sequence numbers are different
SEQ 0
SEQ 1
ACK
RTO

## Slide 17: Coping with packet loss: (3) Sequence #s
Sender
Receiver
RTO
A good scenario: packet successfully received and ACK returned within RTO
Sequence numbers of successively transmitted packets are different
RTO
Receiver knows these are not duplicate, because sequence numbers are different
ACK
ACK
ACK
SEQ 0
SEQ 1

## Slide 18: Q: What is the seq# of third packet?
Sender
Receiver
ACK
RTO
Goal: Avoid ambiguity on which packet was received/ACK’ed from both the sender and receiver’s perspective
One option: increment seq#: 2, 3, …
Alternative: since seq # 0 was successfully ACK’ed earlier, it is OK to reuse seq #0 for next transmission.
Seq #s reusable if older packets with those seq #s known to be delivered
SEQ 0
SEQ 1
ACK
???
RTO

## Slide 19: Stop-and-Wait Reliability
Sender sends a single packet, then waits for an ACK to know the packet was successfully received. Then the sender transmits the next packet.
If ACK is not received until a timeout (RTO), sender retransmits the packet
Disambiguate duplicate vs. fresh packets using sequence numbers that change on “adjacent” packets
Sender
Receiver
RTT
RTO
SEQ 0
ACK
SEQ 1
Retransmit

## Slide 20
In principle, these three ideas are sufficient to implement reliable data delivery!

## Slide 21: Efficiency problem with stop-and-wait
Sender sends one packet, waits for an ACK (or RTO) before transmitting next one
  Unfortunately, too slow 
Suppose RTO = RTT = 100 milliseconds
Packet size (bytes in 1 packet) = 12,000 bits
Bandwidth of links from sender to receiver = 12 Mbit/s (1 M = 106)
Rate of data transfer = data size / time
Sender
Receiver
RTT
120 Kilobit/s == 1% of bw!
RTO

## Slide 22
Sending one packet per RTT makes the data transfer rate limited by the time between the endpoints, rather than the bandwidth.
Ensure you got the (one) box safely; make N trips
Ensure you get N boxes safely; make just 1 trip!
Keep many packets in flight

## Slide 23: Making reliable data transfer efficient

## Slide 24: Pipelined reliability
Data in flight: data that has been sent, but sender hasn’t yet received ACKs from the receiver
  Note: can refer to packets in flight or bytes in flight
New packets sent at the same time as older ones still in flight
New packets sent at the same time as ACKs are returning
More data moving in same time!
Improves throughput
  Rate of data transfer

## Slide 25: Pipelined reliability
Stop and wait: send 1 packet per RTT
Pipelined: send N packets per RTT
If there are N packets in flight, throughput improves by N times compared to stop-and-wait!
Sender
Receiver
RTT
RTO

## Slide 26
Pipelining makes reliable data transfer efficient.
However, pipelining also makes it more complex.
Which packets were successfully delivered?
Which packets should the sender retransmit?
Which packets are currently in flight?

## Slide 28: Review: Demultiplexing
Machine 1
Machine
Machine 1
Machine 1
IP addr 1
IP addr 2
Port 1
Port 2
…
…
…
…
…
Port 65535
socket()
Ports
Src IP, Dst IP,
Tp Protocol
Src port, Dst port
Denotes an attachment point with the network.
Each IP address comes with a full copy of its own ports.
Connection lookup: The operating system does a lookup using these data to determine the right socket and app.

## Slide 29: Listing sockets and connections
ss
iperf –s and iperf –s -u

## Slide 30: User Datagram Protocol

## Slide 31: UDP: User Datagram Protocol [RFC 768]
Best effort service
  UDP segments may be lost, corrupted, reordered
UDP is connectionless
  Each UDP segment handled independently of others (i.e. no “memory” across packets)
Suitable for one-off req/resp
  E.g., DNS uses UDP
Early multimedia apps used UDP
  Delay-sensitive but loss tolerant
Why are UDP’s guarantees even okay?
Simple & low overhead compared to TCP:
No delays due to “connection establishment” (which TCP does)
  UDP can send a packet immediately
Small segment header (TCP’s is larger)
UDP can blast data without control
  TCP is more balanced and measured
Less memory for connection “state” at sender & receiver relative to TCP

## Slide 32: UDP segment structure
Length of
segment
(UDP header + data)
application
data
(message)
source port #
dest port #
length
checksum
16 bits
16 bits
Link layer
Network
Transport
Applications
Error detection
info
(more to come)

## Slide 33: UDP segment structure
application
data
(message)
source port #
dest port #
length
checksum
Link layer
Network
Transport
Applications
…
Source IP address
Destination IP address
…

## Slide 34: Review: UDP demultiplexing
application
data
(message)
source port #
dest port #
length
checksum
…
Source IP address
Destination IP address
…
Machine 1
Machine 1
Machine 1
IP 1
IP 2
Port 1
Port 2
…
…
…
Port 44262
…
Port 65535
socket()
Ports

## Slide 35: Seeing UDP packets in action
How to craft and send (UDP) packets?
  It’s simpler than you think!
sudo tcpdump -i lo -XAvvv udp # observe packets
sudo scapy # tool used to send crafted packets
Example:
  send(IP(dst="127.0.0.1")/UDP(sport=1024, dport=2048)/"hello world”, iface="lo")
See other fields of UDP using UDP().fields_desc
Scapy can send and receive crafted packets!
  However, it requires sudo (superuser privileges)

## Slide 36: Error Detection in the Transport Layer

## Slide 37: Why error detection?
Network provides best effort service
UDP is a simple and low overhead transport
  Data may be corrupted along the way (e.g., 1 -> 0)
However, simple error detection is possible!
  Was the data I received the same data the remote machine sent?
Error detection is a useful feature for all transport protocols including TCP
Q: Suppose you’re sending a package to a friend. How would you detect tampering with that package?

## Slide 38: Error Detection in UDP and TCP
Key idea: have sender compute a function over the data
  Store the result in the packet
  Receiver can check the function’s value in received packet
An analogy: you’re sending a package of goodies and want your recipient to know if goodies were leaked along the way
Your idea: weigh the package; stamp the weight on the package
  Have the recipient weigh the package and cross-check the weight with the stamped value

## Slide 39: Requirements on error detection function
Function must be easy to compute
Function value must change if the packet changes
  If the packet was modified through “likely” changes, the function value must change
Function must be easy to verify
UDP and TCP use a class of function called a checksum
  Very common idea: used in multiple parts of networks and computer systems

## Slide 40: UDP & TCP’s Checksum function
Sender:
treat segment contents as sequence of 16-bit integers
checksum: addition (1’s complement sum) of segment contents
sender puts checksum value into UDP/TCP checksum field
Receiver:
compute a checksum of the received segment, including the checksum in packet itself
check if the resulting (computed) checksum is 0
NO – an error is detected
YES – assume no error

## Slide 41: Computing 1’s complement sum
Very similar to regular (unsigned) binary addition.
However, when adding numbers, a carryout from the most significant bit needs to be added to the result
Example: add two 16-bit integers
1 1 1 1 0 0 1 1 0 0 1 1 0 0 1 1 0
1 1 1 0 1 0 1 0 1 0 1 0 1 0 1 0 1
1 1 0 1 1 1 0 1 1 1 0 1 1 1 0 1 1
1 1 0 1 1 1 0 1 1 1 0 1 1 1 1 0 0
1 0 1 0 0 0 1 0 0 0 1 0 0 0 0 1 1
wraparound
sum
checksum

## Slide 42: From the UDP specification (RFC 768)
Checksum is the 16-bit one's complement of the one's complement sum of a pseudo header of information from the IP header, the UDP header, and the data, padded with zero octets at the end (if necessary) to make a multiple of two octets.
The pseudo header conceptually prefixed to the UDP header contains the source address, the destination address, the protocol, and the UDP length.
Warning: Technical language ahead