## Slide 1
Lecture 17, Computer Networks (198:552)
Packet Scheduling in
Data Centers

## Slide 2: Datacenter transport
Goal: Complete flows quickly / meet deadlines
Short flows
(e.g., query, coordination)
Large flows
(e.g., data update, backup)
Low Latency
High Throughput

## Slide 3: Low latency cong control (ex: DCTCP)
Keep network queues small (at high throughput)
Can we do better?
Want: implicitly prioritize mice
HOL blocking if long queues

## Slide 4: The opportunity
Many DC apps/platforms know flow size or deadlines in advance
Key/value stores
Data processing
Web search
4
Front end Server
Aggregator
Aggregator
Aggregator
… …
Aggregator
Worker
…
Worker
Worker
…
Worker
Worker

## Slide 5
H1
H2
H3
H4
H5
H6
H7
H8
H9
H1
H2
H3
H4
H5
H6
H7
H8
H9
TX
RX

## Slide 6
H1
H2
H3
H4
H5
H6
H7
H8
H9
H1
H2
H3
H4
H5
H6
H7
H8
H9
Objective?
Minimize avg FCT
Minimize missed deadlines
DC transport =
Flow scheduling on giant switch
ingress & egress
capacity constraints
TX
RX

## Slide 7: Example: Minimize average FCT
Flow A
Size
Flow B
Flow C
1
2
3
arrive at the same time share the same bottleneck link
A
B
B
C
C
C

## Slide 8: Example: Minimize average FCT
A
B
C
3
B
C
5
6
C
Time
Throughput
1
A
B
B
C
C
C
Fair sharing: 3, 5, 6 mean: 4.67
Time
Throughput
1
3
B
A
1
6
C
Shortest flow first: 1, 3, 6 mean: 3.33

## Slide 9: Optimal flow scheduling for avg FCT
NP-hard for multi-link network [Bar-Noy et al.]
  Shortest Flow First: 2-approximation
1
2
3
1
2
3

## Slide 10: How can we schedule flows based on flow criticality in a distributed way?
Some transmission order

## Slide 11: pFabric
Mohammad Alizadeh et al., SIGCOMM’13

## Slide 12: pFabric in 1 slide
Packets carry a single priority #
e.g., priority = remaining flow size
pFabric Switches
Send highest priority / drop lowest priority packets
Very small buffers (20-30KB for 10Gbps fabric)
pFabric Hosts
Send/retransmit aggressively
Minimal rate control: just prevent congestion collapse
Main Idea:
Decouple scheduling from rate control

## Slide 13: Starvation prevention
Use remaining flow size as priority: What happens?
Transmit earliest packet of flow with the highest priority packet
10
9
8
7
6
5
4
4
5
6
7
8
9
10
8
7
6
5
4
5
5
6
6
7
7
8
8
9
10

## Slide 14: pFabric switch
  Boils down to a sort
  Essentially unlimited priorities
  Thought to be difficult in hardware
  Existing switching only support 4-16 priorities
  pFabric queues very small
    51.2ns to find min/max of ~600 numbers
  Binary comparator tree: 10 clock cycles
  Current ASICs: clock ~ 1ns

## Slide 15: pFabric rate control
Minimal version of TCP algorithm
Start at line-rate
  Initial window larger than BDP
No retransmission timeout estimation
  Fixed RTO at small multiple of round-trip time
Reduce window size upon packet drops
  Window increase same as TCP (slow start, congestion avoidance, …)
After multiple consecutive timeouts, enter “probe mode”
  Probe mode sends min. size packets until first ACK
What about queue buildup?
Why window control?

## Slide 16: Why does pFabric work?
Key invariant:
At any instant, have the highest priority packet (according to ideal algorithm) available at the switch.
Priority scheduling
  High priority packets traverse fabric as quickly as possible
What about dropped packets?
  Lowest priority → not needed till all other packets depart
  Buffer > BDP → enough time (> RTT) to retransmit

## Slide 17: Overall mean FCT: Web search workload
Chart: Load
| 0.1 | 0.2 | 0.3 | 0.4 | 0.5 | 0.6 | 0.7 | 0.8
Ideal | 1.0328 | 1.0629 | 1.1142 | 1.1809 | 1.2614 | 1.3645 | 1.4975 | 1.678
pFabric | 1.0405 | 1.0953 | 1.1671 | 1.2578 | 1.3721 | 1.5188 | 1.7144 | 1.9773
PDQ | 1.2874 | 1.3767 | 1.4898 | 1.6316 | 1.82 | 2.0907 | 2.5363 | 3.2155
DCTCP | 1.2576 | 1.5997 | 2.0717 | 2.6692 | 3.3594 | 4.2057 | 5.3579 | 7.1968
TCP-DropTail | 2.1709 | 3.1101 | 4.1956 | 5.6511 | 7.5465 | 10.2482 | 14.3819 | 20.7525

## Slide 18: Mice FCT (<100KB): Web search workload
Average
99th percentile
Chart: Load
| 0.1 | 0.2 | 0.3 | 0.4 | 0.5 | 0.6 | 0.7 | 0.8
Ideal | 1.0066 | 1.0018 | 1.0026 | 1.0035 | 1.0051 | 1.0061 | 1.007 | 1.008
pFabric | 1.0192 | 1.0359 | 1.0528 | 1.0707 | 1.0896 | 1.1088 | 1.1279 | 1.1435
PDQ | 1.4575 | 1.5373 | 1.6248 | 1.7207 | 1.8388 | 1.9861 | 2.1827 | 2.3968
DCTCP | 1.2777 | 1.5442 | 1.7916 | 2.0476 | 2.3294 | 2.662 | 3.0631 | 3.596
TCP-DropTail | 2.7128 | 3.8866 | 5.0537 | 6.5398 | 8.4256 | 11.0812 | 15.0502 | 20.3733
Chart: Load
| 0.1 | 0.2 | 0.3 | 0.4 | 0.5 | 0.6 | 0.7 | 0.8
Ideal | 1.0767 | 1.0729 | 1.0729 | 1.1217 | 1.2259 | 1.2803 | 1.3166 | 1.3535
pFabric | 1.1129 | 1.158 | 1.2136 | 1.3254 | 1.4536 | 1.5605 | 1.6639 | 1.747
PDQ | 2.1723 | 2.5232 | 2.7099 | 2.863 | 3.1297 | 3.5482 | 4.171 | 5.1192
DCTCP | 3.4906 | 4.1598 | 4.5345 | 4.9287 | 5.2966 | 5.7463 | 6.2991 | 7.2011
TCP-DropTail | 27.5707 | 29.8924 | 33.3187 | 40.4708 | 47.6968 | 55.5775 | 63.664 | 72.5742

## Slide 19: Elephant FCT (>10MB): Data mining workload
Why the gap?
Average
Notes: Pkt drop rate at 80% load: 4.3%

## Slide 20: Discussion
Priority-based scheduling: pros and cons
  Gaming?
  Starvation?
Implementation using a small number of priority queues?
  How to set priority thresholds?
When is the “big switch” abstraction appropriate?

## Slide 21: PIAS: Information-agnostic scheduling
Wei Bai et al., NSDI’15

## Slide 22: State of the art for packet/flow scheduling
pFabric, PDQ, PASE
Assume
  Prior knowledge of flow size information
  To approximate ideal preemptive shortest job first (SJF)
  With customized network elements
Can we minimize FCT without flow size information
with commodity components?

## Slide 23: Multi-level feedback queue (MLFQ)
Emulate shortest job first (SJF) without job size information

## Slide 24: Realization with commodity components
Don’t keep per-flow sizes and state in switch
  Endpoint maintains per-flow state
  … sets the priority as a packet tag
Map packets to queues using thresholds on packet priorities
What about bad thresholds? Use ECN to keep queues short
  Use DCTCP at endpoints to react smoothly to ECN

## Slide 25: Discussion
What happens if a flow transmits with a bursty traffic pattern?
  Transmit for x seconds, wait y seconds, transmit again for x
What if a flow transmits just enough to always stay in the highest priority queue?

## Slide 26: MLFQ rules (Arpaci-Dusseau)

## Slide 27: Acknowledgment
Slides heavily adapted from material by Mohammad Alizadeh, Chi-Yao Hong, and Wei Bai