## Slide 1: Switching, Layering & Measurement
Lecture 2
http://www.cs.rutgers.edu/~sn624/352-F24
Srinivas Narayana

## Slide 2: Review of definitions
Endpoint or Host: Machine running user application
Packet: a unit of data transmission (ex: 1500 bytes)
Link: a physical communication channel between two or more machines
Router: A machine that processes packets moving them from one link to another towards a destination
Network: Collection of interconnected machines
Address: a unique name given to a machine (more later)
host/
endpoint
router
router
link
link
link
host/
endpoint
packet

## Slide 3: Today’s lecture
Dive a bit deeper into how Internet communication works
  Links: how does communication work physically?
  Routers: how do they move data between links?
  Endpoints: how is networking organized at endpoints?
Understand how to measure the Internet

## Slide 4: How do machines talk?

## Slide 5: How do machines communicate?
With 1s and 0s
  Digital computers deal with 1s and 0s
How do we transmit 1s and 0s in a network?
Encoding and Decoding problem

## Slide 6: Physical transmission on a single link
Physical signaling (light, AC voltages, etc.) are often analog
Convert bits to signals through modulation of the physical characteristics of signals: encoding
Convert signals back to digital by decoding physical signals

## Slide 7: Physical transmission on a single link
Physical signaling (light, AC voltages, etc.) are often analog
Convert bits to signals through modulation of the physical characteristics of signals: encoding
Convert signals back to digital by decoding physical signals

## Slide 8: Physical transmission on a single link
Physical signaling (light, AC voltages, etc.) are often analog
Convert bits to signals through modulation of the physical characteristics of signals: encoding
Convert signals back to digital by decoding physical signals

## Slide 9: Physical transmission on a single link
Physical signaling (light, AC voltages, etc.) are often analog
Convert bits to signals through modulation of the physical characteristics of signals: encoding
Convert signals back to digital by decoding physical signals

## Slide 10: Routers and Multi-link networks
Routers need a way to move data across links
We use the term switching to denote physically moving data from one link to another
There are different possibilities to switch data across links
Router
Router

## Slide 11: Switching methods
Host applications transfer data containing many messages.
A message could be a single web page, chat message
(1) Circuit Switching
(2) Message Switching
(3) Packet Switching

## Slide 12: Circuit switching
Provides service by setting up the full path of connected links from the origin to the destination
Example: Telephone network
Dedicated path with dedicated resources

## Slide 13: Circuit switching
1. Setup: Control message sets up a path from origin to destination
2. Accept signal informs source that data transmission may proceed
3. Data transmission begins
4. Entire path remains allocated to the transmission (whether used or not)
5. When transmission is complete, source releases the circuit
Time
A
B
C
D
Data
Call accept signal
Call request signal
Data
Transmission
Time
Propagation
Delay
Resource reservation
delay

## Slide 14: Message switching
Each message is addressed to a destination
Header: metadata that denotes how to process a message
  Typically includes a destination address
The message “hops” from node to node through a network while allocating only one link at a time
(Compare to circuit switching, where all links are reserved at the same time, regardless of use.)
Analogy: Postal service

## Slide 15: Message switching
When the entire message is received at a router, the next step and link in its journey are selected (routing)
If this selected link is busy, the message waits in a queue until the link becomes free
Store and forward switching
  Router waits for all bits of a message to arrive on incoming link before sending the first bit of the message on the outgoing link
  Alternative: cut–through switching sends bits as they arrive

## Slide 16: Message Switching
Time
A
B
C
D
Msg
Msg
Msg
Queueing
Delay
Total transfer time
Header
Store and forward
delay

## Slide 17: Packet switching
Messages are split into smaller pieces called packets
  Packets have a maximum length
  Packets are numbered and addressed
  Packets are sent through the network one at a time
Pipelining: different parts of a message concurrently transmitted over different links
  Provides higher utilization of link resources

## Slide 18: Packet switching
Time
A
B
C
D
Pkt 1
Pkt 2
Pkt 3
Pkt 1
Pkt 2
Pkt 3
Pkt 1
Pkt 2
Pkt 3
Total transfer time
Header
Queueing
Delay
Store and forward
delay

## Slide 19: The Internet uses store-and-forward packet switching.

## Slide 20: Comparisons across switching tech
Circuit switching incurs an initial delay in setting up the resources along the path
  Packet (and message) switching can start transmitting data right away
Packet switching doesn’t reserve resources for the conversation
  While circuit switching does. Needs admission control
  Packet switching makes resource reservation decisions per packet
Fewer or no guarantees  easier to build
  Telephone networks are more reliable but harder to build

## Slide 21: Comparisons across switching tech
(1) Total Delay to transfer a message
Short Bursty Messages:
Packet < Circuit
Long Continuous Messages:
Circuit < Packet
(2) Header overhead (wastage, or what % of bits on the wire is metadata?)
If typical messages are larger than typical packets:
Packet > Message

## Slide 22
host/
endpoint
router
router
link
link
link
host/
endpoint
Encoding and decoding
Switching
Many layers…

## Slide 23: Layering and Protocols

## Slide 24: Solving the problems of communication
Communication over the Internet is a complex problem
  Application (e.g., web)
  Guarantees (e.g., reliability)
  Data movement across the Internet (routing)
  Link concerns (encoding/decoding, medium access control)
We solve complex problems by breaking them into simpler ones!
Layering simplifies understanding, testing, and maintaining
It is easy to improve or replace solutions at one layer without affecting others

## Slide 25: Software/hardware organization at hosts
Link: best-effort local pkt delivery
Network: best-effort global pkt delivery
Transport: provide guarantees to apps
Application: useful user-level functions
Communication functions broken up and “stacked”
Each layer depends on the one below it.
Each layer supports the one above it.
The interfaces between layers are well-defined and standardized.

## Slide 26
Internet software and hardware
are arranged in layers.
Layering provides modularity
Each layer: well-defined function
& interfaces to layers above & below it.
Functionality is implemented in protocols.

## Slide 27: Protocols: The “rules” of networking
Protocols consist of two things
Message format
  structure of messages exchanged with an endpoint
Actions
  operations upon receiving, or not receiving, messages
Example of a Zoom conversation:
  Message format: English words and sentences
  Actions: when a word is heard, say “yes”; when nothing is heard for more than 3 seconds, say “can you hear me?”

## Slide 28: The protocols of the Internet
Standardized by the Internet Engineering Task Force (IETF)
  through documents called RFCs (“Request For Comments”)
Layering of protocols
…
FTP
HTTP
SIP
RTSP
TCP
UDP
IP
802.11
X.25
ATM
HTTPS
HTTP
FTP
TFTP
NV
TCP
UDP
IP
Ether
ATM
WiFi
…

## Slide 29
Link layer
Network
Transport
Applications
The Internet
Link layer
Network
Transport
Applications
The Internet
Packet takes on headers at each layer
Packet starts as an
app message

## Slide 30
Link layer
Network
Transport
Applications
Link layer
Network
Transport
Applications
Link layer
Network
Link layer
Network

## Slide 31
Link layer
Network
Transport
Applications
Link layer
Network
Transport
Applications
Link layer
Network
Link layer
Network
Routers have network and link layers too!

## Slide 32: Layering
Communication over the Internet is a complex problem.
Layering simplifies understanding, testing, maintaining
Easy to improve or replace protocol at one layer without affecting others

## Slide 33: This course has layers
Application
Transport
Network
Host-to-Net
…
FTP
HTTP
SIP
RTSP
TCP
UDP
IP
802.11
X.25
ATM
HTTPS

## Slide 34: Measuring the Internet
Speed, by any other name

## Slide 35: What exactly do we mean by speed?
A packet consists of many bits, including header and data
  Packet size: length of the packet (bits or bytes) incl. header and data
Bandwidth: For a single link, amount of data it can transmit per unit time (bits/second or Bytes/second or packets/second)
Total packet delay: time from the first bit@sender to the last bit@receiver

## Slide 36
Total packet delay = time for a box to travel the length of the belt
Bandwidth = the number of boxes put on the belt per minute (“rate”)
Bandwidth and delay are related but distinct
Bandwidth
Propagation delay

## Slide 37
High
Bandwidth
Low
Bandwidth
High delay
Low delay
Trans-continental optic fiber
Satellite link
(e.g., on a foggy day)
GPU—GPU link in an AI compute cluster
Bluetooth link

## Slide 38: Total Packet Delay has a few pieces
Propagation delay: Time needed to move one bit across (second)
  Imposed by the communication medium; depends on the link “length”
Transmission delay: Time from first bit@sender to last bit@sender
  Determined by link bandwidth and packet size
  Packet size / link bandwidth
Queueing delay: Time that a packet waits for transmission
  Determined by contention for the link
Total packet delay = propagation delay + queueing delay + transmission delay for a single packet

## Slide 39: Visualizing the components of delay
Increasing time
Transmission delay at the first link
Propagation delay of first link
Queueing at the router
Propagation delay of second link
Transmission delay at the second link

## Slide 40: Bandwidth and delay demo
Throughput (related to bandwidth)
  iperf –s # at the destination
  iperf –c <destination> # at the source,
  e.g., iperf –c localhost
(total) delay
  ping <destination>
  e.g., ping google.com
(you can try it!)