## Slide 1
Srinivas Narayana
Fall 2020
Resource Allocation in the
Network Core

## Slide 2
The approach that the Internet takes to allocate resources in the network core is to use a
distributed algorithm (congestion control)
running at endpoints.
However, it also places trust in endpoints.
This allows the Internet to scale to a large # of endpoints.

## Slide 3: Are endpoint algorithms alone enough?
What if an endpoint is buggy, or malicious?
We’d like the network core to do something better than best-effort

## Slide 4: Why packet scheduling?

## Slide 5: Recall: Packet queueing in routers
Outgoing
network interface
switch
fabric
packet
buffer
queueing
Buffer management / AQM
Incoming
network interface
packet
buffer
queueing
switch
fabric
Output queuing
Input queuing
Scheduling

## Slide 6: Simplified model of bottleneck link
Bottleneck queue
(max size B)
Queuing delay
Flows
Packet-switched core network
Link rate

## Slide 7: FIFO scheduling + Tail-drop buffer mgmt
1
1
2
a
b
a
2
b
Buffer size
Dropped packets

## Slide 8: FIFO scheduling + Tail-drop buffer mgmt
1
2
a
b
3
4
5
6
1
a
2
3
5
6
4
b
Buffer size
Dropped packets
Head of the line blocking (HOL)

## Slide 9: Next RTT: ACK-clocking makes it worse
7
8
b
c
9
10
11
12
7
13
8
9
11
12
10
b
Buffer size
Dropped packets
13
ACK signals sender: prior packet left the network => resource available!

## Slide 10: Network can be monopolized by bad endpoints
ACK clocking synchronizes senders to when resource is available
  Conversely, packet losses desynchronize the sender
Contending packet arrivals may not be random enough
  e.g., Blue flow can’t capture buffer space for a few round-trips
Can observe this effect when many TCP flows compete
  Some TCP flows can never get off the ground
A FIFO tail-drop queue incentivizes sources to misbehave!

## Slide 11: Packet scheduling disciplines @ routers
Significantly influences how packets are treated regardless of the endpoint’s transmissions
  Implementations of Quality of Service (QoS) within large networks
  Implications for net neutrality debates
Intellectually interesting and influential (“top 10”) question
  Classic WFQ paper has ~ 1500 citations
  Important connections to sched literature (e.g., job scheduling)
Scheduling algorithms influence many daily life decisions!

## Slide 12: Fair Resource Allocation
Allocate how? among who?
Following slides adapted heavily from Dr. Jennifer Rexford

## Slide 13: Fair and efficient use of a resource
Suppose n users share a single resource
  Like the bandwidth on a single link
  E.g., 3 users sharing a 30 Gbit/s link
What is a fair allocation of bandwidth?
  Suppose user demand is “elastic” (i.e., unlimited)
  Allocate each a 1/n share (e.g., 10 Gbit/s each)
But fairness is not enough
  Which allocation is best: [5, 5, 5] or [18, 6, 6]?
  [5, 5, 5] is fair but [18, 6, 6] is more efficient
  What about [5, 5, 5] vs. [22, 4, 4]?

## Slide 14: Fair use of a single resource
What if some users have inelastic demand?
  E.g., 3 users where 1 user only wants 6 Gbit/s
  And the total link capacity is 30 Gbit/s
Should we still do an “equal” allocation?
  E.g., [6, 6, 6]
  But that leaves 12 Gbps unused
Should we allocate in proportion to demand?
  E.g., 1 user wants 6 Gbps, and 2 each want 20 Gbit/s
  Allocate [4, 13, 13]?
Or, give the least demanding user all she wants?
  E.g., allocate [6, 12, 12]?

## Slide 15: Max-min fairness
Protect the less fortunate
  Any attempt to increase the allocation of one user necessarily decreases the allocation of another user with equal or lower allocation
Fully utilize a bottleneck resource
  If demand exceeds capacity, the link is fully used

## Slide 16: Max-min fairness for a single resource
Progressive filling algorithm (also called waterfilling)
  Grow all rates until some users stop having demand
  Continue increasing all remaining rates until link is fully utilized
If all users have elastic demands, single resource shared evenly
Link rate L
Link rate L/N
Link rate L/N
Link rate L/N
N elastic users
…

## Slide 17: Allocation over multiple resources
Maximum throughput: [30, 30, 0]
  Unfair: total throughput of 60, but user C starves
Max-min fairness: [15, 15, 15]
  Inefficient: everyone gets equal share, but throughput is just 45
Proportional fairness: [20, 20, 10]
  Allocate inversely proportional to resource use per bit
  C is penalized for using 2 busy links rather than 1
Three users A, B, and C
Two 30 Gbit/s links
A
B
C
TCP Reno implements proportional fairness.
Kelly, Maulloo, Tan’98

## Slide 18: Allocate fairly among who?
Traffic sources?
  Web servers, video servers, etc. need more than their fair share
Traffic destinations?
  Vulnerable to malicious sources denying service to receivers
Application-level flows? (i.e., src + dst + transport ports)
  Malicious app can start up many such flows
Administrative entities? (e.g., Rutgers NetID, ISP, …)
  How should a router identify packets belonging to an entity?
Abstract entity:
flow