## Slide 1: CS 352 Routing for the Internet
CS 352, Lecture 19.1
http://www.cs.rutgers.edu/~sn624/352
Srinivas Narayana

## Slide 2: Making routing scalable
scale: with billions of destinations:
can’t store all destinations in routing tables!
routing table exchange would swamp links!
administrative autonomy
Internet = network of networks
each network admin may want to control routing in its own network
our routing study thus far - idealized
all routers identical
network “flat”
… not true in practice

## Slide 3: Internet’s approach to scalable routing
aggregate routers into regions known as “autonomous systems” (AS) (a.k.a. “domains”)
inter-AS routing
routing among AS’es
gateways perform inter-domain routing as well as intra-domain routing
All networks run the same inter-domain routing protocol
intra-AS routing
routing among hosts, routers in same AS (“network”)
all routers in the same AS must run same intra-domain protocol
routers in different AS can run different intra-domain routing protocols
gateway router: at “edge” of its own AS, has link(s) to router(s) in other AS’es

## Slide 4: Making routing scalable
Key principle: Hierarchy
… by separation into ASes
… within ASes, using intra-domain areas.
Hierarchy enables autonomy of separate regions.
Compare: federal -> state -> district -> …

## Slide 5
Routing protocols
Link state protocols
e.g., OSPF, IS-IS
Distance vector protocols
e.g., RIP, IGRP
Intra-AS protocols
same protocol within an AS
different algorithms across ASes
(semi-)global view of the network
Also called interior gateway protocols (IGP)
Path vector protocols
e.g., BGP
Inter-AS protocols
common across Ases
each AS knows little about the others