## Slide 1
Lecture 10, Computer Networks (198:552)
Network Verification

## Slide 2: Traditional IP network
Switching
fabric
Processor
Net interface
Net interface
Net interface
Net interface
Data plane
Control plane
BGP
OSPF
Management plane
Management plane
  Configure routers
  Ex: OSPF link weights
  Ex: BGP local prefs
Control plane
  Track the topology
  Exchange messages
  Compute fwding rules
Data plane
  Fwd packets using computed fwding rules

## Slide 3: Software-Defined Network (SDN)
Data plane
Data plane
Data plane
Centralized control plane
Data plane

## Slide 4: Why verify networks?
High-profile outages
  Caused by human errors more than 50% of the time 
“Complex systems break in complex ways”
  Interactions between protocols
  Interactions between different administrative domains
Networks change all the time
Security is increasingly important
Intellectually interesting
  Computer-Aided Design (CAD) for networks [George Varghese]
BGP
OSPF

## Slide 5: Verification: A problem statement

## Slide 6: for all M, does N satisfy P?
Sequence of messages:
Packets,
Routing protocol
Link failures
Network representation:
Data plane
Control plane
Property of interest:
Loop freedom
Blackholes
Reachability
Equivalence
Decision Procedure: An algorithm that answers yes/no
Can ask the question under a network change model:
static, incremental, or dynamic

## Slide 7: Example: Verifying firewall rules
Assume packets just have 2 bits; there are only 2 ports
Firewall config: 10 -> fwd(2); *1 -> fwd(1). All others dropped
Boolean representation of the network:
  N: (d1 & ~d0) | ((d1 | ~d1) & d0)
Property: only the packets from 00 are dropped
  P: (~d1 & ~d0)
Messages (M): all combinations of boolean variables d0, d1
Verification question: for all d0, d1, is formula N | P valid? i.e.,
  Is ((d1 & ~d0) | ((d1 | ~d1) & d0)) | (~d1 & ~d0) a tautology?
Decision procedure: SAT solver!

## Slide 8: Typical considerations for verification
Size of network representations
  O(# rules)? # packets? Some product of these things?
Speed of decision procedure, e.g., SAT solving
  Typically NP-hard or worse in the worst case
  Verification: leveraging average-case complexity
Coverage of possible network events
  Does property hold under firewall rule changes? New protocol messages? Link failures?
Strength of properties and counter-examples
  Does P hold for all packets? Are we looking for one counterexample, or the whole set of violating packets?

## Slide 9: Verification, testing, synthesis, eq checks
Verification: for all M, does N satisfy P?
Testing: For the given M, does N satisfy P?
Synthesis: Given P, can you produce an N that satisfies it
  For all M?
  For a given set of M?
Let N1 be another network representation
Equivalence checking: For all M, do N and N1 behave in the same way?, i.e.,
  Either both satisfy P or both violate it

## Slide 10: Properties to verify
Reachability, isolation, loop freedom
Equivalence between data plane rules
  Replicated configurations (for availability or performance)
  Reduce to simpler configurations
Waypoint properties
  e.g., does traffic always go through a monitoring node?
  Ordering constraints on processing: e.g., DPI must follow ACLs
Temporal properties, e.g.:
  After first message from a source, don’t broadcast traffic destined to it
Performance properties: e.g., arrival distributions & congestion

## Slide 11: 10,000 ft overview of the literature
Data plane verification
  Static: header space analysis
  Incremental: Veriflow
  Dynamic: NICE
Control and data plane verification
  Static: p4v
  Incremental: Batfish
  Dynamic: Minesweeper

## Slide 12: Scaling challenges
Too many messages and events
  Packet headers
  Link failures
  Protocol messages
Orderings between events matters!
Too many network rules
Too large a network

## Slide 13: Discussion of Header Space Analysis
Compact boolean representation + composition operations
Why is an inverse always well-defined?
Linear fragmentation assumption
Representation as difference of two HSAs
Generic loops and infinite loops
Per-port loop detection vs. stopping at any port: pros & cons?
What else could you run on the propagation tree?

## Slide 14: Discussion of VeriFlow
Trie-like representation of packet headers
Forwarding equivalence classes: help scale!
Implicit assumption that many FECs aren’t affected at once
What computations could you do over the forwarding graph?
How do you check for blackholes using VeriFlow?
Could you extend the trie for performance verification?
Are there bad wildcard rules that make the “affected FEC” set grow really large with a rule insertion (e.g., exponentially)?
What changes are required for packet modification?