## Slide 1: Quality of Service
Lecture 25 http://www.cs.rutgers.edu/~sn624/352-S22
Srinivas Narayana

## Slide 2
The network layer is all about reachability.
Net layer
AT&T
Comcast
Verizon
Internet is federated! Incomplete visibility
Border Gateway Protocol (BGP)
“I am p’ton”
Dst: 91.1/16
AS path: p’ton
“I can reach p’ton”
Dst: 91.1/16
AS path: comcast, p’ton
Dst: 91.1/16
AS path:
comcast, p’ton
BGP announcements
Messages
Algorithms
Import policy
Verizon: “OK to use route from Comcast”
Best route selection
Export policy
Rutgers: “use AT&T to get to Princeton”
Verizon: Don’t announce Princeton route to AT&T
Distance
Vector
Routing protocols
Link
state
Path
Vector

## Slide 3: Computing the forwarding table
1b
1d
1c
1a
2b
2d
2c
2a
3b
3d
3c
3a
AS2
AS3
AS1
X
Suppose a router in AS1 wants to forward a packet destined to external prefix X.
How is the forwarding table entry for X at 1d computed?
How is the forwarding table entry for X at 1c computed?

## Slide 4: eBGP and iBGP announcements
Based on AS2 import policy, AS2 router 2c imports and selects path AS3,X, propagates (via iBGP) to all AS2 routers
1b
1d
1c
1a
2b
2d
2c
2a
3b
3d
3c
3a
AS2
AS3
AS1
X
AS3,X
AS2,AS3,X
AS2 router 2c receives path announcement AS3,X (via eBGP) from AS3 router 3a
Based on AS2 export policy, AS2 router 2a announces (via eBGP) path AS2, AS3, X to AS1 router 1c

## Slide 5: eBGP and iBGP announcements
AS1 gateway router 1c learns path AS2,AS3,X from 2a (next hop 2a)
1b
1d
1c
1a
2b
2d
2c
2a
3b
3d
3c
3a
AS2
AS3
AS1
X
AS3,X
AS2,AS3,X
A given router may learn about multiple paths to destination:
AS3,X
AS1 gateway router 1c learns path AS3,X from 3a (next hop 3a)
Through BGP route selection process, AS1 gateway router 1c chooses path AS3,X, and announces path within AS1 via iBGP (next hop 1c)

## Slide 6: Setting forwarding table entries
1b
1d
1c
1a
2b
2d
2c
2a
3b
3d
3c
3a
AS2
AS3
AS1
X
AS3,X
AS2,AS3,X
AS3,X
recall: 1a, 1b, 1d learn about dest X via iBGP from next-hop 1c: “path to X goes through 1c”
1d: intra-domain routing: to get to 1c, forward over outgoing local interface 1
NH
interface
…
…
1c
…
…
1
dest
Next-Hop
…
…
X
…
…
1c
1
2
3
IP Dst
Out port
X
1
Forwarding table

## Slide 7: Setting forwarding table entries
1b
1d
1c
1a
2b
2d
2c
2a
3b
3d
3c
3a
AS2
AS3
AS1
X
AS3,X
AS2,AS3,X
AS3,X
recall: 1c learns about dest X via eBGP from next-hop 3a: “path to X goes through 3a”
1c: to get to link-local neighbor 3a, forward out interface 2
NH
interface
…
…
3a
…
…
2
dest
Next-Hop
…
…
X
…
…
3a
1
2
3
IP Dst
Out port
X
2
Forwarding table

## Slide 8: Summary: Inter-domain routing
Federation and scale introduce new requirements for routing on the Internet
BGP is the protocol that handles Internet routing
Path vector: exchange paths to a destination with attributes
Policy-based import of routes, route selection, and export

## Slide 9: BGP’s impact: October ’21 FB++ outage
https://engineering.fb.com/2021/10/05/networking-traffic/outage-details/
By Doug Madory - https://www.kentik.com/blog/facebooks-historic-outage-explained/, CC BY 4.0, https://commons.wikimedia.org/w/index.php?curid=110816752
FB network
FB’s DNS servers
Rest of the Internet
BGP route withdrawal:
“I can’t reach FB anymore”
BGP route withdrawal: don’t use me to get to FB
No remote access (no more reachability due to BGP withdrawal of DC and DNS servers)
Restricted physical access (prox can’t verify, can’t access prox server)

## Slide 10: Beyond best effort networking

## Slide 11: Network support for applications
A best effort Internet architecture does not offer any guarantees on delay, bandwidth, and loss
  Network may drop, reorder, corrupt packets
  Network may treat traffic randomly regardless of their “importance”
However, many apps require special treatment & guarantees
  E.g., voice over IP (phone calls) require strict delay guarantees
  E.g., HD video requires a reasonable minimum bandwidth
  E.g., remote surgery with 3D-vision requires strict sync & latency
Q: How to provide quality of service (QoS) for apps?

## Slide 12: Why best effort isn’t enough: Contention
Resource contention occurs in the core of the network
Congestion control will react, but may be too little & too late:
  Congestion control can’t prevent packet drops “now”
  Congestion control won’t prevent high-sending-rate flows from inflicting large delays or recurring drops
Conf call: Requires low latency
BitTorrent: Requires high throughput
High delay
Packet drops
FIFO queue

## Slide 13
Can networks help improve the quality of service for applications?
Yes, but networks must become
better than best-effort.

## Slide 14: Approach 1: Provision more capacity
If you’re an ISP (e.g., AT&T), you might deploy enough capacity so that contention doesn’t occur any more
  Low complexity: can use current “best effort” network
However, this approach incurs high costs (e.g., bandwidth)
A key challenge: estimating how much bandwidth is enough
  Need to estimate demand over time
  Network operators can do this quite well usually
  But there are exceptional circumstances: pandemics, Superbowl, etc.

## Slide 15: Approach 2: Classes of service
Have the network treat different traffic differently
  Also called traffic differentiation
Analogy: lines at an airport (e.g., first class vs. economy)
Partition traffic into classes and offer service guarantees per class and across classes
  Classes may be indicated using the IP type of service header bits
  Classes may be inferred from IP & transport headers (e.g., src/dst/ports)
Packet classification: assigning packets to classes
  (Not in scope: we won’t discuss packet classification)

## Slide 16: Kinds of Service Guarantees

## Slide 17: (1) Strict prioritization
R1
R2
H1
H2
H3
H4
1.5 Mbps link
Suppose a 1Mbps interactive flow and an HTTP connection share a 1.5 Mbps link.
A network operator (e.g., Rutgers admin) might choose to prioritize the interactive app strictly over the HTTP flow.
HTTP
Conf call
Transmitted immediately regardless of HTTP packets

## Slide 18: (2) Rate limiting
What if a flow doesn’t respect its allocation?
  Example: Say, conf call flow goes beyond 1 Mbit/s
  Don’t want to starve HTTP flow!
An operator might want to limit a flow to a certain max rate
Isolation: HTTP should not be impacted by the conf call
R1
R2
H1
H2
H3
H4
1.5 Mbps link
HTTP
Rate limited to 1 Mbit/s
Conf call

## Slide 19: (3) Weighted fair sharing
An operator might want to partition the link’s rate C into separate allocations for each class
  Partitions may have weights w (example: 2, 1)
Usually, class i gets the illusion of traversing a logical link of rate
  wi * C / ∑j wj
R1
R2
H1
H2
H3
H4
Allocated 1/3rd of the link
HTTP
Allocated 2/3rd of the link
Conf call
w=2
w=1

## Slide 20: (3) Weighted fair sharing
Customary to think of different classes as belonging to different queues
For this reason, weighted fair sharing is also called weighted fair queueing (WFQ)
Each queue is first-in-first-out (FIFO)
The link multiplexes among these queues
Intuitively, packets of one queue should not influence the behavior of other queues
Hence, fair queueing is also a form of isolation across traffic classes
Link
Class 1
Class 2
Class 3

## Slide 21: (3) Weighted fair sharing
But what if one class doesn’t use its share?
  Can other classes use the spare capacity?
Yes! WFQ is work-conserving: a router implementing WFQ will allow other classes to use the unused capacity
Work conservation makes WFQ different from rate limits applied separately to each class
  Class i’s usage can exceed wi * C / ∑j wj
  (only if spare capacity is available, of course.)
Link
Class 1
Class 2
Class 3

## Slide 22: Q: Where are guarantees enforced?
We’ve seen three kinds of service guarantees: prioritization, rate limiting, and fair sharing
Common goal: allocate the bottleneck link capacity across packets from traffic classes
This allocation occurs in the packet scheduler in the bottleneck router
  Recall: scheduling is the task of choosing the packet (among buffered packets) which is transmitted over the output link
A router is said to implement packet scheduling policies

## Slide 23: Why care about service guarantees?
Influences how packets are treated at contentious resources in the core of the network
  Regardless of the endpoint transport
Service guarantees: prioritization, rate limiting, fair sharing
Implementations of scheduling (QoS) within large networks have implications for debates on network neutrality
Scheduling is a fundamental problem in computer networks
Next lecture: a deeper look at mechanisms for one kind of service guarantee

## Slide 24: Rate Limiting

## Slide 25: Measures of transmission rate
Long-term/average rate: data rate transmitted per unit time, over a long period
  Crucial question: what is the time interval over which rate is measured?
Average and instantaneous behaviors can be very different
Time
Rate
Time
Rate
Same average rate
Measurement duration
Measurement duration

## Slide 26: Measures of transmission rate
Peak rate: largest instantaneous rate that is transmitted
  Measurement duration is typically very small
Burst size: maximum amount of data sent consecutively without any intervening idle periods
Time
Rate
peak rate
Measurement duration

## Slide 27: Rate enforcement
There are two kinds of rate enforcement policies:
  shaping and policing
Two specific mechanisms to implement those:
  leaky buckets and token buckets

## Slide 28: Shaping
Enforces rate by queueing excess packets in a buffer
  Drop only if buffer is full
Requires memory to buffer packets
Can inflate round-trip time (queueing in shaping buffer)
Enforces rate by dropping excess packets immediately
  Can result in high loss rates
Does not require a memory buffer
No additional inflation in round-trip times
vs. Policing

## Slide 29: Leaky bucket shaper

## Slide 30: Intuition: release packets at steady rate
Bucket
leaking water
at a steady
rate
Packets leaving at steady rate
Packets from source
Leaky
Bucket
Shaper
Shaping buffer
Timed release mechanism for packets

## Slide 31: Leaky Bucket Shaper
Packets may enter in a bursty manner
However, once they pass through the leaky bucket, they are evenly spaced
The shaping buffer holds packets up to a certain point
  If the buffer is full, packets are dropped
Setting the rate is a policy concern
  Assume an admin provides us the rate
Shapers may be used in the core of a network to limit bandwidth use, or at the edge to pace packets entering the network in the first place

## Slide 32: Leaky Bucket Shaper
For a leaky bucket shaper, assume average rate == peak rate
However, many Internet transfers just have a few packets
  For example, web requests and responses
  Enforcing rate limit for those can significantly delay completion
We often wish to have peak rate higher than avg rate
  Especially at the beginning of a connection
  If so, use a token bucket: burst-tolerant version of a leaky bucket

## Slide 33: Token bucket shaper

## Slide 34: Token bucket shaper
Remove token
Limits traffic class to a specified average rate r and burst size B
Tokens are filled in at rate r
The token bucket can hold a maximum of B tokens. Further tokens dropped
  Note: distinct from shaping buffer size
Suppose a packet is at the head of the shaping buffer
If a token exists in the bucket, remove token, and transmit the packet
  If not, wait.
Transmit
Fill at rate r
Shaping buffer
Bucket size B
Packets

## Slide 35: Token bucket shaper
Remove token
In time t, the maximum number of packets that depart the shaper is (r * t) + B
A full bucket of tokens would allow small flows to go through unaffected
  A maximum burst of B packets
Longer flows have average rate r
  Bucket emptied initially, the rest of the flow must respect the token fill rate
  As t  ∞, the average rate approaches r
  That is, (1/t) * (r*t + B)  r
Transmit
Fill at rate r
Shaping buffer
Bucket size B
Packets

## Slide 36: Token bucket policers

## Slide 37: Token bucket policer
Remove token
A token bucket policer is just a token bucket shaper without the shaping buffer
No place for packets to wait if there are no tokens
If token exists, packet transmitted.
If not, packet dropped
Simple and efficient to implement.
The internet has tons of token bucket policers
Transmit
Fill at rate r
Shaping buffer
Bucket size B
Packets

## Slide 38: Google study from 2016
Flach et al., An Internet-Wide Analysis of Traffic Policing, SIGCOMM 2016
Small but non-trivial fraction of policed links
Significant impact on packet loss rate

## Slide 39: Impact on TCP
Slow start period: burst allowed with a full bucket of tokens
Policers drop multiple packets in a burst: causing RTOs and retransmissions after emptying of token bucket

## Slide 40: Effect on actual apps: YouTube
Video rebuffer rate: rebuffer time / overall watch time

## Slide 41: Summary of rate limiting
Rate limiting is a useful mechanism to isolate traffic classes from each other
Two strategies: policing and shaping
  Leaky bucket and token bucket
The Internet has a lot of token bucket policers, causing real impact on TCP connections and app performance
Understand how ISPs treat consumer Internet traffic

## Slide 42: Synthesis of protocols

## Slide 43: Synthesis: a day in the life of a web request
Our journey down protocol stack complete!
  application, transport, network, link
putting-it-all-together: synthesis!
  Goal: identify, review, understand protocols (at all layers) involved in seemingly simple scenario: requesting www page
  Scenario: student attaches laptop to campus network, requests/receives www.google.com

## Slide 44: A day in the life: scenario
Comcast network
68.80.0.0/13
Google’s network
64.233.160.0/19
64.233.169.105
web server
DNS server
school network
68.80.2.0/24
web page
browser

## Slide 45: A day in the life… connecting to the Internet
router
(runs DHCP)
connecting laptop needs to get its own IP address, addr of first-hop router, addr of DNS server: use DHCP
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
DHCP
DHCP
DHCP
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
DHCP
DHCP
DHCP
DHCP request encapsulated in UDP, encapsulated in IP, encapsulated in link layer Ethernet
Packet broadcast (dest: FFFFFFFFFFFF) on the local network, received at a router running DHCP server
Ethernet decapsulated to IP decapsulated to UDP decapsulated to DHCP

## Slide 46: A day in the life… connecting to the Internet
router
(runs DHCP)
DHCP server formulates DHCP ACK containing client’s IP address, IP address of first-hop router for client, name & IP address of DNS server
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
DHCP
DHCP
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
DHCP
DHCP
DHCP
Client now has IP address, knows name & addr of DNS
server, IP address of its first-hop router
DHCP client receives DHCP ACK reply

## Slide 47: A day in the life… ARP (before DNS, before HTTP)
router
(runs DHCP)
before sending HTTP request, need IP address of www.google.com: DNS
DNS
UDP
IP
Eth
Phy
DNS
DNS
DNS
DNS query created, encapsulated in UDP, encapsulated in IP, encapsulated in Eth. To send frame to router, need MAC address of router interface: ARP
ARP query broadcast, received by router, which replies with ARP reply giving MAC address of router interface
client now knows MAC address of gateway router, so can now send packet containing DNS query
ARP query
Eth
Phy
ARP
ARP
ARP reply

## Slide 48: A day in the life… using DNS
router
(runs DHCP)
DNS
UDP
IP
Eth
Phy
DNS
DNS
DNS
DNS
DNS
IP datagram containing DNS query from client to gateway router
IP datagram forwarded from campus network into Comcast network, routed (tables created by EIGRP, OSPF, and/or BGP routing protocols) to DNS server
decapsulated to DNS server
DNS server replies to client with IP address of www.google.com
Comcast network
68.80.0.0/13
DNS server
DNS
UDP
IP
Eth
Phy
DNS
DNS
DNS
DNS

## Slide 49: A day in the life…TCP connection carrying HTTP
router
(runs DHCP)
HTTP
TCP
IP
Eth
Phy
HTTP
to send HTTP request, client first opens TCP socket to web server
TCP packet routed using inter-domain routing (BGP) and intra-domain routing (OSPF, EIGRP) to web server
64.233.169.105
web server
SYN
SYN
SYN
SYN
TCP
IP
Eth
Phy
SYN
SYN
SYN
SYNACK
SYNACK
SYNACK
SYNACK
SYNACK
SYNACK
SYNACK

## Slide 50: A day in the life… HTTP request/reply
router
(runs DHCP)
HTTP
TCP
IP
Eth
Phy
HTTP
HTTP request sent into TCP socket
IP datagram containing HTTP request routed to www.google.com
IP datagram containing HTTP reply routed back to client
64.233.169.105
web server
HTTP
TCP
IP
Eth
Phy
web server responds with HTTP reply (containing web page)
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
web page finally (!!!) displayed