## Slide 1: Sliding Windows
Lecture 12 http://www.cs.rutgers.edu/~sn624/352-S22
Srinivas Narayana

## Slide 2: Quick recap of concepts
Tp layer
Error detection
UDP
Connectionless
TCP
Connection-oriented
Sender
f(.)
Receiver
f(.)
Checksum
Checksum
Compare*
Detecting errors is insufficient.
Need to correct errors.
Also, data may simply be lost.
(checksum is also lost)
Need better mechanisms for reliable data delivery!
TCP uses 3 simple ideas
Note: actual impl more nuanced

## Slide 3: Review:
Sender sends a single packet, then waits for an ACK to know the packet was successfully received. Then the sender transmits the next packet.
If ACK is not received until a timeout (RTO), sender retransmits the packet
Disambiguate duplicate vs. fresh packets using sequence numbers that change on adjacent packets
Sender
Receiver
RTT
RTO
SEQ 0
SEQ 1
Retransmit
Stop-and-Wait Reliability
ACK delayed
ACK dropped
Pkt dropped
Pkt corrupted

## Slide 4
Let’s talk a bit more about sequence numbers…
In principle, these three ideas are sufficient to implement reliable data delivery!

## Slide 5: Sequence #s: Scenario 1
Sender
Receiver
ACK
RTO
A bad scenario: Suppose an ACK was delayed beyond the RTO; sender ended up retransmitting the packet.
At the receiver: sequence number helps disambiguate a fresh transmission from a retransmission
  Sequence number same as earlier: retransmission
  Fresh sequence number: fresh data
0
0

## Slide 6: Sequence #s: Scenario 2
Sender
Receiver
RTO
A good scenario: packet successfully received and ACK returned within RTO
Sequence numbers of successively transmitted packets are different
Receiver knows these are not duplicate, because sequence numbers are different
SEQ 0
SEQ 1
ACK
RTO

## Slide 7: Q: How to number pkt sequences?
Sender
Receiver
ACK
RTO
One possibility: keep incrementing the seq #: 2, 3, …
Alternative: since seq # 0 was successfully ACK’ed earlier, it is OK to reuse seq #0 for next transmission.
  No chance of confusion with a previous packet with the same sequence number
Principle: Seq #s can be reused if older packets with those seq #s have surely been delivered
SEQ 0
SEQ 1
ACK
???
RTO

## Slide 8: Making reliable data transfer efficient

## Slide 9: Efficiency problem with stop-and-wait
Sender sends one packet, waits for an ACK (or RTO) before transmitting next one
  Unfortunately, too slow 
Suppose RTO = RTT = 100 milliseconds
Packet size (bytes in 1 packet) = 12,000 bits
Bandwidth of links from sender to receiver = 12 Mbit/s (1 M = 106)
Rate of data transfer = data size / time
Sender
Receiver
RTT
120 Kilobit/s == 1% of bw!
RTO

## Slide 10
Sending one packet per RTT makes the data transfer rate limited by the time between the endpoints, rather than the bandwidth.
Ensure you got the (one) box safely; make N trips
Ensure you get N boxes safely; make just 1 trip!
Keep many packets in flight

## Slide 11: Pipelined reliability
Data in flight: data that has been sent, but sender hasn’t yet received ACKs from the receiver
  Note: can refer to packets in flight or bytes in flight
New packets sent at the same time as older ones still in flight
New packets sent at the same time as ACKs are returning
More data moving in same time!
Improves throughput
  Rate of data transfer

## Slide 12: Pipelined reliability
Stop and wait: send 1 packet per RTT
Pipelined: send N packets per RTT
If there are N packets in flight, throughput improves by N times compared to stop-and-wait!
Sender
Receiver
RTT
RTO

## Slide 13
Pipelining makes reliable data transfer efficient.
However, pipelining also makes it more complex.
Which packets were successfully delivered?
Which packets should the sender retransmit?
Which packets are currently in flight?

## Slide 14: Sliding Windows

## Slide 15: Setup
Assume packets are labeled by sequence numbers
  Increasing from 0, …, N-1, then roll back to 0
Assume ACKs indicate the sequence numbers of data that was received
  Note: Didn’t need this for stop-and-wait
Convention: ACK#s carry the next sequence number expected
  Used in TCP.
Sender
Receiver
SEQ 0
ACK 1
SEQ 1
SEQ N-1
SEQ 0
…
ACK 2

## Slide 16: Sliding window (sender side)
Window: Sequence numbers of in-flight data
Window size: The amount of in-flight data (unACKed)
Sender’s point of view:
Window size = 3
Last seq # known to be received (ACK recv’d at sender)
Last sequence # sent
0
1
2
3
4
5
6
7
1
0
Sequence numbers restart from 0 beyond a point (finite space on header)
Transmissions later in time
0
4
2
6
7
5
1
3

## Slide 17: Sliding window (sender side)
Suppose sequence number 2 is acknowledged by the receiver
  Sender receives the ACK. Sender can transmit sequence # 5
  The window “slides” forward
0
1
2
3
4
5
6
7
1
0
Window size = 3
Last seq # known to be received (ACK recv’d at sender)
Last sequence # sent
Sender’s point of view:
0
4
2
6
7
5
1
3

## Slide 18: Sliding window (sender side)
Suppose sequence number 2 is acknowledged by the receiver
  Sender receives the ACK. Sender can transmit sequence # 5
  The window “slides” forward
0
1
2
3
4
5
6
7
1
0
Window size = 3
Last seq # known to be received (ACK recv’d at sender)
Last sequence # sent
Sender’s point of view:
0
4
2
6
7
5
1
3

## Slide 19: Sliding window (receiver side)
Window of in-flight packets can look different between sender and the receiver
Receiver only accepts sequence #s allowed by the current receiver window
0
1
2
3
4
5
6
7
1
0
Window size = 3
Last seq # received and ACK’ed by receiver
Highest sequence # accepted
Receiver’s point of view:
Receiver will not accept this seq #. Packet dropped

## Slide 20: Summary of sliding windows
Sender and receiver can keep several packets of in-flight data
  Book-keep the sequence numbers using the window
Windows slide forward as packets are ACKed (at receiver) and ACKs are received (at sender)
Common case: Improve throughput by sending and ACKing more packets in the same duration

## Slide 21
Pipelining makes reliable data transfer efficient.
However, pipelining also makes it more complex.
Which packets were successfully delivered?
Which packets should the sender retransmit?
Which packets are currently in flight?

## Slide 22: Which packets to retransmit?

## Slide 23: Pipelined Reliability
If there are N packets in flight, throughput improves by N times relative to stop-and-wait.
  Stop and wait: send 1 packet per RTT
  Pipelined: send N packets per RTT
Q1: how should sender efficiently identify which pkts were dropped and (hence) retransmitted?
Q2: how much data to keep in flight (i.e., what is N?) to reduce drops/retransmits?
Sender
Receiver
RTT
RTO

## Slide 24: How to identify dropped packets?
Suppose 4 packets sent, but 1 dropped. How does sender know which one(s) dropped?
Recall: Receiver writes sequence numbers on the ACK indicating successful reception
Key idea: Sender can infer which data was received successfully using the ACK #s!
  Hence, sender can know which data to retransmit
Q1: Should receivers ACK subsequent packets upon detecting data loss?
Q2: If so, what sequence number should receiver put on the ACK?
Sender
Receiver
RTT
RTO
Should this ACK exist ???
SEQ 1
SEQ 2
SEQ 3
SEQ 4
ACK 2
ACK 3
ACK ??

## Slide 25: Receiver strategies upon packet loss
Sender
Receiver
1
2
3
4
5
ACK pkts after a drop?
Go-back-N
Selective Repeat
What # on ACK?
Last seq# in order
Cumulative ACK
Seq# ranges received so far
Selective ACK
No
Yes
TCP’s default

## Slide 26: Sliding Window with Go Back N
When the receiver notices missing data:
It simply discards all data with greater sequence numbers
  i.e.: the receiver will send no further ACKs
The sender will eventually time out (RTO) and retransmit all the data in its sending window
Subtle: conceptually, separate timer per byte to infer RTO

## Slide 27: Go back N
Discarded by
receiver
Dropped packet
(or) Packet with
error
RTO
ACK 1
Time
Sender
Receiver
Maximum
window size = 8
Maximum
window size = 8
0
0
1
1
ACK 2
2
E
3
D
4
D
2
3
2
ACK 3
4
5
6
3
4
5
ACK 4
ACK 5
ACK 6
6
ACK 7

## Slide 28: Go back N
Go Back N can recover from erroneous or missing packets.
But it is wasteful.
If there are errors, the sender will spend time and network bandwidth retransmitting data the receiver has already seen.

## Slide 29: Selective repeat with cumulative ACK
Idea: sender should only retransmit dropped/corrupted data.
The receiver stores all the correct frames that arrive following the bad one. (Note that the receiver requires memory to hold data for each sequence number in the receiver window.)
When the receiver notices a skipped sequence number, it keeps acknowledging the first in-order sequence number it wants to receive. This is termed cumulative ACK.
When the sender times out waiting for an acknowledgement, it just retransmits the first unacknowledged data, not all its successors.
Recall that RTO applies independently to each sequence #

## Slide 30: Selective repeat with cumulative ACK
Buffered by
receiver in
its memory
Packet with
error (or)
dropped packet
RTO
ACK 1
Time
Sender
Receiver
Maximum
window size = 8
Maximum
window size = 8
0
0
1
1
ACK 2
2
E
3
4
2
5
2
ACK 5
6
5
ACK 6
6
ACK 7
3
4
ACK 2
ACK 2

## Slide 31: Selective repeat with selective ACK
Buffered by
receiver in
its memory
Frame with
error
RTO
ACK 1
Time
Sender
Receiver
Maximum
window size = 8
Maximum
window size = 8
0
0
1
1
ACK 2
2
E
3
4
2
5
2
ACK 5
6
5
ACK 6
6
ACK 7
3
4
ACK 2
SACK 0--1, 3
ACK 2
SACK 0,--1, 3--4

## Slide 32: TCP: Cumulative & Selective ACKs
Sender retransmits the seq #s it thinks aren’t received successfully yet
Pros & cons: selective vs. cumulative ACKs
  Precision of info available to sender
  Redundancy of retransmissions
  Packet header space
  Complexity (and bugs) in transport software
On modern Linux, TCP uses selective ACKs by default
Sender
Receiver
1
2
3
4
2
3
4
5
5