## Slide 1: Network Layer: Protocols (Part 2)
Lecture 21 http://www.cs.rutgers.edu/~sn624/352-S22
Srinivas Narayana

## Slide 2: Quick recap of concepts
Net layer
high-speed
switching
fabric
route
processor
router input ports
router output ports
Blocking
Nonblocking
In nonblocking fabrics, queues form only due to contention for output port.
Output port contention is fundamental; unavoidable.
Scheduling and buffer management crucial.
IPv4 datagram
Forwarding Table
Longest prefix matching on dst IP address

## Slide 3: Mapping routes
ip route (Linux)
  Try ip route get ____
route (Mac OS X)

## Slide 4
The network layer is all about reachability.
Every protocol we’ll see solves a sub-problem.
How does an endpoint get an address?
DHCP
How does an endpoint talk to another within the same network?
ARP
How does an endpoint talk to another outside its network?
Routing protocols
OSPF, RIP, BGP
Gateways
NAT & IPv6
Debugging?
ICMP

## Slide 5: Dynamic Host Configuration Protocol (DHCP)

## Slide 6: How does an endpoint get its IP addr?
One possibility: hard-code the IP address on the endpoint
  e.g., a system admin writing addresses in a file
  Linux: /etc/network/interfaces
  Mac OS X (10.14.6): system preferences > Network > name of interface > advanced > TCP/IP > “Manually”
Another possibility: dynamically receive an address “from the network”
  DHCP: Dynamic Host Configuration Protocol
  Provide plug-and-play functionality for endpoints (e.g., phones, laptops)

## Slide 7: Many similar bootstrapping problems
How does a host get its IP address?
How does a host know its local DNS server?
How does a host know its netmask?
  i.e., so that it can know which other hosts are in the same network
  Note: the details how A and B talk to each other changes significantly when A and B are in the same network vs. different network
How does a host know how to reach other networks?
  i.e., which router is at the “border” of the current network?
  This router is also called the gateway router: crucial for an endpoint to communicate with another endpoint external to the network

## Slide 8: How DHCP works
An endpoint that just joined a network knows nothing about it
  Endpoint doesn’t even have an IP address for its point of attachment
We solved a similar bootstrapping problem before:
  Domain Name Service (DNS) to retrieve addresses
Often, it makes little sense to have the endpoint contact a “known” server to receive an IP address
  E.g., connecting to a brand-new network you’ve never been in
The only idea that really works is to ask everyone
  Broadcast a “query”

## Slide 9: How DHCP works
DHCP allows a host to dynamically obtain its IP address from a server on a network when it joins the network
DHCP can allow a host to be mobile across different networks, obtaining IP addresses as needed
DHCP uses leases on addresses
  Host must renew lease periodically
  Allows network to reuse an IP with an expired lease, reclaiming addresses from inactive hosts
223.1.1.0/24
223.1.2.0/24
223.1.3.0/24
223.1.1.1
223.1.1.3
223.1.1.4
223.1.2.9
223.1.3.2
223.1.3.1
223.1.1.2
223.1.3.27
223.1.2.2
223.1.2.1
DHCP
server
DHCP
Client program on the endpoint broadcasts message requesting an IP address.

## Slide 10: DHCP client-server scenario
DHCP server:
223.1.2.5
Arriving
client
DHCP discover
src : 0.0.0.0, 68
dest.: 255.255.255.255,67
yiaddr: 0.0.0.0
transaction ID: 654
DHCP offer
src: 223.1.2.5, 67
dest: 255.255.255.255, 68
yiaddrr: 223.1.2.4
transaction ID: 654
lifetime: 3600 secs
DHCP request
src: 0.0.0.0, 68
dest:: 255.255.255.255, 67
yiaddrr: 223.1.2.4
transaction ID: 655
lifetime: 3600 secs
DHCP ACK
src: 223.1.2.5, 67
dest: 255.255.255.255, 68
yiaddrr: 223.1.2.4
transaction ID: 655
lifetime: 3600 secs
Broadcast: is there a DHCP server out there?
Broadcast: I’m a DHCP server! Here’s an IP address you can use
Broadcast: OK. I’ll take that IP address!
Broadcast: OK. You’ve got that IP address!
DHCP runs on UDP ports 67 (server) and 68 (client)
Client’s initial IP address is set to 0.0.0.0
Yiaddr stands for “your IP address” – an address value the server sends to the client for consideration
Note that the IP allocation has an associated lifetime (lease period)
223.1.2.4

## Slide 11: Multiple DHCP servers can coexist
Server 1
Server 2
Client
DHCPDISCOVER
DHCPDISCOVER
DHCPOFFER
DHCPOFFER
DHCPREQUEST
DHCPREQUEST
DHCPACK
Collects replies
Selects server 2

## Slide 12: DHCP returns more than an IP address
Name and IP address of the local DNS server
Netmask of the IP network the host is on
  Useful to know whether another endpoint is inside or outside the current IP network
Address of the gateway router to enable the endpoint to reach other IP networks

## Slide 13: Your home router runs DHCP
Likely, your home devices (laptops, tablets, phones) are all using DHCP-assigned IP addresses
The DHCP server is running on the control processor of your home’s access router (e.g., WiFi router)
You can access the DHCP client program on Linux using the command dhclient

## Slide 14: Summary of DHCP
Want endpoints to have plug and play functionality
  Avoid tedious manual configuration of IP addresses and other information
DHCP: a general bootstrapping mechanism for critical information required for network layer functionality
Hosts can be simple: receive information from DHCP servers by broadcasting over the network

## Slide 15: Internet Control Message Protocol (ICMP)

## Slide 16: Internet Control Message Protocol
A protocol for troubleshooting and diagnostics
Works over IP: unreliable delivery of packets
Some functions of ICMP:
  Determine reachability and network errors
  Specify that packets have been in the network for too long

## Slide 17: ICMP message
IP header
ICMP header
Message type, Code, Checksum,
ICMP data
https://en.wikipedia.org/wiki/Internet_Control_Message_Protocol#Control_messages

## Slide 18: Specific uses of ICMP
Echo request reply
  Check remotely if an endpoint is alive and connected
  Without running an app remotely or controlling that endpoint
An unreachable destination
  Invalid address and/or port
Knowing if packet’s IP time-to-live expired
  Example, due to routing loops
Look at two tools built using ICMP: ping and traceroute

## Slide 19: Ping
Uses ICMP echo request (type=8, code=0) and reply (type=0, code=0)
Source sends ICMP echo request message to dst address
Destination network stack replies with an ICMP echo reply message
Source can calculate round trip time (RTT) of packets
If no echo reply comes back, then the destination is unreachable
Don’t need to have a server program running on the other side
  In general, the remote endpoint can be completely outside your control

## Slide 20: Ping
Time
Echo
request
Echo reply
A
B
R1
R2
R3
Ping time
A small demo…

## Slide 21: Traceroute
A tool that can record the router-level path taken by packets
A clever use of the IP time-to-live (TTL) field
In general, when a router receives an IP packet, it decrements the TTL field on the packet
  A failsafe mechanism to ensure packets don’t keep taking up network resources for too long
If a router receives a packet with TTL=0, it sends an ICMP time exceeded message (type=11, code=0) to the source endpoint

## Slide 22: Traceroute
Traceroute sends multiple packets to a destination endpoint
But it progressively increases the TTL on those packets: 1, 2, ...
Every time a time exceeded message is received, record the router’s IP address
Process repeated until the destination endpoint is reached
If the packet reaches the destination endpoint (i.e.: TTL is high enough), then the endpoint sends a port unreachable message

## Slide 23: Traceroute
Time
TTL=1, dest = B, dstport = invalid
A
B
R1
R2
R3
A small demo…
Time exceeded
Source: R1
TTL = 2
TE(R2)
Port un- reachable
Source: B
Similarly, capture IP addresses of routers at distance 3, 4, …
Have full router-level path until destination

## Slide 24: Summary of ICMP
A protocol for network diagnostics and troubleshooting
Two useful tools: ping and traceroute
Ping: test connectivity to a machine totally outside your control
  Use ICMP echo request and reply
Traceroute: determine router-level path to a remote endpoint
  A smart use of the TTL field in the IP header

## Slide 25: Address Resolution Protocol

## Slide 26: Background: Let’s peek into the link layer
Each network adapter has a hardware address or a MAC address
  E.g., the Wi-Fi adapter on your laptop has one
Assigned by the manufacturer, not expected to vary over time
  Think about it as an identifier for the device
To communicate over a single link, a sender needs the destination hardware address
Directory mechanisms like DNS and bootstrapping mechanisms like DHCP provide IP addresses
Given an IP address, how does an endpoint find the hardware address?

## Slide 27: Address Resolution Protocol (ARP)
ARP solves the following problem. Given an IP, find the machine’s hardware address
  IP  MAC resolution
All endpoints that are looked up are expected to be within the same network
Hence, address resolution can use broadcast:
  We don’t need to develop directory mechanisms like DNS
  Send (ARP) queries to everyone, asking for a MAC given an IP

## Slide 28: ARP packet format
Hardware type: link-layer protocol
  Example: Ethernet (1)
Hardware address length:
  Example: Ethernet = 6 bytes
Protocol Type: network-layer protocol
  Example: IPv4 (0x0800)
Protocol address length
  Example: IPv4 = 4 bytes
Operation:
  ARP request: 1, reply: 2
Sender’s addresses
Address to be resolved (or response)

## Slide 29: ARP operation
Ethernet Address:
05:23:f4:3d:e1:04
IP Address:
128.195.1.20
Ethernet Address:
98:22:ee:f1:90:1a
IP Address:
128.195.1.38
Ethernet Address:
12:04:2c:6e:11:9c
IP Address:
128.195.1.122
Wants to transmit
to 128.195.1.38
ARP request
Who has 128.195.1.38?
Tell 128.195.1.20
Different target IP address: ignore ARP
ARP request broadcast
Hardware type: Ethernet
Protocol type: IPv4
Hardware addr length: 6
Protocol addr length: 4
Operation: 2 (reply)
Sender hardware addr: 05:23:f4:3d:e1:04
Sender protocol addr:
128.195.1.20
Target HW addr:
98:22:ee:f1:90:1a
Target protocol addr:
128.195.1.38
Matching target IP: send reply
A
B
C

## Slide 30: Communicating outside the local net?
Suppose endpoint A wants to communicate with endpoint B that is in a different network
ARP broadcast outside the local network is too expensive
  How does one limit the scope of the broadcast? Internet-wide?
Besides, the hardware address format used by B’s network might be different from that of A’s network!
ARPs are not meaningful across network boundaries
Communicating to a network-external endpoint just means sending the packet to the gateway router
  Host can know that a destination is external using IP addr and netmask
  Host can talk to the gateway using DHCP (to get IP) and ARP (to get MAC)

## Slide 31: Summary of ARP
A useful mechanism to allow hosts inside a network to communicate:
ARP protocol helps resolve IP addresses into MAC addresses using a broadcast mechanism
Communication outside the local network requires ARP-ing for and sending packets to the gateway