## Slide 1: CS 352 Internet Protocol (IP)
CS 352, Lecture 16.1
http://www.cs.rutgers.edu/~sn624/352
Srinivas Narayana

## Slide 2: Network
Application
Transport
Network
Host-to-Net
…
FTP
HTTP
SMTP
DNS
TCP
UDP
IP
802.11
X.25
ATM
HTTPS
The main function of the network layer is to
move packets from one endpoint to another.
The network will make its best effort to deliver packets
but doesn’t guarantee anything.

## Slide 3: IP datagram format
ver
length
32 bits
data
(variable length,
typically a TCP
or UDP segment)
16-bit identifier
header
checksum
time to
live
32 bit source IP address
IP protocol version
number
header length
(bytes)
max number
remaining hops
(decremented at
each router)
for
fragmentation/
reassembly
total datagram
length (bytes)
upper layer protocol
to deliver payload to
head.
len
type of
service
“type” of data
flgs
fragment
offset
upper
layer
32 bit destination IP address
Options (if any)
E.g. timestamp,
record route
taken, specify
list of routers
to visit.
how much overhead with TCP?
20 bytes of TCP
20 bytes of IP
= 40 bytes + app layer overhead

## Slide 4: IP Fragmentation & Reassembly
network links have MTU (max.transfer size) - largest possible link-level frame.
  different link types, different MTUs
large IP datagram divided (“fragmented”) within net
  one datagram becomes several datagrams
  reassembled only at the destination, at the IP layer
  IP header bits used to identify, order related fragments
fragmentation:
in: one large datagram
out: 3 smaller datagrams
reassembly

## Slide 5: IP Fragmentation and Reassembly
ID
=x
offset
=0
fragflag
=0
length
=4000
ID
=x
offset
=0
fragflag
=1
length
=1500
ID
=x
offset
=185
fragflag
=1
length
=1500
ID
=x
offset
=370
fragflag
=0
length
=1040
One large datagram becomes
several smaller datagrams
Example
4000 byte datagram
MTU = 1500 bytes
(includes IP headers)
1480 bytes in data field
offset =
1480/8

## Slide 7: CS 352 Dynamic Host Configuration
CS 352, Lecture 16.2
http://www.cs.rutgers.edu/~sn624/352
Srinivas Narayana

## Slide 8: How does an endpoint gets its IP addr?

## Slide 9: IP addresses: how to get one?
Q: How does a host get IP address?
Hard-coded by system admin in a file
  UNIX: /etc/network/interfaces
  Windows: controlpanel -> network -> configuration -> tcp/ip -> properties
DHCP: Dynamic Host Configuration Protocol: dynamically get address from as server
  “plug-and-play”

## Slide 10: Similar bootstrapping problems
How does a host get its IP address?
How does a host know its local DNS server?
How does a host know its subnet mask?
How does a host know which router is its “gateway” to other networks?

## Slide 11: DHCP: Dynamic Host Configuration Protocol
goal: allow host to dynamically obtain its IP address from network server when it joins network
  can renew its lease on address in use
  allows reuse of addresses (only hold address while connected/“on”)
  support for mobile users who want to join network
DHCP overview:
  host broadcasts “DHCP discover” msg [optional]
  DHCP server responds with “DHCP offer” msg [optional]
  host requests IP address: “DHCP request” msg
  DHCP server sends address: “DHCP ack” msg

## Slide 12: DHCP client-server scenario
223.1.1.0/24
223.1.2.0/24
223.1.3.0/24
223.1.1.1
223.1.1.3
223.1.1.4
223.1.2.9
223.1.3.2
223.1.3.1
223.1.1.2
223.1.3.27
223.1.2.2
223.1.2.1
DHCP
server
arriving DHCP
client needs
address in this
network

## Slide 13: DHCP client-server scenario
DHCP server: 223.1.2.5
arriving
client
DHCP discover
src : 0.0.0.0, 68
dest.: 255.255.255.255,67
yiaddr: 0.0.0.0
transaction ID: 654
DHCP offer
src: 223.1.2.5, 67
dest: 255.255.255.255, 68
yiaddrr: 223.1.2.4
transaction ID: 654
lifetime: 3600 secs
DHCP request
src: 0.0.0.0, 68
dest:: 255.255.255.255, 67
yiaddrr: 223.1.2.4
transaction ID: 655
lifetime: 3600 secs
DHCP ACK
src: 223.1.2.5, 67
dest: 255.255.255.255, 68
yiaddrr: 223.1.2.4
transaction ID: 655
lifetime: 3600 secs
Broadcast: is there a DHCP server out there?
Broadcast: I’m a DHCP server! Here’s an IP address you can use
Broadcast: OK. I’ll take that IP address!
Broadcast: OK. You’ve got that IP address!

## Slide 14: DHCP Protocol
Server 1
Server 2
Client
DHCPDISCOVER
DHCPDISCOVER
DHCPOFFER
DHCPOFFER
DHCPREQUEST
DHCPREQUEST
DHCPACK
Collects replies
Selects server 2

## Slide 15: DHCP: more than IP addresses
DHCP can return more than just allocated IP address on subnet:
  address of first-hop router for client to reach other subnets
    Also called the gateway router
  name and IP address of the local DNS server
  subnet mask of the IP network the host is on
    Useful to know whether other endpoint is inside or outside the current IP network

## Slide 16: DHCP Relay Agents
DHCP relay agents allow DHCP servers to handle requests from other subnets
DHCP
Relay
Agent
Client
IP
Gateway
Router
IP
Gateway
Router
DHCP
Server

## Slide 17: DHCP: An example
connecting laptop needs its IP address, addr of first-hop router, addr of DNS server: use DHCP
router with DHCP
server built into
router
DHCP request encapsulated in UDP, encapsulated in IP, encapsulated in 802.1 Ethernet
Ethernet frame broadcast (dest: FFFFFFFFFFFF) on LAN, received at router running DHCP server
Ethernet demuxed to IP demuxed, UDP demuxed to DHCP
168.1.1.1
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
DHCP
DHCP
DHCP
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
DHCP
DHCP
DHCP

## Slide 18: DHCP: An example
router with DHCP
server built into
router
168.1.1.1
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
DHCP
DHCP
DHCP
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
DHCP
DHCP
DHCP
DHCP server formulates DHCP ACK containing client’s IP address, subnet mask, IP address of first-hop router for client, name & IP address of DNS server
encapsulation of DHCP server, frame forwarded to client, demuxing up to DHCP at client
client now knows its IP address, name and IP address of DNS server, IP address of its first-hop router

## Slide 19: Summary
IP addresses don’t have to be manually configured into hosts
DHCP allows “ignorant” hosts to receive IP addresses (and more) at start-up time
DHCP solves important bootstrapping problems in attaching new hosts to a network

## Slide 21: CS 352 Internet Control Message Protocol
CS 352, Lecture 16.3
http://www.cs.rutgers.edu/~sn624/352
Srinivas Narayana

## Slide 22: ICMP
Protocol for error detection and reporting
    tightly coupled with IP, unreliable
ICMP messages delivered in IP packets
ICMP functions:
  Announce reachability and network errors
  Announce “time exceeded” errors for IP packets
  Announce network congestion
ICMP assists network troubleshooting in general

## Slide 23: ICMP message
IP header
Source, Destination Address, TTL, ...
ICMP MSG
Message type, Code, Checksum,
Data

## Slide 24: ICMP: Internet Control Message Protocol
Type Code description
0 0 echo reply (ping)
3 0 dest. network unreachable
3 1 dest host unreachable
3 2 dest protocol unreachable
3 3 dest port unreachable
3 6 dest network unknown
3 7 dest host unknown
4 0 source quench (congestion
control - not used)
8 0 echo request (ping)
9 0 route advertisement
10 0 router discovery
11 0 TTL expired
12 0 bad IP header
Time for an activity!

## Slide 25: Specific uses of ICMP
Echo request reply
  Can be used to check if a host is alive
Destination unreachable
  Invalid address and/or port
TTL expired
  Routing loops, or too far away

## Slide 26: Ping
Uses ICMP echo request/reply
Source sends ICMP echo request message to the destination address
Destination replies with an ICMP echo reply message containing the data in the original echo request message
Source can calculate round trip time (RTT) of packets
If no echo reply comes back, then the destination is unreachable

## Slide 27: Ping (cont’d)
R1
R2
R3
A
B
Time
Echo request
Echo reply

## Slide 28: Ping example

## Slide 29: Traceroute
Traceroute records the route that packets take
A clever use of the IP TTL (time to live) field
In general, when a router receives a packet, it decrements the TTL on that packet
If TTL=0, router sends an ICMP time exceeded message back to sender
traceroute progressively increases TTL of the packets it sends out
  Every time an ICMP time exceeded message is received, record the sender’s (router’s) address
  Repeat until the destination host is reached or an error message occurs
If packet reaches the destination, the dest host usually sends an ICMP port unreachable

## Slide 30: Traceroute (cont’d)
R1
R2
R3
A
B
TTL=1, Dest = B,
port = invalid
TTL=2, Dest = B
TTL=3, Dest = B
TTL=4, Dest = B
Te (R1)
Te (R2)
Te (R3)
Pu (B)
Time
Te = Time exceeded
Pu = Port unreachable

## Slide 31: Traceroute example