## Slide 1: CS 352 Congestion Control: Intro
CS 352, Lecture 12.1
http://www.cs.rutgers.edu/~sn624/352
Srinivas Narayana

## Slide 2: How do apps get perf guarantees?
The network core provides no guarantees on packet delivery
Transport software on the endpoint oversees implementing guarantees on top of a best-effort network
Three important kinds of guarantees
  Reliability
  Ordered delivery
  Resource sharing in the network core
Transmission Control Protocol (TCP)

## Slide 3: Congestion
Amount of useful data that gets across to the receiver
Link load
~100%
Queueing delay
Link load
~100%
Packets get dropped beyond max buffer
Max amount of useful data that link can support, ~ link rate
Too many retransmissions due to packet drops!
Amount of useful (fresh) data plummets.
Congestion collapse
∞

## Slide 4: How should multiple endpoints share net?
It is difficult to know where the bottleneck link is
It is difficult to know how many other endpoints are using that link
Endpoints may join and leave at any time
Network paths may change over time, leading to different bottleneck links (with different link rates) over time

## Slide 5
The approach that the Internet takes is to use a distributed algorithm to converge to an efficient and fair outcome.

## Slide 6
The approach that the Internet takes is to use a distributed algorithm to converge to an efficient and fair outcome.
No one can centrally view or control all the endpoints and bottlenecks in the Internet.
Every endpoint must try to reach a globally good outcome by itself: i.e., in a distributed fashion.
This also puts a lot of trust in endpoints.

## Slide 7
The approach that the Internet takes is to use a distributed algorithm to converge to an efficient and fair outcome.
If there is spare capacity in the bottleneck link, the endpoints should use it.

## Slide 8
The approach that the Internet takes is to use a distributed algorithm to converge to an efficient and fair outcome.
If there are N endpoints sharing a bottleneck link, they should be able to get equitable shares of the link’s capacity.
For example: 1/N’th of the link capacity.

## Slide 9: Flow Control vs. Congestion Control
Avoid overwhelming the receiving application
Sender is managing the receiver’s socket buffer
Avoid overwhelming the bottleneck network link
Sender is managing the bottleneck link capacity and bottleneck router buffers

## Slide 10
The approach that the Internet takes is to use a distributed algorithm to converge to an efficient and fair outcome.
How to achieve this?
Approach: sense and react
Example: taking a shower
Use a feedback loop with signals and knobs

## Slide 11: Signals and Knobs in Congestion Control
Signals
  Packets being ACK’ed
  Packets being dropped (e.g. RTO fires)
  Packets being delayed (RTT)
  Rate of incoming ACKs
Knobs
  What can you change to “probe” the available bottleneck capacity?
  Suppose receiver buffer is unbounded:
  Increase window/sending rate: e.g., add x or multiply by a factor of x
  Decrease window/sending rate: e.g., subtract x or reduce by a factor of x
Implicit feedback signals measured directly at sender.
(There are also explicit signals that the network might provide.)

## Slide 12: Subsequent modules/lectures
Feedback loops used by 2 important TCPs
  TCP New Reno and TCP BBR
Strategies to react “proportionately” to network signals like loss
  Fast retransmit and fast recovery
Strategies to measure loss accurately
  How to predict the RTT of a packet successfully received (in the future)?

## Slide 14: CS 352 The Steady State
CS 352, Lecture 12.2
http://www.cs.rutgers.edu/~sn624/352
Srinivas Narayana

## Slide 15
Congestion Control: The approach that the Internet takes is to use a distributed algorithm to converge to an efficient and fair outcome.
How to achieve this?
Design a feedback loop: measure signals, apply knobs, and repeat.

## Slide 16: Efficiency with a Single Conversation

## Slide 17: What does efficiency look like?
Suppose we want to achieve an efficient outcome for one TCP conversation by observing network signals from the endpoint
Q1: How should the endpoint behave at steady state?
Q2: How should the endpoint get to steady state? (next module)
Challenge: bottleneck link is remotely located

## Slide 18: Steady state: Ideal goal
High sending rate: Use the full capacity of the bottleneck link
Low delay: Minimize the overall delay of packets to get to the receiver
  Overall delay = propagation + queueing + transmission
  Assume other components fixed
“Low delay” reduces to low queueing delay
i.e., don’t push so much data into the network that packets have to wait in queues
Key question: When to send the next packet?

## Slide 19: When to send the next packet?
Sender
Receiver
1. Send packet burst (as allowed by window)
Fast link
Bottleneck link
Inter-packet delay T
T
T
T
T
2. Receive data packet
3. Send ACK
4. Receive ACK
Data
ACKs
5. Send data packet on ACK

## Slide 20: Rationale
When the sender receives an ACK, that’s a signal that the previous packet has left the bottleneck link (and the rest of the network)
Hence, it must be safe to send another packet without congesting the bottleneck link
Such transmissions are said to follow packet conservation
ACK clocking: “Clock” of ACKs governs packet transmissions

## Slide 21: ACK clocking: analogy
How to avoid crowding a grocery store?
Strategy: Send the next waiting customer exactly when a customer exits the store
However, this strategy alone can lead to inefficient use of resources…

## Slide 22: ACK clocking alone can be inefficient
Sender
Receiver
Large delay T
T
Data
ACKs
Send data packet on ACK
T
T
T
Sender pushing data slowly

## Slide 23: ACK clocking alone can be inefficient
Sender
Receiver
T
Data
The sending rate should be high enough to keep the “pipe” full
Analogy: a grocery store with only 1 customer in entire store
If the store isn’t “full”, you’re using store space inefficiently
Large delay T
Send data packet on ACK
Sender pushing data slowly

## Slide 24: Steady State of Congestion Control
Send at the highest rate possible (to keep the pipe full)
while being ACK-clocked (to avoid congesting the pipe)
Q: How to get to steady state? (subject of next module)

## Slide 26: CS 352 Getting to Steady State
CS 352, Lecture 12.3
http://www.cs.rutgers.edu/~sn624/352
Srinivas Narayana

## Slide 27: Congestion control
Goal: at the steady state, send at the highest rate possible (to keep the pipe full) while being ACK-clocked (to avoid congesting the pipe)
So, how to get to steady state?
TCP uses a feedback loop

## Slide 28: An example of a feedback loop
You
Your bathroom shower
Signals:
Water temperature
Water pressure
Knobs:
Turn temperature up/down
Open the tap wider

## Slide 29: The congestion control feedback loop
TCP congestion control algorithm
Bottleneck link
Signals:
ACKs
Loss (RTOs), etc.
Knobs:
Sending rate
Congestion window

## Slide 30: Congestion window
The sender maintains an estimate of the amount of in-flight data needed to keep the pipe full without congesting it.
This estimate is called the congestion window (cwnd)
There is a relationship between the sending rate and the sender’s window: sender transmits a window’s worth of data over an RTT duration
  rate = window / RTT

## Slide 31: Interaction b/w flow & congestion control
Use window = min(congestion window, receiver advertised window)
Overwhelm neither the receiver nor network links & routers
0
1
2
3
4
5
6
7
1
0
Last cumulative
ACK’ed seq #
Last transmitted
seq #
Sender’s view:
Window <= Congestion window (congestion control)
Window <= Advertised window (flow control)

## Slide 32: Finding the Right Congestion Window

## Slide 33: Let’s play a game
Suppose I’m thinking of a positive integer. You need to guess the number I have in mind.
Each time you guess, I will tell you whether your number is smaller or larger than (or the same as) the one I’m thinking of
Note that my number can be very large
How would you go about guessing the number?

## Slide 34: Finding the right congestion window
TCP congestion control algorithms solve a similar problem!
There is an unknown bottleneck link rate that the sender must match
If sender sends more than the bottleneck link rate:
  packet loss, delays, etc.
If sender sends less than the bottleneck link rate:
  all packets get through; successful ACKs

## Slide 35: Quickly finding a rate: TCP slow start
Initially cwnd = 1 MSS
  MSS is “maximum segment size”
Upon receiving an ACK of each MSS, increase the cwnd by 1 MSS
Effectively, double cwnd every RTT
Initial rate is slow but ramps up exponentially fast
On loss (RTO), restart from cwnd := 1 MSS
Host A
one segment
RTT
Host B
time
two segments
four segments

## Slide 36: Behavior of slow start
1 MSS
Congestion Window
Time
Packet drops/
RTO
Slow start
Slow start
Slow start

## Slide 37: Slow start has problems
Congestion window increases too rapidly
  Example: suppose the right window size cwnd is 17
  cwnd would go from 16 to 32 and then dropping down to 1
  Result: massive packet drops
Congestion window decreases too rapidly
  Suppose the right cwnd is 31, and there is a loss when cwnd is 32
  Slow start will resume all the way back from cwnd 1
  Result: unnecessarily low throughput
Instead, perform finer adjustments of cwnd based on signals

## Slide 38: Use slow start mainly at the beginning
You might accelerate your car a lot when you start, but you want to make only small adjustments after.
  Want a smooth ride, not a jerky one!
Slow start is a good algorithm to get close to the bottleneck link rate when there is little info available about the bottleneck, e.g., starting of a connection
Once close enough to the bottleneck link rate, use a different set of strategies to perform smaller adjustments to cwnd
  Called TCP congestion avoidance

## Slide 39: TCP Congestion Avoidance

## Slide 40: Two congestion control algorithms
TCP New Reno
The most studied, classic “textbook” TCP algorithm
The primary knob is congestion window
The primary signal is packet loss (RTO)
Adjustment using additive increase
TCP BBR
Recent algorithm developed & deployed by Google
The primary knob is sending rate
The primary signal is rate of incoming ACKs
Adjustment using gain cycling and filters

## Slide 41: TCP New Reno: Additive Increase
Remember the recent past to find a good estimate of link rate
The last good cwnd without packet drop is a good indicator
  TCP New Reno calls this the slow start threshold (ssthresh)
Increase cwnd by 1 MSS every RTT after cwnd hits ssthresh
  Effect: increase window additively per RTT
Host A
RTT
Host B
time
four segments
five segments
six segments
RTT
say ssthresh=4
seven segments
…
RTT

## Slide 42: TCP New Reno: Additive increase
Start with ssthresh = 64K bytes (TCP default)
Do slow start until ssthresh
Once the threshold is passed, do additive increase
  Add one MSS to cwnd for each cwnd worth data ACK’ed
  For each MSS ACK’ed, cwnd = cwnd + (MSS * MSS) / cwnd
Upon a TCP timeout (RTO),
  Set cwnd = 1 MSS
  Set ssthresh = max(2 * MSS, 0.5 * cwnd)
  i.e., the next linear increase will start at half the current cwnd

## Slide 43: Behavior of Additive Increase
1K
Time
Packet drops/
RTO
Slow start
Slow start
Congestion Window
Say MSS = 1 KByte
Default ssthresh = 64KB = 64 MSS
54 MSS
Set ssthresh to
27 MSS
Loss occurs at cwnd = 40K
Loss occurs at cwnd = 54K
Set ssthresh to
20 MSS
Additive increase
Slow
start
Additive increase

## Slide 44: TCP BBR: finding the bottleneck link rate
Sender
Receiver
1. Send data at a specific rate
Data gets across the bottleneck at the bottleneck link rate.
2. Receive data packet
3. Send ACK
4. Measure rate of incoming ACKs
Data
ACKs
Use ACK receive rate to determine sending rate

## Slide 45: TCP BBR: finding the bottleneck link rate
Assuming that the link rate of the bottleneck
  == the rate of data getting across the bottleneck link
  == the rate of data getting to the receiver
  == the rate at which ACKs are generated by the receiver
  == the rate at which ACKs reach the sender
Measuring ACK rate provides an estimate of bottleneck link rate
BBR: Send at the maximum ACK rate measured in the recent past
  Update max with new bottleneck rate estimates, i.e., larger ACK rate
  Forget estimates last measured a long time ago
  Incorporated into a rate filter

## Slide 46: TCP BBR: Adjustments by gain cycling
BBR periodically increases its sending rate by a gain factor to see if the link rate has increased (e.g., due to a path change)
…
Time
Sending rate
Steady state operation: constant sending rate
Gain cycle
Detect higher ACK rate:
Update sending rate
Last max ACK rate was measured a while ago. Forget it & use a more recent max ACK rate
…
No change
in ACK rate
Bottleneck link rate increase
Bottleneck link rate decrease

## Slide 47: Summary: Getting to Steady State
Want to get to highest sending rate that doesn’t congest the bottleneck link
Slow start: Exponential increase towards a reasonable estimate of link rate
Congestion avoidance: milder adjustments to get close to correct link rate estimate.
TCP New Reno: additive increase
TCP BBR: gain cycling and filters