## Slide 1
Lecture 20, Computer Networks (198:552)
Fall 2019
Multi-Path Congestion Control

## Slide 2: Review: TCP congestion control
Keep some in-flight (un-ACK’ed) packets: congestion window
Adjust window based on several algorithms:
  Startup: slow start
  Steady state: AIMD
  Loss: fast retransmission, fast recovery
Classically, TCP uses a single path provided by the underlying network routing

## Slide 3: If a TCP conn could use multiple paths…
Better resilience
  If one path becomes unavailable, keep traffic flowing over others
Higher throughput
  Use multiple paths to overcome single-path bottlenecks
Seamless mobility
  More paths as they become available, “handing off” as needed
Example uses
  Mobile phone (WiFi/cellular)
  High-end servers (multiple NICs)
  Data centers (many paths available)
Goal: Do all this without application-level changes

## Slide 4: TCP throughput equation
Steady-state behavior

## Slide 5: Model of single-path TCP
AIMD: W := W + 1 (RTT), W := W/2 (drop)
Only a single flow using the bottleneck link
Congestion
Window
halved
Loss
time

## Slide 6: Model of single-path TCP
Idealization: Repeat exactly same window evolution over multiple epochs of a single packet loss
Congestion
Window
halved
Loss
time
Epoch

## Slide 7: Model of single-path TCP
Window goes from Wmin to 2 * Wmin
Loss rate p: number of packets dropped per packet sent
Congestion
Window
halved
Loss
time
Wmin
2Wmin

## Slide 8: Model of single-path TCP
Loss rate assumed to be independent of sending rate
  In reality: more you send, more links traversed, more you drop
Loss assumed deterministic (e.g., buffer full)
  In reality: AQM, stochastic channel loss (e.g., cellular)
Congestion
Window
halved
time
Wmin
2Wmin

## Slide 9: Model of single-path TCP
Goal: Find TCP’s throughput as a function of link rate, RTT, and packet loss rate
Throughput = (#packets sent per epoch) / (time per epoch)
Congestion
Window
halved
time
Wmin
2Wmin

## Slide 10: TCP throughput equation
Throughput depends inversely on sqrt of loss rate, p-1/2
  Throughput drops steeply with increasing loss rate
  Ideal: want it to be linear drop, ie: C*(1-p)
Throughput depends inversely on the RTT
  An issue known as RTT unfairness: lower-RTT connection on a bottleneck gets higher throughput than higher-RTT connection
  Ideal: independent of RTT
Is throughput independent of the link rate and buffer size?

## Slide 11: Multipath TCP
Design of the congestion control algorithm
Slides adapted from Damon Wischik’s

## Slide 12: Goal #1: Fairness at Shared Bottlenecks
Why not just open multiple TCP connections?
To be fair, Multipath TCP should take as much capacity as TCP at a bottleneck link, no matter how many paths it is using.
A multipath TCP flow with two subflows
Regular TCP
Notes: This is the very first thing that comes to mind with multipath TCP, and it’s something that many other people have solved in different ways.
This is just a warm-up... Design Goal 3 is a much “richer” generalization of this goal, which accommodates different topologies, different RTTs. So there’s no point giving an evaluation here.

## Slide 13: Goal #2: Use Efficient Paths
Each flow has a choice of a 1-hop and a 2-hop path.
How should each flow split its traffic?
12Mb/s
12Mb/s
12Mb/s
Notes: I’m thinking of the paths as given. MPTCP has the choice of how to split its traffic over those given paths.

## Slide 14: Use Efficient Paths
Equal-window TCP (EWTCP): split flow traffic 1:1 over paths
Achieve fairness using Ws := Ws + a (RTT), a < 1
8Mb/s
8Mb/s
8Mb/s
12Mb/s
12Mb/s
12Mb/s

## Slide 15: Use Efficient Paths
Move some traffic to better paths:
What if each flow split its traffic 2:1?
9Mb/s
9Mb/s
9Mb/s
12Mb/s
12Mb/s
12Mb/s

## Slide 16: Use Efficient Paths
Best: Each connection on its one-hop path
 Least congested path
12Mb/s
12Mb/s
12Mb/s
12Mb/s
12Mb/s
12Mb/s

## Slide 17: Use Efficient Paths
Goal: Get each flow to send all its traffic on the least-congested path
Achieve by coupling the subflow TCP window updates
Ws := Ws + 1/Wtotal (ack), Ws := Ws – Wtotal/2 (drop)
12Mb/s
12Mb/s
12Mb/s
12Mb/s
12Mb/s
12Mb/s

## Slide 18: Use Efficient Paths
Ws := Ws + 1/Wtotal (ack), Ws := Ws – Wtotal/2 (drop)
Consequence: the more drops a subflow sees, the faster its window Ws reduces (note: increments same across all paths)
More lossy paths have zero window in the limit
12Mb/s
12Mb/s
12Mb/s
12Mb/s
12Mb/s
12Mb/s

## Slide 19: Use Efficient Paths
Ws := Ws + 1/Wtotal (ack), Ws := Ws – Wtotal/2 (drop)
Consequence: Remaining paths have balanced loss rate  equal window if RTTs same
If loss not balanced, window would drop to zero
12Mb/s
12Mb/s
12Mb/s
12Mb/s
12Mb/s
12Mb/s

## Slide 20: Coupled CC can get trapped
Keep a little traffic on each path (even if congested) to probe for capacity always
i.e., keep your options open 

## Slide 21: Coupled CC can get trapped
Semi-coupled TCP
Ws := Ws + a/Wtotal (ack), Ws := Ws – Ws/2 (drop)
Compare with coupled:
Ws := Ws + 1/Wtotal (ack), Ws := Ws – Wtotal/2 (drop)

## Slide 22: Goal #3: Be Fair Compared to TCP
Least-congested paths may not be best
  Low loss rate, but low throughput due to differences in RTT
Example: Two paths
  WiFi: high loss, low RTT
  Cellular: low loss, high RTT
Using the least-congested path
  Choose the cellular path, due to low loss
  But, the RTT is high
  So throughput is low!
Formalize fairness requirement using actual throughput

## Slide 23: Be Fair Compared to TCP
To be fair, Multipath TCP should give a connection at least as much throughput as it would get with a single-path TCP on the best of its paths, given the same loss rate
  Ensure incentive for deploying MPTCP
A Multipath TCP should take no more capacity on any path (or collection of paths) than if it was a single-path TCP flow using the best of those paths, given the same loss rate
  Do no harm

## Slide 24: Achieving These Goals
Regular TCP
  Maintain a congestion window w
  On an ACK, increase by 1/w (increase 1 per window)
  On a loss, decrease by w/2
MPTCP
  Maintain a congestion window per path ws
  On an ACK on path s, increase ws
  On a loss on path s, decrease by ws/2
How much to increase ws on an ACK?
  If s is the only path at that bottleneck, increase by 1/ws

## Slide 25: If Multiple Paths Share Bottleneck?
Don’t take any more bandwidth on a link than the best of the TCP paths would
  But, where might the bottlenecks be?
  Multiple paths might share the same bottleneck
  This is hard to know across the Internet
So, consider all possible subsets of the paths
  Set R of paths
  Subset S of R that includes path r
E.g., consider path 3
  Suppose paths 1, 3, and 4 share a bottleneck
  … but, path 2 does not
  Then, we care about S = {1,3,4}

## Slide 26: Achieving These Goals
What is the best of these subflows achieving?
  Path s is achieving throughput of ws/RTTs
  So best path is getting maxs(ws/RTTs)
What total bandwidth are these subflows getting?
  Across all subflows sharing that bottleneck
  Sum over s in S of ws/RTTs
Consider the ratio of the two
  Increase by less if many subflows are sharing
And pick the results for the set S with min ratio
  To account for the most paths sharing a bottleneck

## Slide 27: MPTCP Implementation

## Slide 28: Implementation Issues
Buffer space: per-subflow or shared for entire connection?
Reassembly across multiple paths
  Different sequence spaces across subflows
  But shared flow control
  Ensure packets across subflows reach at approx. the same time
Middleboxes
  Avoid impact due to rewritten sequence numbers
Initiating new subflow: new TCP flag; auth token