## Slide 1: The Transport Layer: Reliability
CS 352, Lecture 7, Spring 2020
http://www.cs.rutgers.edu/~sn624/352
Srinivas Narayana

## Slide 2: Course announcements
Project 1 released. Need partners?
Quiz 2 completed, no quiz 3
Mid-term 1 next Wednesday
  In class, 1 h 20 m
  Covers lectures 1 through 8 (coming Friday)
  Closed book
  Only calculators allowed. No cell phones
Pattern: multiple choice, reasoning, problem solving
  A review will be released later this week

## Slide 3: Review of concepts
Mail access protocols: POP, IMAP, HTTP
Transport-layer protocols: UDP, TCP
Support communication between processes
  vs. network layer: endpoints
Transport guarantees: reliability, ordering, performance
  You get two of these at most
Demultiplexing: map packet to app-level socket
User Datagram Protocol (UDP): thin wrapper around net layer
  Connectionless, best-effort service, simple
  Demultiplex using dst IP address, dst port
  Who uses UDP?

## Slide 4: Error Detection
Necessary, but insufficient, for reliability

## Slide 5: Data may get corrupted along the way…
Bits flipped from 01 or 10
Packet bits lost
How to detect errors?
Idea: compute a function over the data
  Store the result along with the data
Function must be easy to compute
Function & stored data efficient to verify
Ideas for functions?
source port #
dest port #
32 bits
application
data
(message)
UDP segment format
length
checksum

## Slide 6: From the UDP specification (RFC 768)
Checksum is the 16-bit one's complement of the one's complement sum of a pseudo header of information from the IP header, the UDP header, and the data, padded with zero octets at the end (if necessary) to make a multiple of two octets.
The pseudo header conceptually prefixed to the UDP header contains the source address, the destination address, the protocol, and the UDP length.

## Slide 7: UDP Checksum
Sender:
treat segment contents as sequence of 16-bit integers
checksum: addition (1’s complement sum) of segment contents
sender puts checksum value into UDP checksum field
Receiver:
compute checksum of received segment
check if computed checksum equals checksum field value:
NO - error detected
YES - no error detected.

## Slide 8: UDP checksum example
Note: when adding numbers, a carryout from the most significant bit needs to be added to the result
Example: add two 16-bit integers
1 1 1 1 0 0 1 1 0 0 1 1 0 0 1 1 0
1 1 1 0 1 0 1 0 1 0 1 0 1 0 1 0 1
1 1 0 1 1 1 0 1 1 1 0 1 1 1 0 1 1
1 1 0 1 1 1 0 1 1 1 0 1 1 1 1 0 0
1 0 1 0 0 0 1 0 0 0 1 0 0 0 0 1 1
wraparound
sum
checksum

## Slide 9: User Datagram Protocol
A thin shim around best-effort network delivery
  Lightweight to send one-off request/response messages
  Lightweight transport for loss-tolerant delay-sensitive applications
Provides basic multiplexing/demultiplexing for applications
No reliability, performance, or ordering guarantees
  Need Transmission Control Protocol (TCP)
Can do basic error detection (bit flips) using checksums
  Error detection is a necessary condition for reliability
But need to do a lot more to achieve reliable data delivery
  Subject of the rest of this lecture
  Mechanisms in general; some of them implemented in TCP

## Slide 10: Reliable data delivery
Stop and Wait

## Slide 11: Packet loss
Sender
Receiver
How might a sender and receiver ensure that data is delivered reliably (despite some packets being lost)?
TCP uses three mechanisms

## Slide 12: Coping with packet loss: (1) ACK
Key idea: Receiver returns an acknowledgment (ACK) per packet sent
If sender receives an ACK, it knows that the receiver got the packet.
Sender
Receiver
ACK
packet
ACK
packet

## Slide 13: Coping with packet corruption: (1) ACK
ACKs also work to detect packet corruption on the way to the receiver
  A receiver could send a negative acknowledgment, or a NAK, if it receives a corrupted packet
TCP only uses positive acknowledgments (ACKs).
What if a packet was lost and ACK never arrives?
Sender
Receiver
NAK
packet
ACK
packet

## Slide 14: Coping with packet loss: (2) RTO
Key idea: Wait for a duration of time (called retransmission timeout or RTO) before re-sending the packet
In TCP, the onus is on the sender to retransmit lost data when ACKs are not received
Note that retransmission works also if ACKs are lost or delayed
Sender
Receiver
ACK
RTO

## Slide 15: Coping with packet loss
Sender
Receiver
ACK
RTO
What if ACKs are delayed?
  Sender may retransmit the same data
  Receiver wouldn’t know that it just received duplicate data from this retransmitted packet
Add some identification to each packet to help distinguish between adjacent transmissions
  This is known as the sequence number
Duplicate
packet received!
(Receiver doesn’t know…)

## Slide 16: Coping with packet loss: (3) Seq nums
Sender
Receiver
ACK
RTO
Bad cases: packet dropped or ACK dropped or ACK delayed beyond RTO
Sequence numbers of adjacent transmitted packets are exactly the same!
  Receiver can disambiguate a fresh packet from a retransmission
Duplicate
can be detected using repeated sequence number
0
0

## Slide 17: Coping with packet loss: (3) Seq nums
Sender
Receiver
ACK 1
RTO
Good case: packet received and ACK received within the RTO
Sequence numbers of adjacent transmitted packets are different
Q1: where are the sequence numbers written to, exactly?
Q2: what is the seq# of third packet?
Not duplicate, because sequence numbers are different
0
1
ACK 0
???
RTO

## Slide 18: Stop-and-Wait Reliability
Scheme so far: sender waits for an ACK/RTO before sending another packet
  Also called “stop and wait” reliability
Suppose no packets are dropped
  Round-trip-time: 100 milliseconds
  Packet size: 12,000 bits
  Link rate: 12 Mega bits/s
At what rate is the sender getting data across to the receiver?
Sender
Receiver
RTT
120 Kilo bit/s (1% of link rate)
RTO

## Slide 19: Reliable data delivery
Pipelined Transmission, a.k.a. Sliding Window Protocols

## Slide 20: Amount of “in-flight” data
We term the amount of unACKed data as data “in flight”
With just one packet in flight, the data rate is limited by the packet delay (RTT) rather than available bandwidth (link rate)
Idea: Keep many packets in flight
  Also referred to as pipelined transmission
More packets in flight improves throughput
  Throughput is the amount of data delivered per unit time.

## Slide 21: Keeping many packets in flight
With link rate 12 Mega bits/s and packet size 12,000 bits, what is the transmission delay of a single packet?
Remember the earlier throughput of 120 Kbit/s. If there are, say 4 packets in flight, throughput is 480 Kbits/s!
We just improved the throughput 4 times by keeping 4 packets in flight
Sender
Receiver
RTT
RTO

## Slide 22: TCP is a pipelined transmission protocol
Sender allows multiple, “in-flight”, yet-to-be-acknowledged packets
A few packets aon the way while, concurrently, new packets are transmitted

## Slide 23: What if some packets/ACKs dropped?
Sequence numbers help associate an ACK with its packet
  Note: In TCP, every byte has a sequence #
  We will often simplify our examples by assuming each packet has a sequence #
In TCP, the ACK contains the sequence number of the next byte expected
  Note: example uses packet seq #s
Q1: If a packet is dropped, should the receiver ACK subsequent packets?
  Q2: If so, with what sequence number?
Sender
Receiver
1
2
3
4
2
3
4
5
5

## Slide 24: Receiver strategies upon packet loss
Sender
Receiver
1
2
3
4
5
ACK subsequent pkts?
Go-back-N
Selective Repeat
What seq # on ACK?
Last pkt in order
Cumulative ACK
Seq # ranges received so far
Selective ACK
No
Yes
TCP’s default

## Slide 25: Sliding Window with Go Back N
When the receiver notices a missing or erroneous frame:
It simply discards all frames with greater sequence numbers
  The receiver will send no ACK
The sender will eventually time out and retransmit all the frames in its sending window

## Slide 26: Go back N
Discarded by
receiver
Frame with
error
Timeout interval
ACK 0
Time
Sender
Receiver
Maximum
window size = 8
Maximum
window size = 8
0
0
1
1
ACK 1
2
E
3
D
4
D
2
3
2
ACK 2
4
5
6
3
4
5
ACK 3
ACK 4
ACK 5
6
ACK 6

## Slide 27: Go Back N (cont’d)
Go Back N can recover from erroneous or missing frames
But…
It is wasteful. If there are errors, the sender will spend time retransmitting frames the receiver has already seen

## Slide 28: Selective repeat with cumulative ACK
Idea: sender should only retransmit dropped/corrupted segments.
The receiver stores all the correct frames that arrive following the bad one. (Note that the receiver requires a memory buffer for each sequence number in its receiver window.)
When the receiver notices a skipped sequence number, it keeps acknowledging the last good sequence number,. i.e., cumulative ACK
When the sender times out waiting for an acknowledgement, it just retransmits the one unacknowledged frame, not all its successors.

## Slide 29: Selective repeat
Buffered by
receiver
Frame with
error
Timeout interval
ACK 0
Time
Sender
Receiver
Maximum
window size = 8
Maximum
window size = 8
0
0
1
1
ACK 1
2
E
3
4
2
5
2
ACK 4
6
5
ACK 5
6
ACK 6
3
4
NACK 2
NACK 2

## Slide 31: Keeping track of packets (and ACKs)
Cumulative ACKs: ACK the latest seq# up to which all packets received
Selective ACKs: return one cumulative seq# and ranges of other seq# received
Sender retransmits those packets whose sequence numbers haven’t been ACKed
What are the implications of selective vs. cumulative ACKs here?
Sender
Receiver
1
2
3
4
1
2
3
4
5

## Slide 32: How should the RTO be set?
Clearly, RTO must be related to RTT
  But how exactly?
Sender
Receiver
1
2
3
4
1
2
3
4
5
RTT
RTO